## Slide 1: CCVPN Support for Intent

## Slide 2
Timeline of CCVPN and its relation with Net Slicing and IBN use-case
CCVPN Use-case
ONAP Releases
Year 2018
Frankfurt
Guilin
Honolulu
El Alto
Developed CSMF and NSMF
Transport Slicing solution, integrated with E2E NS in Guilin
Year 2019
Year 2020
Year 2021
Dublin
Casablanca
Beijing
Istanbul
May 2018
June 2019
Sept 2019
June 2020
Phase III
Phase I
E2E Network Slicing Use-case
Phase II
Phase I
Phase IV
Phase II
Phase III
Developed AN, TN, CN NSSMF
Achieved E2E network slicing across AN, TN, and CN
Modify and reuse of existing NSI and NSSI
Phase IV
Nov2020
May2021
Developed multi-domain L2 Service (EPL and EVPL service creation)
Developed Multi-domain L1 Service (OTN service creation)
Implemented both IETF/ACTN L1 and MEF/ONF L1 (i.e., MDONS use-case)
Modify/reuse of existing TN NSSI (Honolulu)
FAN+OTN for cloud leased private line service
Intent support for CCVPN
IBN use-case
Phase I
Phase II

## Slide 3
Background (1): CCVPN developed as ESTI ZSM Management Domain
CCVPN can be implemented as a Transport Management Domain, which offers management services via standardized interfaces and also offers closed loop capability.
This modular design enables CCVPN services to be consumed by or work with other usecases. E.g., The IBN usecase can consume CCVPN management services to deliver a complete E2E intent solution.
Transport management services exposed by CCVPN to its consumers.
Closed loop

## Slide 4
Background (2): Intent-based Networking Concepts
[1] https://tools.ietf.org/html/draft-irtf-nmrg-ibn-concepts-definitions-03
Based on draft-irtf-nmrg-ibn-concepts-definitions [1]:
Intent Fulfillment
  Intent ingestion and interaction with users
  Intent translation
  Orchestration: configure/provision
Intent Assurance
  Performance data monitoring
  Intent compliance assessment
    continuously monitor & compare actual vs. intended configs
  Intent compliance actions: learn/plan/render
  Abstraction and reporting
Intent Control Loops
  “Inner” loop: classic zero-touch closed loop within a management domain
  “Outer” loop: E2E service manage domain closed loop; intent exchange – involves end user

## Slide 5
How IBN and CCVPN work together to offer an E2E intent solution
[1] https://tools.ietf.org/html/draft-irtf-nmrg-ibn-concepts-definitions-03
SO
SDNC
Domain network controllers
AAI
CPS
Policy
Holmes
DCAE
ONAP CCVPN
ONAP IBN
ZSM Management services exposed by CCVPN

## Slide 6: Proposed CCVPN Architecture as Transport MD supporting Intent
SO
SDNC
Domain network controllers
AAI
CPS
Policy
DCAE
AI analytics algorithms
Closed loop
Network performance data and events
Network service config
ONAP IBN
CCVPN
Transport domain Control & orchestration
Transport domain analytics
Intent service creation flow
CCVPN (or Transport MD) offers the so-called “Service Intent”. Its NBI is a model-driven, intent-like interface. And it enables closed-loop to support service assurance.
IBN and CCVPN, when federated together, may offer the complete implementation of an Intent-Based System (IBS).

## Slide 7: Cloud Leased Line Use-case
Enterprise/campus network
CE
OLT
CO
Cloud PE
Cloud PE
Cloud PE
Cloud 3
Cloud POP
Cloud 2
Cloud POP
Cloud 1
Cloud POP
Access network
Core network
One VPN service that connects an enterprise network to multiple clouds
Multiple VPNs can co-exist (service isolation; performance monitoring)

## Slide 8: CCVPN Support for Cloud Leased Line (CLL)

## Slide 9: Intent Fulfillment for Cloud leased line (CLL)
SO
SDNC
Domain network controllers
Intent Fulfillment call flow
ONAP IBN
Intent-based API (technology agnostic)
ONAP Internal API
ACTN MPI
Physical network
CLL definition model
CLL implementation models
AAI
2
3
4
5
6
user
1
7
User expresses his/her intent (in natural language? )
IBN does Intent Translation and maps natural language into the parameters needed by the CLL definition model (i.e., Intent model of CLL)
IBN calls SO NBI passing intent model parameters
SO creates CLL definition model based on the input parameters
SO calls SDNC for CLL service provisioning
SDNC renders CLL definition model into implementation models and writes them into AAI
SDNC calls Domain Network Controllers, based on the implementation models, to configure the physical network

## Slide 10: CCVPN closed-loop design (based on ZSM 009)
SO
SDNC
AAI
Policy
DCAE
D2E
decision
M2A
monitoring
A2D
analysis
E2M
execution
data
Closed loop control flow contains the following stages:
M2A (monitoring): SDNC receives (or collects) telemetry and performance data from the domain network controllers, and forwards the data to DCAE
A2D (analysis): DCAE performs data analytics on the received data changes, and generates and sends the data insights to Policy
D2E (decision): Policy makes the decision on how to modify the existing services based on the data insights and calls SO to make service modification
E2M (execution): SO executes the service modification by instructing SDNC to apply new network configurations to domain controllers
Service creation
Data collector
Domain controllers

## Slide 11: Putting together: Intent-based system for Cloud Leased Line usecase
“Inner” intent loop
control
orchestration
intelligence
analytics
data collection
CCVPN
IBN
Input/recognize
instantiate
translate
verify
report
Cloud leased line network configurations
“Outer” intent loop

## Slide 12
Thanks!

## Slide 13: Backup

## Slide 14
Applicability of Intent CCVPN: Network Slicing usecase
https://www.itu.int/en/ITU-T/Workshops-and-Seminars/2019101416/Documents/Intent%20Based%20Networking%20the%20technology-ITU.pdf
“E2E Network Slicing is too complex, transport part of it is a perfect candidate for intent based network”
CCVPN “inner” intent loop
ONAP IBN “outer” intent loop