## Slide 1: 5G Network Deployment, Slicing, Network Optimization and Automation Framework – Use Case Deep Dive
5G Use Case Team

## Slide 2: Contributors:
Supporting Companies
Contributing Members
Alla Goldner | Kaniz Mahdi | Erik Westerberg
Trung Nguyen | Tim Strickland | Oskar Malm
Karpura Suryadevara | Paul Bullock | Peter Loborg
Vimal Begwani | Denis Fluet | Vivien Yang
Shekar Sundaramurthy | Todd Morris | Ranjit Cavatur
Tom Tofigh | Alex Dodin | Rajesh Gadiyar
Gil Bullard | Rodney Wilson | Eng Wei Koo
Sarat Puthenpura | Raghu Ranganathan | Dmitriy Andrushko
Cagatay Buyukkoc | Stephen Terrill | George Lapiotis
Slawek Stawiarski | John Quilty | Vladimir Yanover

## Slide 3: Business Drivers:
5G and network slicing are emerging technologies that are complex and distributed
Multiple service providers are getting ready to deploy
This will help 5G technology vendors to understand ONAP requirements and deliver PNF / VNF capabilities that can be managed using ONAP
This use case is expected to:
    Enhance ONAP platform capabilities for supporting hybrid network consisting of PNFs & VNFs in a multi-domain (RAN vs WAN vs EPC) scenario
    demonstrate use of ONAP platform to realize following:
      A planned list of 5G Nodes are on-boarded into ONAP, and ONAP configures the Nodes to the level they are ready to handle traffic. ONAP begins to actively monitor and manage the nodes
      CRUD operations on RAN-only slice(s) and RAN-to-EPC slice(s)
      Optimizations of 5G & E2E Slice, Slice Segment, etc.

## Slide 4: Scope of Use Case
Onboard, Deploy & Manage Disaggregated 5G Radio Access Network Elements
Design, Deploy and Manage Network Slices Supporting Multiple Services
Enhance ONAP Platform to Create an Open Environment for Optimization of Network / Services / Slices using µServices from Multiple Sources
A
B
C

## Slide 5: A: 5G Radio Access Network
Requirement Statement
The use case describes a Service Provider (SP) need to deploy a disaggregated 5G Radio Access Network (3GPP 5G Option 2-2 configuration). Some of the disaggregated network functions are expected to be virtualized (VNF), running on a cloud infrastructure and while others will be PNF (e.g. appliance based peripherals)
The network elements in scope for such a disaggregated 5G RAN (in this release) are:
  Distributed Radio Element
  Distributed BBU
  Virtualized Centralized BBU and nrt-L2 function (CU-UP)
  Virtualized Centralized Radio Control Unit (CU-CP)
This disaggregation can include moving processing closer to the edge, and require deployment of Multi-access Edge Computing (MEC) components and applications in order to meet 5G performance goals
An Illustrative Example of Disaggregated Radio Access Network
Distributed Radio Unit
(UP + CP)
Distributed BBU-DU, L1+L2rt Function (UP+CP)
Virtualized BBU-CU & UP
L2nrt Components
Virtualized Radio Control Function (CU-UP)

## Slide 6: A: 5G Radio Access Network Deployment
ONAP Design Platform Requirements:
Onboard SW packages, descriptors and any other artefacts provided by the RAN vendor
Design RAN-level templates, recipes and workflows covering common network elements, transport network, data collection and analytics, policies and corrective actions
Design node-level templates, recipes and workflows covering network elements (PNFs and VNFs), transport network, placement or QoS constraints, data collection and analytics, policies and corrective actions
Service Design
1
Verify Design
2
Deploy Shared Services
3
Verify templates and recipes from step 1, using dedicated test environment or limited trial following steps below. If necessary, make adjustments accordingly to step 1
Distribute the completed design as well as vendor-provided artefacts to the various run-time components

## Slide 7: A: 5G Radio Access Network Deployment – Continued
ONAP Execution Platform Requirements:
On receiving service instantiation request via Portal or external API, SO will decompose the request, and allocate and connect the various resources
A sub-flow includes the onboarding process for related PNFs
In this step node-specific data from planning is also inserted
Application Controller will Configure RAN VNF / PNF in scope
Update Inventory and VNF / PNF State in AAI
DCAE will start fault, performance, and log data collection as described during design time
DCAE will perform data analytics as configured in recipes, to monitor the environment and detect anomalous conditions. Output from analytics is forwarded to Policy and dashboard
Instantiate 5G Radio Access Network
4
Verify Operation
5
React to Incident
6
Verify that service is provided and can be monitored through dashboard using basic observability data and calculated KPIs
Corrective/remedial action for network impairments or for violations of service levels as described by defined policies are initiated using the SO and/or controllers
For verification purposes this may require fault injection
Verify that policy definitions and their corrective actions have intended effect

## Slide 8: B: Slice & Service Definition, Deployment, and Management
Requirement Statement
Each Service Provider (SP) needs to support a rich set of advanced 5G wireless services, such as enhanced Mobile Broad Band (eMBB), massive Internet of Things (mIoT), and Ultra-Reliable, Low-latency Communications (URLLC ), for mission critical communications
These services have very different requirements on latency, reliability, availability, mobility, and bandwidth
Deploying multiple separate networks to support these varying requirements is not practical
End to End network slicing as defined by 3GPP provides specifications for efficient creation of multiple logical networks sharing a common network infrastructure while meeting the specified service levels for each of the services
ONAP must support the complete lifecycle management of such network slicing
Automated configuration of a slice during the instantiation, configuration, and activation phases, a newly created set of identifying parameters collection is automatically configured
Automated reconfiguration happens during run-time e.g. an active slice can be reconfigured automatically because of a change in the service requirements or service conditions

## Slide 9: B: Terminology and Abbreviations
Term | Definition
Network Slice | A logical network that provides specific network capabilities and network characteristics
Network Slice Instance (NSI) | A set of Network Function instances and the required resources (e.g. compute, storage and networking resources) which form a deployed Network Slice NSI contains Core Network part and Access Network part
NSSI | Network Slice Subnet Instance
NST | Network Slice Template
NSST | Network Slice Subnet Template
NSMF | Network Slice Management Function
NSSAI | Network Slice Selection Assistance Information
PNF | Physical Network Function
DP | Data Plane
OOB | Out of Band

## Slide 10: B: Slicing – Network Architecture
Access Network
Core Network
Communication Services
Service 1
Service 2
Service 3
NSSI - Best Effort
NSSI - Normal
NSSI - Premium
NSSI - HB
NSSI - Normal
NSI A
NSI B
NSI C

## Slide 11: B: Network Slice Support
Key Assumptions & Observations
In order to enable both an e2e service view and re-usable services from the different segments/domains in the network, the design must be done in such a way as to support:
    Abstraction of the services offered by the different domains/segments
        Ability to tie the services offered by the different domains/segments into an e2e service
        Support the network to provide isolation of physical resources and between the slices (to the extent that is reasonable according to the networks capabilities)
In order simplify the use case, a network plan containing only a few participating network elements will be used

## Slide 12: B: Slice Definition and Design:
ONAP Design Platform Requirements
The ONAP Service Designer define TOSCA templates for the reusable tasks, examples could be:
    Create a VLAN to be used for control and user data within an NSI
    Per CN node type: Create template connect to the proper VLAN
    Per RAN resource to be shared (e.g. the EUtranCell): Reconfigure to use yet another PLMN and a specific VLAN for that PLMN
    Create a CN NSSI using provided VLAN tags and PLMNI-ID value with a specified “capacity” (the “capacity” value to be used to select number of CN nodes to spin up). This also includes filtering or aggregation rules for DCAE to produce NSSI related FM/PM/Event data.
    Create a RAN NSSI template using provided VLAN tags and PLMN-ID covering a specified set of cells.
    This also includes filtering or aggregation rules for DCAE to produce NSSI related FM/PM/Event data.
    Create a Service model for NSI used to instantiate, modify, and remove.
    This also includes filtering or aggregation rules for DCAE to produce NSI related FM/PM/Event data, aggregating that data into KPI values for SLA evaluation.

## Slide 13: B: Slice Instantiation & Monitoring
ONAP Execution Platform Requirements
  Service Operator Initiates Creation of one or more Needed Slice Segments (NSSI) in Radio Access Network
    Orchestrator executes Slice Segment Creation / Modification recipe
    Pass configuration specifications, as per abstraction standards, to RAN controller for radio slice segment created
  Service Operator Initiates Creation of one or more Needed Slice Segments (NSSI) in Core Network
    Orchestrator executes Slice Segment Creation / Modification recipe
    Pass configuration specifications, as per abstraction standards, to App-C controller for EPC Slice Segment Creation
  Service Operator Initiates Creation of E2E Slice Segment
    Establish net VLAN connectivity
    Pass QoS, bandwidth, resiliency requirements for transport network to SDN-Controller
  Start data collection and SLA / SLO monitoring with right DCAE(s)
    Monitor Needed KPI / Counter to Monitor Each Slice Segment and Compute Needed SLA / SLO Values
    Take Needed Corrective Action when SLA / SLOs are violated by any Slice Segment
    Compute and Validate SLA / SLO for active E2E slices and Services
    Take Needed Corrective Action when SLA / SLOs are violated by any Slice Segment

## Slide 14: C: Optimization Framework Need
Requirement Statement
Service Provider (SP) must, in real-time, optimize the performance of the 5G Radio Access Network (RAN)
This optimization may be effected via dynamic configuration of relevant 5G radio and backhaul network parameters
Such optimization is part of the so-called “Self-Organized Networking” or SON
ONAP will enable the design and implementation of an open SON ecosystem for 5G RAN optimization by providing a common open framework
    Enables multiple identity (Vendor, Open Source, SPs, etc.) to design & implement their SON solutions using Open ONAP Platform
    ONAP must provide facilities for managing and coordinating the concurrent application of multiple independently developed and deployed these algorithms, identifying, avoiding or resolving conflicts that might arise
      Conflict Resolution Must be Done at Design as well as Execution Time (Not all conflicts can be identified and resolved during design time)

## Slide 15: C: RAN Network & Slice Optimization:
ONAP Design Platform Requirements
The ONAP Design Studio (SDC) must support the following Capabilities:
Design per slice segment Data Collection, Analytics, SLA / SLO calculations
Design E2E Slice & Services Analytics and SLA / SLO calculation
Define policies / anomalies that indicate sub-optimal slice segment / E2E slice, and service performance
Define policy evaluation to identify best possible slice / slice segment and service optimization action(s)
Create recipes for addressing slice / slice segment performance degradation
Design data collection and analytics for various network optimization functions
Define policies / anomalies that indicate sub-optimal network performance
Define policy evaluation to identify the best possible optimization action(s)
Define SON coordination policies for the prevention, detection and resolution of conflicts or negative interactions of individual SON functions
Create recipes for executing network optimization steps (e.g. new configurations for RAN elements)

## Slide 16: C: RAN Network & Slice Optimization:
ONAP Execution Platform Requirements
ONAP execution framework should provide all needed support to the optimization micro-services developed by multiple organizations:
    Access to the network performance data via certain DCAE instances
    Access to historical data when needed
    Access to the analytics needed for SON operations e.g. for computation of the KPIs and KQIs that are targeted in the optimization and/or involved in optimization conditions (restrictions). The micro services (MSs) implementing such analytics can be directly called or set to generate an event if/when certain condition is met
    Access to the configuration management (controllers) in the network domains where the SON actions are executed
    Access to the policies, defined by the operator, that influence (e.g. restrict) execution of SON actions

## Slide 17: ONAP Platform Impact:
Functional Platform Requirements | SDC | AAI | SO | SDN-C | APP-C | Portal | DCAE | Policy | OOF
Support for PNF - Onboarding |  |  |  |  |  |  |  |  | 
Support for PNF - Configuration & Control |  |  |  |  |  |  |  |  | 
Support for PNF - Data Collection & Monitoring |  |  |  |  |  |  |  |  | 
Slice Management - Definition |  |  |  |  |  |  |  |  | 
Slice Management - Composition |  |  |  |  |  |  |  |  | 
Slice Management - Orchestration & Control |  |  |  |  |  |  |  |  | 
Slice Management - Data Collection & Monitoring |  |  |  |  |  |  |  |  | 
Optimization - Onboarding |  |  |  |  |  |  |  |  | 
Optimization - Configuration & Control |  |  |  |  |  |  |  |  | 
Optimization - Data Collection & Monitoring |  |  |  |  |  |  |  |  | 
Optimization - Conflict Resolution |  |  |  |  |  |  |  |  | 
OOF - Multi-cloud |  |  |  |  |  |  |  |  | 
OOF - Optimization |  |  |  |  |  |  |  |  | 
New / Enhancement
Applicable to Slicing Subcase Only

## Slide 18: ONAP R2+ Architecture – Current Draft View
Run-time
Infrastructure
OpenStack
Azure
VMware
RackSpace
Peripherals
Design-time (SDC)
Policy Creation & Validation
Analytic Application Design
Recipe / Engineering Rules & Policy Distribution
VNF/PNF SDK
ONAP Portal – Design Studio & Dashboard
Resource Onboarding
Service & Product Design
OSS
BSS
Catalog
Products
Resources
Eng. Rules
Services
Policies
Analytics
Testing & Certification
ONAP Operations Management (OOM)
External Data Movement & APIs
Common
Services
Micro Services Bus
DMaaP
AAF
Logging
Data Collection Layer
Data & Analytics (DCAE)
Data Distribution
CDAP
Holmes
DCAE Analytic µServices
Policy Execution Engine
Resource / Service Topology
Active / Available
Entitlements
Inventory/Topology (AAI)
…
Policy
ESR
Orchestration (SO)
sVNFM
sVNFM
sVNFM
VNF2
VNF1
VNF3
VNFn
PNF 1
…
Adaption Layer
Service Logic
Interpreter
Config
Database
Yang
Netconf
CLI
Life Cycle Mgmt Func
L0-3 Network Controller (SDN-C)
3rd Party Network
controller
Config Database
Standard Adaption Layer
Service Logic Interpreter
Life Cycle Mgmt funcs
Chef
Netconf
Ansible
L4-7 Controller (App-C)
Vendor OA&M Adaptor
Vendor
B
Vendor
A
Vendor VNFM
Adaption Layer
(VF-C)
Life Cycle Mgmt funcs
Multi-VIM Interface
Open
Stack
AWS
Azure
MEC
Infrastructure
Adaption Layer
Service Level Orchestration
Resource Level Orchestration
Expand scope of SDK to include PNFs
Enhance SDC to support PNF onboarding, PNF management design, slice / slice segment modeling and management. Network Optimization design and conflict detection / resolution
Enhance SO to support PNF, slice segment and slice instantiation and life cycle management
Enhance AAI to support PNF, slice segment and slice inventory and topology
Expand DCAE to monitor PNF, Slice Segment, E2E slices and services monitoring. Open Platform for hosting optimization micro services
Support run time conflict detection & resolution
VIM to support interfaces to Mobile Edge Cloud (MEC)
App-C & SDN-C to support RAN elements, Slice Segments, E2E slices and services configuration

## Slide 19
Thank You!

## Slide 20
BACKUP SLIDES

## Slide 21: New Challenges in 5G Use Case
Support a hybrid network consisting of PNF & VNF across RAN, WAN and EPC
Support Design, Deploy, Monitor and Management of Network Slice(s)
Design studio (SDC) enhancement
  Component models: e.g., RAN VNFs, Core VNFs, PNFs, etc.
  E2E model(s): e.g. service chain (tosca) topology, policy model(s)
AAI enhancements to capture topology & inventory
SO / App-C / DCAE / Policy enhancements to support for PNF and slice lifecycle management, slice deployment and management
DCAE / Policy enhancements to support open framework for near-real time network optimization, conflict resolution during design time as well as run time across multiple microservices
OOF enhancements to support multi-cloud and 5G network optimizations