## Slide 1
Factory
Software
PNF Bootstrapping Steps
SEGW
Initial
EM
Local
DHCP
DHCP Discover
VLAN Scanning
IPv4/IPv6 discovery
DHCP Response
PNF IP@(m)*, Initial EM IP@ (m), SEGW IP@(o), CA IP@(o)
HW Install
3
1
PNF Restart
Activates SW
2
4
ONAP Bootstrap Software Download
IPSec Tunnel Setup (optional)
8
Identity Service (Identifies NE), Gives ONAP IP@
7
Certificate Enrollment (optional)
5
6
9
Preplanning, Pre-provisioning
CA/RA
*Temporary PNF IP@

## Slide 2
vAAA
SDN-C
vDHCP
PNF Registration Steps (Option 1)
DCAE
PNF
(DU)
AAI
Authenticate & ID PNF
DHCP Response
PNF IP@, DCAE IP@
VES Event contains
PNF ID, PNF IP@, Vendor Name
DHCP Request
This would be the “real” PNF IP@. Maybe the ONAP assigned PNF ID is also returned.
PNF ID could be serial number, MAC address or some other unique identifier to use as the Key for AAI
Not sure of the order of events or who does what between vDHCP, vAAA and SDN-C
Register PNF (Key, IP@)
New PNF DMaap Event
How does this request get to vDHCP and not local DHCP?
10
11
12
13
14
15
OPTION 1

## Slide 3
vAAA
SDN-C
vDHCP
PNF Registration Steps (Option 2)
DCAE
PNF
(DU)
AAI
Register PNF (Key, real IP@)
New PNF DMaap Event
VES Event contains
PNF ID, PNF IP@, Vendor Name
Configure real PNF IP@ (optional)
10
11
13
14
OPTION 2
*May Assign “real” PNF IP@
Authenticate & ID PNF*
12

## Slide 4
SDN-C
APP-C
SO
AAI
PNF Activation Steps
SDC
PNF
(DU)
CU
(VNF)
Inventory Query
Service Configuration (CU IP@)
Service Creation* (PNF ID, CU IP@)
Connection to VNF (DU contacts CU)
Target SW Software Download
CU Configures the DU with operational configuration
DU Restart
DU Restart
1
16
17
18
19
20
21
22
*Happens before or after PNF Registration