## Slide 1: NSI/NSSI Selection based on resource occupancy level

## Slide 2: Important Points
RAN NF NSSI Selection based on capacity level is concentrated on J-release
If RAN NF NSSI is shareable, make an assumption that the RAN NSSI and subsequently the NSI also can be reused. Later, this needs to be enhanced to consider the Core and TN NSSIs. It is applicable for NSI and NSSI selection.
OOF handles this selection process with the help of the details received from DCAE component.
https://wiki.onap.org/pages/viewpage.action?pageId=103420908

## Slide 3: RAN NF NSSI Selection based on resource occupancy level
Subnet: RAN
Radio Resources utilization:
    DL PRB used for data traffic (RRU.PrbUsedDl) & UL PRB used for data traffic (RRU.PrbUsedUl) – Ref. TS 28552
    This data is received from RAN Simulator for a sNSSAI at cell level
    <measData>
    <managedElement localDn="110" swVersion="r0.1"/>
    <measInfo measInfoId="measInfoIsVal">
    <job jobId="5924"/>
    <granPeriod duration="PT900S" endTime="2021-06-06T22:00:56.409"/>
    <repPeriod duration="PT900S"/>
    <measType p="1">SM.PrbUsedDl.01-66645DC8</measType>
    <measType p="2">SM.PrbUsedUl.01-66645DC8</measType>
    <measValue measObjLdn="15289">
    <r p="1">101</r>
    <r p="2">17</r>
    <suspect>false</suspect>
    </measValue>
    <measValue measObjLdn="15290">
    <r p="1">123</r>
    <r p="2">357</r>
    <suspect>false</suspect>
    </measValue>
    …..
gNBDUId
PM types
Cell Id
PM values

## Slide 4: Radio Resources Utilization
PrbUsedDl & PrbUsedUl are calculated at RAN simulator using a simple logic
Each cell is assumed to have certain PRBs and the PRB usage is computed based on the ratio of current slice's throughput (dLThptPerSlice, uLThptPerSlice) per cell
Total PRBs can be fixed as 132 as per the below two tables from TS 38.101-1, TS 38.101-2
FR1 Maximum transmission bandwidth configuration NRB
FR2 Maximum transmission bandwidth configuration NRB
SCS (kHz) | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 70 MHz | 80 MHz | 90 MHz | 100 MHz
 | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB
15 | 25 | 52 | 79 | 106 | 133 | 160 | 216 | 270 | N/A | N/A | N/A | N/A | N/A
30 | 11 | 24 | 38 | 51 | 65 | 78 | 106 | 133 | 162 | 189 | 217 | 245 | 273
60 | N/A | 11 | 18 | 24 | 31 | 38 | 51 | 65 | 79 | 93 | 107 | 121 | 135
SCS (kHz) | 50 MHz | 100 MHz | 200 MHz | 400 MHz
 | NRB | NRB | NRB | NRB
60 | 66 | 132 | 264 | N.A
120 | 32 | 66 | 132 | 264

## Slide 5: Data Aggregation at DCAE and OOF Solution
DCAE - DL Feeder stores the PM data (PrbUsedDl & PrbUsedUl )
When OOF requests DCAE Slice Analysis MS for the utilization details, Slice Analysis MS fetches the PM data from DES for that slice for a week of time to understand the utilization
Convert this to data per unit time and convert it to RAN Configuration (dLThptPerSlice, uLThptPerSlice) using an existing logic in slice Analysis MS
If the RAN NF NSSI is already shared by more than one sNSSAI, the above details should be calculated for all the sNSSAIs and sum it
OOF finds the difference between the actual configuration requested by the operator for this RAN Slice and the current configuration effectively in use
This difference will mean the throughput which can be further supported by the RAN Slice
This value will be checked against the operator requirement for the new slice. If the calculated value is greater than or equal to the new requirement, OOF decides the RAN Slice is a suitable candidate for reuse.

## Slide 6: Steps in brief
Store PM data
  Ran Sim received UL/DL throughput from SDN-R
  No. of PRBs are calculated based on a random value. It should be based on throughput
  send file ready event
  Store the pm data using Feeder
Aggregate the PM data – DCAE SLA MS
  Get the pm data for the slice (RAN NF NSSI ==> more than one sNSSAIs) for one week
  Calculate the average PRB used (UL/DL) ==> current utilization
  PRB <-> throughput conversion
Decision Making - OOF
  Get the throughput actually requested for the RAN NF NSSI
  Calculate the remaining throughput which can be supported by this RAN Slice
  Compare it against the throughput requirement from the slice profile
  Note: Open items are highlighted in yellow

## Slide 7
Thank You!