## Slide 1
CASABLANCA SECURITY ENHANCEMENTS
FOR 5G USE CASE
5G Use Case A : Deployment
5G Use Case C : Optimization
May 2, 2018 v1

## Slide 2
Casablanca 5G Use Cases with Security Impacts
5G Use Case A Deployment : PNF Plug and Play
JSON encoded asynchronous Registration event sent via HTTP/TLS from PNF to DCAE.
SSH from ONAP to PNF for configuration management (CM) using NetConf or Ansible.
5G Use Case C Optimization : Performance Measurements (PM) and Faults
JSON encoded asynchronous Periodic PM event sent via HTTP/TLS from NF to DCAE.
GPB encoded asynchronous Real Time PM event streamed via TLS/TCP from NF to DCAE.
JSON encoded asynchronous Fault event sent via HTTP/TLS from NF to DCAE.
SSH from ONAP to NF for CM using NetConf or Ansible.

## Slide 3
Security capabilities needed in ONAP for Casablanca
HTTP
Create username and password for NF access in ONAP. Secure storage of password.
Provision username and password on NF. Could be out of band manual provisioning on PNF for R3.
Authenticate username and password for HTTP connection in DCAE.
Support integration with Service Provider 3rd Party Identity Management Server (AAA, LDAP) in ONAP.
Note that ONAP is considering eliminating username and password for HTTP when TLS is used.
TLS
Authenticate Vendor or Service Provider certificate for TLS connection in DCAE.
Install Vendor root CA chain in ONAP. Support 3 level chain (Root CA, Sub CA and End-Entity certificates).
Install ONAP root CA chain on NF for mutual authentication. Could be skipped for R3.
CA
Provide CA services to NFs in ONAP for development and testing; enrollment, authentication.
Support certificate management for NF over CMPv2 for real-time certificate enrollment and end-entity key renewal.
Support integration with Service Provider 3rd Party CA/PKI in ONAP.
SSH
Create RSA public/private key pair for ONAP Controllers to use for SSH access into the NF for CM.
Provision SSH public keys on NF for Ansible or NetConf access from ONAP Controllers for CM.

## Slide 4
5G USE CASE C : OPTIMIZATION
Performance Measurements and Faults
5G RAN Periodic Performance Measurements
5G RAN Real Time Performance Measurements
5G RAN Alarms and Events

## Slide 5
Measurements Analyzed
Analytics Application subscribes to PM topics. Data used to assess performance trends to evaluate modifications in parameter settings that will result
in improved performance in the NF or the Network.
Anomaly identified
Analytics Application identifies anomaly in the data and informs Policy that a change in the value of a parameter may be warranted.
Data Collection and Optimization Steps
DCAE authenticates
NF Modeling
Run-Time
NF Provides Measurements
DCAE authenticates connection.
NF sends PM events to DCAE.
NF streams high volume RTPM events via TLS/TCP encoded in a high efficiency format like GPB.
NF sends moderate volume PM events via HTTPS encoded in JSON.
DCAE publishes events to appropriate DMaaP topic.
Design Time
Resource Definition
Service Design
Distribution of service artifacts
PNF discovered/VNF instantiated, configured and put in service. IP address of DCAE VES collector known for event delivery.
Policy determines that optimization of parameters is warranted and informs SO. SO initiates Work Flow and instructs SDN-R to modify config parameters.
SDN-R sends a modify config command to the NF via Ansible, Chef or Netconf.
Optimization Policy Triggered
NF Optimized
G
A
D
E
F
C
B
NF Service Deployment

## Slide 6
SO
DMaaP
Real Time PM and NF Optimization
SDN-R
DCAE
HV VES
Collector
Analytics
Application
PNF
VNF
Modify Config
Modify Parameters
Authenticate connection
Analyzes data
AA notifies Policy of Anomaly
GPB/TLS/TCP
AA gets data
Request that NF Modifies Configuration (change parameter value for optimization)
Policy
Opt workflow
Optimization workflow SO informs SDN-R
Optimization triggered
Policy tells SO to change parameter
SSH
DCAE authenticates new TLS connection using functionality provided by AAF
NF sends PM data in near real time—high volume data to DCAE HV VES Collector GPB/TLS/TCP for performance
Publish Event
DCAE publishes data to DMaaP topic
TLS/TCP
NF sends Real Time PM event
Real Time PM
NF establishes a TLS/TCP connection to the DCAE High Volume (HV) VES Collector.
DCAE authenticates the certificate for TLS. Certificate is X.509v3 and can be a Vendor or Service Provider certificate.
NF sends RTPM Event to DCAE. Event is encoded in GPB and streamed over TLS/TCP. GBP is an efficient binary protocol. TLS/TCP is a persistent connection for the life of the RTPM session.
DCAE publishes the data to an appropriate DMaaP topic.
Analytics Application (AA) retrieves the data from DMaaP. AA analyzes the data and identifies an anomaly that may need action.
AA notifies Policy of anomaly.
Policy determines whether the anomaly requires action. If yes, Policy notifies SO.
SO runs the appropriate workflow to optimize the performance by modifying the NF configuration. SO triggers SDN-R to modify a parameter.
SDN-R establishes an SSH connection to NF and updates the parameter via one of the approved configuration management protocols: Ansible, Chef or Netconf.
SSH uses public key authentication. SSH public key must be securely provisioned on the NF.
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8

## Slide 7
SO
DMaaP
Periodic PM and NF Optimization
SDN-R
DCAE
VES
Collector
Analytics
Application
PNF
VNF
Modify Config
Modify Parameters
Authenticate connection
Analyzes data
AA notifies Policy of Anomaly
JSON/HTTP/TLS
AA gets data
Request that NF Modifies Configuration (change parameter value for optimization)
Policy
Opt workflow
Optimization workflow SO informs SDN-R
Optimization triggered
Policy tells SO to change parameter
SSH
DCAE authenticates new HTTP and TLS connection using functionality provided by AAF
Publish Event
DCAE publishes data to DMaaP topic
HTTP/TLS
NF sends Periodic PM event
Periodic PM
NF establishes a HTTP/TLS connection to the DCAE VES Collector.
DCAE authenticates the certificate for TLS. Certificate is X.509v3 and can be a Vendor or Service Provider certificate. DCAE authenticates HTTP username and password, if required.
NF sends PM Event to DCAE. Event is encoded in JSON and sent via HTTP/TLS. HTTP/TLS connection is set up and torn down every time a periodic PM event is sent.
DCAE publishes the data to an appropriate DMaaP topic.
Analytics Application (AA) retrieves the data from DMaaP. AA analyzes the data and identifies an anomaly that may need action.
AA notifies Policy of anomaly.
Policy determines whether the anomaly requires action. If yes, Policy notifies SO.
SO runs the appropriate workflow to optimize the performance by modifying the NF configuration. SO triggers SDN-R to modify a parameter.
SDN-R establishes an SSH connection to NF and updates the parameter via one of the approved configuration management protocols: Ansible, Chef or Netconf.
SSH uses public key authentication. SSH public key must be securely provisioned on the NF.
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
NF sends Periodic (15 or 30 minute) PM Event to DCAE VES Collector
JSON/REST/HTTP/TLS

## Slide 8
5G USE CASE A : DEPLOYMENT
PNF Plug and Play
5G RAN PNF Discovery and Registration with ONAP

## Slide 9
PNF
Registration
PNF establishes connection to DCAE.
PNF sends PNF Registration Event.
PNF Registration Handler (PRH) registers PNF in AAI.
PNF
Activation
PRH triggers SO to complete service instantiation.
Second part of PNF Service Instantiation occurs.
PNF is configured and ready to provide service.
PNF Plug and Play Stages
PNF
Plug and Play
PNF powers up and performs Plug and Play procedure.
5G PNF follows 3GPP TS.508 PnP procedure.
ONAP compatible SW is downloaded to PNF.
C
D
E
PNF Modeling
A
Run-Time
PNF Service
Instantiation
PNF Service Instantiation is triggered.
First part of PNF service instantiation occurs.
AAI Entry for PNF Service is created with PNF ID.
B
Design Time
PNF Resource Definition
PNF Service Design
Distribution of service artifacts

## Slide 10
SO
Controller
SDC
Stage A : PNF Modeling
DCAE
AAI
Resource Definition
Service Design
PNF type
Artifacts Distribution
Design Time
RESOURCE DEFINITION - VID User can provide the following information about a PNF:
RESOURCE TYPE– Type of resource; PNF in this case
NAME – Name of the PNF type
CATEGORY – PNF category; e.g. Mobility
TAGS – User-defined tags
DESCRIPTION – Text description
CONTACT ID – Designer of the resource; i.e. user of ONAP
VENDOR – PNF vendor; e.g. Nokia
VENDOR RELEASE – Vendor release
VENDOR MODEL NUMBER – PNF model
EVENTS – Monitoring event definitions
SERVICE DESIGN – User can design a service that uses a PNF type. For VNF, VNF package is onboarded which moves the VNF type into the SDC Catalog. From there, VNF can be used to build services. Note that SDC does not currently support PNF onboarding but this is a desired enhancement.
ARTIFACTS DISTRIBUTION – When User is satisfied with the service design, User can promote the service and the artifacts are distributed to the appropriate run time components. Note that SDC does not currently support artifacts for PNFs but this is a desired enhancement.
A1
A2
A3
A1
A2
A3

## Slide 11
Stage B : PNF Service Instantiation Part 1
SO
OOF
BSS / OSS / VID
AAI
Service Instantiation for PNF ID
Work Order
(PNF ID)
Homing
(N/A for Casablanca)
Resource level flow RLF
Update AAI entry & continue service instantiation
RLF thread terminates
Pending on Stage D PNF Registration event with PNF ID
Create AAI Entry with PNF ID
Subscribe
VES event
PNF ID
ALT If Found
Inactive PNF AAI entry
Resource Level Flow
B1
B2
B3
B4
B5
B6
B7
B8
PNF Service Instantiation Part 1
A Work Order is created for this PNF ID.
VID User or BSS/OSS system triggers Service Instantiation for PNF ID.
SO triggers OOF for Homing assignment. For 5G PNF in Casablanca, this step is not applicable and can be skipped.
SO starts Resource Level Flow (RLF) for this service.
SO queries AAI for an entry for this PNF ID.
Alternative 1: If AAI Entry is Found
  SO updates AAI entry with service instance and continues with the service instantiation.
Alternative 2: If AAI Entry is Not Found
  SO creates AAI entry with service instance for PNF ID.
  SO subscribes for the PNF Ready event for this PNF ID.
  SO stops the RLF and waits for PNF Registration Handler to trigger the completion of the service instantiation.
B2
B3
B4
Query AAI Entry for PNF ID
B9
B8
B9
B7
ALT If Not Found
B6
B5

## Slide 12
Stage C : PNF Plug and Play
Factory
Software
SEGW
Initial
EM
Local
DHCP
DHCP Discover
VLAN Scanning
IPv4/IPv6 discovery
DHCP Response
PNF IP@(m)*, Initial EM IP@(m), SEGW IP@(o), CA IP@(o)
HW Install
PNF Restart
Activates SW
ONAP Compatible Software Download
Bootstrap or Operational SW
IPSec Tunnel Setup (optional)
Identity Service (Identifies NE), Gives DCAE IP@
Certificate Enrollment (optional)
Preplanning, Pre-provisioning
CA/RA
PNF Plug and Play – 3GPP TS32. 508
This scenario is for 3GPP Compliant PNFs like 5G DU which follow 3GPP TS 32.508. Other PNF types follow other PnP standards.
Radio network planning determines where to place the 5G PNFs and how to configure them. DHCP, SEGW, CA/RA, Initial EM must be provisioned for this PNF ID.
Technician installs and cables HW and powers it on.
PNF performs DHCP Discover procedure to determine OAM VLAN and IP version.
DHCP response returns PNF IP@ and Initial EM@. May also return SEGW@ and/or CA@.
PNF performs IPsec tunnel setup using X.509v3 certificates for mutual authentication if SEGW IP@ is returned by DHCP.
PNF performs service provider certificate enrollment via CMPv2 to request the Service Provider certificates if CA/RA IP@ is returned by DHCP.
PNF contacts Initial EM which determines the PNF identity and provides the DCAE IP@ to the PNF.
Initial EM downloads ONAP compatible SW; either a temporary bootstrap SW or the operational SW.
PNF resets and activates the SW. PNF is now capable of sending PNF Registration Event to DCAE.
C1
C1
C2
C3
C4
C5
C6
C7
C8
C9
C2
C3
C4
C5
C6
C7
C8
C9

## Slide 13
Stage D : PNF Registration
DMaaP
DCAE VES
Collector
PRH
AAI
PNF
Update PNF Entry
PNF Registration (periodic)
PNF ID, PNF IP@, Vendor Name, etc.
Update A&AI entry with PNF info
Authenticate Connection
Inventory Query
PNF Not Found, Ignore Registration
PNF Found, Continue to step D6
Stage B: PNF Service Instantiation Part 1 occurs
JSON/HTTP/TLS
HTTP/TLS
Publish to Reg topic
Retrieve Reg event
B
Repeat Steps D1 to D5 until Stage B occurs
D1
D2
D3
D4
D5
D6
PNF Registration
PNF establishes a HTTP/TLS connection to the DCAE VES Collector.
DCAE authenticates the certificate for TLS. Certificate is X.509v3 and can be a Vendor or Service Provider certificate. DCAE authenticates HTTP username and password, if required.
PNF sends Registration Event to DCAE. Event contains PNF instance info such as a unique PNF ID, IP@, Vendor Name and PNF Model Number. PNF sends this event periodically.
DCAE publishes the event to a DMaaP topic.
PRH retrieves the event from DMaaP.
PRH queries AAI for an entry for this PNF ID.
If Not Found:
  Stage B : PNF Service Instantiation Part 1 has not yet occurred and the entry for this PNF ID does not exist in AAI. PRH ignores the event. Steps D1 to D5 repeat until an AAI entry is found for this PNF ID.
If Found:
  Stage B : PNF Service Instantiation Part 1 has occurred and the entry for this PNF ID has been created. PRH updates AAI entry with IP@ and other PNF inventory info.
  PRH publishes a PNF Ready event to trigger SO to complete the PNF service instantiation.
D1
D2
D3
D4
D5
D6
Publish PNF Ready event
D7
D7

## Slide 14
SO
Controller
SDN-C
DMaaP
Stage E : PNF Activation
PNF
(DU)
Activate Service
Network Assignments
Service Configuration
Service Configured
AAI
DCAE
Monitor Service
Monitoring Info
Inform User
Retrieve PNF Ready event
Rehydrate PNF RLF
Update Service Configuration
Update Network Assignments
Service Monitored
Network Assign Complete
PNF Activation
SO receives the PNF Ready event for this PNF ID and rehydrates the RLF from Stage B to finish the service instantiation for this PNF.
SO triggers SDN-C to make the necessary network assignments. For PNF in Casablanca, this step is not needed and is skipped.
SDN-C updates AAI with the network assignments. For PNF in Casablanca, this step is skipped.
SDN-C notifies SO that network assignment is complete. For PNF in Casablanca, this step is skipped.
SO triggers the appropriate Controller (APP-C, SDN-R) to activate the service.
Controller configures the PNF for service via Ansible or NetConf over SSH. The service configuration is PNF specific.
SSH uses public key authentication. SSH public key must be securely provisioned on the PNF.
Controller updates AAI with configuration.
Controller notifies SO that service is configured.
SO triggers DCAE to monitor this new service.
DCAE queries AAI for information about the service and starts monitoring.
DCAE notifies SO that service is monitored.
SO informs service initiator (VID user or OSS/BSS) that service is active.
E1
E1
E2
E3
E4
E5
E6
E7
E8
E9
E10
E11
E12
E2
E3
E4
E5
E6
E7
E8
E10
E11
E12
E9
SSH