## Slide 1: OOF-SON: 5G Self-Organizing Network (SON) using ONAP Optimization Framework (OOF): Release 10 Jakarta
Collaborators : STL, Wipro, AT&T, highstreet technologies, Ericsson, IBM, Nokia, Reliance Jio, Rutgers Winlab, Tech Mahindra, Verizon
Acknowledgments : Feedback and support from participants in ONAP OOF-SON team calls
Presenter : N.K. Shankaranarayanan
Feb 1, 2022

## Slide 2: Roadmap
ML-based SON – first steps (training done offline), additional input from ML-model for PCI optimization (based on PM data)
Preparation work for 3GPP/ORAN yang model
O-RAN alignment preparation (O1 for CM notification & FM)
CPS - RAN config data base: first steps
CSIT and use case automation
O-RAN alignment (FM notifications over O1 for SON)
CPS – Full-fledged RAN data base, full alignment with 3GPP NRM
CM-Notify handling (partial)
R7 Guilin
R8 Honolulu
R9 Istanbul
Improved O-RAN alignment
Updated VES message format (stndDefined) for PM/FM/CM
CM-Notify handling and CPS DB update
Inclusion of A1 action with simulated Near-RT RIC and E2 (stretch goal)
R10 Jakarta
Improved Harmonization with O-RAN OSC for implementing end-to-end use case
Improved RAN Simulation/Emulation with Near-RT RIC functions
Control Loop Co-ordination, SON function co-ordination
LCM for SON
R11 and beyond

## Slide 3: ONAP-based SON: O-RAN O1 focus (Rel.3 – Rel.9)
RIC (non-RT)
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SDN-R)
OOF-SON use case has built a foundation for ONAP/O-RAN integration
Radio network uses common netconf/yang model
Data flows
SDN-R to RAN: netconf-based configuration
RAN to DCAE: VES format for FM alarms, PM KPI, CM Notification
Config ack
Data, CM, FM, PM
O1
O1
O-RAN Radio Network
(RAN-Sim)
CM notify
SON  Control Loop (CL)
ONAP: Open-source platform, with basic open-source code
Companies can use framework to add proprietary SON solutions, including optimization algorithms, etc.

## Slide 4: ONAP-based SON: Target - with O-RAN O1, A1, O2
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SDN-R)
OOF-SON use case has built a foundation for ONAP/O-RAN integration
Radio network uses common netconf/yang model
Data flows
SDN-R to RAN: netconf-based configuration
RAN to DCAE: VES format for FM alarms, PM KPI, CM Notification
RAN to SDN-R: Netconf ack
CM, FM, PM
Data
O1
O2
RIC (near RT)
O-RAN Network
(RAN-Sim)
SON  Control Loop (CL)
ONAP: Open-source platform, with basic open-source code
Companies can use framework to add proprietary SON solutions, including optimization algorithms, etc.
O1
A1
CU, DU, RU
Cloud Infra.
O1
A1
VES Collector

## Slide 5: ONAP / O-RAN Control Loops
Non-RT Control Loop
(>= ~1sec)
SMO Framework
Non-RT RIC
Framework
O-CU and O-DU
O-RU
rApp1
rApp2
rApp3
O1 Term
O2 Term
O-Cloud
O1
O1
O2
O2
O1
R1
R1
R1
O1-Related
O2-Related
Data Mgmnt & Exposure
R1 Exposure Service
External Capabilities
AI/ML Workflow
Non-RT Loop
  Time scale: ~ secs/mins
  Direct config of CU/DU
  Policy Guidance, Coordination
Near-RT Loop
  Near-Real-Time (~100ms)
  Based on E2 service models
SON examples
  Non-RT: Changes based on config state / averaged PM Near-RT: Changes based on radio channel, mobility
ONAP
RAN
(RAN-Sim)

## Slide 6: ONAP / O-RAN Control Loops
Non-RT Control Loop
(>= ~1sec)
SMO Framework
Non-RT RIC
Framework
Near-RT RIC
O-CU and O-DU
O-RU
rApp1
rApp2
rApp3
xApp1
xApp2
xApp3
O1 Term
A1 Term
O2 Term
O-Cloud
A1
E2
O1
O1
O2
O2
O1
R1
R1
R1
O1-Related
O2-Related
Data Mgmnt & Exposure
R1 Exposure Service
External Capabilities
AI/ML Workflow
O1
Near-RT Control Loop
(~10 ms to
~1 sec)
Guidance for
Near-RT
Control Loop
Non-RT Loop
  Time scale: ~ secs/mins
  Direct config of CU/DU
  Policy Guidance, Coordination
Near-RT Loop
  Near-Real-Time (~100ms)
  Based on E2 service models
SON examples
  Non-RT: Changes based on config state / averaged PM
  Near-RT: Changes based on fast changes in radio channel, mobility
ONAP
RAN
(RAN-Sim)

## Slide 7: ONAP SON Use Case – Control Loop with O1 (Rel 3-9)
SON
Handler
MS
OOF
SDN-R (SDN-C)
Policy
Config Change
VES
Collector
DES
MS
Data
Lake
O-RAN O1
CPS DB
RAN-Sim
O1
REST API
DMaaP
FM/PM DB
TBDMT
CM-VES
Parser
FM, PM, CM
2,5
3a-CM
3d-FM,PM
4c,4d
4a
4b
4e
6,8
7
4f
7b
9,13
10,12
11b
Steps 3a,4a,4b,4c: CM data received from RAN, update of state in CPS DB
Steps 3d,4d: FM/PM data received from RAN, processing in SON MS
Steps 2,4e,4f, 5: SON MS analyzes need for optimization
Steps 6,7,7b,8: Optimization using OOF
Steps 9,10,11b: Automated action to make change in RAN (O1)
Steps 11,12,13: Action status
Control
Loop
O1
O1
Feedback to O-RAN
on O1 message specs
(esp. PM streaming)
Notes: When is CPS updated with new PCI values?

## Slide 8: ONAP SON Use Case – Control Loop with O1 & A1 (Rel 10/11)
Steps 3a,4a,4b,4c: CM data received from RAN, update of state in CPS DB
Steps 3d,4d: FM/PM data received from RAN, processing in SON MS
Steps 2,4e,4f, 5: SON MS analyzes need for optimization
Steps 6,7,7b,8: Optimization using OOF
Steps 9,10,11b,11c: Automated action to make change in RAN (O1 and A1)
Steps 11,12,13: Action status
SON
Handler
MS
OOF
SDN-R (SDN-C)
Policy
Config Change
VES
Coll
DES
MS
Data
Lake
O-RAN O1
CPS DB
RAN-Sim
O1
REST API
DMaaP
FM/PM DB
TBDMT
CM-VES
Parser
FM, PM, CM
2,5
3a-CM (for O1 & A1 actions)
3d-FM,PM (for O1 & A1 actions)
4c,4d
4a
4b
4e
6,8
7
4f
7b
9,13
10,12
11b
A1
O-RAN A1
A1 Policy
11c
O1
A1
Control
Loop
O-RAN O1
O1
Jakarta Release:
New VES Message format to align with O1
Complete CM-Notify carryover work
Include A1-based action (stretch goal, may be planning only)
1
1
2
2
2
1
3
3
3
3
2
Near-RT RIC
CU
DU
Notes: When is CPS updated with new PCI values?

## Slide 9: Summary of Requirements
Category | Requirement | Content | Priority
Interoperability | O-RAN alignment (VES, O1 interface) | Define VES message format (using stndDefined domain) for PM, FM, CM Modify RAN-Sim and SON-Hander MS to use new VES format for PM,FM | HIGH
 |  | Configuration Management (CM) notifications over VES | HIGH
Functional | RAN Config Data(base) (CPS), including new RAN models | Use 3GPP NRM/O-RAN yang models for O1 Config | HIGH
 |  | Use CPS for storing/retrieving RAN config data for this use case | HIGH
Functional | Include A1-based action (stretch goal, may be implemented partially) | Enhance RAN-Sim to include Near-RT RIC and xApp Implement A1 Adapter in SDN-R Addition of new CL msg for A1-based action | MEDIUM (stretch)
Platform | Control Loop Coordination (CLC) extensions | Collaborate on CLC extensions (queueing, priority, …) | LOW
Functional | SON co-ordination | Co-ordination across SON functions | LOW
Target for I-release

## Slide 10: ONAP Component Impacts for Jakarta release
COMPONENT | IMPACT(S)
SDN-C (SDN-R) | Use new Yang model for netconf config Receive and parse Configuration Management (CM) notifications from VES Collector Interface to CPS Implementation of A1 interface (stretch goal)
DCAE | Define O-RAN aligned modified VES message format for PM, FM, CM (no DCAE impact) Interface to CPS (test-only? - work done in Istanbul) Adapt to modified VES message format for PM, FM, CM Generate CL message for A1 action (stretch goal, needs to be coordinated with other reqs)
OOF (test-only) | No change
CPS (test-only) | No change
RAN-Sim (Simulators) | Support of new yang models for SON use case (leverage work done for Slicing Use Case) Plan for modification of RAN-Sim to use netopeer Reporting PM, FM, CM messages using new VES format (stndDefined) Enhancements for Near-RT RIC and xApp (stretch goal)

## Slide 11: Problem: RAN-Sim Upgrade is Needed
All SON Use Case planned work has impact on RAN-Sim
RAN-Sim uses Honeycomb netconf server
Honeycomb project ( https://wiki.fd.io/view/Honeycomb ) has been archived, and future support is an issue
  There is a new project Hc2VPP ( https://wiki.fd.io/view/Hc2vpp ) which used Honeycomb
Other parts of RAN-Sim provide great value for ONAP and OSC Use Cases
  Controller, Database, GUI for Usecase logic
  VES message generation for PM, FM, CM
Need to develop plan for:
  Replacement of Honeycomb in RAN-Sim
  Adding simulated Near-RT RIC and xApp in RAN-Sim for Use Cases
  Harmonization of RAN-Sim with OSC projects (sim, o1)

## Slide 12
RAN-Simulator (RAN-Sim)

## Slide 13: Approach for RAN Simulator (RANSim) – Dublin - FM
GUI
  Provide Control to User in UI to select a cell and modify neighbor list to simulate collision/confusion
Controller
  Send message to corresponding Netconf Server about the collision/confusion
Netconf Server
  Send configChangeNotification to SDNR
  Send FM/alarm message to VES Collector for collision/confusion. Thus the control loop starts
ONAP
VES Collector
Config DB
(MariaDB)
DCAE
SON Handler
RANSim
Controller
Web GUI
Simulated
Network
Netconf server 1
Honeycomb
Extension
Yang Model
Netconf server n
Honeycomb
Extension
Yang Models
Netconf
OOF
SDNR
Policy
REST
Websocket
REST
GUI
  Show the modified PCI values
Controller
  When the modified RAN configuration received, same is updated into DB and informed to UI
Netconf Server
  When the SDNR provides the modified RAN configuration, same is forwarded to Controller

## Slide 14: Approach for RAN Simulator (RANSim) – Dublin - PM
GUI
  Provide Control to User in UI to select a cell and generate PM data
Controller
  Send PM message to corresponding Netconf Server with KPI values. Initially send good values and after few minutes send bad values for selected cell.
Netconf Server
  Send PM message to VES Collector with given KPI values. Thus the control loop starts.
ONAP
VES Collector
Config DB
(MariaDB)
DCAE
SON Handler
RANSim
Controller
Web GUI
Simulated
Network
Netconf server 1
Honeycomb
Extension
Yang Model
Netconf server n
Honeycomb
Extension
Yang Models
Netconf
OOF
SDNR
Policy
REST
Websocket
REST
GUI
  Show the ANR updates as dotted lines.
Controller
  When the modified RAN configuration received, same is updated into DB and informed to UI
Netconf Server
  When the SDNR provides the modified RAN configuration, same is forwarded to Controller

## Slide 15: Enhancement to include xApp and A1
O-CU (Honeycomb)
O-DU (Honeycomb)
RANSIM controller
Non-RT-RIC (SDNR)
O1
O1
O1
O1
A1
xapp
xapp
Near-RT-RIC(Honeycomb)
E2
E2
RAN-Sim

## Slide 16
O1 simulator in OSC sim

## Slide 17: O-RAN Software Community (OSC) sim project
Ref: https://wiki.o-ran-sc.org/display/SIM/Architecture
Contact: Alex Stancu
Simulated devices in Simulated RAN are netconf (netopeer) devices representing CU/DU O1 instances with CU/DU yang models
NTS (Network Topology Simulator) Manager uses netconf to connect to devices using yang model of simulation entities
NTS also has NB netconf interface for external entity (e.g. SDN-R) to control simulation
Datastore in NTS provided by netopeer

## Slide 18: O-RAN-SC O1 Simulator architecture
Simulated NF (O-CU/O-DU/O-RU)
Sysrepo
Docker container
NETCONF Datastore
NETCONF Server
Exposed port
YANG Models (O-CU/O-DU/O-RU)
Process (C/C++ Code)
VES Client
FTPes / SFTP Server
Connection to VES Endpoint
Use Case logic
Internal communication
NETCONF Server framework – Netopeer2

## Slide 19: Comparing RAN-Sim and OSC sim
Config DB
(MariaDB)
RANSim
Controller
Web GUI
Simulated
Network
O1 sim n
Extension
Yang Model
O1 sim 1
(with VES client)
Honeycomb
Extension
Yang Models
Netconf
REST
Websocket
REST
Datastore
(sysrepo: xml database with yang)
NTS
Manager
SDNR
Simulated
Network
Netconf
REST
Netconf/yang
Netconf
SDNR GUI
REST
(docker daemon)
O1 sim n
Extension
Yang Model
O1 sim 1
(with VES client)
netopeer
Extension
Yang Models
RAN-Sim was developed for ONAP Use case
Has use case specific logic (e.g. analyze cell relations and generate fault message)
Netconf devices are mounted manually
VES message details are generated in Controller as per usecase logic
RAN-Sim
OSC sim
OSC sim developed as O1 building block
NTS can be used by SDN-R to spawn O1 (CU/DU) instances. SDNR GUI can be used to configure NTS
FM VES messages are pre-configured in O1 sim
NTS uses netconf to each O1 sim netopeer device, and REST to the docker
SDNR
SDNR
VES Collector
VES Collector

## Slide 20: A1 Functions in ONAP / OSC
Ref: https://wiki.onap.org/pages/viewpage.action?pageId=84672221
A1-related message can be sent from Policy to SDN-R/CCSDK
Current Control Loop architecture would use DMaaP CL message
A1 Policy Management Service can connect to A1-termination in the Near-RT RIC with or without an A1 Adapter
In the SON Use Case context, the A1-termination in Near-RT RIC would be part of the simulated RAN (RAN-Sim) with usecase logic in the simulated/abstracted xApp which results in events from CU/DU over O1

## Slide 21: OSC A1 (Near-RT RIC) Simulator
Stateful A1 test stub for “South-end” of A1 Interface
Used to create multiple stateful A1 providers (simulated near-rt-rics)
  Supports A1-Policy and A1-Enrichment Information
Does not include and app-specific behavior – just what is defined in A1 Application Protocol specs
Implemented as a lightweight Python application
Swagger-based northbound interface, so easy to change the A1 profile exposed (e.g. A1 version, A1 Policy Types, A1-E1 consumers, etc)
  All A1-AP versions supported as configurable profiles
Source: https://gerrit.o-ran-sc.org/r/admin/repos/sim/a1-interface
Docs: https://docs.o-ran-sc.org/projects/o-ran-sc-sim-a1-interface
Wiki: https://wiki.o-ran-sc.org/display/RICNR

## Slide 22: Requirements

## Slide 23
Thank You!