## Slide 1: OOF-SON: 5G Self-Organizing Network (SON) using ONAP Optimization Framework (OOF): Release 11 Kohn
Collaborators : STL, Wipro, CapGemini, Ericsson, AT&T, highstreet technologies, Rutgers Winlab, IBM, Tech Mahindra, Nokia, Verizon
Acknowledgments : Feedback and support from participants in ONAP OOF-SON team calls
Presenters : N. K. Shankaranarayanan
May 31, 2022

## Slide 2: Roadmap
O-RAN alignment (FM notifications over O1 for SON)
CPS – Full-fledged RAN data base, full alignment with 3GPP NRM
CM-Notify handling (partial)
R9 Istanbul
Improved O-RAN alignment
Update of RAN-Sim and SDN-R to use O-RAN O1 yang model for config
Updated VES message format (stndDefined) for PM/FM/CM
R10 Jakarta
Support A1-based SON action
Enhance RAN-Sim (A1 Term, RANApp)
SON-Handler MS and Policy changes for A1 control loop
CPS DB updates for CM notification
Work towards alignment with O-RAN rApp and R1
Align PoC to new VES msg formats
R11 Kohn
Harmonization with O-RAN OSC for SON use cases using O1 and A1
Align with O-RAN rApp and R1
Co-ordination across SON functions
LCM for SON
R12 and beyond

## Slide 3: ONAP-based SON: O-RAN O1 focus (Rel.3 – Rel.10)
RIC (non-RT)
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SDN-R)
OOF-SON use case has built a foundation for ONAP/O-RAN integration
Radio network uses common netconf/yang model
Data flows
SDN-R to RAN: netconf-based configuration
RAN to DCAE: VES format for FM alarms, PM KPI, CM Notification
Config ack
Data, CM, FM, PM
O1
O1
O-RAN Radio Network
(RAN-Sim)
CM notify
SON  Control Loop (CL)
ONAP: Open-source platform, with basic open-source code
Companies can use framework to add proprietary SON solutions, including optimization algorithms, etc.

## Slide 4: ONAP / O-RAN Control Loops
Non-RT Control Loop
(>= ~1sec)
SMO Framework
Non-RT RIC
Framework
O-CU and O-DU
O-RU
rApp1
rApp2
rApp3
O1 Term
O2 Term
O-Cloud
O1
O1
O2
O2
O1
R1
R1
R1
O1-Related
O2-Related
Generic SMO Functions
Data Mgmnt & Exposure
R1 Exposure Service
External Capabilities
AI/ML Workflow
Non-RT Loop
  Time scale: ~ secs/mins
  Direct config of CU/DU
  Policy Guidance, Coordination
Near-RT Loop
  Near-Real-Time (~100ms)
  Based on E2 service models
SON examples
  Non-RT: Changes based on operational state, averaged behavior
  Near-RT: Changes based on radio channel, mobility
ONAP
RAN
(RAN-Sim)

## Slide 5: ONAP / O-RAN Control Loops
Non-RT Control Loop
(>= ~1sec)
SMO Framework
Non-RT RIC
Framework
Near-RT RIC
O-CU and O-DU
O-RU
rApp1
rApp2
rApp3
xApp1
xApp2
xApp3
O1 Term
A1 Term
O2 Term
O-Cloud
A1
E2
O1
O1
O2
O2
O1
R1
R1
R1
O1-Related
O2-Related
Generic SMO Functions
Data Mgmnt & Exposure
R1 Exposure Service
External Capabilities
AI/ML Workflow
O1
Near-RT Control Loop
(~10 ms to
~1 sec)
Guidance for
Near-RT
Control Loop
Non-RT Loop
  Time scale: ~ secs/mins
  Direct config of CU/DU
  Policy Guidance, Coordination
Near-RT Loop
  Near-Real-Time (~100ms)
  Based on E2 service models
SON examples
  Non-RT: Changes based on operational state, averaged behavior
  Near-RT: Changes based on radio channel, mobility
ONAP
RAN
(RAN-Sim)

## Slide 6: ONAP-based SON: O-RAN O1 focus (Rel.3 – Rel.10)
RIC (non-RT)
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SDN-R)
OOF-SON use case has built a foundation for ONAP/O-RAN integration
Radio network uses common netconf/yang model
Data flows
SDN-R to RAN: netconf-based configuration
RAN to DCAE: VES format for FM alarms, PM KPI, CM Notification
Config ack
Data, CM, FM, PM
O1
O1
O-RAN Radio Network
(RAN-Sim)
CM notify
SON  Control Loop (CL)
ONAP: Open-source platform, with basic open-source code
Companies can use framework to add proprietary SON solutions, including optimization algorithms, etc.

## Slide 7: ONAP-based SON: Target - with O-RAN O1, A1, O2
Co-ordination, Decisions (Policy)
Data Collection, & Analysis
(DCAE)
Optimization (OOF)
Control loop
Action
(SDN-R)
OOF-SON use case has built a foundation for ONAP/O-RAN integration
Radio network uses common netconf/yang model
Data flows
SDN-R to RAN: netconf-based configuration
RAN to DCAE: VES format for FM alarms, PM KPI, CM Notification
RAN to SDN-R: Netconf ack
CM, FM, PM
Data
O1
O2
RIC (near RT)
O-RAN Network
(RAN-Sim)
SON  Control Loop (CL)
ONAP: Open-source platform, with basic open-source code
Companies can use framework to add proprietary SON solutions, including optimization algorithms, etc.
O1
A1
CU, DU, RU
Cloud Infra.
O1
A1
VES Collector

## Slide 8: ONAP SON Use Case – Control Loop with O1 (Rel 3-10)
SON
Handler
MS
OOF
SDN-R (SDN-C)
Policy
Config Change
VES
Collector
DES
MS
Data
Lake
O-RAN O1
CPS DB
RAN-Sim
O1
REST API
DMaaP
FM/PM DB
TBDMT
CM-VES
Parser
FM, PM, CM
2,5
3a-CM
3d-FM,PM
4c,4d
4a
4b
4e
6,8
7
4f
7b
9,13
10,12
11b
Steps 3a,4a,4b,4c: CM data received from RAN, update of state in CPS DB
Steps 3d,4d: FM/PM data received from RAN, processing in SON MS
Steps 2,4e,4f, 5: SON MS analyzes need for optimization
Steps 6,7,7b,8: Optimization using OOF
Steps 9,10,11b: Automated action to make change in RAN (O1)
Steps 12,13: Action status
Control
Loop
O1
O1
O1
CU/DU
Notes: When is CPS updated with new PCI values?

## Slide 9: SON Use Case: O1 and A1 based action
Current
  O1 based action for PCI config-change to NRCellDU/nRPCI value (based on analysis in SON Handler MS)
  O1 based action for ANR config-change to NRCellCU/NRCellRelation/isHOAllowed value (based on analysis of poor HO kpi values by SON Handler MS)
Planned Change for Rel 11 Kohn
  O1 based action for PCI config-change to NRCellDU/nRPCI value (based on analysis in SON Handler MS)
  A1 based action for ANR guidance message to RAN App for CellRelation (send poor HO kpi values to RAN App) – with end result of config change to NRCellCU/CellRelation/isHOAllowed value

## Slide 10: High-level options for A1 based action
A1 support in SDN-R to work with A1 Termination in RAN-Sim
Option 1 - Minimal change to existing code
  No change to header of ANR Control Loop (DMaaP) message
  Change in payload of ANR Control Loop message (from O1 to A1)
  SDN-R processes new A1 payload in Control Loop message
  No/minimal change in Policy
Option 2 – Changes in Policy and Control Loop design
  Separate control message format for O1 and A1 based message
  Separate policies in Policy module- different DMaaP topics?
  Work towards packaging application as an rApp
  Policy to A1 policy manager message may not be DMaaP

## Slide 11: ONAP SON Use Case – Control Loop with O1 & A1 (Rel 11)
RAN-Sim
SON
Handler
MS
SDN-R (SDN-C)
Policy
Config Change
VES
Coll
CPS DB
O1
REST API
DMaaP
FM/PM DB
TBDMT
CM-VES
Parser
FM, PM, CM
2,5
3a-CM (for O1 & A1 actions)
3d-FM,PM (for O1 & A1 actions)
4c,4d
4a
4b
4e
4f
9,13
10a,12a
A1
O-RAN A1
A1 Policy
O1
A1
Control
Loop
O-RAN O1
O1
*
A1
O1
CU/DU
O-RAN O1
RAN App
*
*
*
*
Changes needed to support A1 based SON action
*
*
*
Carry over CM update work to fully support A1
A1 PMS
SLI
Steps 9: Request msg from MS for O1/A1
Steps 10,11: Automated action to make change in RAN (O1 and A1)
Steps 12,13: Action status
10o,12o
11a
11o
Notes: When is CPS updated with new PCI values?

## Slide 12: SON Use Case: A1 based CL msg without change to header
#Current ANR message (O1 based action)
{
"closedLoopControlName":"ControlLoop-vSONH-7d4baf04-8875-4d1f-946d-06b874048b61",
"closedLoopAlarmStart":1606805921693,
"closedLoopEventClient":"microservice.PCI",
"closedLoopEventStatus":"ONSET",
"target":"pnf.pnf-name",
"from":"PCIMS",
"version":"1.0.2",
"policyName":"PCI",
"policyVersion":"1.0.2",
"target_type":"PNF",
"requestID":"82feb01e-4f3e-40e2-b8df-683adabae893",
"AAI":{"generic-vnf.prov-status":"ACTIVE",
"generic-vnf.is-closed-loop-disabled":"false",
"pnf.pnf-name":"ncserver1"},
"Action":"ModifyConfigANR",
"payload":
"{"Configurations":
[{"data":{"FAPService":
{"alias":"Chn0014","CellConfig":{"LTE":{"RAN":{"Common":
{"CellIdentity":"Chn0014"},
"NeighborListInUse":
{"LTECell":[
{"PNFName":"ncserver1","PLMNID":"ran-1","CID":"Chn0000","PhyCellID":0,"Blacklisted":"true"},
{"PNFName":"ncserver1","PLMNID":"ran-1","CID":"Chn0001","PhyCellID":0,"Blacklisted":"true"}],"LTECellNumberOfEntries":"2"}}}}}}}]}"
}
#Sample New ANR DMaaP message format to be sent to SDN-R (A1-based)
{
"closedLoopControlName":"ControlLoop-vSONH-7d4baf04-8875-4d1f-946d-06b874048b61",
"closedLoopAlarmStart":1606805921693,
"closedLoopEventClient":"microservice.PCI",
"closedLoopEventStatus":"ONSET",
"target":"pnf.pnf-name",
"from":"PCIMS",
"version":"1.0.2",
"policyName":"PCI",
"policyVersion":"1.0.2",
"target_type":"PNF",
"requestID":"82feb01e-4f3e-40e2-b8df-683adabae893",
"AAI":{"generic-vnf.prov-status":"ACTIVE",
"generic-vnf.is-closed-loop-disabled":"false",
"pnf.pnf-name":"ncserver1"},
"Action":"ModifyConfigANR"
#Keep same header for no change. Interpret ModifyConfigANR action in SDNR.
#Assuming that payload has been changed to carry A1 policy information.
"payload":
"{
“action”:”CreatePolicy”, #TBD if this can be removed if there is an action in the header
“policy_id”: 1,
“policy_type_id”: 1, #currently implemented as integer
“ric_id”:”ric1”,
“policy_data”:
”{
"PNFName":"ncserver1",
"PLMNID":"ran-1",
"CellID":"Chn0014', #source cell
"neighbours": [
{
"PNFName":"ncserver1",
"PLMNID":"ran-1",
"CellID":"Chn0000", #first neighbor
"ho-kpi1": 100 #integer
},
{
"PNFName":"ncserver1",
"PLMNID":"ran-1",
"CellID":"Chn0001",
"ho-kpi1": 90 #integer
}
}"
}"
}

## Slide 13: Control Loop for A1-based action
Use similar solution for SON and Slicing use case
DMaaP msg from Policy to SDN-R
  reuse control loop methodology, visibility to other modules
  Separate DMaaP topics for O1 and A1

## Slide 14: Kafka Message Format
Need further changes in message format, to support policy instance id etc.
{
“action”:”CreatePolicy/DeletePolicy/GetPolicyStatus/..”,
“payload”:”{}”,
“policy_type_id”:” ORAN_QoSTarget_2.0.0”
‘’ric_id”:””
}

## Slide 15: A1 Termination & RAN App are different Modules
A1 Termination
Push Policies towards
policy type id specific topic
RAN App
RAN SIM CTRL
WebSocket/Netconf
A1-P Policy
K
A
F
K
A
A1 Termination hold Mapping of PolicyTypeId to TopicName:
{
“PolicyTypeID”:”TopicName”,
“ORAN_QoSTarget_2.0.0”:”TopicA”,
“ORAN_QoETarget_2.0.0”:”TopicB”
}
Get Topic Mapping
Subscribe to Topic
RAN-Sim Enhancement for A1
RAN-Sim

## Slide 16: Current RAN-Sim - support for O1-based config
Config DB
(MariaDB)
RANSim
Controller
Web GUI
VES(REST)
Websocket
RAN-Sim
SDNR
VES Collector
Extension
Yang Model
(O1-netconf/VES) NF
Honeycomb
Extension
Yang Models
CU/DU NF
Extension
Yang Model
(O1-netconf/VES) NF
Honeycomb
Extension
Yang Models
CU/DU NF
REST
Netconf
VES(REST)
New module in RAN-Sim
Near-RT RIC
xApp
A1 termination
Areas of work
A1 termination
xApp functionality
O1 functionality in Near-RT RIC (netopeer)
Connection from Controller* to xApp/Near-RT RIC
  websocket (simpler?)
  Netconf (need client in Controller)
E2 abstraction options:
  Via controller (simpler?)
  Direct interfaces (working towards E2)
* From Alex:
Choice of interface will depend on team doing the development. RAN-Sim is Java based, netopeer is C/C++ based
For netconf client in RAN-Sim for netconf options, see for example https://github.com/Juniper/netconf-java
O1-Config
O1-VES

## Slide 17: Enhancing RAN-Sim to support both O1 and A1
(RAN App)
Config DB
(MariaDB)
RANSim
Controller
Web GUI
Netconf
VES(REST)
Websocket
RAN-Sim
SDNR
VES Collector
(A1-Termn)
A1
App
Extension
Yang Model
(O1-netconf/VES) NF
Honeycomb
Extension
Yang Models
CU/DU NF
Extension
Yang Model
(O1-netconf/VES) NF
Honeycomb
Extension
Yang Models
CU/DU NF
REST
A1
Netconf
VES(REST)
New module in RAN-Sim
Near-RT RIC
xApp
A1 termination
Areas of work
A1 termination
xApp functionality
O1 functionality in Near-RT RIC (netopeer)
Connection from Controller* to xApp/Near-RT RIC
  websocket (simpler?)
  Netconf (need client in Controller)
E2 abstraction options:
  Via controller (simpler?)
  Direct interfaces (working towards E2)
* From Alex:
Choice of interface will depend on team doing the development. RAN-Sim is Java based, netopeer is C/C++ based
For netconf client in RAN-Sim for netconf options, see for example https://github.com/Juniper/netconf-java
O1-Config
O1-VES
Kafka
netopeer

## Slide 18: A1 Functions in ONAP / OSC
Ref: https://wiki.onap.org/pages/viewpage.action?pageId=84672221
A1-related message can be sent from Policy to SDN-R/CCSDK
Current Control Loop architecture would use DMaaP CL message
A1 Policy Management Service can connect to A1-termination in the Near-RT RIC with or without an A1 Adapter
In the SON Use Case context, the A1-termination in Near-RT RIC would be part of the simulated RAN (RAN-Sim) with usecase logic in the simulated/abstracted xApp which results in events from CU/DU over O1

## Slide 19: Requirements
SON Use Case: https://jira.onap.org/browse/REQ-1212
A1 Support in SDN-R/CCSDK: https://jira.onap.org/browse/CCSDK-3644
DCAE: https://jira.onap.org/browse/DCAEGEN2-3148
Policy: https://jira.onap.org/browse/POLICY-4108

## Slide 20: ONAP Component Impacts for Kohn release
COMPONENT | IMPACT(S)
SDN-C (SDN-R) | Implementation of A1 interface Receive and parse Configuration Management (CM) notifications from VES Collector (support TBD) Interface to CPS (support TBD)
DCAE | Generate modified CL message for A1 action Interface to CPS (test-only?) Adapt to modified VES message format for PM, FM, CM (?stretch goal)
Policy | Modification of policy and control loop to support both O1 and A1 based control action (Impact on DCAE and SDN-R TBD)
OOF (test-only) | Interface to CPS (test-only? )
CPS (test-only) | TBDMT to support required APIs (test-only? )
RAN-Sim (Simulators) | Enhancements for A1 Termination and RAN App Reporting PM, FM, CM messages using new VES format (stndDefined)

## Slide 21: Summary of Requirements
Category | Requirement | Content | Priority
Functional | Include A1-based action | Implement A1 Support in SDN-R Enhance RAN-Sim to include A1 Termination and RAN App Addition of new CL msg for A1-based action | HIGH
Interoperability | O-RAN alignment (VES, O1 interface) | Modify RAN-Sim and SON-Hander MS to use new VES format for PM,FM | MED
 |  | Modify RAN-Sim and SON-Hander MS to use new VES format for CM | MED
Functional | Maintain RAN Config Data | Process CM Notification and update CPS DB | HIGH
Functional | Package application as rApp | Ongoing discussion | HIGH

## Slide 22
Thank You!