## Slide 1: Introduction
The ONAP target functional architecture is being developed by the architecture tiger team (see slide 7).
In order to complete the architecture specification we need to provide the following information:
  Definition of each component in a simple high level way using the attached template,
We also need to define the Beijing architecture with detailed implementation view (with projects) including functional (and non-functional) requirements, features, APIs, interfaces and full scope of each project for R2.

## Slide 2: Functional Architecture View
Proposal of what to include for the Functional View
For each component shown in the high level functional architecture we could include one slide that describes:
  The component definition
  The interfaces that are offered (with a name and a short description)
  The interfaces that are consumed (with the name, but no description)
  The models that are consumed.
Such a functional view should be agnostic to the implementation.

## Slide 3: Function
Function 1
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N
Note: Can be more than one page
Here we put the services provided
Here we put the services used

## Slide 4: Function Definitions

## Slide 5: Service Design and Creation
Service Design and Creation
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N
We could discuss whether to have one slide per SDC part?

## Slide 6: Orchestration (1/2)
Orchestration
Definition:
Provides functionality for the execution of specified process and automated sequencing of activities, task, rules and policies needed for creation, modification, removal of network application, infrastructure services or resources.
Supports different specializations with specific orchestration scopes.
Specialization scopes include, but are not limited to, network service LCM (i..e VNFO specialization), network slice specialization, domain specific specialization.
Provided Interfaces:
Service Management Interface
  Provides the interface to manage the services that orchestration provides.
Network Service LCM interface
  Provides the specific network service LCM interface.
Actuation Request Interface
  Provides support of actuation requests towards the services.
Service Management Interface
Network Service LCM Interface
Actuation Request Interface
Service Definition Reception interface
Service Management Interface
VNF LCM Interface
NF Config Interface
Optimization request Interface
Inventory Service Interface
Transport Service Interface
Network Service LCM interface
Draft

## Slide 7: Orchestration (2/2)
Orchestration
Consumed interface Interfaces:
Service Management Interface, from: Orchestration
VNF LCM Interface, from: Generic NF controller
Optimization Request Interface, from: Optimization Framework
NF Config Interface, from: Generic NF controller
Inventory Service Interface, from: Available and Active Inventory
Transport Service Interface, from: SDN Controller.
Network Service LCM interface, from: Orchestrator
Consumed Models:
Network Service Descriptor
Rest to be filled in.
Service Management Interface
Network Service LCM Interface
Actuation Request Interface
Service Definition Reception Interface
Service Management Interface
VNF LCM Interface
NF Config Interface
Optimization request Interface
Inventory Service Interface
Transport Service Interface
Network Service LCM interface
Draft

## Slide 8: Dashboard OA&M
Dashboard OA&M
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N

## Slide 9: Active & Available Inventory, External Registry
Active & Available Inventory, External Registry
Definition:
Maintains the view of the managed systems services and resources, as well as information of the external systems that ONAP will connect to.
It provides real-time views of a managed systems resources, services and relationships with each other.
Provided Interfaces:
Inventory Service Interface: <interface name>
  Provides the ability to store, read, update inventory information
External Register interface
  Provides the ability to provision and read external system information
Consumed interface Interfaces:
Consumed Models: Inventory Model???
Inventory Service Interface
External Register Interface
Interface N

## Slide 10: Data Collection, Analytics, and Events
Data Collection, Analytics, and Events
Definition:
DCAE is the ONAP subsystem that supports closed loop control and higher-level correlation for business and operations activities. DCAE collects performance, usage, and configuration data; provides computation of analytics; aids in trouble-shooting and management; and publishes event, data, and analytics to the rest of the ONAP system for FCAPS functionality.
Provided Interfaces:
Interface 1: Data collection interface (used by VNFs and others from which data is collected)
  Interface for various FCAPS data entering DCAE/ONAP.
Interface 2: Deployment interface (used by CLAMP)
  Interface for triggering the deployment and changes of a control loop
Consumed interface Interfaces:
Interface 1: Data movement platform interface (provided by DMaaP)
  Interface for data transportation between DCAE subcomponents and between DCAE and other ONAP components
  This interface can also be used for publishing events to other ONAP components.
Interface 2: Data enrichment interface (provided by A&AI)
  Interface used by DCAE for enriching collected raw data by adding information not contained in original data, e.g. identifying the VNF type from VNF identity by querying this interface.
Interface 2: Service model change interface (Provided by SDC)
  Interface for fetching control loop models and updates.
Interface 4: Policy interface (Provided by Policy)
  Interface for fetching configuration and operation policies on control loop and control loop components into DCAE for application.
Consumed Models: TOSCA models descripting control loop construction (e.g. collection and analytics apparatus)
Interface 1
Interface N

## Slide 11: Policy Framework
Policy Framework
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N

## Slide 12: Function
Function 1
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N

## Slide 13: Multi-Cloud Adaptation
Multi-Cloud adaptation
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N

## Slide 14: SDN Controller
SDN Controller
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N

## Slide 15: Generic NF Controller
Generic NF Controller
Definition:
Interfaces and controls the management state of the network functions.
Supports network function LCM
Supports network function configuration
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Inventory Interface, from: AAI
Generic VIM Interface, From: Multicloud
VNF virtual resource management interface: from VNF/S-VNFM
To be filled in
NF Config Interface
VNF LCM Interface
Service Definition Reception Interface
Actuation Request Interface
Inventory Interface
Generic VIM Interface
VNF virtual resource management interface
Draft

## Slide 16: Common Services
Function 1
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N
We could discuss whether to have one slide per common service?

## Slide 17: ONAP Operations Manager
ONAP Operations Manager
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N

## Slide 18: ONAP API
ONAP API
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N

## Slide 19: ONAP CLI
ONAP CLI
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N

## Slide 20: ONAP Portal
ONAP Portal
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N

## Slide 21: Micro Services Bus / Data Movement
Micro Servies Bus / Data Movement
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N

## Slide 22: VNF/PNF onboarding
VNF/PNF onboarding
Definition:
A
B
C
Provided Interfaces:
Interface 1: <interface name>
  Short description
Interface 2: <interface name>
  Short description
Consumed interface Interfaces:
Interface name, from:
Consumed Models
Interface 1
Interface N

## Slide 23: Interface Definitions
Note: describe from the provider perspective

## Slide 24: Interface Definitions
< interface name > | 
Provided Service | 
Supplementary Information | 
Interface Provider(s) | 
Provided Capabilities | 
Draft

## Slide 25: Interface Definitions
Service Management Interface | 
Provided Service | Provide Lifecycle Management actions for the service (e.g. instantiate, update, remove)
Supplementary Information | Maybe used between orchestrators
Interface Provider(s) | Orchestrator
Provided Capabilities | To be filled in Instantiate Service Scale Service Update Service Query Service Terminate Service Heal Service Get operational status Subscribe Query subscription information Notify Terminate Subscription
Draft

## Slide 26: Interface Definitions
Network Service LCM Interface | 
Provided Service | Provide Lifecycle Management actions for a network service
Supplementary Information | Corresponds to the NS interface capabilities described in ETSI-NFV SOL 005
Interface Provider(s) | Orchestrator
Provided Capabilities | Create NS Identifier Instantiate NS Scale NS Update NS Query NS Terminate NS Delete NS identifier Heal NS Get operational status Subscribe Query subscription information Notify Terminate Subscription
Draft

## Slide 27: Interface Definitions
Actuation Request Interface | 
Provided Service | Actuate a defined request via orchestration
Supplementary Information | Policy, DCAE, VID can request specific actions to be performed. This can be part of closed loop control of change management.
Interface Provider(s) | Orchestrator
Provided Capabilities | Actuate requested action Query requested action Cancel requested action Subscribe to action notifications Cancel subscription Query Action Status Notify of Action (up on subscription)
Draft

## Slide 28: Interface Definitions
Service Definition Request Interface | 
Provided Service | Storage and management of the service definitions the ONAP components act on. This can be the service and resource related models and recipes
Supplementary Information | 
Interface Provider(s) | Orchestrator, Generic VN Controller, SDN-C, Policy, DCAE
Provided Capabilities | To be filled in Update service definitions Query service definitions Remove service definitions
Draft

## Slide 29: Interface Definitions
VNF LCM interface |  | 
Provided Service | A set of operations supporting the VNF LCM, operation granting interface, Resource quota notifications | 
Supplementary Information | A subset of the SOL-003 (Or-VNFM) interface. This subset is the VNF Lifecyle management Interface, VNF Indicator Interface, VNF lifecycle operation granting interface and virtualized resource quota availability interface. | 
Interface Provider(s) | Generic NF manager | 
Provided Capabilities | Create VNF Identifier Query VNF Modify VNF information Delete VNF identifier Instantiate VNF Scale VNF Scale VNF to Level Change VNF Flavour Terminate VNF Heal VNF | Operate VNF Change external VNF connectivity Get Operation Status Subscribe Query subscription information Terminate subscription Notify Get Indicator Value Grant Lifecyle Operation
Draft

## Slide 30: Interface Definitions
NF Config Interface | 
Provided Service | Configure the Network Function
Supplementary Information | 
Interface Provider(s) | Generic NF controller
Provided Capabilities | Configuration Update Configuration Query
Draft

## Slide 31: Interface Definitions
Optimization Request Interface | 
Provided Service | Provide optimization decision
Supplementary Information | 
Interface Provider(s) | Optimization Framework
Provided Capabilities | Optimization Information Request
Draft

## Slide 32: Interface Definitions
Transport Service Interface | 
Provided Service | Transport Service/Resource LCM
Supplementary Information | 
Interface Provider(s) | SDN-C
Provided Capabilities | To be filled in
Draft

## Slide 33: Interface Definitions
Transport Service Interface | 
Provided Service | Create, read, update, delete Inventory information
Supplementary Information | Operations are performed against the inventory data model
Interface Provider(s) | AAI
Provided Capabilities | To be filled in.
Draft

## Slide 34: Interface Definitions
Generic VIM interface | 
Provided Service | VIM operations
Supplementary Information | 
Interface Provider(s) | Muti-Cloud
Provided Capabilities | To be filled in.
Draft

## Slide 35: Interface Definitions
External Register Information Interface | 
Provided Service | Manage external Register information
Supplementary Information | 
Interface Provider(s) | Available and Active Inventory
Provided Capabilities | Create External Register Information Read External Register Information Update External Register Information Delete External Register Information
Draft

## Slide 36: Definitions

## Slide 37: Used Definitions
Term | Definition
Managed System | The system that ONAP is automating
External System | An external system that is part of the Managed system that ONAP needs to connect to.
Network Service | composition of Network Function(s) and/or Network Service(s), defined by its functional and behavioural specification (Source ETSI GS NFV 003) Note: Network service is agnostic to the service delivered by the network functions.