## Slide 1: ONAP Controllers (GNFC, SDNC, VF-C, APPC) and CCSDK
AT&T Labs

## Slide 2: Issues for Resolution within ONAP Arch Tiger Team
GNFC disposition
Relationship of SDNC, APPC & VF-C to GNFC
Role of CCSDK
GNFC, SDNC External Interfaces (applies to External Controller too)
Also …
Address SDN-R path to GNFC
Align to 5G use case

## Slide 3: ONAP Target Architecture (High-Level Functional View)
Key Takeaways:
Today, ONAP Architecture has the Controller Layer with 2 controllers – SDNC and GNFC. We need to consolidate into a single generic NF controller – namely GNFC.
SDNC, APPC and VF-C should evolve to GNFC
SDNC, APPC and VF-C should consolidate code into CCSDK as a superset controller library for creating different controller persona instances by Operators

## Slide 4: GNFC, APPC, VF-C and SDNC
GNFC was introduced into the ONAP architecture shortly after the Amsterdam release
  Goals: 1) Achieve alignment between APPC and VF-C; 2) Reduce functional overlap; 3) Simplify software framework/complexity to realize a model driven controller layer; 4) Enable faster feature delivery
GNFC’s software repo will be CCSDK
CCSDK was created and approved to be a common software library for controllers
  Superset of ONAP controller software modules that can be used by any operator to instantiate a controller persona (see later slides for more info on controller persona based library)
  Currently APPC and SDNC inherit some base code from CCSDK
  Expectation is that APPC, VF-C as well as SDNC will transition toward the GNFC framework, committing most/all of their code into CCSDK to form the library superset
  The approach will enable any operator to create any controller personas using CCSDK for a specific domain(s), providing a full set of Configuration and Life Cycle Management functions via a consistent set of NB/SB APIs
Work is needed to organize CCSDK repo and define profiles (during build process) associated with the desired controller personas (including default profiles/personas for each release testing)
Coordination work might also be needed with OOM team to define the Configuration Management details in deploying various controller personas
Some example controller persona use cases:
  Small operator instantiates single controller persona for its wireline and wireless network (mobility/enterprise use cases)
  Large operator instantiates a WAN controller persona, a mobility controller persona, and an IMS controller persona

## Slide 5: CCSDK based Controller Personas
Common microservices
Common health checks
Common APIs
Common logging
Common model management
Common resource management
Common
GNFC_Core
Base Config
sdnc-core
sdnc-parent
sdnc-plugins
sdnc-oam
sdnc-adapters
sdnc-northbound
sdnc-logic
WAN
new adapters
wan-logic
CCSDK Repo
Base LCM
lcm-logic-health
lcm-logic-heal
lcm-logic-scale
…
lcm-adapters
Underlay-Overlay
new adapters
ul-ol-logic
CPE
new adapters
cpe-logic
L2 Ethernet
new adapters
L2-logic
…
micro
services
micro
services
micro
services
micro
services
micro
services
micro
services
micro
services
micro
services
micro
services
micro
services
micro
services
micro
services
new-northbound
Mobility
RAN-adapters
ran-logic
packet-core-logic
spectrum-logic
micro
services
micro
services
micro
services
Network Domain n
…
Controller Personas | Build Profile & Configuration
Default GNFC – Wireline | GNFC_Core+WAN+L2+CPE
Default GNFC – Wireless | GNFC_Core+Mobility
Wireline/Wireless GNFC | GNFC_Core+Mobility+WAN+L2+CPE
Underlay/overlay GNFC | GNFC_Core+Underlay-overlay
Customer Prem GNFC | GNFC_Core+CPE
Etc. | 
In transition period, CCSDK could have multiple core modules that do similar functions (due to merging of APPC, VF-C and SDNC)
But the APIs, models, model driven behavior have to be consistent

## Slide 6: GNFC & SDNC Architecture and Interfaces
AT&T Labs

## Slide 7: Generic NF Controller Architecture
Generic NF Controller configures and maintains the health of VNFs/PNFs/services* (L1-7) throughout their lifecycle.
  The Lifecycle Management Functions are a normalization of the controller aspects of VF-C and APP-C functions into a common, extensible library
Programmable network application management platform
  Behavior patterns programmed via models and policies
  Standards based models & protocols for multi-vendor implementation
  Extensible SB adapter set including vendor specific VNF-Managers
  Operational control, version management, software updates, etc.
Manages the health of VNFs/PNFs within its scope
  Policy-based optimization to meet SLAs
  Event-based control loop automation to solve local issues near real-time
Local source of truth
  Manages inventory within its scope
  All stages/states of lifecycle
  Configuration audits
Key Attributes of Generic NF Controllers
  Intimate with network protocols
  Manages the state of services
  Provide Deployment Flexibility to meet user scalability / resilience needs
Key
CE-x
CI-x
Controller External API
Controller Internal API
*How the services are to be handled is for further study
** Configuration Design Tool (CDT) to be integrated into SDC
***CE-6 not needed - see External Controller materials
Configuration Design Tool UI**
Run time catalog
OOF (for queries)
Policy
Generic NF
Controller
Adapters
Service Logic Processing
Chef
Assigned Resources Inventory:
Service* Topology & VNF/PNF State
Netconf
API Handler
Active & Available Inventory
Service Design & Creation
Ansible
Others
…
Orchestration
Data Collection, Analytics & Events
Closed Loop Actions
Inventory
Updates
Orchestration
Configure
Audit
SW upgrade
Scale in/out
Stop/start
Health check
L4-7 Service Create
Supports Model-Driven Lifecycle Mgmt.
Service Logic
Service Logic
Service Logic
…
Artifact Distribution
*Not E2E service view. The “Service” view in the Generic NF Controller is limited its scope of control
Applications
VNFs
PNFs
Multi-Cloud Adapter
Multi-VIM/Cloud
MSB/Data Movement
MSB/Data Movement
MSB/Data Movement
CE-2
CE-3
CE-5
External System Adapter (s)
External
3rd Party Controllers
Specific VNF Managers
Element Mgt. Systems
CI-2
CI-1
CI-4
VNF Descriptors
Repository
Config Templates
Engineering Rules
Service Logic
Policy Cache/Event Match
Operational Tree/Config Tree (Service Model)
CI-7
CI-6
CI-3
CE-6
CI-5
CE-4
…
CE-1
CE-6 not needed***

## Slide 8: Generic NF Controller – External/Internal Interface Definitions
 | Interface Definitions
CE-1 | Distribution of artifacts from Service Design and Creation – artifacts distributed to Run Time Catalog, GNFC receives notification and pulls from Run Time Catalog Note: Configuration Design Tool UI to be integrated into Service Design & Creation
CE-2 | Service requests from Orchestration ONAP Optimization Framework (OOF) queries for VNF state and available capacity
CE-3 | Closed Loop action requests from Data Collection, Analytics & Events/Policy
CE-4 | Inventory retrieval from Active & Available Inventory by Service Logic Processing engine Inventory updates to Active & Available Inventory by Assigned Resources Inv
CE-5 | Lifecycle management requests to Multi-Cloud (e.g., stop/start VM)
CE-6 | Lifecycle management requests to an external controller or system that has responsibility of the target VNF
CI-1 | API Handler looks up or retrieves the corresponding Service Logic instance that maps to NB service request (service/network yang)
CI-2 | API Handler calls Service Control Processing to perform the Service Logic on the target service or network
CI-3 | Prior to CI-2, API Handler might query the (in-memory) Operational/Config Trees for the network or service details (if already existing)
CI-4 | Service Control Processing retrieves the Service Logic, Config Templates, Engineering rules, and Policies as part of processing the requested action
CI-5 | Service Control Processing queries and/or updates Operational/Config Trees as part of making changes to the network (VNFs/PNFs)
CI-6 | Service Control Processing requests adapter layer to update/configure VNF/PNF update using the appropriate adapter for the VNF/PNF
CI-7 | Service Control Processing queries and/or updates local Assigned Resources Store/Inventory as part of making changes to the network (VNFs/PNFs)

## Slide 9: GNFC – External Interface Details
 | Interface Definitions | Beijing Rel. | Casablanca Rel. | Protocol/Service | Comments
CE-1 | Distribution of artifacts from Service Design and Creation | SDC[no GNFC] | SDC  GNFC (trigger) GNFC  Run Time Catalog (pull) | DMaaP | 
CE-2 | Service requests from Orchestration Queries from ONAP Optimization Framework (OOF) for VNF state and available capacity | SO, Portal [no GNFC] OOF  [no GNFC] | SO, Portal  GNFC OOF queries – not in scope? | REST | Generic Request API. See next slide for orchestration requests for LCM actions.
CE-3 | Closed Loop action requests from Data Collection, Analytics & Events & Policy | DCAE  [no GNFC] Policy – not in scope | DCAE  GNFC Policy – not in scope | DMaaP | 
CE-4 | Inventory retrieval from Active & Available Inventory by Service Logic Processing engine Inventory updates to Active & Available Inventory by Assigned Resources Inventory | A&AI  [no GNFC] | A&AI  GNFC | REST | 
CE-5 | Configuration requests for cloud infrastructure networking Lifecycle management requests to Multi-Cloud (e.g., stop/start VM) | Multi-Cloud – not in scope | GNFC  M-Cloud | REST | 
Controllers are to be Model-Driven – APIs in Dev, Design, Run-Time catalogs
Payloads: parameter values defined in the platform Data Dictionary (model/meta-data driven)
CE-6 interface (to external controllers) is not needed and has been deleted. External controller will be interfacing to the whole ONAP platform – via CE-1 thru CE-4
Beijing Release does not have an implementation of GNFC
For Casablanca it is recommended that VF-C and APPC begin to transition toward GNFC

## Slide 10: Proposed LCM Actions for GNFC
Action | Netconf-XMLRestconf | Ansible | Chef | REST | OpenStack (VM Level) | Protocol is NotApplicable
ActionStatus |  |  |  |  |  | NA
AttachVolume |  |  |  |  | YES | 
Audit | YES | YES | YES | YES |  | 
CheckLock |  |  |  |  |  | NA
Configure | YES | YES | YES |  |  | 
Config Modify | YES | YES | YES |  |  | 
Config Backup |  | YES | YES |  |  | 
Config Restore |  | YES | YES |  |  | 
ConfigScaleOut | YES | YES | YES |  |  | 
DetachVolume |  |  |  |  | YES | 
Evacuate |  |  |  |  | YES | 
HealthCheck |  | YES | YES | YES |  | 
Lock |  |  |  |  |  | NA
Migrate |  |  |  |  | YES | 
QuiesceTraffic |  | YES | YES |  |  | 
Rebuild |  |  |  |  | YES | 
Restart |  |  |  |  | YES | 
ResumeTraffic |  | YES | YES |  |  | 
Snapshot |  |  |  |  | YES | 
Start |  |  |  |  | YES | 
Start Application |  | YES | YES |  |  | 
Stop |  |  |  |  | YES | 
Stop Application |  | YES | YES |  |  | 
Sync | YES | YES | YES | YES |  | 
Unlock |  |  |  |  |  | NA
UpgradeBackout |  | YES | YES |  |  | 
UpgradeBackup |  | YES | YES |  |  | 
UpgradePostCheck |  | YES | YES |  |  | 
UpgradePreCheck |  | YES | YES |  |  | 
UpgradeSoftware |  | YES | YES |  |  | 
Assign (new) |  |  |  |  |  | 
CapacityCheck (new) |  |  |  |  |  | 
Source: ONAP readthedocs

## Slide 11: SDN-Controller Architecture
SDN Controller configures and maintains the health of VNFs/PNFs for cloud networking (underlay/overlay) and WAN transport services* throughout their lifecycle
Programmable network application management platform
  Behavior patterns programmed via models and policies
  Standards based models & protocols for multi-vendor implementation
  Extensible SB adapter set supporting various network config protocols, including 3rd party controllers
  Operational control, coordinated state changes across devices, source of telemetry/events, etc.
Manages the health of VNFs/PNFs/transport services in its scope
  Policy-based optimization to meet SLAs
  Event-based control loop automation to solve local issues near real-time
  Action executor for outer control loop automation
Local source of truth
  Manages inventory within its scope
  All stages/states of lifecycle
  Configuration audits
Key Attributes of Controllers
  Intimate with network protocols
  Manages the state of services
  Single service/network domain scope per instance
Key
CE-x
CI-x
Controller External API
Controller Internal API
*How the services are to be handled is for further study
** Configuration Design Tool (CDT) to be integrated into SDC
***CE-6 not needed - see External Controller materials
MSB/Data Movement
MSB/Data Movement
MSB/Data Movement
OOF (for queries)
Policy
Service Control
Processing
SDN
Controller
NB Service/Network Yang Models
SB Device Yang Models
API Handler
Adapters
NetConf/ YANG
Multi-Cloud Network Adapter
BGP LS/
PCEP
Others
…
Multi-VIM/Cloud
Active & Available Inventory
Service Design & Creation
Orchestration
Data Collection, Analytics & Events
Closed Loop Actions
Inventory
Updates
Orchestration
Artifact Distribution
External System Adapter (s)
External
3rd Party Controllers
Element Mgt. Systems
CE-2
CE-3
CE-5
Service Logic
Repository
Service Logic
Service Logic
Service Logic
IP/VRF Assign
L2 Service Create
L3 VPN Service Create
SD-WAN Create
TE Tunneling
BGP Config
SW Upgrade
…
…
Configuration Templates
Service/Network Design & Engineering Rules
Policies
VNFs
PNFs
OpenFlow
Assigned Resources Inventory: Service* Topology &
VNF/PNF State
Operational Tree/
Config Tree
(Service Model)
CI-2
CI-4
CI-5
CI-3
CI-1
CI-6
CI-7
*Not E2E service view. The “Service” view in the SDN Controller is limited its scope of control
CE-6
CE-4
Configuration Design Tool UI**
Run time catalog
CE-1
CE-6 not needed***
Note: Beyond Casablanca, SDNC functionality and software will begin to merge into GNFC

## Slide 12: SDN-Controller – External/Internal Interface Definitions
Key
CE-x
CI-x
Controller External API
Controller Internal API
 | Interface Definitions
CE-1 | Distribution of artifacts from Service Design and Creation – artifacts distributed to Run Time Catalog, SDNC receives notification and pulls from Run Time Catalog Note: Configuration Design Tool UI to be integrated into Service Design & Creation
CE-2 | Service requests from Orchestration Queries from ONAP Optimization Framework (OOF) for VNF state and available capacity
CE-3 | Closed Loop action requests from Data Collection, Analytics & Events/Policy
CE-4 | Inventory retrieval from Active & Available Inventory by Service Control Processing engine Inventory updates to Active & Available Inventory by Assigned Resources Inventory
CE-5 | Configuration requests for cloud infrastructure networking Lifecycle management requests to Multi-Cloud (e.g., stop/start VM)
CE-6 | Lifecycle management or configuration requests to an external controller or system that has responsibility of the target VNF
CI-1 | API Handler looks up or retrieves the corresponding Service Logic instance that maps to NB service request (service/network yang)
CI-2 | API Handler calls Service Control Processing to perform the Service Logic on the target service or network
CI-3 | Prior to CI-2, API Handler might query the (in-memory) Operational/Config Trees for the network or service details (if already existing)
CI-4 | Service Control Processing retrieves the Service Logic, Config Templates, Engineering rules, and Policies as part of processing the requested action
CI-5 | Service Control Processing queries and/or updates Operational/Config Trees as part of making changes to the network (VNFs/PNFs)
CI-6 | Service Control Processing requests adapter layer to update/configure VNF/PNF update using the appropriate adapter for the VNF/PNF
CI-7 | Service Control Processing updates the local Assigned Resources Store/Inventory once network updates are made successfully

## Slide 13: SDNC – External Interface Definitions
 | Interface Definitions | Beijing Rel. | Casablanca | Protocol/Service | Comments
CE-1 | Distribution of artifacts from Service Design and Creation | SDC  SDNC | SDC  SDNC SDNC  Run Time Catalog | DMaaP | More artifacts distributed over time
CE-2 | Service requests from Orchestration Queries from ONAP Optimization Framework (OOF) for VNF state and available capacity | SO  SDNC OOF not in scope | SO  SDNC OOF  SDNC ?? | REST | Generic Resource API supports and config functions Limited LCM functions
CE-3 | Closed Loop action requests from Data Collection, Analytics & Events and Policy | DCAE  Not in scope Policy  Not in scope | DCAE  Not in scope? Policy  Not in scope? | DMaaP | 
CE-4 | Inventory retrieval from Active & Available Inventory by Service Logic/mServices Inventory updates to Active & Available Inventory by Assigned Resources Inv | A&AI  SDNC | A&AI  SDNC | REST | 
CE-5 | Configuration requests for cloud infrastructure networking Lifecycle management requests to Multi-Cloud (e.g., stop/start VM) | Multi-Cloud Not in scope | SDNC  M-Cloud | REST | 
DRAFT
Controllers are to be Model-Driven – APIs in Dev, Design, Run-Time catalogs
Payloads: parameter values defined in the platform Data Dictionary (model/meta-data driven)
CE-6 interface (to external controllers) is not needed and has been deleted. External controller will be interfacing to the whole ONAP platform – via CE-1 thru CE-4

## Slide 14: Common Software Library Approach for Creating ONAP Sub-System Personas
AT&T Labs

## Slide 15: SDK-Driven Sub-System – Libraries (including CCSDK)
*Plugins/Adapters can include:
3rd party VNFM Drivers • 3rd party EMS Drivers
3rd party SFC Drivers • Ansible/Chef/Puppet
Netconf/Yang • CLI
SNMP • etc.
SDK Libraries
Orchestrators
Rackspace
IBM
Google
Orchestration Function SDK
Multi-Cloud Adaptation SDK
Controllers
OpenStack
Azure
AWS
OSSs
VNFs
PNFs
Multi-Cloud
μServices
Control Function SDK (CCSDK)
ODL
Imperative Models
BPMN orchestration
engine
Sub-Models
TOSCA-Cloud
Translation/Mapper
Declarative Models
TOSCA orchestration
engine
Library of
Common Control/NFV Lifecycle Mgt. Functions
Rebuild
VNF Configure
Network Config.
Stop/Start
A udit
Upgrade
Scale
Svc Function Chain
Heal
Library of
Common Cloud Translations (shims)
Telemetry
Scale
Heal
Register
Cloud Resource
Instantiation
LB
…
SB API SDK
(Adapters)
Plugins/Adapters*
M-Cloud APIs
etc.
NB API SDK
API Handler
API Catalog
Library of Flows
Service, Resource, Etc.
Orchestration APIs
Controller APIs
Cloud APIs
API Configurator
Controller APIs
OSS APIs
μServices APIs
Netconf/Yang
Ansible
Collectors
OpenStack
Azure
AWS
API Catalog
ONOS
Open
ROADM
…
…
Resource Orchestration APIs
Assign
Health Check
…
…
Improve agility
Reduce SW footprint
Reusable framework
Enable technology swap
Consistent NB/SB APIs
Flexible platform extensions
Benefits

## Slide 16: Controller Personas Based on CCSDK Libraries
CCSDK Libraries
Controller Personas Examples
(created from CCSDK)
SDN-C Persona
NB API
Controller APIs
Control Functions
ODL/
Service Control
Library
VNF Configure
Network Config
Svc Function Chain
Assign
SB
API
Other Adapters
OSS APIs
μServices APIs
Netconf/Yang
…
…
Mobility NF Controller Persona
NB API
Controller APIs
Configure & LCM Functions
Service Logic
Engine
Library
SB
API
Ansible
μServices APIs
Netconf/Yang
Rebuild
Stop/Start
Audit
HealthCk
Scale
Heal
Other engines
3rd VNFM/EMS
3rd Party SFC
VNF Configure
Svc Function Chain
OSS APIs
Other Adapters
…
…
…
Wireline NF Controller Persona
NB API
Controller APIs
Configure & LCM Functions
Service Logic
Engine
Library
SB
API
Ansible
μServices APIs
Netconf/Yang
Rebuild
Stop/Start
Audit
HealthCk
Scale
Heal
Other engines
3rd VNFM/EMS
3rd Party SFC
VNF Configure
Svc Function Chain
OSS APIs
Other Adapters
…
…
…