## Slide 1: ONAP Reference Architecture for R2 and Beyond Tiger Team Presentation Parviz Yegani – Futurewei Technologies Contributors: Vimal Begwani (AT&T), Jamil Chawki (Orange), Andrew Mayer (AT&T), Ramki Krishnan (VMware), Maopeng Zhang (ZTE), Stephen Terrill (Ericsson) Dec. 8, 2017

## Slide 2: ONAP High-Level Architecture for R1 (Amsterdam)

## Slide 3: Progress from the Architecture Subcommittee
For Amsterdam (R1), the architecture was agreed, as discussed since ONS.
  This was to reduce risk of late changes to the project teams, who have built their plans based on the current baseline.
Starting with R2, there is consensus to resolve the following two architectural inconsistencies:
  Orchestration Architecture
    - Architecture team agreed that Orchestration layer should be separate from Controller layer
  Consistent Controller Layer Architecture and better alignment between App-C & VF-C
  Projects are drilling down to the next level of detail on interfaces and project alignment, and then the projects will review their R2 plans with the ARC.
The next slide illustrates high-level architectures that was approved by TSC to meet R1 schedule.

## Slide 4: ONAP Amsterdam Architecture
Policy Creation & Validation
VNF SDK
Portal Framework, U-UI, ONAP CLI
Resource Onboarding
Service & Product Design
Recipe/Eng Rules & Policy Distribution
ONAP Operations Manager (OOM)
Dashboard OA&M (VID)
A&AI/ESR
External API Framework
Micro Services Bus (MSB)
DMaaP
AAF
DCAE
Correlation Engine
(Holmes)
Logging
Policy Framework
SDN-C
(L0-L3 Controller)
Multi-VIM/Cloud
Infrastructure Adaptation Layer
CCSDK
External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Commercial VIM
Public Cloud
…
3rd Party Controller
sVNFM
EMS
VNFs
PNFs
…
Service Orchestration
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Application Controller
(L4-L7)
Virtual Function Controller
(ETSI-aligned)
CLAMP
Catalog
DESIGN-TIME (SDC)
RUN-TIME
Public
Cloud
Common Services
Notes: Key points:
Unified framework for design-time & run-time
  Common platform for service design and netops to drive collaboration
Simultaneous orchestration of physical and virtual networks
  Vendor-agnostic orchestration can only happen in open source context
Real-time analytics and closed-loop automation
  Easy re-use of service concepts
  Iterative service improvements based on network feedback

## Slide 5: ONAP Reference Architecture for R2 and Beyond

## Slide 6: Architecture Design Considerations
Architecture Principles Were Reviewed Earlier and Agreed Upon by the Architecture Team:
  https://wiki.onap.org/display/DW/Contributions?preview=/8225716/8232492/Architectural%20principles_v3.docx
ONAP is a layered architecture – Orchestration, Multi-Cloud, Controller, etc.
Functional role of each layer should be well defined per the architecture principles agreed by the architecture team (see the above link).
ONAP should support integrated design studio to capture full lifecycle management models (TOSCA models for NF, simple / nested services augmented with BPMN, Policy / Analytic design models, etc.)
ONAP Should Support Cloud Agnostic Model and Multi-Cloud adaption layer while hiding infrastructure details
ONAP Target Goal is: Modular, Model-driven, Microservices-based architecture
  Models drive interfaces between layers/components
ONAP should define well described NB-APIs at all layers
Keep flexible capability for commercial solution (no vendor lock-in)
Agree to unified modeling for integration across all modules: VES in DCAE, Logging & monitor inside ONAP and more

## Slide 7: ONAP Target Architecture for R2 and Beyond (High-Level Functional View)
DESIGN-TIME
Policy Creation & Validation
Analytic Application Design
VNF / PNF Onboarding
Resource Onboarding
Service Design
Catalog
Recipe/Eng Rules & Policy Distribution
ONAP Optimization Framework
ONAP Operations Manager
Dashboard OA&M
ONAP External APIs
Common
Services
Application
Authorization
Framework
Logging
Policy Framework
Active & Available Inventory
External Registry
Generic NF Controllers (L4-L7)
Data Collection, Analytics, and Events
Event Correlation
ONAP Optimization Framework
SDN Controller
(L0-L3)
Adaptation Layer
External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Azure
VMware
RackSpace
…
3rd Party Controller
AMZ
VNFs
PNFs
Public
Cloud
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Orchestration
Micro Services Bus / Data Movement (see Note 1)
Others
Closed Loop Design
Change Management Design
Adaptation Layer
Life Cycle Management & Config
Design Test & Certification
Common Controller SDK
External Gateway
CLI
OSS / BSS
ONAP Portal
Note 1 – Not all components use DMaaP (e.g., NFVO)
Specific VNF Manager
Element Management System
RUN-TIME
Common Services
Multi-Cloud
Adaptation
Infrastructure
Adaptation Layer
U-UI

## Slide 8: ONAP Beijing Architecture (High-Level View with Projects)
DESIGN-TIME (SDC)
Policy Creation & Validation
VNF SDK
Resource Onboarding
Service & Product Design
Catalog
Recipe/Eng Rules & Policy Distribution
ONAP Operations Manager
Dashboard OA&M (VID)
ONAP External APIs
Common
Services
AAF
Logging
Policy Framework
A&AI/ESR
DCAE
Correlation
Engine (Holmes)
OOF
SDN-C
(L0-L3 Controller)
External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Azure
VMware
RackSpace
…
3rd Party Controller
AMZ
VNFs
PNFs
Public
Cloud
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Service Orchestration
Project
MSB/DMAAP
…
Change Management Design
Design Test & Certification
CCSDK
External Gateway
ONAP CLI
OSS / BSS
ONAP Portal
sVNFM
EMS
RUN-TIME
Common Services
Multi-VIM/Cloud
Infrastructure Adaptation Layer
CLAMP
Application Controller
(APPC)
(L4-L7)
Virtual
Function Controller
(VF-C)
(Note 1)
U-UI
Note 1 - VF-C is ETSI-aligned.

## Slide 9: ONAP Orchestration Alignment:

## Slide 10: ONAP Orchestrator Functions
Orchestrate Network Functions (VNF/PNF), and Network Services (NSes), and services provided by the managed environment
Coordinate cross-controller activities driven by orders and events to
  LCM (instantiate/modify/upgrade/configure/remove) VNFs/PNFs, Nses, and services from the managed environment
  perform multi-control layer remedy actions.
Key Attributes of Orchestrator:
Model Driven Orchestration
  Process behavior driven by resource / service model designed in SDC
  Orchestrates network functions and service LCM (Instantiations, ..) , including compound / nested services (parts already in R1)
    Nesting may be domain-specific orchestrator (does not require SO clone)
  Support software upgrade and planned change management
  Support open & closed-loop control actions initiated by DCAE /Policy or external API (e.g. OSS for Open Loop)
  Tracks orchestrated activity for the life of the request but doesn’t control state of orchestrated components
Interfaces to External OSS / BSS Systems
  Standard APIs exposed northbound to create, modify or remove services and resources
  Request decomposition of service request into service / network function components
  Selects model / recipe that supports the request and maps order data to recipe / model
Coordinating Activities Across Various ONAP Controllers
  Coordinates activities across Multi-Cloud (infrastructure) / SDN-C / APPC / VF-C controllers
  Manage recording of service configurations
Orchestrator Performs Following Additional Services
  Coordinates current inventories and placement/optimization recommendations
  Enforces business & technical policies
  Support standards-based workflows
  Validates and records network functions / service implementations

## Slide 11: Examples of Orchestration Requests
Install/Configure a single network function (VNF or PNF) – e.g. Deploy a new virtual PE / P router
  A virtual network element might have one or more components (e.g VNFCs or VDUs)
Install multiple copies of network functions in one or more data centers – e.g. Deploy new virtual PE / P routers across multiple locations
Deploy one or more instances of network services – e.g. RAN at Multiple sites, one or more sites of EPC, etc.
Deploy E2E network services (e.g. RAN + EPC + IMS) and services from the managed environment
Instantiate and LCM a customer services – e.g. multi-site VPN or IP SEC
  Could require deploying new instances of network elements (e.g. vCE) and using existing elements (e.g. vPE)
  Could be using existing elements without any new VNF / PNF being deployed (e.g. “Allocated Resources” – configuring a service to existing components)
Create a new instance of a network slice segment
  Could be leveraging existing network services (RAN, vEPC, etc.)
Create a new instance of a network service slice – e.g. IoT or eMBB slice
  Could be leveraging previously created network slice segments
Implement a software upgrade / change management
  Could require Coordination of activities across Multi-VIM (infrastructure)/SDN-C/app-C/VF-C controllers
Orchestrate remedial actions requested as part of Closed or open loop action
  Could require adding new compute / network resource to the existing functional elements (i.e. VNF)
  Create a new instance of VNF and migrate traffic
  Could require Coordination of activities across Multi-Cloud (infrastructure)/SDN-C/App-C/VF-C controllers)

## Slide 12
Service X:
topology_template:
node_templates:
PNF
Network
VNF
Allotted Resource
PNF
Model-Driven Orchestration (Recursive Structure)
Service Orchestration
Network
VNF
Allotted Resource
requirement: A
VF Module
Service Y:
topology_template:
node_templates:
PNF
Network
VNF
Allotted Resource
capability: A
PNF
Service Orchestration
Network
VNF
Allotted Resource
Resource Orchestration
Cloud Resource Orchestration
Resource Orchestration
An Allotted Resource can be homed to an existing “underlying” network function or Service Instance, or homing could determine that a new network function Service Instance is needed. This would result in a 2nd level of Service Orchestration.
Each Resource Type has its own “Generic” model-driven flow. There currently exist such flows for “VNF” and “Network” Resource Types.
“Generic” model-driven Service flow
Note recursion
Service Y is being treated as a “Resource” from the perspective of Service X.

## Slide 13: Nested / Compound Services:
Service W:
topology_template:
node_templates:
VNF_W
Service_X
Service X:
topology_template:
node_templates:
VNF_X
Service_Y
Service Y:
topology_template:
node_templates:
VNF_Y
Service_Z
Service Z:
topology_template:
node_templates:
VNF_Z

## Slide 14: Conclusions
Service Providers require the ability to define Services that can be leveraged by higher order Services and other compounded services / segments / slices.
Consistent with ETSI MANO, ONAP should NOT separate Service Orchestration and Resource Orchestration into two separate named components, because each Resource can be exposed as a Service
      What appears as a “Resource” from one Service’s perspective, may actually be a Service from another perspective
      In Addition, ONAP scope is much broader than ETSI MANO (MANO limited to Cloud infrastructure services and management of VNF as a basic resource (ignoring the application of the VNF)), therefore SO should support full orchestration scope of ONAP
      To achieve alignment with MANO for common functionality, SO should expose APIs for basic resource onboarding/LCM (VNF) or simple network service onboarding/LCM (composed of one or more VNFs) and related models. This is SOL-001, SOL-004 and SOL-005.
      In addition, ONAP SO should Support “Service reuse” to drive model driven run-time behavior for complex services:
        Compounded Services (e.g. Residential vCPE, Network Slicing Segments, etc.)
        Nested Services (e.g. E2E Slice)
      ONAP should provide Service Providers deployment flexibility to address scalability, geographic distribution and redundancy / resiliency
      But should not impose extra complexity and cost on service providers by separating service / resource orchestration that provides little known benefit

## Slide 15: APPC & VF-C Convergence Note – A major goal of the ONAP platform (R2 or a later release) is to specify a common set of functions to unify the APP-C and VF-C functionalities.

## Slide 16: Role Of Controllers in ONAP
ONAP Controllers configure and maintain the health of network functional elements and services throughout their lifecycle.
Programmable network application management platform
  Behavior patterns programmed via models and policies
  Standards based models & protocols for multi-vendor implementation
  Operational control, coordinated state changes across devices, etc.
Manages the health of the network services & VNFs in its scope
  Policy-based optimization to meet SLAs
  Event-based control loop automation to solve local issues in near real-time
  Executes action for outer control loop automation (Driven by DCAE, Policy, etc.)
Local source of truth
  Manages inventory within its scope
  All stages/states of lifecycle
  Configuration audits
  ONAP has a layered architecture, with the role of controller clearly defined
  Need to avoid duplicating functions across layers within the controller layer (e.g. DCAE, Service/Resource Orchestration, etc.)

## Slide 17: Generic VNFM Functions
To Be Updated

## Slide 18: Next Steps – Solidify Beijing Architecture with Projects
Agree and approve the proposed R2+ architecture
      Identify project impact to realize target orchestration implementation in R2
      Create a small team from SO, VF-C, App-C and CCSDK teams to identify phased approach to achieve controller alignment in ONAP Platform

## Slide 19: ONAP Target Functional Architecture (Detailed View) (Work in progress)

## Slide 20: ONAP R2+ Architecture – Merged View
Design-time (SDC)
Policy Creation & Validation
Analytic Application Design
VNF/PNF SDK
Portal Framework – UI,
ONAP CLI
Resource Onboarding
Service Design
Catalog
Testing & Certification
Recipe/Eng Rules & Policy Distribution
ONAP Optimization Framework (OOF)
ONAP Operations Manager (OOM)
Run-time
Dashboard OA&M (VID)
External API
Common
Services
AAF
Logging
OOF
External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Azure
VMware
RackSpace
…
3rd Party Controller
sVNFM
AMZ
EMS
VNFs
PNFs
…
Public
Cloud
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Micro Services Bus/DMaaP
Orchestration (SO)
(recursive)
  Service Level
  Resource Level
Resources
Eng. Rules
Services
Policies
Analytics
Adaptation Layer
SLI
Config/
Oper. DB
Yang
Netconf
CLI
SDN-C DB
SDN-C (L0-L3)
Controller
Driver
Config Database
Standard Adaptation Layer
SLI
LCM-DG
Chef
Netconf
Ansible
Generic VNF Controller (L4-L7)
VNFM/EMS
Driver
Multi-Cloud Adapt.
Discovery
Cloud/VIM Drivers
Workload
Networking
Telem. Coll.
Cloud Models
Data Collection Layer
Data Distribution
CDAP
Holmes
DCAE Analytic µServices
Policy Framework
Resource /Service Topology
Active / Available
A&AI
…
ESR
DCAE
CCSDK
Work in Progress

## Slide 21: ONAP Orchestration Federation (Work in progress)

## Slide 22: External API Functional Requirements
The ONAP External API supports
  Interactions between ONAP and the Service Provider’s BSS/OSS,
  Interactions between ONAP of a Service Provider and other Partner Providers.
  MEF LSO characterizes these Service Provider to Partner Provider interactions at the Service Level as the Interlude Interface Reference Point
    This Interface Reference Point provides for the coordination of a portion of Services within the Partner domain that are managed by a Service Provider’s Orchestration Functionality within the bounds and policies defined for each Service.
It is envisioned that from a Service Provider to Partner Provider interaction context (i.e. MEF Interlude), the ONAP External API supports the following types of interacts:
  Service Provider controls aspects of the Service within the Partner domain (on behalf of the Customer) by requesting changes to dynamic parameters as permitted by service policies,
  Service Provider queries state of the Service,
  Service Provider requests change to administrative state or permitted attributes of a Service,
  Service Provider request creation of connectivity between two Service Interfaces as permitted by established business arrangement,
  Service Provider request instantiation of functional service components as permitted by established business arrangement,
  Service Provider queries the Partner for detailed information related to Services provided by the Partner to the Service Provider,
  Service Provider receives Service specific event notifications (e.g., Service Problem Alerts) from the Partner,
  Service Provider receives Service specific performance information from the Partner,
  Service Provider request Service related test initiation and receive test results from the Partner.
Work in Progress

## Slide 23: Backup Slides Functional Description of ONAP Architecture Components Under Review … (both contributions & comments)

## Slide 24: Service Design and Creation Architecture
Comprehensive design studio that enables technology integration
Design studio modules interoperate to enable complex relationships & models
Create or consume models to represent services, resources & management functions
Models, APIs/functions, flows, analytics & policies cataloged together or independently
Service Design & Creation
  Design Studio with Guided User Workflow
  Resource Onboarding
  Define/Compose Services & Products
  Define/Compose Policy-Driven Recipes
  Open Catalog-based Platform for Model/Object Reuse
Policy Creation Framework
  Policy Editor & Library
  Conflict Identification
  Closed-loop, Security & Audit Behavior
Analytic Application Design Environment
  Analytic App Design
  Tools for Analytic Development
  Security & Traffic Analytics
  Analytic Lifecycle Management
Certification
  Simulate, test, track & certify the create/mod processes
  Certify Readiness & Adherence to Standards
  Track and manage versions of models and catalog entries
Metadata Distribution
  Publish Definitions via SDK, API or Distribution
  Notifications & Version Control
  Real-Time Reference Data

## Slide 25: SDC Catalog Architecture
Design Catalog
  Product/Service/Resource objects
  The instruction to manage D2 objects
  Resource and Service design lifecycle management processes
  Node based presentation to provide sequencing and relationships of different objects and technologies
  Generic re-usable management methods
Development Catalog
  Common toolsets for creation of ONAP capabilities and management procedures
  Interact with external software development teams and suppliers to onboard custom software, adapters or new VNFs
Runtime Catalog
  Certified models are distributed to runtime catalog for ONAP execution components runtime consumption
  Provide runtime access to models
A smart repository for storing products ,services , resources and artifacts
Manages catalog’s elements versions, lifecycle and access policy
All certified asset definitions available for re-use and composition
Developer Contribution & Self-Serve Models
Product????????
D2????????
Onboard services as well if they are already defined??

## Slide 26: Service Orchestrator
Model Driven Orchestration and APIs
  Runtime behavior driven by service and resource models and policies (including compound/nested services) designed in SDC
  Orchestrates service delivery, change management as well as open and closed-loop control actions
  Provides standard, model driven APIs for requested actions
  Tracks orchestrated activity for the life of the request, but doesn’t control or maintain state of orchestrated components
Service Orchestrator (SO) orchestrates service, resources and associated cross-controller activity driven by requests and events that indicate the need to create, modify or remove service and resource instances, or to perform multi-control layer remedy actions.
Processing of Service Requests:
  Performs Decomposition, Recipe Selection, Recipe Execution (including Rainy Day)
  Triggers and Records Results for:
  Homing
  Assign, Create, Configure (Controller/multi-cloud activity)
  Validation
  Monitoring
  Separate execution threads for service, decomposed resources, and any subtending service(s) provide nested service orchestration in a recursive manner
Orchestration of Controllers
  Coordinates activities across Multi-Cloud/SDN-C/Generic VNF controllers, including data sourcing and mapping to Controller inputs
Orchestrator now
MSO????
I don’t understane the VNF adapater part here

## Slide 27: Generic VNF Controller (L4-7) Architecture
Generic VNF Controller for L4-7 configures and maintains the health of applications throughout its lifecycle.
  The Lifecycle Management Functions are a normalization of VF-C and APP-C functions into a common, extensible library
Programmable network application management platform
  Behavior patterns programmed via models and policies
  Standards based models & protocols for multi-vendor implementation
  Extensible SB adapter set including vendor specific VNF-Managers
  Operational control, version management, software updates, etc.
Manages the health of the applications/VNFs within its scope
  Policy-based optimization to meet SLAs
  Event-based control loop automation to solve local issues near real-time
Local source of truth
  Manages inventory within its scope
  All stages/states of lifecycle
  Configuration audits
Key Attributes of VNF Controllers
  Intimate with network protocols
  Manages the state of services
  Provide Deployment Flexibility to meet user scalability / resilience needs
Generic VNF
Controller
Adapters
Service Logic Interpreter
VNF Manager Adapter (s)
Chef
Configuration Repository
Config Templates
REST
Service Topology & VNF State
Service Logic
Service Logic
Service Logic
Config mS
Auto-Recovery mS
Audit mS
Netconf
Operational/ Config Tree
(Service Model)
Web Server
Policy Cache & Event Matching
…
API Handler
A&AI
SDC
Ansible
Others
Lifecycle Management mS Library
…
Multi-Cloud Adapter
NF
I don’t see the VNFM part and the interface to the S-VNFM/EM here

## Slide 28: SDN-Controller Architecture
SDN Controller configures and maintains the health of L1-3 VNFs/PNFs and network services throughout their lifecycle
Programmable network application management platform
  Behavior patterns programmed via models and policies
  Standards based models & protocols for multi-vendor implementation
  Extensible SB adapter set supporting various network config protocols, including 3rd party controllers
  Operational control, coordinated state changes across devices, source of telemetry/events, etc.
Manages the health of network services & VNFs/PNFs in its scope
  Policy-based optimization to meet SLAs
  Event-based control loop automation to solve local issues near real-time
  Action executor for outer control loop automation
Local source of truth
  Manages inventory within its scope
  All stages/states of lifecycle
  Configuration audits
Key Attributes of Controllers
  Intimate with network protocols
  Manages the state of services
  Single service/network domain scope per instance
Service Control
Interpreter
SDN Controller
Network Resource
Controller
Service
Element
Resources
Core &
Transport
Resources
Access
Service
Features
Flow
Service
Features
Configuration Repository
Svc Template A
Svc Template B
Svc Comp 1
Svc Comp 2
API Handler
Adapters
NetConf/ YANG
Multi-Cloud Network Adapter
BGPCEP
SDC
A&AI
3rd Party
Controllers
Network/Service Design/Engineering Policies/Rules
Others
…

## Slide 29: Data Collection, Analytics and Events (DCAE) Architecture
DCAE enables real-time fault, performance and other data/event collection from service, network and infrastructure
  Collect Data & Events once and make available to multiple applications
  Telemetry records from VNFs and PNFs (fault, performance, usage, etc.)
Makes collected data available to real-time analytic µ-services to:
  Identify anomalies and other events for closed loop remediation
  Enable closed-loop automation to remedy fault/performance conditions
  Enable closed-loop automation to scale resources up/down
  Enable analysis at edge and central locations
  Extensible framework to integrate applications from various sources
Provides Correlation & Analysis to manage service at various layers
  Multi-Cloud Infrastructure layer, network element layer, Network & Complex Services layer, Operational Management layer
  Cross-layer, Intra-domain and cross-domain correlation
Streaming
Data
Batch
Data
SNMP
Syslog
Other
Unstructured & Structured Data Persistence
Analytic Frameworks:
Holmes, CDAP, Other
Stream Data Collection
Events
Flows
Other
Batch Data Collection
Analytic µServices
Capacity Management
DCAE
Congestion Detection
Fault Correlation
QoS Monitoring
Security Analysis
Managed Environment
Storage
Compute
VNFs / PNFs
Applications
Networking
Logs
Files
Other
Multi-Cloud Telemetry Adaption
…
VES
DMaaP (Pub/Sub for Events/Data within DCAE & across ONAP)
OOM – DCAE Controller

## Slide 30: Active and Available Inventory
A&AI tracks the global inventory of the networks, services & resources that ONAP manages.
  The what, where, when of the managed assets and their relationships, and which controller or orchestrator manages them.
Real-time, logically centralized view of topology & inventory
  Map and broker of data sources in the global network
  Federates across controllers, cloud infrastructure, partners, etc.
  Real-time access to authoritative sources with ability to aggregate views
  Real-time awareness of network elements, applications and service instances
  Aware of all the assets in scope, organized by their type, state & location
  Keeps track of the dynamic relationships of the virtual assets
  Aware of resource assignments, availability & relationships to customer
Network events used to maintain the integrity of inventory
  Monitors network events to register services, networks & resources
  Tracks creation, modification or removal of entities and relationships
A&AI
API Handler
A&AI Application Management Functions
Data Audits
History
Archival
OA&M
Notifications
Event Subscriptions
A&AI Data Management Services
Inventory & Topology Management
Service
Network
Resource
Infrastructure
Active
Topology
Assignment
Available
Entitlement
Reference
Inventory & Topology
Entitlements & Reference
Graph Layer
Metadata Engine
API Generation
Schema Generation
Version Management
Metadata Management
Model-driven
  Schema, APIs, database views, data integrity mechanisms generated from models expressed in TOSCA.

## Slide 31: Multi-Cloud Adaptation Layer
Ramki to provide this slide