## Slide 1: ONAP Reference Architecture for R2 and Beyond Tiger Team Presentation Parviz Yegani – Futurewei Technologies Contributors: Vimal Begwani (AT&T), Jamil Chawki (Orange), Andrew Mayer (AT&T), Alex Vul (Intel), Ramki Krishnan (VMware), Maopeng Zhang (ZTE), Stephen Terrill (Ericsson) Dec. 8, 2017

## Slide 2: ONAP High-Level Architecture for R1 (Amsterdam)

## Slide 3: Progress from the Architecture Subcommittee
For Amsterdam (R1), the architecture was agreed, as discussed since ONS.
  This was to reduce risk of late changes to the project teams, who have built their plans based on the current baseline.
Starting with R2, there is consensus to resolve the following two architectural inconsistencies:
  Orchestration Architecture
    - Architecture team agreed that Orchestration layer should be separate from Controller layer
  Consistent Controller Layer Architecture and better alignment between App-C & VF-C
  Projects are drilling down to the next level of detail on interfaces and project alignment, and then the projects will review their R2 plans with the ARC.
The next slide illustrates high-level architectures that was approved by TSC to meet R1 schedule.

## Slide 4: ONAP Amsterdam Architecture
Policy Creation & Validation
VNF SDK
Portal Framework, U-UI, ONAP CLI
Resource Onboarding
Service & Product Design
Recipe/Eng Rules & Policy Distribution
ONAP Operations Manager (OOM)
Dashboard OA&M (VID)
A&AI/ESR
External API Framework
Micro Services Bus (MSB)
DMaaP
AAF
DCAE
Correlation Engine
(Holmes)
Logging
Policy Framework
SDN-C
(L0-L3 Controller)
Multi-VIM/Cloud
Infrastructure Adaptation Layer
CCSDK
External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Commercial VIM
Public Cloud
…
3rd Party Controller
sVNFM
EMS
VNFs
PNFs
…
Service Orchestration
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Application Controller
(L4-L7)
Virtual Function Controller
(ETSI-aligned)
CLAMP
Catalog
DESIGN-TIME (SDC)
RUN-TIME
Public
Cloud
Common Services
Notes: Key points:
Unified framework for design-time & run-time
  Common platform for service design and netops to drive collaboration
Simultaneous orchestration of physical and virtual networks
  Vendor-agnostic orchestration can only happen in open source context
Real-time analytics and closed-loop automation
  Easy re-use of service concepts
  Iterative service improvements based on network feedback

## Slide 5: ONAP Reference Architecture for R2 and Beyond

## Slide 6: Architecture Design Considerations
Architecture Principles Were Reviewed Earlier and Agreed Upon by the Architecture Team:
  https://wiki.onap.org/display/DW/Contributions?preview=/8225716/8232492/Architectural%20principles_v3.docx
ONAP is a layered architecture – Orchestration, Multi-Cloud, Controller, etc.
Functional role of each layer should be well defined per the architecture principles agreed by the architecture team (see the above link).
ONAP should support integrated design studio to capture full lifecycle management models (TOSCA models for NF, simple / nested services augmented with BPMN, Policy / Analytic design models, etc.)
ONAP Should Support Cloud Agnostic Model and Multi-Cloud adaption layer while hiding infrastructure details
ONAP Target Goal is: Modular, Model-driven, Microservices-based architecture
  Models drive interfaces between layers/components
ONAP should define well-described and consistent NB-APIs at all layers
Keep flexible capability for commercial solution (no vendor lock-in)
Agree to unified modeling for integration across all modules: VES in DCAE, Logging & monitor inside ONAP and more

## Slide 7: ONAP Target Architecture for R2 and Beyond (High-Level Functional View)
DESIGN-TIME
Policy Creation & Validation
Analytic Application Design
VNF / PNF Onboarding
Resource Onboarding
Service Design
Catalog
Recipe/Eng Rules & Policy Distribution
ONAP Optimization Framework
ONAP Operations Manager
Dashboard OA&M
ONAP External APIs
Common
Services
Application
Authorization
Framework
Logging
Policy Framework
Active & Available Inventory
External Registry
Generic NF Controllers (L4-L7)
Data Collection, Analytics, and Events
Event Correlation
ONAP Optimization Framework
SDN Controller
(L0-L3)
Optional External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Azure
VMware
RackSpace
…
3rd Party Controller
AMZ
VNFs
PNFs
Public
Cloud
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Orchestration
Micro Services Bus / Data Movement (see Note 1)
Closed Loop Design
Change Management Design
Life Cycle Management & Config
Design Test & Certification
External Gateway
CLI
OSS / BSS
ONAP Portal
Note 1 – Consistent APIs between Orchestration layer and Controllers
Specific VNF Manager
Element Management System
RUN-TIME
Common Services
Multi-Cloud
Adaptation
U-UI
Others
(see Note 1)
(see Note 1)

## Slide 8: ONAP Beijing Architecture (High-Level View with Projects)
DESIGN-TIME (SDC)
Policy Creation & Validation
VNF SDK
Resource Onboarding
Service & Product Design
Catalog
Recipe/Eng Rules & Policy Distribution
ONAP Operations Manager
Dashboard OA&M (VID)
ONAP External APIs
Common
Services
AAF
Logging
Policy Framework
A&AI/ESR
DCAE
Correlation
Engine (Holmes)
OOF
SDN-C
(L0-L3 Controller)
External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Azure
VMware
RackSpace
…
3rd Party Controller
AMZ
VNFs
PNFs
Public
Cloud
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Service Orchestration
Project
MSB/DMAAP
…
Design Test & Certification
CCSDK
External Gateway
ONAP CLI
OSS / BSS
ONAP Portal
sVNFM
EMS
RUN-TIME
Common Services
Multi-VIM/Cloud
Infrastructure Adaptation Layer
CLAMP
Application Controller
(APPC)
(L4-L7)
Virtual
Function Controller
(VF-C)
(Note 1)
U-UI
Note 1 - VF-C is ETSI-aligned.
Change Management Design
      Tiger team agreed to take the following steps to create the project view for the Beijing Release based on the target functional architecture (see slide 7):
      Create a small team from SO, VF-C, APPC and CCSDK teams to identify
        project impact to realize target orchestration and controllers implementation in R2 as well as the
        phased approach to achieve controller alignment in ONAP Platform.
      Provide recommendations as to what subset might be reasonable in Beijing, given current resources and other “carrier grade” priorities.
      The deadline to make the final architecture deck ready for the ARC Subcommittee is Jan. 5th, 2018.

## Slide 9: ONAP Orchestration Alignment:

## Slide 10: ONAP Orchestrator Functions
Orchestrate Network Functions (VNF/PNF), and Network Services (NSes), and services provided by the managed environment
Coordinate cross-controller activities driven by orders and events to
  LCM (instantiate/modify/upgrade/configure/remove) VNFs/PNFs, Nses, and services from the managed environment
  perform multi-control layer remedy actions.
Key Attributes of Orchestrator:
Model Driven Orchestration
  Process behavior driven by resource / service model designed in SDC
  Orchestrates network functions and service LCM (Instantiations, ..) , including compound / nested services (parts already in R1)
    Nesting may be domain-specific orchestrator (does not require SO clone)
  Support software upgrade and planned change management
  Support open & closed-loop control actions initiated by DCAE /Policy or external API (e.g. OSS for Open Loop)
  Tracks orchestrated activity for the life of the request but doesn’t control state of orchestrated components
Interfaces to External OSS / BSS Systems
  Standard APIs exposed northbound to create, modify or remove services and resources
  Request decomposition of service request into service / network function components
  Selects model / recipe that supports the request and maps order data to recipe / model
Coordinating Activities Across Various ONAP Controllers
  Coordinates activities across Multi-Cloud (infrastructure) / SDN-C / APPC / VF-C controllers
  Manage recording of service configurations
Orchestrator Performs Following Additional Services
  Coordinates current inventories and placement/optimization recommendations
  Enforces business & technical policies
  Support standards-based workflows
  Validates and records network functions / service implementations

## Slide 11: Examples of Orchestration Requests
Install/Configure a single network function (VNF or PNF) – e.g. Deploy a new virtual PE / P router
  A virtual network element might have one or more components (e.g VNFCs or VDUs)
Install multiple copies of network functions in one or more data centers – e.g. Deploy new virtual PE / P routers across multiple locations
Deploy one or more instances of network services – e.g. RAN at Multiple sites, one or more sites of EPC, etc.
Deploy E2E network services (e.g. RAN + EPC + IMS) and services from the managed environment
Instantiate and LCM a customer services – e.g. multi-site VPN or IP SEC
  Could require deploying new instances of network elements (e.g. vCE) and using existing elements (e.g. vPE)
  Could be using existing elements without any new VNF / PNF being deployed (e.g. “Allocated Resources” – configuring a service to existing components)
Create a new instance of a network slice segment
  Could be leveraging existing network services (RAN, vEPC, etc.)
Create a new instance of a network service slice – e.g. IoT or eMBB slice
  Could be leveraging previously created network slice segments
Implement a software upgrade / change management
  Could require Coordination of activities across Multi-VIM (infrastructure)/SDN-C/app-C/VF-C controllers
Orchestrate remedial actions requested as part of Closed or open loop action
  Could require adding new compute / network resource to the existing functional elements (i.e. VNF)
  Create a new instance of VNF and migrate traffic
  Could require Coordination of activities across Multi-Cloud (infrastructure)/SDN-C/App-C/VF-C controllers)

## Slide 12
Service X:
topology_template:
node_templates:
PNF
Network
VNF
Allotted Resource
PNF
Model-Driven Orchestration (Recursive Structure)
Service Orchestration
Network
VNF
Allotted Resource
requirement: A
VF Module
Service Y:
topology_template:
node_templates:
PNF
Network
VNF
Allotted Resource
capability: A
PNF
Service Orchestration
Network
VNF
Allotted Resource
Resource Orchestration
Cloud Resource Orchestration
Resource Orchestration
An Allotted Resource can be homed to an existing “underlying” network function or Service Instance, or homing could determine that a new network function Service Instance is needed. This would result in a 2nd level of Service Orchestration.
Each Resource Type has its own “Generic” model-driven flow. There currently exist such flows for “VNF” and “Network” Resource Types.
“Generic” model-driven Service flow
Note recursion
Service Y is being treated as a “Resource” from the perspective of Service X.

## Slide 13: Nested / Compound Services:
Service W:
topology_template:
node_templates:
VNF_W
Service_X
Service X:
topology_template:
node_templates:
VNF_X
Service_Y
Service Y:
topology_template:
node_templates:
VNF_Y
Service_Z
Service Z:
topology_template:
node_templates:
VNF_Z

## Slide 14: Conclusions
Service Providers require the ability to define Services that can be leveraged by higher order Services and other compounded services / segments / slices.
Consistent with ETSI MANO, ONAP should NOT separate Service Orchestration and Resource Orchestration into two separate named components, because each Resource can be exposed as a Service
      What appears as a “Resource” from one Service’s perspective, may actually be a Service from another perspective
      In Addition, ONAP scope is much broader than ETSI MANO (MANO limited to Cloud infrastructure services and management of VNF as a basic resource (ignoring the application of the VNF)), therefore SO should support full orchestration scope of ONAP
      To achieve alignment with MANO for common functionality, SO should expose APIs for basic resource onboarding/LCM (VNF) . This is SOL-001, SOL-004 and SOL-005.
      or simple network service onboarding/LCM (composed of one or more VNFs) and related modelsIn addition, ONAP SO should Support “Service reuse” to drive model driven run-time behavior for complex services:
        Compounded Services (e.g. Residential vCPE, Network Slicing Segments, etc.)
        Nested Services (e.g. E2E Slice)
      ONAP should provide Service Providers deployment flexibility to address scalability, geographic distribution and redundancy / resiliency
      But should not impose extra complexity and cost on service providers by separating service / resource orchestration that provides little known benefit

## Slide 15: APPC & VF-C Convergence Note – A major goal of the ONAP platform (R2 or a later release) is to specify a common set of functions to unify the APP-C and VF-C functionalities.

## Slide 16: Role Of Controllers in ONAP
ONAP Controllers configure and maintain the health of network functional elements and services throughout their lifecycle.
Programmable network application management platform
  Behavior patterns programmed via models and policies
  Standards based models & protocols for multi-vendor implementation
  Operational control, coordinated state changes across devices, etc.
Manages the health of the network services & VNFs in its scope
  Policy-based optimization to meet SLAs
  Event-based control loop automation to solve local issues in near real-time
  Executes action for outer control loop automation (Driven by DCAE, Policy, etc.)
Local source of truth
  Manages inventory within its scope
  All stages/states of lifecycle
  Configuration audits
  ONAP has a layered architecture, with the role of controller clearly defined
  Need to avoid duplicating functions across layers within the controller layer (e.g. DCAE, Service/Resource Orchestration, etc.)

## Slide 17: Next Steps – Solidify Beijing Architecture with Projects
Agree and approve the proposed target architecture
      Identify project impact to realize target orchestration and controllers implementation in R2
      Create a small team from SO, VF-C, App-C and CCSDK teams to identify phased approach to achieve controller alignment in ONAP Platform