## Slide 1: ONAP Reference Architecture for R2 and Beyond Tiger Team Presentation Parviz Yegani – Futurewei Technologies Contributors: Vimal Begwani (AT&T), Jamil Chawki (Orange), Andrew Mayer (AT&T), Alex Vul (Intel), Ramki Krishnan (VMware), Maopeng Zhang (ZTE), Stephen Terrill (Ericsson), <more contributors to be added> Jan. 9, 2018

## Slide 2: ONAP High-Level Architecture for R1 (Amsterdam)

## Slide 3: Progress from the Architecture Subcommittee
For Amsterdam (R1), the architecture was agreed, as discussed since ONS.
  This was to reduce risk of late changes to the project teams, who have built their plans based on the current baseline.
Starting with R2, there is consensus to resolve the following two architectural inconsistencies:
  Orchestration Architecture
    - Architecture team agreed that Orchestration layer should be separate from Controller layer
  Consistent Controller Layer Architecture and better alignment between App-C & VF-C
  Projects are drilling down to the next level of detail on interfaces and project alignment, and then the projects will review their R2 plans with the ARC.
The next slide illustrates high-level architectures that was approved by TSC to meet R1 schedule.

## Slide 4: ONAP Amsterdam Architecture
Policy Creation & Validation
VNF SDK
Portal Framework, U-UI, ONAP CLI
Resource Onboarding
Service & Product Design
Recipe/Eng Rules & Policy Distribution
ONAP Operations Manager (OOM)
Dashboard OA&M (VID)
A&AI/ESR
External API Framework
Micro Services Bus (MSB)
DMaaP
AAF
DCAE
Correlation Engine
(Holmes)
Logging
Policy Framework
SDN-C
(L0-L3 Controller)
Multi-VIM/Cloud
Infrastructure Adaptation Layer
CCSDK
External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Commercial VIM
Public Cloud
…
3rd Party Controller
sVNFM
EMS
VNFs
PNFs
…
Service Orchestration
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Application Controller
(L4-L7)
Virtual Function Controller
(ETSI-aligned)
CLAMP
Catalog
DESIGN-TIME (SDC)
RUN-TIME
Public
Cloud
Common Services
Notes: Key points:
Unified framework for design-time & run-time
  Common platform for service design and netops to drive collaboration
Simultaneous orchestration of physical and virtual networks
  Vendor-agnostic orchestration can only happen in open source context
Real-time analytics and closed-loop automation
  Easy re-use of service concepts
  Iterative service improvements based on network feedback

## Slide 5: ONAP Reference Architecture for R2 and Beyond

## Slide 6: Architecture Design Considerations
Architecture Principles Were Reviewed Earlier and Agreed Upon by the Architecture Team:
  https://wiki.onap.org/display/DW/Contributions?preview=/8225716/8232492/Architectural%20principles_v3.docx
ONAP is a layered architecture – Orchestration, Multi-Cloud, Controller, etc.
Functional role of each layer should be well defined per the architecture principles agreed by the architecture team (see the above link).
ONAP should support integrated design studio to capture full lifecycle management models (TOSCA models for NF, simple / nested services augmented with BPMN, Policy / Analytic design models, etc.)
ONAP Should Support Cloud Agnostic Model and Multi-Cloud adaption layer while hiding infrastructure details
ONAP Target Goal is: Modular, Model-driven, Microservices-based architecture
  Models drive interfaces between layers/components
ONAP should define well-described and consistent NB-APIs at all layers
Keep flexible capability for commercial solution (no vendor lock-in)
Agree to unified modeling for integration across all modules: VES in DCAE, Logging & monitor inside ONAP and more

## Slide 7: ONAP Target Architecture (High-Level Functional View)
DESIGN-TIME
Policy Creation & Validation
Analytic Application Design
VNF / PNF Onboarding
Resource Onboarding
Service Design
Catalog
Recipe/Eng Rules & Policy Distribution
ONAP Optimization Framework
ONAP Operations Manager
Dashboard OA&M
ONAP External APIs
Common
Services
Application
Authorization
Framework
Logging
Policy Framework
Active & Available Inventory
External Registry
Generic NF Controllers (L4-L7)
Data Collection, Analytics, and Events
Event Correlation
ONAP Optimization Framework
SDN Controller
(L0-L3)
Optional External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Azure
VMware
RackSpace
…
3rd Party Controller
AMZ
VNFs
PNFs
Public
Cloud
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Orchestration
Micro Services Bus / Data Movement (see Note 1)
Closed Loop Design
Change Management Design
Life Cycle Management & Config
Design Test & Certification
CLI
OSS / BSS
ONAP Portal
Note 1 – Consistent APIs between Orchestration layer and Controllers
Specific VNF Manager
Element Management System
RUN-TIME
Common Services
Multi-Cloud
Adaptation
U-UI
Controller SDK
(see Note 1)
(see Note 1)

## Slide 8: ONAP Beijing Architecture (High-Level View with Projects)
DESIGN-TIME (SDC)
Policy Creation & Validation
VNF SDK
Resource Onboarding
Service Design
Catalog
Recipe/Eng Rules & Policy Distribution
ONAP Operations Manager
Dashboard OA&M (VID)
ONAP External APIs
Common
Services
AAF
Logging
Policy Framework
A&AI/ESR
DCAE
Correlation
Engine (Holmes)
OOF
SDN-C
(L0-L3 Controller)
External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Azure
VMware
RackSpace
…
3rd Party Controller
AWS
VNFs
PNFs
Public
Cloud
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Service Orchestration
Project
MSB/DMAAP
Design Test & Certification
Others
ONAP CLI
OSS / BSS
ONAP Portal
sVNFM
EMS
RUN-TIME
Common Services
Multi-VIM/Cloud
Infrastructure Adaptation Layer
CLAMP
Application Controller
(APPC)
(L4-L7)
Virtual
Function Controller
(VF-C)
(Note 1)
U-UI
Note 1 - VF-C is ETSI-aligned.
Change Management Design

## Slide 9: ONAP Orchestration Alignment

## Slide 10: ONAP Orchestrator Functions (1/2)
Orchestrate Network Functions (VNF/PNF), and Network Services (NSes), and services provided by the managed environment
Coordinate cross-controller activities driven by orders and events to
  LCM (instantiate/modify/upgrade/configure/remove) VNFs/PNFs, Nses, and services from the managed environment
  perform multi-control layer remedy actions.
Key Attributes of Orchestrator:
Model Driven Orchestration
  Process behavior driven by resource / service model designed in SDC
  Orchestrates network functions and service LCM (Instantiations, ..) , including compound / nested services (parts already in R1)
    Nesting may be domain-specific orchestrator (does not require SO clone)
  Support software upgrade and planned change management
  Support open & closed-loop control actions initiated by DCAE /Policy or external API (e.g. OSS for Open Loop)
  Tracks orchestrated activity for the life of the request but doesn’t control state of orchestrated components

## Slide 11: ONAP Orchestrator Functions (2/2)
Interfaces to External OSS / BSS Systems
  Standard APIs exposed northbound to create, modify or remove services and resources
  Request decomposition of service request into service / network function components
  Selects model / recipe that supports the request and maps order data to recipe / model
Coordinating Activities Across Various ONAP Controllers
  Coordinates activities across Multi-Cloud (infrastructure) / SDN-C / APPC / VF-C controllers
  Manage recording of service configurations
Orchestrator Performs Following Additional Services
  Coordinates current inventories and placement/optimization recommendations
  Enforces business & technical policies
  Support standards-based workflows
  Validates and records network functions / service implementations

## Slide 12: Examples of Orchestration Requests (1/2)
Install/Configure a single network function (VNF or PNF) – e.g. Deploy a new virtual PE / P router
  A virtual network element might have one or more components (e.g VNFCs or VDUs)
Install multiple copies of network functions in one or more data centers – e.g. Deploy new virtual PE / P routers across multiple locations
Deploy one or more instances of network services – e.g. RAN at Multiple sites, one or more sites of EPC, etc.
Deploy E2E network services (e.g. RAN + EPC + IMS) and services from the managed environment
Instantiate and LCM a customer services – e.g. multi-site VPN or IP SEC
  Could require deploying new instances of network elements (e.g. vCE) and using existing elements (e.g. vPE)
  Could be using existing elements without any new VNF / PNF being deployed (e.g. “Allocated Resources” – configuring a service to existing components)

## Slide 13: Examples of Orchestration Requests (2/2)
Create a new instance of a network slice segment
  Could be leveraging existing network services (RAN, vEPC, etc.)
Create a new instance of a network service slice – e.g. IoT or eMBB slice
  Could be leveraging previously created network slice segments
Implement a software upgrade / change management
  Could require Coordination of activities across Multi-VIM (infrastructure)/SDN-C/app-C/VF-C controllers
Orchestrate remedial actions requested as part of Closed or open loop action
  Could require adding new compute / network resource to the existing functional elements (i.e. VNF)
  Create a new instance of VNF and migrate traffic
  Could require Coordination of activities across Multi-Cloud (infrastructure)/SDN-C/App-C/VF-C controllers)

## Slide 14
Service X:
topology_template:
node_templates:
PNF
Network
VNF
Allotted Resource
PNF
Model-Driven Orchestration (Recursive Structure)
Service Orchestration
Network
VNF
Allotted Resource
requirement: A
VF Module
Service Y:
topology_template:
node_templates:
PNF
Network
VNF
Allotted Resource
capability: A
PNF
Service Orchestration
Network
VNF
Allotted Resource
Resource Orchestration
Cloud Resource Orchestration
Resource Orchestration
An Allotted Resource can be homed to an existing “underlying” network function or Service Instance, or homing could determine that a new network function Service Instance is needed. This would result in a 2nd level of Service Orchestration.
Each Resource Type has its own “Generic” model-driven flow. There currently exist such flows for “VNF” and “Network” Resource Types.
“Generic” model-driven Service flow
Note recursion
Service Y is being treated as a “Resource” from the perspective of Service X.

## Slide 15: Nested / Compound Services:
Service W:
topology_template:
node_templates:
VNF_W
Service_X
Service X:
topology_template:
node_templates:
VNF_X
Service_Y
Service Y:
topology_template:
node_templates:
VNF_Y
Service_Z
Service Z:
topology_template:
node_templates:
VNF_Z

## Slide 16: Conclusions
Service Providers require the ability to define Services that can be leveraged by higher order Services and other compounded services / segments / slices.
Consistent with ETSI MANO, ONAP should NOT separate Service Orchestration and Resource Orchestration into two separate named components, because each Resource can be exposed as a Service
      What appears as a “Resource” from one Service’s perspective, may actually be a Service from another perspective
      In Addition, ONAP scope is much broader than ETSI MANO (MANO limited to Cloud infrastructure services and management of VNF as a basic resource (ignoring the application of the VNF)), therefore SO should support full orchestration scope of ONAP
      To achieve alignment with MANO for common functionality, SO should expose APIs for basic resource onboarding/LCM (VNF) . This is SOL-001, SOL-004 and SOL-005.
      or simple network service onboarding/LCM (composed of one or more VNFs) and related modelsIn addition, ONAP SO should Support “Service reuse” to drive model driven run-time behavior for complex services:
        Compounded Services (e.g. Residential vCPE, Network Slicing Segments, etc.)
        Nested Services (e.g. E2E Slice)
      ONAP should provide Service Providers deployment flexibility to address scalability, geographic distribution and redundancy / resiliency
      But should not impose extra complexity and cost on service providers by separating service / resource orchestration that provides little known benefit

## Slide 17: APPC & VF-C Convergence Note – A major goal of the ONAP platform (R2 or a later release) is to specify a common set of functions to unify the APP-C and VF-C functionalities.

## Slide 18: Role Of Controllers in ONAP
ONAP Controllers configure and maintain the health of network functional elements and services throughout their lifecycle.
Programmable network application management platform
  Behavior patterns programmed via models and policies
  Standards based models & protocols for multi-vendor implementation
  Operational control, coordinated state changes across devices, etc.
Manages the health of the network services & VNFs in its scope
  Policy-based optimization to meet SLAs
  Event-based control loop automation to solve local issues in near real-time
  Executes action for outer control loop automation (Driven by DCAE, Policy, etc.)
Local source of truth
  Manages inventory within its scope
  All stages/states of lifecycle
  Configuration audits
  ONAP has a layered architecture, with the role of controller clearly defined
  Need to avoid duplicating functions across layers within the controller layer (e.g. DCAE, Service/Resource Orchestration, etc.)

## Slide 19: Functional Description of ONAP Components

## Slide 20: VF-C Functions
NFVO
NFVI&VIM
VNF Package ( VNFD)
NS Package ( NSD)
NFVO Functions
Support NS Lifecycle Management including NS instantiate, scale, heal, operate (query /update/…)and terminate. In R1, most of NSLCM interfaces align with SOL005 Os-Ma-nfvo reference point
Support integration with multi VNFMs via drivers which include vendors VNFM and generic VNFM. The interfaces between NFVO and driver comply with Or-Vnfm reference point.
Support integration with multi VIM via Multi-Cloud
In R1, NFVO also supports integration with vendor EMS via driver
Instantiate
Scale
Heal
Terminate
SVNFM
Driver
Multi-Cloud
Operate
GVNFM
Vi-Vnfm
Vi-Vnfm
Vi-Vnfm
Or- Vnfm
Or- Vnfm
Or-Vi
EMS
Driver
SO
Policy
UUI
Os-Ma-nfvo

## Slide 21: Service Design and Creation (SDC) Functional Architecture
Import Management Functions
  Import ONAP base capability definitions from Development Catalog to Design Catalog as building blocks in a standard format
Create Flows & Policies
  Create reusable management flows using building blocks & associated events & Policies
Onboard Network Functions
  Create VF model to include vendor’s description, scripts, & license model
  Customize models to include Service Provider specific attributes
Design Service & Operations Methods
  Create Service models with resources
  Design and associate operations processes & policies (e.g., Instantiation, DCAE/Control Loop, Change Management, etc.) and configure them to be service specific
Certification
  Simulate & test the design in Sandbox environment
  Certify Readiness & Adherence to Standards
Metadata Distribution
  Publish certified models for distribution to runtime catalog
  Notifications & Version Control
Service Provider’s Design environment to: 1. Catalog management capabilities, 2. Onboard vendor provided Network Functions, 3. Design Services and Operations, 4. Test, certify, and distribute models for Runtime Execution

## Slide 22: Catalog Architecture
Partially Existing:
Design Catalog (ONAP Design Platform - SDC)
  Catalog imported ONAP generic re-usable management software function & policy definitions
  Enable SP to onboard standard VNF packages
  Support SP users in design & lifecycle management of Resource and Service models
  Provide presentation to support service compositions & management flow associations
  Manages catalog’s elements versions, lifecycle and access policy
  All certified asset definitions available for re-use and composition
Yet to be implemented:
Development Catalog (ONAP Development)
  Common toolsets and data store for creation of ONAP software models & management flows/policies
  Interact with external software development teams and suppliers to onboard custom software, adapters or new capabilities
Runtime Catalog (ONAP Execution Platform)
  Provide a common data store for distributed certified models
  Provide ONAP runtime component’s subscription to access component view of the model data
  Maintain executable images and other runtime artifacts
The overall ONAP Catalog architecture includes Development Catalog, Design Catalog, and Runtime Catalog

## Slide 23: Service Orchestrator
Model Driven Orchestration and APIs
  Runtime behavior driven by service and resource models and policies (including compound/nested services) designed in SDC
  Orchestrates service delivery, change management as well as open and closed-loop control actions
  Provides standard, model driven APIs for requested actions
  Tracks orchestrated activity for the life of the request, but doesn’t maintain state of orchestrated components
Service Orchestrator (SO) orchestrates service, resources and associated cross-controller activity driven by requests and events that indicate the need to create, modify or remove service and resource instances, or to perform multi-control layer remedy actions.
Processing of Service Requests:
  Performs Decomposition, Recipe Selection, Recipe Execution (including Rainy Day)
  Triggers and Records Results for:
  Homing
  Assign, Create, Configure (Controller/multi-cloud activity)
  Validation
  Monitoring
  Separate execution threads for service, decomposed resources, and any subtending service(s) provide nested service orchestration in a recursive manner
Orchestration of Controllers
  Coordinates activities across Multi-Cloud/ SDN-C/Generic VNF controllers, including data sourcing and mapping to Controller inputs

## Slide 24: SO Internal Architecture (R2 Proposed)
API Handler (J2EE)
Data Store (MariaDB)
Request DB
A&AI/ESR
MSO
Service
Catalog
Request
Handler
Store
Request
Select Recipe
Track
Requests
Select Adapter Template
Map Data to Template
Execute Transaction
SDC
Dashboard OA&M (VID)
External API
OOF
REST
Camunda DB
HEAT Templates
Service Models
SO
SDC Distribution Client
Resource/Controller Adapters (J2EE)
Orchestration Execution Engine
Service-Level Recipe
Resource-Level Recipe
Model Driven Routing Function
Resource-Level Recipe
BPMN
BPMN
BPMN
TOSCA Orch
REST
REST
REST
DCAE
Multi-Cloud
SDN-C
VNF/Network Adapter
Controller Adapter
Generic VNF Controller
REST
REST
Micro Services Bus / DMaaP
Micro Services Bus / DMaaP
Micro Services Bus / DMaaP
Cloudify/ARIA would be invoked by BPMN after “Assignments” have been obtained from SDNC, once a full “deployment” set of data is available across all Resources.
REST
REST
REST
REST
REST
Map Request Data to Recipe & Invoke BPEL Execution

## Slide 25: Generic VNF Controller (L4-7) Architecture
Generic VNF Controller for L4-7 configures and maintains the health of applications throughout its lifecycle.
  The Lifecycle Management Functions are a normalization of VF-C and APP-C functions into a common, extensible library
Programmable network application management platform
  Behavior patterns programmed via models and policies
  Standards based models & protocols for multi-vendor implementation
  Extensible SB adapter set including vendor specific VNF-Managers
  Operational control, version management, software updates, etc.
Manages the health of the applications/VNFs within its scope
  Policy-based optimization to meet SLAs
  Event-based control loop automation to solve local issues near real-time
Local source of truth
  Manages inventory within its scope
  All stages/states of lifecycle
  Configuration audits
Key Attributes of VNF Controllers
  Intimate with network protocols
  Manages the state of services
  Provide Deployment Flexibility to meet user scalability / resilience needs
Generic VNF
Controller
Adapters
Service Logic Interpreter
VNF Manager Adapter (s)
Chef
Configuration Repository
Config Templates
REST
Service Topology & VNF State
Service Logic
Service Logic
Service Logic
Config mS
Auto-Recovery mS
Audit mS
Netconf
Operational/ Config Tree
(Service Model)
Web Server
Policy Cache & Event Matching
…
API Handler
A&AI
SDC
Ansible
Others
Lifecycle Management mS Library
…
Multi-Cloud Adapter

## Slide 26: SDN-Controller Architecture
SDN Controller configures and maintains the health of L1-3 VNFs/PNFs and network services throughout their lifecycle
Programmable network application management platform
  Behavior patterns programmed via models and policies
  Standards based models & protocols for multi-vendor implementation
  Extensible SB adapter set supporting various network config protocols, including 3rd party controllers
  Operational control, coordinated state changes across devices, source of telemetry/events, etc.
Manages the health of network services & VNFs/PNFs in its scope
  Policy-based optimization to meet SLAs
  Event-based control loop automation to solve local issues near real-time
  Action executor for outer control loop automation
Local source of truth
  Manages inventory within its scope
  All stages/states of lifecycle
  Configuration audits
Key Attributes of Controllers
  Intimate with network protocols
  Manages the state of services
  Single service/network domain scope per instance
Service Control
Interpreter
SDN Controller
Network Resource
Controller
Service
Element
Resources
Core &
Transport
Resources
Access
Service
Features
Flow
Service
Features
Configuration Repository
Svc Template A
Svc Template B
Svc Comp 1
Svc Comp 2
API Handler
Adapters
NetConf/ YANG
Multi-Cloud Network Adapter
BGPCEP
SDC
A&AI
3rd Party
Controllers
Network/Service Design/Engineering Policies/Rules
Others
…

## Slide 27: Data Collection, Analytics and Events (DCAE) Architecture
DCAE enables real-time fault, performance and other data/event collection from service, network and infrastructure
  Collect Data & Events once and make available to multiple applications
  Telemetry records from VNFs and PNFs (fault, performance, usage, etc.)
Makes collected data available to real-time analytic µ-services to:
  Identify anomalies and other events for closed loop remediation
  Enable closed-loop automation to remedy fault/performance conditions
  Enable closed-loop automation to scale resources up/down
  Enable analysis at edge and central locations
  Extensible framework to integrate applications from various sources
Provides Correlation & Analysis to manage service at various layers
  Multi-Cloud Infrastructure layer, network element layer, Network & Complex Services layer, Operational Management layer
  Cross-layer, Intra-domain and cross-domain correlation
Streaming
Data
Batch
Data
SNMP
Syslog
Other
Unstructured & Structured Data Persistence
Analytic Frameworks:
Holmes, CDAP, Other
Stream Data Collection
Events
Flows
Other
Batch Data Collection
Analytic µServices
Capacity Management
DCAE
Congestion Detection
Fault Correlation
QoS Monitoring
Security Analysis
Managed Environment
Storage
Compute
VNFs / PNFs
Applications
Networking
Logs
Files
Other
Multi-Cloud Telemetry Adaption
…
VES
DMaaP (Pub/Sub for Events/Data within DCAE & across ONAP)
OOM – DCAE Controller

## Slide 28: Active and Available Inventory
A&AI tracks the global inventory of the networks, services & resources that ONAP manages.
  The what, where, when of the managed assets and their relationships, and which controller manages them, etc.
Real-time, logically centralized view of topology & inventory
  Map and broker of data sources in the global network
  Federates across controllers, cloud infrastructure, partners, etc.
  Real-time access to authoritative sources with ability to aggregate views
  Real-time awareness of network elements, applications and service instances
  Aware of all the assets in scope, organized by their type, state & location
  Keeps track of the dynamic relationships of the virtual assets
  Aware of resource assignments, availability & relationships to customer
Network events used to maintain the integrity of inventory
  Monitors network events to register services, networks & resources
  Tracks creation, modification or removal of entities and relationships
A&AI
API Handler
A&AI Application Management Functions
Data Audits
History
Archival
OA&M
Notifications
Event Subscriptions
A&AI Data Management Services
Inventory & Topology Management
Service
Network
Resource
Infrastructure
Active
Topology
Assignment
Available
Entitlement
Reference
Inventory & Topology
Entitlements & Reference
Graph Layer
Metadata Engine
API Generation
Schema Generation
Version Management
Metadata Management
Model-driven
  Schema, APIs, database views, data integrity mechanisms generated from models expressed in TOSCA.

## Slide 29: Active & Available Inventory, External Registry
Active & Available Inventory, External Registry
Definition:
AAI maintains a live view of services and resources in the network, providing the state and relationships of the service components
Maintains the view of the managed systems services and resources, as well as information of the external systems that ONAP will connect to.
It provides real-time views of a managed systems resources, services and relationships with each other.
AAI provides a GUI to provide users the ability to find and inspect inventory data. This includes a free-text search, inspection of specific entities and their relationships, and aggregated views of data.
Provided Interfaces:
Inventory Service Interfaces:
  AAI Resources REST API - Provides the ability to store, read, update inventory information
  Gizmo: a low-level REST CRUD API that provides targeted and simple access to entities, relationships, and their properties. Gizmo also provides lightweight collections, and transactional bulk write support
Complex Query Interface: AAI Traversal REST API – Provides the ability to perform complex traversals of the AAI Graph
External Register interface
  Provides the ability to provision and read external system information
Consumed interface Interfaces:
DMaaP
SDC
Multivim
Consumed Models: TOSCA Service and Resource Models
Inventory Service Interface
External Register Interface
Interface N

## Slide 30: Microservices Bus (1/2)
Micro Servies Bus / Data Movement
Definition:
Provides a reliable, resilient and scalable communication and governance infrastructure to support ONAP Microservice Architecture(OMSA).
Provides RESTFul API for service registration/discovery
Provides JAVA SDK for service registration and access
Provides a transparent service registration proxy with OOM-Kube2MSB
Provides a transparent service communication proxy which handles service discovery, load balancing, routing, failure handling, and visibility-Internal API Gateway(Implemented) and Mesh Sidecar(WIP)
Provides an External API Gateway to expose ONAP services to the outside world
Service Registration REST Interface
Service Discovery RES Interface
JAVA SDK for Service Registration/Access
Interface N

## Slide 31: Microservices Bus (2/2)
Micro Servies Bus / Data Movement
Consumed interface Interfaces: (None)
Consumed Models:
Swagger for RESTFul APIs definition
Service definition in kubernetes config files for Kube2MSB service registration
Service Registration REST Interface
Service Discovery RES Interface
JAVA SDK for Service Registration/Access
Interface N
Provided Interfaces:
Service Registration REST Interface
  Provides the RESTFul interface to register ONAP services.
Service Discovery REST Interface
  Provides the RESTFul interface to discover ONAP services.
JAVA SDK
  Provides JAVA SDK to register ONAP services.
  Provides JAVA SDK to access ONAP services.
  Note: ONAP components don' t need interfaces to leverage the transparent service registration proxy and communication proxy.

## Slide 32: Optimization Framework (1/4)
Optimization Framework (OOF)
Definition:
ONAP Optimization Framework (OOF) provides functionality for creating and running optimization applications by leveraging a policy-driven, declarative approach.
Supports different specializations (applications) with specific domain and optimization needs.
Initial specialization scopes include, but are not limited to, VNF placement support via Homing and Allocation Service (HAS) with different use cases, and change management scheduling service.
  For R2, the OOF will support vUCPE use case (as a MVP). From R3 and beyond, the OOF will also support VoLTE, VNF scale-in/out (higher order control loop), and RAN-5G.
  For R2, the OOF will demonstrate an example of Change Management Scheduling Optimization using the OOF design framework with simple, representative constraints. This effort will be will be closely aligned to support Change Management scheduling use case in R3 and beyond
Service Orchestrator (SO)
Change Management Portal
Policy Interface
Inventory Service Interface
Service/Policy Models Interface
R3 and Beyond
Infrastructure Metrics Interface
Application Metrics Interface

## Slide 33: Optimization Framework (2/4)
Optimization Framework (OOF)
Provided Interfaces:
Placement Optimization Interface
  Provides functionality for the Service Orchestrator to specify placement services [initially to support vUCPE use case, but will support VoLTE, VNF scale-in/out (higher order control loop), and RAN-5G in R3 and beyond]
Change Management Portal Interface
  Provides functionality for schedules that satisfy different constraints on scheduling and conflicts [initially as a demonstration of he design framework with simple, representative constraints; will be closely aligned to support Change Management scheduling use case]
Service Orchestrator (SO)
Change Management Portal
Policy Interface
Inventory Service Interface
Service/Policy Models Interface
R3 and Beyond
Infrastructure Metrics Interface
Application Metrics Interface
Consumed Interfaces:
Policy Interface, from: Policy
Inventory Service Interface, from: Available and Active Inventory
Service/Policy Models Interface, from: SDC
Infrastructure Metrics Interface, from: Multi Cloud [R3 and Beyond]
Application Metrics Interface, from: DCAE [R3 and Beyond]
Consumed Models:
Policy Models (constraints) and License Models from: SDC
Infrastructure Metrics Models, from: Multi Cloud [R3 and Beyond]
Application Metrics Models, from: DCAE [R3 and Beyond]

## Slide 34: Interface Definitions (3/4)
Optimization Request Interface | 
Provided Service | Homing Service API (HAS-API)
Supplementary Information | The OOF will provide a list of possible candidates for placement, which the service orchestrator can use to instantiate the service
Interface Provider(s) | Optimization Framework
Provided Capabilities | Optimization Information Request

## Slide 35: Interface Definitions (4/4)
Scheduling Optimization Request Interface | 
Provided Service | Change Management Scheduling API (CMSO API)
Supplementary Information | The OOF will provide a possible schedule of VNF actions (e.g. upgrades) that satisfy the constraints on availability periods and constraints related to conflicts
Interface Provider(s) | Optimization Framework
Provided Capabilities | Optimization Information Request

## Slide 36: ONAP SDK-Driven Sub-System Approach
Goal: Move toward a common platform architecture, starting with Controllers, Orchestration and Multi-Cloud
Improve agility for on-demand/situational creation of instances
Reduce software footprint of platform component instances
Reusable tool chain and framework across components
Facilitate agile introduction and swap-out of technologies
Consistent use of NB and SB APIs
Enable flexible options to add and extend platform capabilities

## Slide 37: SDK-Driven Sub-System – Libraries (including CCSDK)
*Plugins/Adapters can include:
3rd party VNFM Drivers • 3rd party EMS Drivers
3rd party SFC Drivers • Ansible/Chef/Puppet
Netconf/Yang • CLI
SNMP • etc.
SDK Libraries
Orchestrators
Rackspace
IBM
Google
Orchestration Function SDK
Multi-Cloud Adaptation SDK
Controllers
OpenStack
Azure
AWS
OSSs
VNFs
PNFs
Multi-Cloud
μServices
Control Function SDK (CCSDK)
ODL
Imperative Models
BPMN orchestration
engine
Sub-Models
TOSCA-Cloud
Translation/Mapper
Declarative Models
TOSCA orchestration
engine
Library of
Common Control/NFV Lifecycle Mgt. Functions
Rebuild
VNF Configure
Network Config.
Stop/Start
A udit
Upgrade
Scale
Svc Function Chain
Heal
Library of
Common Cloud Translations (shims)
Telemetry
Scale
Heal
Register
Cloud Resource
Instantiation
LB
…
SB API SDK
(Adapters)
Plugins/Adapters*
M-Cloud APIs
etc.
NB API SDK
API Handler
API Catalog
Library of Flows
Service, Resource, Etc.
Orchestration APIs
Controller APIs
Cloud APIs
API Configurator
Controller APIs
OSS APIs
μServices APIs
Netconf/Yang
Ansible
Collectors
OpenStack
Azure
AWS
API Catalog
ONOS
Open
ROADM
…
…
Resource Orchestration APIs
Assign
Health Check

## Slide 38: Controller Personas Based on SDK Libraries
SDK Libraries
Controller Personas Examples
(created from CCSDK)
SDN-C Persona
NB API
Controller APIs
Control Functions
ODL
Library
VNF Configure
Network Config
Svc Function Chain
Assign
SB
API
Other Adapters
OSS APIs
μServices APIs
Netconf/Yang
…
Generic VNF Controller Persona
NB API
Controller APIs
LCM Functions
ODL
Library
SB
API
Ansible
μServices APIs
Netconf/Yang
Rebuild
Stop/Start
Audit
HealthCk
Scale
Heal
???
3rd VNFM/EMS
3rd Party SFC
VNF Configure
Svc Function Chain
OSS APIs
Other Adapters
…
…
…

## Slide 39: ONAP APIs Work in Progress …

## Slide 40: MEF and ONAP Joint Collaboration
Work jointly with MEF and ONAP External API Project in defining Use Cases and Information Model for Legato and Interlude
Leverage MEF Operational Threads and revise MEF 56, Interface Profile Specification: Service Configuration and Activation, to reflect consistent Use Cases
The Service Descriptor Model is key to Model Driven Orchestration
Work with ONAP and TM Forum define the Service Catalog and Service Instantiation API is a model driven and extensible fashion

## Slide 41
E
SP Domain
Customer Domain
Partner Domain
Network Infrastructure
Customer
Application Coordinator
Element Control and Management
Infrastructure Control and Management
Service Orchestration Functionality
Presto
(SOF:ICM)
Allegro
(CUS:SOF)
LEGATO
(BUS:SOF)
Cantata
(CUS:BUS)
Element Control and Management
Infrastructure Control and Management
ADAGIO (ICM:ECM)
LEGATO
(BUS:SOF)
Presto
(SOF:ICM)
ADAGIO (ICM:ECM)
Interlude (SOF:SOF)
Sonata
(BUS:BUS)
Business Applications
Business Applications
Service Orchestration Functionality
REFERENCE ARCHITECTURE

## Slide 42: SOF Interface Reference Points
Service Orchestration Functionality
Dynamic service control;
Service state info;
Service performance & quality;
Service related alerts;
Dynamic service control;
Service parameter config;
Service state info;
Service performance info;
Service problem alerts
Service feasibility;
Service provisioning configuration & activation;
Request fallout;
Usage events & metrics;
License accounting;
Service performance & quality (e.g., KPI);
Service trouble management;
Service policy;
Capacity engineering;
Address allocation management;
Connectivity and network function feasibility;
Configuration, activation, and management of connectivity and logical network functions;
Topology and routing;
Performance and Fault;
Connectivity policy
LEGATO
PRESTO
ALLEGRO
INTERLUDE

## Slide 43: The ONAP “Black Box” View
OAP
OOM
Design Tools
ONAP Management Interfaces
OOM Interfaces
External APIs (Service Centric)
External APIs (Resource Centric)
Resource Interfaces
APIs
UX/CX
CLIs/SDKs
PNFs
VIMs
IaaS
PaaS
SaaS
Legato
Interlude
Presto

## Slide 44: Legato Interface Reference Point
It is envisioned that from a Service Provider to BSS/OSS interaction context (i.e. MEF Legato), the ONAP External API will support the following types of interacts:
BSS/OSS retrieves Service Models
BSS/OSS requests service feasibility determination.
BSS/OSS requests reservations of capabilities related to a potential Service.
BSS/OSS requests activation of Service.
BSS/OSS receives Service activation tracking status updates.
BSS/OSS retrieves Service Inventory
BSS/OSS receives usage events due to a Customer initiating dynamic activity on their Service (e.g., increase in bandwidth).
BSS/OSS receives a summary of Service quality and usage information.
BSS/OSS receives Service state and fault event information
BSS/OSS receives Service Activation Testing results.
BSS/OSS receive capability information about the Service layer.
BSS/OSS manages Licenses
BSS/OSS receives License Usage information

## Slide 45: Interlude Interface Reference Point
It is envisioned that from a Service Provider to Partner Provider interaction context (i.e. MEF Interlude), the ONAP External API will support the following types of interacts:
Service Provider controls aspects of the Service within the Partner domain (on behalf of the Customer) by requesting changes to dynamic parameters as permitted by service policies.
Service Provider queries state of the Service.
Service Provider requests change to administrative state or permitted attributes of a Service.
Service Provider request creation of connectivity between two Service Interfaces as permitted by established business arrangement.
Service Provider request instantiation of functional service components as permitted by established business arrangement.
Service Provider queries the Partner for detailed information related to Services provided by the Partner to the Service Provider.
Service Provider receives Service specific event notifications (e.g., Service Problem Alerts) from the Partner.
Service Provider receives Service specific performance information from the Partner.
Service Provider request Service related test initiation and receive test results from the Partner.

## Slide 46: Information Domains in ONAP
Governance/Processes
Policy/Rule/Constraints, SLA/OLA Definition,
Asset/Capacity Management, Configuration/Change/Incident Management, Catalog Management
Service Design
Network function on-boarding
Service definition, including Service blueprints
Service Access
User/Tenant Management, Identity Management, RBAC
Entitlement Control
Offered Services
Policy/Rule/Constraints, SLA/OLA Definition
Asset/Capacity Management, Configuration/Change/Incident Management
Services Components
Decomposition/Instantiation/Assurance/Remediation
Service Level Optimization, QoS Optimization, Policy Enforcement,
Logical Resource
Resource Matchmaking/Optimization
Resource Reservations/Allocations, Installation/Configuration
Real Infrastructure
Provider Registration, Infrastructure Discovery/Monitoring
Capacity Optimization
Governance/Processes
Offered Services (What’s offered; Catalog)
Service Components (Service Function Topology; Abstract Network Functions)
“Logical” Resource
(VNFs; VNF Forwarding Graphs)
External APIs
“Real” Infrastructure
(Physical/Virtual/Cloud – On/Off-Premise)
Service Access
Service Design
Micro-service Bus /Integration Backplane

## Slide 47: Orchestration Approach Comparison ONAP vs ETSI MANO (Gil) Work in Progress … Note - Attached slides provide a side-by-side comparison of the ETSI MANO approach to orchestration vs the ONAP (ECOMP) approach.

## Slide 51: Vodafone Orchestration Proposal (Susana) Work in Progress …

## Slide 52: ONAP Target Architecture focus for orchestration/NF controller discussion
DESIGN-TIME
Policy Creation & Validation
Analytic Application Design
VNF / PNF Onboarding
Resource Onboarding
Service Design
Catalog
Recipe/Eng Rules & Policy Distribution
ONAP Optimization Framework
ONAP Operations Manager
Dashboard OA&M
Common
Services
Application
Authorization
Framework
Logging
Policy Framework
Active & Available Inventory
External Registry
Data Collection, Analytics, and Events
Event Correlation
ONAP Optimization Framework
SDN Controller
(L0-L3)
Optional External Systems
Hypervisor / OS Layer
OpenStack
Azure
VMware
RackSpace
3rd Party Controller
AMZ
Public
Cloud
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Closed Loop Design
Change Management Design
Design Test & Certification
CLI
OSS / BSS
ONAP Portal
Note 1 – Consistent APIs between Orchestration layer and Controllers
RUN-TIME
Common Services
Multi-Cloud
Adaptation
U-UI
Others
(see Note 1)
CCSDK
ONAP External APIs
Generic NF Controllers (L4-L7)
Network Function Layer
…
VNFs
PNFs
Micro Services Bus / Data Movement (see Note 1)
Life Cycle Management & Config
Specific VNF Manager
Element Management System
(see Note 1)
Orchestration

## Slide 53: ONAP Target Architecture for Orchestration layer and NF controller (High-Level Functional View)
ONAP External APIs
Generic NF Controllers (L4-L7)
Optional External Systems
Network Function Layer
…
VNFs
PNFs
Life Cycle Management & Config
Specific VNF Manager
Element Management System
RUN-TIME
Orchestration
(end-to-end)
Orchestration
(domain/region)
Micro Services Bus / Data Movement
VNFs
Domain/region versus end-to-end orchestration are depicted here for the sake of examples to depict interfaces. Expectation is to have a model driven orchestration functionality
VES and YANG not included in this figure for simplicity and also currently not in ETSI-NFV
Note: Both VNF and Element management may trigger actions to be executed by the generic NF controller
Note

## Slide 54: ONAP Target Architecture for Orchestration layer and NF controller (APIs detailed)
ONAP External APIs
Generic NF Controllers (L4-L7)
Optional External Systems
Network Function Layer
…
VNFs
PNFs
Life Cycle Management & Config
Specific VNF Manager
Element Management System
RUN-TIME
Orchestration
(end-to-end)
Orchestration
(domain/region)
Micro Services Bus / Data Movement
VNFs
Os-Ma nfvo (SOL 005)
Os-Ma nfvo (SOL 005)
Or-VNFM (SOL 003)
Or-VNFM (SOL 003)
ONAP additions
ONAP additions
ONAP additions
Os-Ma nfvo (SOL 005)
Ve-Vnfm-Vnf (SOL 002)
Note: The depicted interfaces consists of sets of APIs that may be exposed by different ONAP modules. This needs to be detailed further
Ve-Vnfm-Vnf (SOL 002)
Automation is key for the success of 5G
Management standards are partly incomplete and fragmented
ETSI MANO defines key interfaces (API)
ONAP creates an automation framework with the help of TMF/MEF
3GPP drives information models and network slices