## Slide 1: ONAP Reference Architecture for R2 and Beyond (Tiger Team Presentation) Leader: Parviz Yegani – Futurewei Technologies Contributors (R3+ Architecture): Vimal Begwani (AT&T), Lingli Deng (China Mobile), Jamil Chawki (Orange), Andrew Mayer (AT&T), Alex Vul (Intel), Gil Bullard (AT&T), Ramki Krishnan (VMware), Maopeng Zhang (ZTE), Stephen Terrill (Ericsson), Jianguo Zeng (Huawei), John Ng (AT&T), Fariborz Behi (AT&T), Chaker Al Hakim (Huawei), Nagel Davis (Ciena), Susana Sabator (Vodafone), Manoj K Nair (Netcracker), Huabing Zhao (ZTE), Nemes Denes (Nokia) Other Contributors (Beijing Architecture): Project Technical Leaders (PTLs) of various ONAP projects Jan. 19, 2018

## Slide 2: ONAP High-Level Architecture for R1 (Amsterdam)

## Slide 3: Progress from the Architecture Subcommittee
For Amsterdam (R1), the architecture was agreed, as discussed since ONS.
  This was to reduce risk of late changes to the project teams, who have built their plans based on the current baseline.
Starting with R2, there is consensus to resolve the following two architectural inconsistencies:
  Orchestration Architecture
    - Architecture team agreed that Orchestration layer should be separate from Controller layer
  Consistent Controller Layer Architecture and better alignment between App-C & VF-C
  Projects are drilling down to the next level of detail on interfaces and project alignment, and then the projects will review their R2 plans with the ARC.
The next slide illustrates high-level architectures that was approved by TSC to meet R1 schedule.

## Slide 4: ONAP Amsterdam Architecture
Policy Creation & Validation
VNF SDK
Portal Framework, U-UI, ONAP CLI
Resource Onboarding
Service & Product Design
Recipe/Eng Rules & Policy Distribution
ONAP Operations Manager (OOM)
Dashboard OA&M (VID)
A&AI/ESR
External API Framework
Micro Services Bus (MSB)
DMaaP
AAF
DCAE
Correlation Engine
(Holmes)
Logging
Policy Framework
SDN-C
(L0-L3 Controller)
Multi-VIM/Cloud
Infrastructure Adaptation Layer
CCSDK
External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Commercial VIM
Public Cloud
…
3rd Party Controller
sVNFM
EMS
VNFs
PNFs
…
Service Orchestration
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Application Controller
(L4-L7)
Virtual Function Controller
(ETSI-aligned)
CLAMP
Catalog
DESIGN-TIME (SDC)
RUN-TIME
Public
Cloud
Common Services
Notes: Key points:
Unified framework for design-time & run-time
  Common platform for service design and netops to drive collaboration
Simultaneous orchestration of physical and virtual networks
  Vendor-agnostic orchestration can only happen in open source context
Real-time analytics and closed-loop automation
  Easy re-use of service concepts
  Iterative service improvements based on network feedback

## Slide 5: ONAP Reference Architecture for R2 and Beyond

## Slide 6: Architecture Design Considerations
Architecture Principles Were Reviewed Earlier and Agreed Upon by the Architecture Team:
  https://wiki.onap.org/display/DW/Contributions?preview=/8225716/8232492/Architectural%20principles_v3.docx
ONAP is a layered architecture – Orchestration, Multi-Cloud, Controller, etc.
Functional role of each layer should be well defined per the architecture principles agreed by the architecture team (see the above link).
ONAP should support integrated design studio to capture full lifecycle management models (TOSCA models for NF, simple / nested services augmented with BPMN, Policy / Analytic design models, etc.)
ONAP Should Support Cloud Agnostic Model and Multi-Cloud adaption layer while hiding infrastructure details
ONAP Target Goal is: Modular, Model-driven, Microservices-based architecture
  Models drive interfaces between layers/components
ONAP should define well-described and consistent NB-APIs at all layers
Keep flexible capability for commercial solution (no vendor lock-in)
Agree to unified modeling for integration across all modules: VES in DCAE, Logging & monitor inside ONAP and more

## Slide 7: ONAP Target Architecture (High-Level Functional View)
DESIGN-TIME
Policy Creation & Validation
Analytic Application Design
VNF / PNF Onboarding
Resource Onboarding
Service Design
Catalog
Recipe/Eng Rules & Policy Distribution
ONAP Optimization Framework
ONAP Operations Manager
Dashboard OA&M
ONAP External APIs
Common
Services
Application
Authorization
Framework
Logging
Policy Framework
Active & Available Inventory
External Registry
Generic NF Controllers (L4-L7)
Data Collection, Analytics, and Events
Event Correlation
ONAP Optimization Framework
SDN Controller
(L0-L3)
Optional External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Azure
VMware
RackSpace
…
3rd Party Controller
Kubernetes
VNFs
Public
Cloud
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Orchestration
Micro Services Bus / Data Movement (see Note 1)
Closed Loop Design
Change Management Design
Configuration & Life Cycle Management
Design Test & Certification
CLI
OSS / BSS
ONAP Portal
Note 1 – Consistent APIs between Orchestration layer and Controllers
Specific VNF Manager
Element Management System
RUN-TIME
Common Services
Multi-Cloud
Adaptation
U-UI
Others
(see Note 1)
(see Note 1)
CCSDK
PNFs

## Slide 8: ONAP Beijing Architecture (High-Level View with Projects)
New projects to be added following TSC approval
Integration
VNF Requirements
Modeling (Utilities)
VNF Validation Program
PNFs
K8s

## Slide 9: ONAP Orchestration Alignment

## Slide 10: ONAP Orchestrator Functions (1/2)
Orchestrate Network Functions (VNF/PNF), and Network Services (NSes), and services provided by the managed environment
Coordinate cross-controller activities driven by orders and events to
  LCM (instantiate/modify/upgrade/configure/remove) VNFs/PNFs, Nses, and services from the managed environment
  perform multi-control layer remedy actions.
Key Attributes of Orchestrator:
Model Driven Orchestration
  Process behavior driven by resource / service model designed in SDC
  Orchestrates network functions and service LCM (Instantiations, ..) , including compound / nested services (parts already in R1)
    Nesting may be domain-specific orchestrator (does not require SO clone)
  Support software upgrade and planned change management
  Support open & closed-loop control actions initiated by DCAE /Policy or external API (e.g. OSS for Open Loop)
  Tracks orchestrated activity for the life of the request but doesn’t control state of orchestrated components

## Slide 11: ONAP Orchestrator Functions (2/2)
Interfaces to External OSS / BSS Systems
  Standard APIs exposed northbound to create, modify or remove services and resources
  Request decomposition of service request into service / network function components
  Selects model / recipe that supports the request and maps order data to recipe / model
Coordinating Activities Across Various ONAP Controllers
  Coordinates activities across Multi-Cloud (infrastructure) / SDN-C / APPC / VF-C controllers
  Manage recording of service configurations
Orchestrator Performs Following Additional Services
  Coordinates current inventories and placement/optimization recommendations
  Enforces business & technical policies
  Support standards-based workflows
  Validates and records network functions / service implementations

## Slide 12: Examples of Orchestration Requests (1/2)
Install/Configure a single network function (VNF or PNF) – e.g. Deploy a new virtual PE / P router
  A virtual network element might have one or more components (e.g VNFCs or VDUs)
Install multiple copies of network functions in one or more data centers – e.g. Deploy new virtual PE / P routers across multiple locations
Deploy one or more instances of network services – e.g. RAN at Multiple sites, one or more sites of EPC, etc.
Deploy E2E network services (e.g. RAN + EPC + IMS) and services from the managed environment
Instantiate and LCM a customer services – e.g. multi-site VPN or IP SEC
  Could require deploying new instances of network elements (e.g. vCE) and using existing elements (e.g. vPE)
  Could be using existing elements without any new VNF / PNF being deployed (e.g. “Allocated Resources” – configuring a service to existing components)

## Slide 13: Examples of Orchestration Requests (2/2)
Create a new instance of a network slice segment
  Could be leveraging existing network services (RAN, vEPC, etc.)
Create a new instance of a network service slice – e.g. IoT or eMBB slice
  Could be leveraging previously created network slice segments
Implement a software upgrade / change management
  Could require Coordination of activities across Multi-VIM (infrastructure)/SDN-C/app-C/VF-C controllers
Orchestrate remedial actions requested as part of Closed or open loop action
  Could require adding new compute / network resource to the existing functional elements (i.e. VNF)
  Create a new instance of VNF and migrate traffic
  Could require Coordination of activities across Multi-Cloud (infrastructure)/SDN-C/App-C/VF-C controllers)

## Slide 14
Service X:
topology_template:
node_templates:
PNF
Network
VNF
Allotted Resource
PNF
Model-Driven Orchestration (Recursive Structure)
Service Orchestration
Network
VNF
Allotted Resource
requirement: A
VF Module
Service Y:
topology_template:
node_templates:
PNF
Network
VNF
Allotted Resource
capability: A
PNF
Service Orchestration
Network
VNF
Allotted Resource
Resource Orchestration
Cloud Resource Orchestration
Resource Orchestration
An Allotted Resource can be homed to an existing “underlying” network function or Service Instance, or homing could determine that a new network function Service Instance is needed. This would result in a 2nd level of Service Orchestration.
Each Resource Type has its own “Generic” model-driven flow. There currently exist such flows for “VNF” and “Network” Resource Types.
“Generic” model-driven Service flow
Note recursion
Service Y is being treated as a “Resource” from the perspective of Service X.

## Slide 15: Nested / Compound Services:
Service W:
topology_template:
node_templates:
VNF_W
Service_X
Service X:
topology_template:
node_templates:
VNF_X
Service_Y
Service Y:
topology_template:
node_templates:
VNF_Y
Service_Z
Service Z:
topology_template:
node_templates:
VNF_Z

## Slide 16: Conclusions
Service Providers require the ability to define Services that can be leveraged by higher order Services and other compounded services / segments / slices.
Consistent with ETSI MANO, ONAP should NOT separate Service Orchestration and Resource Orchestration into two separate named components, because each Resource can be exposed as a Service
      What appears as a “Resource” from one Service’s perspective, may actually be a Service from another perspective
      In Addition, ONAP scope is much broader than ETSI MANO (MANO limited to Cloud infrastructure services and management of VNF as a basic resource (ignoring the application of the VNF)), therefore SO should support full orchestration scope of ONAP
      To achieve alignment with MANO for common functionality, SO should expose APIs for basic resource onboarding/LCM (VNF) . This is SOL-001, SOL-004 and SOL-005.
      or simple network service onboarding/LCM (composed of one or more VNFs) and related modelsIn addition, ONAP SO should Support “Service reuse” to drive model driven run-time behavior for complex services:
        Compounded Services (e.g. Residential vCPE, Network Slicing Segments, etc.)
        Nested Services (e.g. E2E Slice)
      ONAP should provide Service Providers deployment flexibility to address scalability, geographic distribution and redundancy / resiliency
      But should not impose extra complexity and cost on service providers by separating service / resource orchestration that provides little known benefit

## Slide 17: APPC & VF-C Convergence Note – A major goal of the ONAP platform (R2 or a later release) is to specify a common set of functions to unify the APP-C and VF-C functionalities.

## Slide 18: Role Of Controllers in ONAP
ONAP Controllers configure and maintain the health of network functional elements and services throughout their lifecycle.
Programmable network application management platform
  Behavior patterns programmed via models and policies
  Standards based models & protocols for multi-vendor implementation
  Operational control, coordinated state changes across devices, etc.
Manages the health of the network services & VNFs in its scope
  Policy-based optimization to meet SLAs
  Event-based control loop automation to solve local issues in near real-time
  Executes action for outer control loop automation (Driven by DCAE, Policy, etc.)
Local source of truth
  Manages inventory within its scope
  All stages/states of lifecycle
  Configuration audits
  ONAP has a layered architecture, with the role of controller clearly defined
  Need to avoid duplicating functions across layers within the controller layer (e.g. DCAE, Service/Resource Orchestration, etc.)

## Slide 19: Functional Description of ONAP Components

## Slide 20: Service Design and Creation (SDC) Functional Architecture
Import Management Functions
  Import ONAP base capability definitions from Development Catalog to Design Catalog as building blocks in a standard format
Create Flows & Policies
  Create reusable management flows using building blocks & associated events & Policies
Onboard Network Functions
  Create VF model to include vendor’s description, scripts, & license model
  Customize models to include Service Provider specific attributes
Design Service & Operations Methods
  Create Service models with resources
  Design and associate operations processes & policies (e.g., Instantiation, DCAE/Control Loop, Change Management, etc.) and configure them to be service specific
Certification
  Simulate & test the design in Sandbox environment
  Certify Readiness & Adherence to Standards
Metadata Distribution
  Publish certified models for distribution to runtime catalog
  Notifications & Version Control
Service Provider’s Design environment to: 1. Catalog management capabilities, 2. Onboard vendor provided Network Functions, 3. Design Services and Operations, 4. Test, certify, and distribute models for Runtime Execution

## Slide 21: Catalog Architecture
Partially Existing:
Design Catalog (ONAP Design Platform - SDC)
  Catalog imported ONAP generic re-usable management software function & policy definitions
  Enable SP to onboard standard VNF packages
  Support SP users in design & lifecycle management of Resource and Service models
  Provide presentation to support service compositions & management flow associations
  Manages catalog’s elements versions, lifecycle and access policy
  All certified asset definitions available for re-use and composition
Yet to be implemented:
Development Catalog (ONAP Development)
  Common toolsets and data store for creation of ONAP software models & management flows/policies
  Interact with external software development teams and suppliers to onboard custom software, adapters or new capabilities
Runtime Catalog (ONAP Execution Platform)
  Provide a common data store for distributed certified models
  Provide ONAP runtime component’s subscription to access component view of the model data
  Maintain executable images and other runtime artifacts
The overall ONAP Catalog architecture includes Development Catalog, Design Catalog, and Runtime Catalog

## Slide 22: Orchestrator
Model Driven Orchestration and APIs
  Runtime behavior driven by service and resource models and policies (including compound/nested services) designed in or onboarded into SDC
  Orchestrates service delivery, change management as well as open and closed-loop control actions
  Provides standard, model driven APIs for requested actions
  Tracks orchestrated activity for the life of the request, but doesn’t maintain state of orchestrated components
The ONAP Orchestrator orchestrates service, resources and associated cross-controller activity driven by requests and events that indicate the need to create, modify or remove service and resource instances, or to perform multi-control layer remedy actions.
Processing of Service Requests:
  Performs Decomposition, Recipe Selection, Recipe Execution (including Rainy Day)
  Triggers and Records Results for:
  Homing
  Assign, Create, Configure (Controller/multi-cloud activity)
  Validation
  Monitoring
  Separate execution threads for service, decomposed resources, and any subtending service(s) provide nested service orchestration in a recursive manner
Orchestration of Controllers
  Coordinates activities across Multi-Cloud/ SDN-C/Generic NF controllers, including data sourcing and mapping to Controller inputs

## Slide 23: Orchestrator Functional Internal View
Key
OE-x
OI-x
SO External API
SO Internal API
APIs labeled on slide relative to SO for reference only.
SO-SO communication across ONAP instances looks like an External API.
OE-8
Orch Execution Engine (BPMN/TOSCA)
Data Store
Request DB
Multi-Cloud
Orch Service & Resource
Catalog
Request
Handler
Store
Request
Select Recipe
Track
Requests
BPMN DB
SDN Controller
Generic NF Controller
Map Request Data to Recipe & Invoke BPEL Execution
Resource
Models
Service Models
Orchestrator
Resource Level Orch
Resource/Controller Adapters
API Handler
Infrastructure/Network Adapter
Select Adapter Template
Map Data to Template
Execute Transaction
Controller Adapter
Service Level
OE-2
OE-1
OE-3
OE-5
OE-6
OE-7
OE-9
OE-10
OI-11
OI-12
OI-5
OI-6
Micro Services Bus / Data Movement
Dashboard OA&M
OE-4
OE-11
External API
Service Design & Creation
Micro Services Bus / Data Movement
OI-7
OI-8
OI-2
OI-3
OI-10
SDC Distribution Client
OI-1
Active & Available Inventory
External Registry
ONAP Optimization Framework
Data Collection, Analytics, and Events
Event Correlation
SO-SO communication within a single ONAP instance is via Micro Services Bus.
Controller functions common to both SDN-C and Generic NF Controller. Note that this may actually be 2 APIs and not a single.
Allotted Resources case
Complex Services case
Controller functions specific only to SDN-C. E.g., “Assign Network Resources” for the VNFs in a L4+ Service.
OI-9
OI-4

## Slide 24: Generic NF Controller (L4-7) Architecture
Generic NF Controller for L4-7 configures and maintains the health of applications throughout its lifecycle.
  The Lifecycle Management Functions are a normalization of VF-C and APP-C functions into a common, extensible library
Programmable network application management platform
  Behavior patterns programmed via models and policies
  Standards based models & protocols for multi-vendor implementation
  Extensible SB adapter set including vendor specific VNF-Managers
  Operational control, version management, software updates, etc.
Manages the health of applications/VNFs/PNFs within its scope
  Policy-based optimization to meet SLAs
  Event-based control loop automation to solve local issues near real-time
Local source of truth
  Manages inventory within its scope
  All stages/states of lifecycle
  Configuration audits
Key Attributes of Generic NF Controllers
  Intimate with network protocols
  Manages the state of services
  Provide Deployment Flexibility to meet user scalability / resilience needs
Generic NF
Controller
Adapters
Service Logic Processing
Chef
Assigned Resources Inventory:
Service* Topology & VNF/PNF State
Netconf
API Handler
Active & Available Inventory
Service Design & Creation
Ansible
Others
…
Orchestration
Data Collection, Analytics & Events
Closed Loop Actions
Inventory
Updates
Orchestration
Service Logic
Service Logic
Service Logic
Config mS
SW Upgrade mS
Audit mS
…
Lifecycle Mgmt. Functions/MicroServices (mS)
…
…
Artifact Distribution
*Not E2E service view. The “Service” view in the Generic NF Controller is limited its scope of control
Applications
VNFs
PNFs
Multi-Cloud Adapter
Multi-VIM/Cloud
MSB/Data Movement
MSB/Data Movement
MSB/Data Movement
CE-1
CE-2
CE-3
CE-5
External System Adapter (s)
External
3rd Party Controllers
Specific VNF Managers
Element Mgt. Systems
CI-2
CI-1
CI-4
VNF Descriptors
Repository
Config Templates
Engineering Rules
Service Logic
Policy Cache/Event Match
Operational Tree/Config Tree
(Service Model)
CE-4
CI-7
CI-6
Key
CE-x
CI-x
Controller External API
Controller Internal API
CI-3
CE-6
CI-5

## Slide 25: SDN-Controller Architecture
SDN Controller configures and maintains the health of L1-3 VNFs/PNFs and network services throughout their lifecycle
Programmable network application management platform
  Behavior patterns programmed via models and policies
  Standards based models & protocols for multi-vendor implementation
  Extensible SB adapter set supporting various network config protocols, including 3rd party controllers
  Operational control, coordinated state changes across devices, source of telemetry/events, etc.
Manages the health of network services & VNFs/PNFs in its scope
  Policy-based optimization to meet SLAs
  Event-based control loop automation to solve local issues near real-time
  Action executor for outer control loop automation
Local source of truth
  Manages inventory within its scope
  All stages/states of lifecycle
  Configuration audits
Key Attributes of Controllers
  Intimate with network protocols
  Manages the state of services
  Single service/network domain scope per instance
Service Control
Processing
SDN
Controller
NB Service/Network Yang Models
SB Device Yang Models
API Handler
Adapters
NetConf/ YANG
Multi-Cloud Network Adapter
BGP LS/
PCEP
Others
…
Multi-VIM/Cloud
Active & Available Inventory
Service Design & Creation
Orchestration
Data Collection, Analytics & Events
Closed Loop Actions
Inventory
Updates
Orchestration
Artifact Distribution
External System Adapter (s)
External
3rd Party Controllers
Element Mgt. Systems
MSB/Data Movement
MSB/Data Movement
MSB/Data Movement
CE-2
CE-3
CE-4
CE-5
CE-1
Key
CE-x
CI-x
Controller External API
Controller Internal API
Service Logic
Repository
Service Logic
Service Logic
Service Logic
IP/VRF Assign
L2 Service Create
L3 VPN Service Create
SD-WAN Create
TE Tunneling
BGP Config
SW Upgrade
…
…
Configuration Templates
Service/Network Design & Engineering Rules
Policies
VNFs
PNFs
OpenFlow
Assigned Resources Inventory: Service* Topology &
VNF/PNF State
Operational Tree/
Config Tree
(Service Model)
CI-2
CI-4
CI-5
CI-3
CI-1
CI-6
CI-7
*Not E2E service view. The “Service” view in the SDN Controller is limited its scope of control
CE-6

## Slide 26: Data Collection, Analytics and Events (DCAE) Architecture
DCAE enables real-time fault, performance and other data/event collection from service, network and infrastructure
  Collect Data & Events once and make available to multiple applications
  Telemetry records from VNFs and PNFs (fault, performance, usage, etc.)
Makes collected data available to real-time analytic µ-services to:
  Identify anomalies and other events for closed loop remediation
  Enable closed-loop automation to remedy fault/performance conditions
  Enable closed-loop automation to scale resources up/down
  Enable analysis at edge and central locations
  Extensible framework to integrate applications from various sources
Provides Correlation & Analysis to manage service at various layers
  Multi-Cloud Infrastructure layer, network element layer, Network & Complex Services layer, Operational Management layer
  Cross-layer, Intra-domain and cross-domain correlation
Streaming
Data
Batch
Data
SNMP
Syslog
Other
Unstructured & Structured Data Persistence
Analytic Frameworks:
Holmes, CDAP, Other
Stream Data Collection
Events
Flows
Other
Batch Data Collection
Analytic µServices
Capacity Management
DCAE
Congestion Detection
Fault Correlation
QoS Monitoring
Security Analysis
Managed Environment
Storage
Compute
VNFs / PNFs
Applications
Networking
Logs
Files
Other
Multi-Cloud Telemetry Adaption
…
VES
DMaaP (Pub/Sub for Events/Data within DCAE & across ONAP)
OOM – DCAE Controller

## Slide 27: Active and Available Inventory
A&AI tracks the global inventory of the networks, services & resources that ONAP manages.
  The what, where, when of the managed assets and their relationships, and which controller manages them, etc.
Real-time, logically centralized view of topology & inventory
  Map and broker of data sources in the global network
  Federates across controllers, cloud infrastructure, partners, etc.
  Real-time access to authoritative sources with ability to aggregate views
  Real-time awareness of network elements, applications and service instances
  Aware of all the assets in scope, organized by their type, state & location
  Keeps track of the dynamic relationships of the virtual assets
  Aware of resource assignments, availability & relationships to customer
Network events used to maintain the integrity of inventory
  Monitors network events to register services, networks & resources
  Tracks creation, modification or removal of entities and relationships
A&AI
API Handler
A&AI Application Management Functions
Data Audits
History
Archival
OA&M
Notifications
Event Subscriptions
A&AI Data Management Services
Inventory & Topology Management
Service
Network
Resource
Infrastructure
Active
Topology
Assignment
Available
Entitlement
Reference
Inventory & Topology
Entitlements & Reference
Graph Layer
Metadata Engine
API Generation
Schema Generation
Version Management
Metadata Management
Model-driven
  Schema, APIs, database views, data integrity mechanisms generated from models expressed in TOSCA.

## Slide 28: ONAP SDK-Driven Sub-System Approach
Goal: Move toward a common platform architecture, starting with Controllers, Orchestration and Multi-Cloud
Improve agility for on-demand/situational creation of instances
Reduce software footprint of platform component instances
Reusable tool chain and framework across components
Facilitate agile introduction and swap-out of technologies
Consistent use of NB and SB APIs
Enable flexible options to add and extend platform capabilities
For Further Study

## Slide 29: SDK-Driven Sub-System – Libraries (including CCSDK)
*Plugins/Adapters can include:
3rd party VNFM Drivers • 3rd party EMS Drivers
3rd party SFC Drivers • Ansible/Chef/Puppet
Netconf/Yang • CLI
SNMP • etc.
SDK Libraries
Orchestrators
Rackspace
IBM
Google
Orchestration Function SDK
Multi-Cloud Adaptation SDK
Controllers
OpenStack
Azure
AWS
OSSs
VNFs
PNFs
Multi-Cloud
μServices
Control Function SDK (CCSDK)
ODL
Imperative Models
BPMN orchestration
engine
Sub-Models
TOSCA-Cloud
Translation/Mapper
Declarative Models
TOSCA orchestration
engine
Library of
Common Control/NFV Lifecycle Mgt. Functions
Rebuild
VNF Configure
Network Config.
Stop/Start
A udit
Upgrade
Scale
Svc Function Chain
Heal
Library of
Common Cloud Translations (shims)
Telemetry
Scale
Heal
Register
Cloud Resource
Instantiation
LB
…
SB API SDK
(Adapters)
Plugins/Adapters*
M-Cloud APIs
etc.
NB API SDK
API Handler
API Catalog
Library of Flows
Service, Resource, Etc.
Orchestration APIs
Controller APIs
Cloud APIs
API Configurator
Controller APIs
OSS APIs
μServices APIs
Netconf/Yang
Ansible
Collectors
OpenStack
Azure
AWS
API Catalog
ONOS
Open
ROADM
…
…
Resource Orchestration APIs
Assign
Health Check
For Further Study

## Slide 30: Controller Personas Based on SDK Libraries
SDK Libraries
Controller Personas Examples
(created from CCSDK)
SDN-C Persona
NB API
Controller APIs
Control Functions
ODL
Library
VNF Configure
Network Config
Svc Function Chain
Assign
SB
API
Other Adapters
OSS APIs
μServices APIs
Netconf/Yang
…
Generic VNF Controller Persona
NB API
Controller APIs
LCM Functions
ODL
Library
SB
API
Ansible
μServices APIs
Netconf/Yang
Rebuild
Stop/Start
Audit
HealthCk
Scale
Heal
Other engines
3rd VNFM/EMS
3rd Party SFC
VNF Configure
Svc Function Chain
OSS APIs
Other Adapters
…
…
…
…
For Further Study

## Slide 31: ONAP High-Level Architecture for R2 (Beijing)

## Slide 32: ONAP Beijing Architecture (High-Level View with Projects)
New projects to be added following TSC approval
Integration
VNF Requirements
Modeling (Utilities)
VNF Validation Program
PNFs
K8s

## Slide 33: Functional Description of Beijing Architecture Components Note – The detailed description of features/capabilities/interfaces for each component planned for the Beijing release will be provided by respective projects.

## Slide 34: Orchestration (1/2)
Orchestration
Definition:
Provides functionality for the execution of specified process and automated sequencing of activities, task, rules and policies needed for creation, modification, removal of network application, infrastructure services or resources.
Supports different specializations with specific orchestration scopes.
Specialization scopes include, but are not limited to, network service LCM (i..e VNFO specialization), network slice specialization, domain specific specialization.
Provided Interfaces:
Service Management Interface
  Provides the interface to manage the services that orchestration provides.
Network Service LCM interface
  Provides the specific network service LCM interface.
Actuation Request Interface
  Provides support of actuation requests towards the services.
Service Management Interface
Network Service LCM Interface
Actuation Request Interface
Service Definition Reception interface
Service Management Interface
VNF LCM Interface
NF Config Interface
Optimization request Interface
Inventory Service Interface
Transport Service Interface
Network Service LCM interface

## Slide 35: Orchestration (2/2)
Orchestration
Consumed interface Interfaces:
Service Management Interface, from: Orchestration
VNF LCM Interface, from: Generic NF controller
Optimization Request Interface, from: Optimization Framework
NF Config Interface, from: Generic NF controller
Inventory Service Interface, from: Available and Active Inventory
Transport Service Interface, from: SDN Controller.
Network Service LCM interface, from: Orchestrator
Consumed Models:
Network Service Descriptor
Rest to be filled in.
Service Management Interface
Network Service LCM Interface
Actuation Request Interface
Service Definition Reception Interface
Service Management Interface
VNF LCM Interface
NF Config Interface
Optimization request Interface
Inventory Service Interface
Transport Service Interface
Network Service LCM interface

## Slide 36: Data Collection, Analytics, and Events
Data Collection, Analytics, and Events
Definition:
DCAE is the ONAP subsystem that supports closed loop control and higher-level correlation for business and operations activities. DCAE collects performance, usage, and configuration data; provides computation of analytics; aids in trouble-shooting and management; and publishes event, data, and analytics to the rest of the ONAP system for FCAPS functionality.
Provided Interfaces:
Interface 1: Data collection interface (used by VNFs and others from which data is collected)
  Interface for various FCAPS data entering DCAE/ONAP.
Interface 2: Deployment interface (used by CLAMP)
  Interface for triggering the deployment and changes of a control loop
Consumed interface Interfaces:
Interface 1: Data movement platform interface (provided by DMaaP)
  Interface for data transportation between DCAE subcomponents and between DCAE and other ONAP components
  This interface can also be used for publishing events to other ONAP components.
Interface 2: Data enrichment interface (provided by A&AI)
  Interface used by DCAE for enriching collected raw data by adding information not contained in original data, e.g. identifying the VNF type from VNF identity by querying this interface.
Interface 2: Service model change interface (Provided by SDC)
  Interface for fetching control loop models and updates.
Interface 4: Policy interface (Provided by Policy)
  Interface for fetching configuration and operation policies on control loop and control loop components into DCAE for application.
Consumed Models: TOSCA models descripting control loop construction (e.g. collection and analytics apparatus)
Interface 1
Interface N

## Slide 37: Active & Available Inventory, External Registry
Active & Available Inventory, External Registry
Definition:
AAI maintains a live view of services and resources in the network, providing the state and relationships of the service components
Maintains the view of the managed systems services and resources, as well as information of the external systems that ONAP will connect to.
It provides real-time views of a managed systems resources, services and relationships with each other.
AAI provides a GUI to provide users the ability to find and inspect inventory data. This includes a free-text search, inspection of specific entities and their relationships, and aggregated views of data.
Provided Interfaces:
Inventory Service Interfaces:
  AAI Resources REST API - Provides the ability to store, read, update inventory information
  Gizmo: a low-level REST CRUD API that provides targeted and simple access to entities, relationships, and their properties. Gizmo also provides lightweight collections, and transactional bulk write support
Complex Query Interface: AAI Traversal REST API – Provides the ability to perform complex traversals of the AAI Graph
External Register interface
  Provides the ability to provision and read external system information
Consumed interface Interfaces:
DMaaP
SDC
Multivim
Consumed Models: TOSCA Service and Resource Models
Inventory Service Interface
External Register Interface
Interface N

## Slide 38: AAF Functional Description
The purpose of AAF (Application Authorization Framework) is to organize software authorizations so that applications, tools and services can match the access needed to perform job functions. This is a critical function for Cloud environments, as Services need to be able to be installed and running in a very short time, and should not be encumbered with local configurations of Users, Permissions and Passwords.
To be effective during a computer transaction, Security must not only be secure, but very fast. Given that each transaction must be checked and validated for Authorization and Authentication, it is critical that all elements on this path perform optimally.
AAF contains some elements of Role Based Authorization, but includes Attribute Based Authorization elements as well.
Essential Functional Components:
The core component to deliver this Enterprise Access is a RESTful service, with runtime instances backed by a resilient Datastore (Cassandra as of release 1.3)
The Data is managed by RESTful API, with Admin functions supplemented by Character Based User interface and certain GUI elements.
The Service accessible by provided Caching Clients and by specialized plugins
CADI (A Framework for providing Enterprise Class Authentication and Authorization with minimal configuration to Containers and Standalone Services)
Cassandra (GRID Core)

## Slide 39: AAF Functional Description
CADI stands for Code, Access, Data and Identity, This Framework addresses the Runtime Elements of Access and Identity.
Many other tools address elements of this vision. For instance, Sonar and Fortify evaluate code for maintainability and security problems, while Voltage provides encryption for Data at Rest.
However, CADI Framework contributes to these for runtime applications by:
Code - CADI provides reusable Security Client code, and ties in with appropriate Security Interfaces (i.e. J2EE Standard Filters)
Access - CADI provides links to Authorization tool(s) (AAF) for Fine-grained Authorization. Also, data from Identity servers is also made available to Coders easily. For instance, CADI provides a clean API to read the Course Grained Authorization information available within the CSP Cookie.
Data - CADI provides simple setup for certificates needed for TLS connectivity, so that barriers to using HTTPS are greatly reduced. It also ensures that no one using CADI uses clear-text passwords in Configuration files.
Identity - CADI Framework obtains the Identity of any callers by delegating to CSO approved Identity servers on behalf of the client, so that Applications can be assured of who is talking to them.

## Slide 40: AAF Functional Description
Entities within AAF
Namespaces
A Namespace, in AAF, is the ensemble of Roles, Permissions and Identities controllable within the domain assigned to a member of the Organization's chain-of-command.
Namespaces are known by domain, in dot-delimited form. ex: com.att.aaf or com.att.wfa, and they are hierarchically managed.
People in Namespaces
Owner (Responsible)
A key feature of how AAF works for an Enterprise is by supporting federated responsibility. This responsibility is clearly delineated by the owner entry. Organizations (i.e. companies) may establish their own policies
Roles
I) "Roles" is a bit of an overloaded term in Security software. It has unfortunately been typically used as a flat, unscoped Group, known only to the Application.
Typical examples such as "user" and "admin" have no meaning outside the immediate context of the application. "admin"??? "admin" of what? What are the behaviors allowed for "admin"? Is the "admin" of Application A, the same as Application B? (answer, no!)
Permissions
Permissions are the other side of the decoupled Authorization equation. Permissions represent some resource that needs to be protected by the Application in question. examples:
A GUI Admin page should be available to only those who job function is to administer this app.
SPI Data that this App accesses should only be accessible to those who are allowed to see SPI data.
Full data reporting dumps should only be accessible to Audit teams.

## Slide 41: AAF Object Model

## Slide 42: DMaaP Functional Description
Data movement as a platform(DMaaP) is a premier platform for high performing and cost effective data movement services that transports and processes data from any source to any target with the format, quality, security, and concurrency required to serve the business and customer needs.
DMaaP consists of three major functional areas:
1. Data Filtering - the data preprocessing at the edge via data analytics and compression to reduce the data size needed to be processed.
2. Data Transport - the transport of data intra & inter data centers. The transport will support both file based and event based data movement. The Data Transport process needs to provide the ability to move data from any system to any system with minimal latency, guaranteed delivery and highly available solution that supports a self-subscription model that lowers initial cost and improves time to market.
3. Data Processing - the low latency and high throughput data transformation, aggregation, and analysis. The processing will be elastically scalable and fault-tolerant across data centers. The Data processing needs to provide the ability to process both batch and near real-time data.
This service is build using Apache Kafka and Restful API is created for message publishing, subscribing and admin activities

## Slide 43: APPC (1/2)
APPC
Definition:
Application Controller (APPC) performs the functions to manage the lifecycle of VNFs and their components.
It provides a comprehensive set of controller actions such as Configure, Modify Configuration, Start, Stop, Migrate, Restart, Rebuild, and so on. Consult readthedocs documentation for the full set of APIs offered/supported.
It supports a set of standard VNF interfaces (Netconf, Chef, Ansible.), and
Is designed to be self-service using a model driven architecture that provides a layer of abstraction making APPC completely service, VNF, and site agnostic.
Information about the APPC architecture and provided APIs can be found in the APPC User Guide and LCM & OAM API Guides on readthedocs
.
Provided Interfaces: (refer to APPC User Guide for details)

## Slide 44: APPC (2/2)
APPC
Consumed Interfaces
Consumed Models:
TOSCA Dependency Model
APP-C also support a variety of models, most of which are created by the APPC Configuration Design Tool (CDT). Examples are:
  Reference Data Model (json)
  VNF Capabilities Model (json)
  Template Model (json or xml)
  Parameter Definition Model (yaml)

## Slide 45: CLAMP (1/2)
CLAMP
Definition:
CLAMP is a platform for designing and managing control loops.
It is used to design a control loop, configure it with specific parameters for a particular network service,
then It interacts with other systems to deploy/undeploy and execute the control loop.
Information about the CLAMP architecture and provided APIs can be found in the CLAMP User Guide and LCM & OAM API Guides on readthedocs
Provided Interfaces: (CLAMP doesn’t expose functional relates API’s except the one below, refer to CLAMP documentation for more details)
Interfaces Service Purpose/Comments
HealthCheck REST Health Check of CLAMP instance

## Slide 46: CLAMP (2/2)
CLAMP
Consumed Models: (No specific models were used in the above interface except for Policy(json))
Consumed Interfaces:
Interfaces Service Purpose/Comments
SDC REST Distribution of service to DCAE
DCAE REST Common Controller Framework
Policy REST(JSON data) Create Configuration and Operational policy

## Slide 47: Use-case UI
Usecase UI
Definition:
Provides portal for service life cycle management
Provides portal for VNF alarm and performance
Provides portal for VM alarm and performance
Provided Interfaces:
None
Note: Can be more than one page
None
Catalog Synchronization Interface
Service Orchestrator Interface
Inventory Service Interface
NS/VNF Onboard Interface
Service Registration Interface
Data Subscription Interface

## Slide 48: Use-case UI
Usecase UI
Consumed Interfaces:
Catalog Synchronization Interface, from: SDC
Service Orchestrator Interface, from: SO
Inventory Service Interface, from: Available and Active Inventory
NS/VNF Onboard Interface, from: VF-C
Service Registration Interface, from: MSB
Data Subscription Interface, from: DMaaP
Note: Can be more than one page
None
Catalog Synchronization Interface
Service Orchestrator Interface
Inventory Service Interface
NS/VNF Onboard Interface
Service Registration Interface
Data Subscription Interface
Consumed Models:
Network Service Descriptor
VNF Descriptor

## Slide 49: ONAP CLI
ONAP CLI
Definition:
Provides Open CLI Platform (OCLIP) – Industry first Model-driven command line interface platform
Provides commands for performing end-end service on-boarding and life cycle management
Provides command console for Linux and web platforms.
Provided Interfaces:
micro-service discovery
  Provides commands for micro service discovery and registration
external system and VNF cloud on-boarding
  Provides commands for registering/unregistering VIM, VNFM, EMS and SDNC
customer and subscription management
  Provides commands for subscription and service-type life cycle management
resource on-boarding
  Provides commands for adding VNF modules
Product and service management
  Provides commands for design time creation and management of VF and NS
network service life-cycle management
  Provides commands for creating and managing Network services (NS)
Consumed interface Interfaces:
REST API from SDC, SO, AAI, MSB.
micro-service discovery Interface (MSB)
external system and VNF cloud on-boarding interface (AAI)
customer and subscription management interface (AAI)
resource on-boarding interface (SDC)
Product and service management interface (SDC)
network service life-cycle management interface (SO)
micro-service discovery commands
external system and VNF cloud on-boarding commands
customer and subscription management commands
resource on-boarding commands
Product and service management commands
network service life-cycle management commands
Consumed Models:
- Open Command Specification (OCS) 1.0

## Slide 50: Microservices Bus (1/2)
Micro Services Bus / Data Movement
Definition:
Provides a reliable, resilient and scalable communication and governance infrastructure to support ONAP Microservice Architecture(OMSA).
Provides RESTFul API for service registration/discovery
Provides JAVA SDK for service registration and access
Provides a transparent service registration proxy with OOM-Kube2MSB
Provides a transparent service communication proxy which handles service discovery, load balancing, routing, failure handling, and visibility-Internal API Gateway(Implemented) and Mesh Sidecar(WIP)
Provides an External API Gateway to expose ONAP services to the outside world
Service Registration REST Interface
Service Discovery RES Interface
JAVA SDK for Service Registration/Access
Interface N

## Slide 51: Microservices Bus (2/2)
Micro Services Bus / Data Movement
Consumed interface Interfaces: (None)
Consumed Models:
Swagger for RESTFul APIs definition
Service definition in kubernetes config files for Kube2MSB service registration
Service Registration REST Interface
Service Discovery RES Interface
JAVA SDK for Service Registration/Access
Interface N
Provided Interfaces:
Service Registration REST Interface
  Provides the RESTFul interface to register ONAP services.
Service Discovery REST Interface
  Provides the RESTFul interface to discover ONAP services.
JAVA SDK
  Provides JAVA SDK to register ONAP services.
  Provides JAVA SDK to access ONAP services.
  Note: ONAP components don' t need interfaces to leverage the transparent service registration proxy and communication proxy.

## Slide 52: Microservices Bus Updated With Swagger SDK(1/2)
Micro Services Bus / Data Movement
Definition:
Provides a reliable, resilient and scalable communication and governance infrastructure to support ONAP Microservice Architecture(OMSA).
Provides RESTFul API for service registration/discovery
Provides JAVA SDK for service registration and access
Provides a transparent service registration proxy with OOM-Kube2MSB
Provides a transparent service communication proxy which handles service discovery, load balancing, routing, failure handling, and visibility-Internal API Gateway(Implemented) and Mesh Sidecar(WIP)
Provides an External API Gateway to expose ONAP services to the outside world
Swagger SDK for auto-generate the client SDK in different languages for every micro-services in ONAP. Also it deploys the generated SDK into the nexus.
Service Registration REST Interface
Service Discovery RES Interface
JAVA SDK for Service Registration/Access
Swagger SDK
Interface N

## Slide 53: Microservices Bus Updated With Swagger SDK(2/2)
Micro Services Bus / Data Movement
Consumed interface Interfaces: (None)
Consumed Models:
Swagger for RESTFul APIs definition
Service definition in kubernetes config files for Kube2MSB service registration
Service Registration REST Interface
Service Discovery RES Interface
JAVA SDK for Service Registration/Access
Swagger SDK
Interface N
Provided Interfaces:
Service Registration REST Interface
  Provides the RESTFul interface to register ONAP services.
Service Discovery REST Interface
  Provides the RESTFul interface to discover ONAP services.
JAVA SDK
  Provides JAVA SDK to register ONAP services.
  Provides JAVA SDK to access ONAP services.
  Note: ONAP components don' t need interfaces to leverage the transparent service registration proxy and communication proxy.
Swagger SDK
  provides Mvn plug-in settings for (JAVA)client sdk generation

## Slide 54: Optimization Framework - R2 (1/4)
Optimization Framework (OOF)
Definition:
ONAP Optimization Framework (OOF) provides functionality for creating and running optimization applications by leveraging a policy-driven, declarative approach.
Supports different specializations (applications) with specific domain and optimization needs.
Initial specialization scopes include, but are not limited to, VNF placement support via Homing and Allocation Service (HAS) with different use cases, and change management scheduling service.
  For R2, the OOF will support vCPE use case (as a MVP).
  For R2, the OOF will demonstrate an example of Change Management Scheduling Optimization using the OOF design framework with simple, representative constraints.
Service Orchestrator (SO)
Change Management Portal
Policy Interface
Inventory Service Interface
Service/Policy Models Interface
Infrastructure Metrics Interface
Provided Interfaces:
Placement Optimization Interface
  Provides functionality for the Service Orchestrator to specify placement services [vCPE use case]
Change Management Portal Interface
  Provides functionality for calculating schedules that satisfy time constraints and conflicts [R2 focus on a demonstration of the design framework; alignment with Change Management scheduling use case]
Consumed Models:
Policy Models (constraints) and License Models from: SDC
Infrastructure Metrics Models, from: Multi Cloud
Consumed Interfaces:
Policy Interface, from: Policy
Inventory Service Interface, from: Available and Active Inventory
Service/Policy Models Interface, from: SDC
Infrastructure Metrics Interface, from: Multi Cloud

## Slide 55: Optimization Framework - R3+ (2/4)
Optimization Framework (OOF)
Additional Provided Interfaces for R3 and beyond:
Placement Optimization Interface
  For R2, the focus is on supporting vCPE use case;
  for R3 and beyond, the OOF will also support VoLTE, VNF/Service scale-in/out (higher order control loop), and RAN-5G.
Change Management Portal Interface
  For R2, the focus is on a demonstration of OOF with simple, representative constraints; this effort will be aligned with the Change Management scheduling use case (for R3 and beyond)
Service Orchestrator (SO)
Change Management Portal
Policy Interface
Inventory Service Interface
Service/Policy Models Interface
Infrastructure Metrics Interface
R3 and Beyond
Application Metrics Interface
Additional Consumed Interfaces for R3 and Beyond:
Application Metrics Interface, from: DCAE [R3 and Beyond]
These are in addition to Policy, Inventory, SDC Models, and Infrastructure metrics from R2
Additional Consumed Models for R3 and beyond:
Application Metrics Models, from: DCAE
Additional Definitions for R3 and beyond:
For R3 and beyond, the OOF will focus on supporting multiple R3 and beyond use case (along with R2 use cases) [supporting VoLTE, VNF/Service scale-in/out (higher order control loop), and RAN-5G].
Synchronization with Change Management Scheduling use case.
Providing additional sample/example optimization applications as documentation.
Proving initial Knowledge Base on OOF (building blocks and recipes for creating complex applications).
Further alignment with S3P objectives.
Note on Functionality for R3 and beyond:
While the items listed below are not part of MVP for R2, the OOF team is initiating discussions and collaborations on these during the R2 time frame, so that the OOF is aligned with the use cases that will mature in R3 and beyond.

## Slide 56: Optimization Framework - Interface Definitions (3/4)
Optimization Request Interface | 
Provided Service | Homing Service API (HAS-API)
Supplementary Information | The OOF will provide a list of possible candidates for placement, which the service orchestrator can use to instantiate the service
Interface Provider(s) | Optimization Framework
Provided Capabilities | Optimization Information Request

## Slide 57: Optimization Framework - Interface Definitions (4/4)
Scheduling Optimization Request Interface | 
Provided Service | Change Management Scheduling API (CMSO API)
Supplementary Information | The OOF will provide a possible schedule of VNF actions (e.g. upgrades) that satisfy the constraints on availability periods and constraints related to conflicts
Interface Provider(s) | Optimization Framework
Provided Capabilities | Optimization Information Request

## Slide 58: VNF SDK (VNF package validation) (1/2)
VNF SDK Marketplace
Definition:
Provides functionality to upload, verify, and download VNFs
VNF Vendors upload VNFs through the Marketplace portal
Marketplace runs package validation tests
VNFs are made available for Onboarding
Marketplace API:
Upload/Re-upload VNF
  Upload VNFs to the Marketplace
Download VNF
  Download VNFs
Query VNF
  Query VNFs by CSAR ID or conditions (name, version, type, provider)
Delete VNF
  Delete VNF from the Marketplace
Consumed Models: SOL-004 (Beijing)
Marketplace API
Note: Can be more than one page
Here we put the services provided

## Slide 59: VNF SDK - Interface Definitions (2/2)
Marketplace API | 
Provided Service | Upload, Download, Query, Delete
Supplementary Information | The VNFSDK APIs are documented on the ONAP Wiki: https://wiki.onap.org/display/DW/API+Documentation
Interface Provider(s) | VNF SDK Marketplace
Provided Capabilities | VNF Pre-onboarding upload/download/validation/query/delete

## Slide 60: VF-C Components
NFVO
NFVI&VIM
VNF Package ( VNFD)
NS Package ( NSD)
NFVO Functions
Support NS Lifecycle Management including NS instantiate, scale, heal, operate (query /update/…)and terminate. In R1, most of NSLCM interfaces align with SOL005 Os-Ma-nfvo reference point
Support integration with multi VNFMs via drivers which include vendors VNFM and generic VNFM. The interfaces between NFVO and driver comply with Or-Vnfm reference point.
Support integration with multi VIM via Multi-Cloud
In R1, NFVO also supports integration with vendor EMS via driver
Instantiate
Scale
Heal
Terminate
SVNFM
Driver
Multi-Cloud
Operate
GVNFM
Vi-Vnfm
Vi-Vnfm
Vi-Vnfm
Or- Vnfm
Or- Vnfm
Or-Vi
EMS
Driver
SO
Policy
UUI
Os-Ma-nfvo

## Slide 61: VF-C – NFVO (1/2)
NFVO
Definition:
Provides reference implementation of NFVO in ETSI MANO architecture
Provides Network service life cycle management
Provides NS/VNF layer’s FCAPS management
Provided Interfaces:
Network Service LCM interface
  Provides Network Service LCM interface
  (NS create/instantiate/scale/heal/terminate/delete/query)
VNF Operation Granting interface
  Provides VNF Operation Granting interface and make granting decision
NS package management interface
  Provides runtime NS package management interface
VNF package management interface
  Provides runtime VNF package management interface
Network Service LCM Interface
VNF Operation Granting Interface
NS package management Interface
VNF package management interface
Note: Can be more than one page
VNF LCM Interface
Inventory Service Interface
Catalog Synchronization interface
Generic VIM Interface
Date report interface
Tosca parser interface
Optimization Request Interface

## Slide 62: VF-C – NFVO (2/2)
NFVO
Consumed Interfaces:
VNF LCM Interface, from: Generic NF controller, SVNFM
Inventory Service Interface, from: Available and Active Inventory
Catalog Synchronization Interface, from: SDC
Generic VIM Interface, From: Multi-cloud
Data report Interface, From: DCAE
Tosca parser Interface, From: Modeling
Service registration and discovery, From: MSB
Optimization Request Interface, from: Optimization Framework -TBD
Consumed Models:
Network Service Descriptor
VNF Descriptor
VES data format
Bpmn Workflow
Network Service LCM Interface
VNF Operation Granting Interface
NS package management interface
VNF package management interface
Note: Can be more than one page
VNF LCM Interface
Inventory Service Interface
Catalog Synchronization interface
Generic VIM Interface
Data report interface
Tosca parser interface
Optimization Request Interface

## Slide 63: VF-C - GVNFM
GVNFM
Definition:
Provides the Generic VNFM
Provides the VNF life cycle management
Supports NFVO to implement Network service LCM management
Provided Interfaces:
VNF LCM interface
  Provides the VNF LCM interface(VNF instantiate/scale/terminate/query)
VNF Package Management interface
  Provides runtime VNF Package management interface
Consumed interface Interfaces:
Catalog and notification Interface, from: NFVO
Inventory Interface, from: A&AI
Tosca parser Interface, From: Modeling
Generic VIM Interface, From: Multi-cloud
Service registration and discovery, From: MSB
VNF Config interface: from VNF -TBD
:
Consumed Models
VNFD
Note: Can be more than one page
VNF LCM Interface
VNF Package management interface
Catalog and notification Interface
Inventory Interface
Tosca parser Interface
Generic VIM Interface
VNF config interface

## Slide 64
64
ONAP Portal
ONAP Portal
Definition:
Portal is a platform that provides the ability to integrate different ONAP applications into a centralized Portal Core.
It allows decentralized applications to run within their own infrastructure while providing common management services and connectivity.
It provides capabilities including application onboarding & user management, and hosted application widgets.
Using the provided SDK, application developers can leverage the built-in capabilities (Services / API / UI controls) along with bundled tools and technologies.
Provided Interfaces:
Portal Admin Interfaces
  Onboarding and User management
SDK Module
  SDK will be used as a base for any ONAP application being built.
  Components using SDK jars: Policy, VID, AAI, and SDC
  SDK bundles together a host of different tools, technologies, and standards that will assist the teams during the development phase.
  SDK includes reusable UI components, authentication & authorization components, visualization & reporting engine, collaborative services, workflow manager, GIS / Map, web component, and widget development framework.
Consumed interface Interfaces:
Restful APIs for fetching available roles to portal’s onboarded application users. from: AAF
Portal Admin Interfaces
SDK Jars (Policy, VID, AAI, and SDC)
AAF

## Slide 65: Logging-analytics (1/2)
Logging-analytics
Definition:
Provides ELK stack where logs are streamed from filebeat sidecar containers per component
Provided Interfaces:
Kibana UI:
  dashboard for indexed logs
Logstash:
  Consumes logs pushed by filebeat containers into elasticsearch indexer
Consumed interface Interfaces:
Filebeat container per microservice exposing logs through a Kubernetes PV:
Consumed Models: none
Kibana
filebeat

## Slide 66
Logging-analytics Interface | 
Provided Service | Kibana dashboard, search service on top of elaticsearch index of ONAP logs – via filebeat
Supplementary Information | 
Interface Provider(s) | AA&I, APPC, SO, Policy, Portal, SDC, SDNC, VID
Provided Capabilities | Search logs using lucene search format Dashboard of configurable search views of logs
Logging-analytics (2/2)

## Slide 67: Multi-Cloud Adaptation (1/2)
Multi-Cloud adaptation
Definition:
enable ONAP to deploy and run on multiple infrastructure environments, including OpenStack and its different distributions, public and private clouds, and micro services containers, etc.
provide a Cloud Mediation Layer supporting multiple infrastructures and network backends so as to effectively prevents vendor lock-in.
decouple the evolution of ONAP platform from the evolution of underlying cloud infrastructure, and minimizes the impact on the deployed ONAP while upgrading the underlying cloud infrastructures independently.
Provided Interfaces:
Resource LCM interface
    Support VNF instantiation/termination
    (Resource create/delete/update/query)
VIM registry/un-registry Interface
  Support registry/un-registry of multiple clouds
  (VIM create/delete/update)
VIM FCAPS management Interface
  Support FCAPS required data collection, event/alert/metrics federation functions
  (message pub/sub)
  VIM capacity/capability query
    Support placement and scheduling purpose
    (capacity/capability query/report)
Resource LCM Interface
VIM registry/un-registry Interface
VIM FCAPS management Interface
  VIM capacity/capability query
ONAP Interface
  Inventory Service Interface
  DMAAP interface
  Logging interface
The third party Cloud interface
  OpenStack Interface
  VMware VIO interface
  Wind River Titanium Interface

## Slide 68: Multi-Cloud Adaptation (2/2)
Multi-Cloud adaptation
Consumed Interfaces:
ONAP
  Inventory Service Interface from Available and Active Inventory
  Message pub/sub interface from DMAAP
  Logging interface from Logging project
The third party Cloud API
    OpenStack Interface
      Ocata
      Mitaka
    VMware VIO interface (Ocata)
    Wind River Titanium Interface (Mitaka)
Consumed Models:
Existing
  VES data format
Underworking
  Hierarchical Infrastructure Resource Information Model
  FCAPS Data Model
ONAP Interface
  Inventory Service Interface
  DMAAP interface
  Logging interface
The third party Cloud interface
  OpenStack Interface
  VMware VIO interface
  Wind River Titanium Interface
Resource LCM Interface
VIM registry/un-registry Interface
VIM FCAPS management Interface
  VIM capacity/capability query

## Slide 69: ONAP Operations Manager (OOM)
ONAP Operations Manager
Definition: OOM is the life cycle manager of the ONAP platform (i.e. SDC, SO, SDNC, etc.). OOM uses the Kubernetes container management system and Consul to provide the following functionality:
  Deployment - with built-in component dependency management (including multiple clusters, federated deployments across sites, and anti-affinity rules)
  Configuration - unified configuration across all ONAP components
  Monitoring - real-time health monitoring feeding to a Consul GUI and Kubernetes
  Restart - failed ONAP components are restarted automatically
  Clustering and Scaling - cluster ONAP services to enable seamless scaling
  Upgrade - change-out containers or configuration with little or no service impact
  Deletion - cleanup individual containers or entire deployments
OOM supports a wide variety of cloud infrastructures to suit your individual requirements.
Provided Interfaces: Consul GUI for health monitoring, Kubernetes CLI for platform management
Consumed interface Interfaces: None
Consumed Models: ONAP Deployment Specifications, ONAP Component Configuration Artifacts
Interface 1
Interface N

## Slide 70: Policy Framework (1/2)
Policy Framework
Definition:
Provides a logically centralized environment for the creation and management of modifiable configurations, rules, assertions and/or conditions to provide real-time decision making on conditions and events that underlie ONAP’s control, orchestration, and management functions
Supports specification, decomposition, distribution and enforcement for various types of policies such as microservice configuration policy, operational policy, decision policy, guard policy, etc.
Policy scopes include, but are not limited to, infrastructure/network management, products and services, operation automation, and security.
Provided Interfaces:
Policy CRUD interface:
  Provide UI and API options to create/query/update/delete configuration, decision and operational policies
Policy deployment interface:
  - Provide UI and API options to deploy configuration, decision and operational policies
Policy model CRUD interface:
  Provide UI and API options to create, query, update and delete policy models
Policy CRUD interface
Policy deployment interface
Policy model CRUD interface
Message Router Pub/Sub Service Interface
Service Registration/Discovery Interface
VNF/VM LCM Interface
NF Config Interface
Inventory Service Interface
Network Service LCM Interface
Service Distribution Interface

## Slide 71: Policy Framework (2/2)
Policy Framework
Consumed interface Interfaces:
Message Router Pub/Sub Service Interface, from: Data Movement as a Platform
Service Registration/Discovery Interface, from: Microservices Bus
VNF/VM LCM Interface, from: Generic NF controller
NF Config Interface, from: Generic NF controller
Inventory Service Interface, from: Available and Active Inventory
Network Service LCM Interface, from: Service Orchestrator
Network Service LCM Interface, from: Virtual Controllers (APPC and VFC)
Service Distribution Interface, from: Service Design & Creation
Consumed Models
Operational policy model
Configuration policy model
Resource model in the catalog
Service model in the catalog
Message Router Pub/Sub Service Interface
Service Registration/Discovery Interface
VNF/VM LCM Interface
NF Config Interface
Inventory Service Interface
Network Service LCM Interface
Service Distribution Interface
Policy CRUD interface
Policy deployment interface
Policy model CRUD interface

## Slide 72: ONAP Beijing Architecture Recommendations

## Slide 73: Recommendations for Beijing Release
Release Theme is Platform Maturity/S3P, key Architecture Principles: Modular, Microservices, Model-driven
Achievable Recommendations for Beijing to begin aligning with target architecture
Modular:
  Improve APIs between components. Document them using Swagger.
  Align interfaces with industry standards, where available/appropriate (for example, ETSI SOL-003, SOL-005, MEF Interlude, Legato, etc.)
Microservices-based
  Use OOM for onboarding, instantiation (support MSB natively), scalability
  Register with MSB
  Use microservices best practices (e.g., separate data from the component, use common KV stores/databases, for KV stores – prefer Consul, etc.)
Model-driven
  Align with info/data models from the Modeling Subcommittee (published December 2017)
  Explore ways to use model-driven principles inside each component as well as across various components (SDC, SO, VFC, APPC, ..)
S3P (see Jason Hunt 1/4 TSC presentation for list of projects providing support for S3P)
  Use common libraries/SDKs/common services where possible to improve overall system resiliency/reliability
  More focus on common services (where possible) also to help reduce testing
  MUSIC for managing various ONAP components states, DB replication in a consistent manner
  Enhanced AAF to support credential management for certificates
  Support Image Management service to enhance security, virus checking, etc.

## Slide 74: Suggestions for Casablanca (in progress)
Still WIP – shared here so PTLs can begin to think about roadmap items
External APIs: External actors view ONAP as a black box. This should simplify the ONAP architecture/interfaces, leveraging the APIs developed by the Ext API project (eg, MEF LSO, TM Forum etc).
Explore Database harmonization: Reduce number of databases in ONAP – perhaps one per type? (SQL/noSQL/KV store/etc).
  Support for DB as a service, rather than independent DB per component?
API Improvements: Currently, ONAP internal interactions are mostly handled via REST-like APIs. We need to enhance the ONAP architecture to support RESTFUL APIs. We also need to ensure that the ONAP platform can handle cloud-native APIs and models.
API Versioning Support
Support for Identity Management in SDC
Support for Security Management.
Support for Beijing->Casablanca upgrade. In-service upgrades per component?
Geo-redundancy – move from real-time (strong) consistency to eventual consistency model
Multi-tenancy support

## Slide 75: ONAP External APIs Work in Progress (R2+ Capabilities)…

## Slide 76: ONAP External APIs
ONAP External APIs expose the capabilities of ONAP. They allow ONAP to be viewed as a “black box” by providing an abstracted view of the ONAP capabilities.
They support that an external consumer of ONAP capabilities can be authenticated and authorized. They can also be used for connecting to systems where ONAP uses the capabilities of other systems.
Note 1: External API does not include all the B2B capabilities of exposure (e.g. partner management)
Note 2: The case where trusted providers of a service (e.g. operator owned transport, or cloud infrastructure) do not need to pass through External API.
For example, External APIs between ONAP and BSS/OSS allow Service Providers to utilize the capabilities of ONAP while using their existing BSS/OSS environment minimizing customization

## Slide 77
E
SP Domain
Customer Domain
Partner Domain
Network Infrastructure
Customer
Application Coordinator
Element Control and Management
Infrastructure Control and Management
Service Orchestration Functionality
Presto
(SOF:ICM)
Allegro
(CUS:SOF)
LEGATO
(BUS:SOF)
Cantata
(CUS:BUS)
Element Control and Management
Infrastructure Control and Management
ADAGIO (ICM:ECM)
LEGATO
(BUS:SOF)
Presto
(SOF:ICM)
ADAGIO (ICM:ECM)
Interlude (SOF:SOF)
Sonata
(BUS:BUS)
Business Applications
Business Applications
Service Orchestration Functionality
REFERENCE ARCHITECTURE
Color Key
ONAP Service Centric External APIs
ONAP Resource Centric External APIs

## Slide 78: SOF Interface Reference Points
Service Orchestration Functionality
Dynamic service control;
Service state info;
Service performance & quality;
Service related alerts;
Dynamic service control;
Service parameter config;
Service state info;
Service performance info;
Service problem alerts
Service feasibility;
Service provisioning configuration & activation;
Request fallout;
Usage events & metrics;
License accounting;
Service performance & quality (e.g., KPI);
Service trouble management;
Service policy;
Capacity engineering;
Address allocation management;
Connectivity and network function feasibility;
Configuration, activation, and management of connectivity and logical network functions;
Topology and routing;
Performance and Fault;
Connectivity policy
LEGATO
PRESTO
ALLEGRO
INTERLUDE
Color Key
ONAP Service Centric External APIs
ONAP Resource Centric External APIs

## Slide 79
E
SP Domain
Customer Domain
Partner Domain
Network Infrastructure
Customer
Application Coordinator
Element Control and Management
Infrastructure Control and Management
Service Orchestration Functionality
Presto
(SOF:ICM)
Allegro
(CUS:SOF)
LEGATO
(BUS:SOF)
Cantata
(CUS:BUS)
Element Control and Management
Infrastructure Control and Management
ADAGIO (ICM:ECM)
LEGATO
(BUS:SOF)
Presto
(SOF:ICM)
ADAGIO (ICM:ECM)
Interlude (SOF:SOF)
Sonata
(BUS:BUS)
Business Applications
Business Applications
Service Orchestration Functionality
ONAP Multi-Domain Federation
BSS
BSS
ONAP
ONAP or
Non-ONAP Orchestration
Color Key
ONAP Service Centric External APIs
ONAP Resource Centric External APIs

## Slide 80: The ONAP “Black Box” View
OAP
OOM
Design Tools
ONAP Management Interfaces
OOM Interfaces
External APIs (Service Centric)
External APIs (Resource Centric)
Resource Interfaces
APIs
UX/CX
CLIs/SDKs
PNFs
VIMs
IaaS
PaaS
SaaS
Legato
Interlude
Presto

## Slide 81: ONAP Target Architecture (High-Level Functional View)
DESIGN-TIME
Policy Creation & Validation
Analytic Application Design
VNF / PNF Onboarding
Resource Onboarding
Service Design
Catalog
Recipe/Eng Rules & Policy Distribution
ONAP Optimization Framework
ONAP Operations Manager
Dashboard OA&M
ONAP External APIs
Common
Services
Application
Authorization
Framework
Logging
Policy Framework
Active & Available Inventory
External Registry
Generic NF Controllers (L4-L7)
Data Collection, Analytics, and Events
Event Correlation
ONAP Optimization Framework
SDN Controller
(L0-L3)
Optional External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Azure
VMware
RackSpace
…
3rd Party Controller
Kubernetes
VNFs
PNFs
Public
Cloud
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Orchestration
Micro Services Bus / Data Movement (see Note 1)
Closed Loop Design
Change Management Design
Life Cycle Management & Config
Design Test & Certification
CLI
OSS / BSS
ONAP Portal
Note 1 – Consistent APIs between Orchestration layer and Controllers
Specific VNF Manager
Element Management System
RUN-TIME
Common Services
Multi-Cloud
Adaptation
U-UI
Controller SDK
(see Note 1)
(see Note 1)
Legato
Interlude
Presto

## Slide 82: Related ONAP Beijing Projects (High-Level View with Projects)
DESIGN-TIME (SDC)
Policy Creation & Validation
VNF SDK
Resource Onboarding
Service & Product Design
Catalog
Recipe/Eng Rules & Policy Distribution
ONAP Operations Manager
Dashboard OA&M (VID)
ONAP External APIs
Common
Services
AAF
Logging
Policy Framework
A&AI/ESR
DCAE
Correlation
Engine (Holmes)
OOF
SDN-C
(L0-L3 Controller)
External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Azure
VMware
RackSpace
…
3rd Party Controller
AMZ
VNFs
PNFs
Public
Cloud
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Service Orchestration
Project
MSB/DMAAP
Design Test & Certification
Others
External Gateway
ONAP CLI
OSS / BSS
ONAP Portal
sVNFM
EMS
RUN-TIME
Common Services
Multi-VIM/Cloud
Infrastructure Adaptation Layer
CLAMP
Application Controller
(APPC)
(L4-L7)
Virtual
Function Controller
(VF-C)
(Note 1)
U-UI
Change Management Design
ONAP Service Centric External APIs
ONAP Resource Centric External APIs
Color Key

## Slide 83: Orchestrator Functional Internal View Example
Key
OE-x
OI-x
SO External API
SO Internal API
APIs labeled on slide relative to SO for reference only.
SO-SO communication within a single ONAP instance is via Micro Services Bus.
Orch Execution Engine (BPMN/TOSCA)
Data Store
Request DB
Multi-Cloud
Orch Service & Resource
Catalog
Request
Handler
Store
Request
Select Recipe
Track
Requests
SDC
BPMN DB
SDN-C
Generic NF Controller
Map Request Data to Recipe & Invoke BPEL Execution
Resource
Models
Service Models
Orchestrator
Resource Level Orch
Resource/Controller Adapters
API Handler
VNF/Network Adapter
Select Adapter Template
Map Data to Template
Execute Transaction
Controller Adapter
Service Level
SDC Distribution Client
A&AI/ESR
OOF
OE-2
OE-1
OE-3
OE-5
OI-1
OE-6
OE-7
OE-8
OE-9
OE-10
OI-2
OI-3
OI-4
OI-5
Micro Services Bus / Data Movement
Dashboard OA&M (VID)
External API
DCAE
OE-4
OE-11
SO-SO communication across ONAP instances is via External API.
Controller functions common to both SDN-C and Generic NF Controller.
Legato
Interlude
Presto

## Slide 84: Legato Interface Reference Point (BSS/OSS-ONAP)
It is envisioned that from a Service Provider to BSS/OSS interaction context (i.e. MEF Legato), the ONAP External API will support the following types of interacts:
BSS/OSS retrieves Service Models
BSS/OSS requests service feasibility determination.
BSS/OSS requests reservations of capabilities related to a potential Service.
BSS/OSS requests activation of Service.
BSS/OSS receives Service activation tracking status updates.
BSS/OSS retrieves Service Inventory
BSS/OSS receives usage events due to a Customer initiating dynamic activity on their Service (e.g., increase in bandwidth).
BSS/OSS receives a summary of Service quality and usage information.
BSS/OSS receives Service state and fault event information
BSS/OSS receives Service Activation Testing results.
BSS/OSS receive capability information about the Service layer.
BSS/OSS manages Licenses
BSS/OSS receives License Usage information

## Slide 85: Interlude Interface Reference Point (ONAP-Partner)
It is envisioned that from a Service Provider to Partner Provider interaction context (i.e. MEF Interlude), the ONAP External API will support the following types of interacts:
Service Provider controls aspects of the Service within the Partner domain (on behalf of the Customer) by requesting changes to dynamic parameters as permitted by service policies.
Service Provider queries state of the Service.
Service Provider requests change to administrative state or permitted attributes of a Service.
Service Provider request creation of connectivity between two Service Interfaces as permitted by established business arrangement.
Service Provider request instantiation of functional service components as permitted by established business arrangement.
Service Provider queries the Partner for detailed information related to Services provided by the Partner to the Service Provider.
Service Provider receives Service specific event notifications (e.g., Service Problem Alerts) from the Partner.
Service Provider receives Service specific performance information from the Partner.
Service Provider request Service related test initiation and receive test results from the Partner.

## Slide 86: Information Domains in ONAP
Governance/Processes
Policy/Rule/Constraints, SLA/OLA Definition,
Asset/Capacity Management, Configuration/Change/Incident Management, Catalog Management
Service Design
Network function on-boarding
Service definition, including Service blueprints
Service Access
User/Tenant Management, Identity Management, RBAC
Entitlement Control
Offered Services
Policy/Rule/Constraints, SLA/OLA Definition
Asset/Capacity Management, Configuration/Change/Incident Management
Services Components
Decomposition/Instantiation/Assurance/Remediation
Service Level Optimization, QoS Optimization, Policy Enforcement,
Logical Resource
Resource Matchmaking/Optimization
Resource Reservations/Allocations, Installation/Configuration
Real Infrastructure
Provider Registration, Infrastructure Discovery/Monitoring
Capacity Optimization
Governance/Processes
Offered Services (What’s offered; Catalog)
Service Components (Service Function Topology; Abstract Network Functions)
“Logical” Resource
(VNFs; VNF Forwarding Graphs)
External APIs
“Real” Infrastructure
(Physical/Virtual/Cloud – On/Off-Premise)
Service Access
Service Design
Micro-service Bus /Integration Backplane
Color Key
ONAP Service Centric External APIs
ONAP Resource Centric External APIs

## Slide 87: ONAP External API Project: Beijing Focus
Deliver points of interoperability between ONAP and External Systems
Development of ONAP External APIs to BSS/OSS (i.e., MEF Legato)
  Service Catalog
  Service Ordering (including Service Instantiation)
  Service Inventory (specification focus) (stretch goal: implementation)
  Service Topology (stretch goal) (specification focus)
  License Usage (stretch goal) (specification focus)
Specification of ONAP External APIs supporting Inter-Provider (i.e., MEF Interlude)
  Service Control (specification focus)
  Service State (operational state) (specification focus)
  Service Inventory / Details (specification focus)
Alignment with MEF Legato, MEF Interlude and TM Forum APIs (explore ETSI SOL005)
Architecture for External APIs
  Identification and involvement of stakeholder ONAP projects (e.g., SDC, SO, AAI, etc.)
  Describe key External API foundation functionalites
  Document the role and requirements of External APIs in Model Driven ONAP and Tool chaining
  Work with Modeling, Architecture and MSB projects

## Slide 88: Orchestration Approach Comparison ONAP vs ETSI MANO (Gil) Work in Progress (R3+ Capabilities) … Note - Attached slides provide a side-by-side comparison of the ETSI MANO approach to orchestration vs the ONAP (ECOMP) approach.

## Slide 92: Vodafone Orchestration Proposal (Susana) Work in Progress (R3+ Capabilities) …

## Slide 93: ONAP Target Architecture focus for orchestration/NF controller discussion
DESIGN-TIME
Policy Creation & Validation
Analytic Application Design
VNF / PNF Onboarding
Resource Onboarding
Service Design
Catalog
Recipe/Eng Rules & Policy Distribution
ONAP Optimization Framework
ONAP Operations Manager
Dashboard OA&M
Common
Services
Application
Authorization
Framework
Logging
Policy Framework
Active & Available Inventory
External Registry
Data Collection, Analytics, and Events
Event Correlation
ONAP Optimization Framework
SDN Controller
(L0-L3)
Optional External Systems
Hypervisor / OS Layer
OpenStack
Azure
VMware
RackSpace
3rd Party Controller
AMZ
Public
Cloud
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Closed Loop Design
Change Management Design
Design Test & Certification
CLI
OSS / BSS
ONAP Portal
Note 1 – Consistent APIs between Orchestration layer and Controllers
RUN-TIME
Common Services
Multi-Cloud
Adaptation
U-UI
Others
(see Note 1)
CCSDK
ONAP External APIs
Generic NF Controllers (L4-L7)
Network Function Layer
…
VNFs
PNFs
Micro Services Bus / Data Movement (see Note 1)
Life Cycle Management & Config
Specific VNF Manager
Element Management System
(see Note 1)
Orchestration

## Slide 94: ONAP Target Architecture for Orchestration layer and NF controller (High-Level Functional View)
ONAP External APIs
Generic NF Controllers (L4-L7)
Optional External Systems
Network Function Layer
…
VNFs
PNFs
Life Cycle Management & Config
Specific VNF Manager
Element Management System
RUN-TIME
Orchestration
(end-to-end)
Orchestration
(domain/region)
Micro Services Bus / Data Movement
VNFs
Domain/region versus end-to-end orchestration are depicted here for the sake of examples to depict interfaces. Expectation is to have a model driven orchestration functionality
VES and YANG not included in this figure for simplicity and also currently not in ETSI-NFV
Note: Both VNF and Element management may trigger actions to be executed by the generic NF controller
Note

## Slide 95: ONAP Target Architecture for Orchestration layer and NF controller (APIs detailed)
ONAP External APIs
Generic NF Controllers (L4-L7)
Optional External Systems
Network Function Layer
…
VNFs
PNFs
Life Cycle Management & Config
Specific VNF Manager
Element Management System
RUN-TIME
Orchestration
(end-to-end)
Orchestration
(domain/region)
Micro Services Bus / Data Movement
VNFs
Os-Ma nfvo (SOL 005)
Os-Ma nfvo (SOL 005)
Or-VNFM (SOL 003)
Or-VNFM (SOL 003)
ONAP additions
ONAP additions
ONAP additions
Os-Ma nfvo (SOL 005)
Ve-Vnfm-Vnf (SOL 002)
Note: The depicted interfaces consists of sets of APIs that may be exposed by different ONAP modules. This needs to be detailed further
Ve-Vnfm-Vnf (SOL 002)
Automation is key for the success of 5G
Management standards are partly incomplete and fragmented
ETSI MANO defines key interfaces (API)
ONAP creates an automation framework with the help of TMF/MEF
3GPP drives information models and network slices