## Slide 1: NFV specifications for VNFD/NSD, VNF package - ONAP Modeling workshop -
Andrei Kojukhov & Shitao Li
ETSI ISG NFV

## Slide 2: Agenda
VNFD and NSD Info Models Specifications – IFA specs
VNFD/NSD and VNF Package TOSCA YAML Data Model Specifications – SOL001 and SOL004

## Slide 3: part 1: The ETSI NFV Information model in context of IFA and SOL specifications

## Slide 4: High Level Overview
NFV-IFA015 Information Model (UML)
NFV-IFA011 VNF Descriptor & VNF Package
NFV-SOL004 VNF Package (TOSCA CSAR)
NFV-IFA014 Network Service Descriptor
NFV-IFA007 Or-Vnfm
NFV-IFA008 Ve-Vnfm
NFV-SOL001 VNF & NS Descriptor (TOSCA)
NFV-SOL003 Or-Vnfm (REST)
NFV-SOL002 Ve-Vnfm (REST)
NFV-IFA013 Os-Ma-Nfvo
NFV-SOL005 Os-Ma-Nfvo (REST)
NFV-IFA024 External IM Touchpoints
“Paper” Requirement Specification (Stage 2)
Protocol & Datamodel Specification (Stage 3)
Information Model
NFV-IFA016 Papyrus Guidelines
NFV-IFA017 UML Modeling Guidelines
Draft
Draft
UML
doc
UML
doc
doc
doc
doc
doc
doc
doc
doc
doc
doc
doc
doc
doc
Link to latest published document
© ETSI 2017. All rights reserved

## Slide 5: ETSI NFV IM and DM standards
ETSI NFV-SOL 001 specifies a TOSCA-based representation for a VNFD and NSD
ETSI NFV-SOL 004 specifies a TOSCA CSAR-based format applicable to a VNF package
ETSI NFV-SOL 006 specifies a YANG-based representation for a VNFD and NSD (just starting)
ETSI NFV-IFA 011 specifies the functional requirements applicable to a VNFD and VNF Package
ETSI NFV-IFA 014 specifies the functional requirements applicable to a NSD

## Slide 6: part 2: VNF Package Data Model

## Slide 7: VNF Package Info Model
The VNF Package contains:
  the VNF descriptor (VNFD) that defines metadata for package onboarding and VNF management,
  the software images needed to run the VNF, and
  Manifest file that provides package integrity and authenticity
  (optional) additional files to manage the VNF (e.g. scripts, vendor-specific files etc.).
The VNF Package is delivered by the VNF provider as a whole and is immutable (protected from modification).
The VNF Package or its Manifest file is digitally signed
The VNF Package is stored in a repository by the NFVO.
The VNF Package can be accessed by VNFM.
VNF Package
Software image(s)
VNFD
Additional files
Reference:
ETSI GS NFV-IFA 011
ETSI GS NFV-SOL 004
Manifest
file
© ETSI 2017. All rights reserved

## Slide 8: VNF Package Data Model (Option 1): TOSCA YAML CSAR with Metadata File
The TOSCA.meta file includes block_0 with the Entry-Definitions keyword pointing to a TOSCA definitions YAML file used as entry for parsing the contents of the overall CSAR archive – MRF.yaml
TOSCA-Meta-File-Version: 1.0
CSAR-Version: 1.1
Created-by: Company Name
Entry-Definitions: Definitions/ MRF.yaml
  Any TOSCA definitions files besides the one denoted by the Entry-Definitions can be found by processing respective imports statements in the entry definitions file (or in recursively imported files)
  Any artifact files (e.g. scripts, binaries, configuration files) can be either declared explicitly through blocks in the TOSCA.meta file or pointed to by relative path names through artifact definitions in one of the TOSCA definitions files contained in the CSAR file.
References:
ETSI GS NFV-SOL 004
TOSCA-Simple-Profile-YAML-v1.1
!------TOSCA-Metadata
!------TOSCA.meta
!------Definitions
!----- MRF.yaml
!----- OtherTemplates (e.g., type definitions)
!------Files
!----- ChangeLog.txt
!----- MRF.cert
!----- image(s)
!----- other artifacts
!------Tests
!----- file(s)
!------Licenses
!----- file(s)
!------Scripts
!----- install.sh
!----- MRF.mf
© ETSI 2017. All rights reserved

## Slide 9: VNF Package Data Model Standard Artifacts and Directories
Change History File
  Humanly readable text file
  All the changes in the VNF package shall be versioned, tracked and inventoried
Testing Files
  Goal is to enable VNF package validation
  VNF Provider includes files containing necessary information (e.g. test description)
Licensing Information for released VNF
  Include a single license term for the whole VNF.
  In addition may include license terms for each of the VNF package artifacts if different from the one of the released VNF
A directory for artifacts serving 3-rd party extensions (work in progress)
  Allow adding artifacts supporting external (non-MANO) extensions e.g. ONAP extensions
© ETSI 2017. All rights reserved

## Slide 10: Adding Security to VNF Package Public Key Based Integrity and Authenticity
Option 1: Manifest file - based if there are both local and external artifacts
  A Digest hash per each artifact
  Manifest file is signed with VNF provider private key
  VNF provider’s certificate includes a VNF provider public key
  The certificate may be a separate artifact or included in the signature container, e.g. CMS
Option 2: CSAR-based if all artifacts are located inside a CSAR
  CSAR file is digitally signed with the VNF provider private key
  VNF provider delivers one zip file containing a CSAR file, a signature file and a certificate file that includes a VNF provider public key
  The certificate may be a separate artifact or included in the signature container, e.g. CMS
VNFPackage.csar Signature
VNFPackage.csar
Signing Certificate
VNFPackage.csar Signature
VNFPackage.csar
Signing Certificate
VNF Package.zip
or
Manifest file Signature
VNF Package metadata
Signing Certificate
Manifest file
Artifact 1
Path/URI
Hash
Artifact N
Path/URI
Hash
. . . . .
Signing Certificate
Both options rely on existence in the NFVO of a root certificate of a trusted certificate authority, delivered via a trusted channel separately from a VNF package
© ETSI 2017. All rights reserved

## Slide 11: VNF Package Data Model Manifest File with Security support
VNF package metadata
A list of blocks each is related to one file in the VNF package, including
Source: artifact URI
Optional Algorithm: name of an algorithm used to generate the hash
Optional Hash: text string corresponding to the hexadecimal representation of the hash
Optional Manifest file Signature
References:
IANA register for Hash Function Textual Names https://www.iana.org/assignments/hash-function-text-names/hash-function-text-names.xhtml
metadata:
vnf_product_name: vMRF-1-0-0
vnf_provider_id: Acme
vnf_package_version: 1.0
vnf_release_data_time: 2017.01.01T10:00+03:00
Source: MRF.yaml
Algorithm: SHA-256
Hash: 09e5a788acb180162c51679ae4c998039fa6644505db2415e35107d1ee213943
Source: scripts/install.sh
Algorithm: SHA-256
Hash: d0e7828293355a07c2dccaaa765c80b507e60e6167067c950dc2e6b0da0dbd8b
Source: https://www.vendor_org.com/MRF/v4.1/scripts/scale/scale.sh
Algorithm: SHA-256
Hash: 36f945953929812aca2701b114b068c71bd8c95ceb3609711428c26325649165
-----BEGIN CMS-----
MIGDBgsqhkiG9w0BCRABCaB0MHICAQAwDQYLKoZIhvcNAQkQAwgwXgYJKoZIhvcN
AQcBoFEET3icc87PK0nNK9ENqSxItVIoSa0o0S/ISczMs1ZIzkgsKk4tsQ0N1nUM
dvb05OXi5XLPLEtViMwvLVLwSE0sKlFIVHAqSk3MBkkBAJv0Fx0=
-----END CMS-----
© ETSI 2017. All rights reserved

## Slide 12: part 3: The VNFD / NSD SPECIFICATION

## Slide 13: VNFD Info Model
The VNFD defines VNF properties and requirements, such as:
  Resources needed (amount and type of Virtual Compute, Storage, Networking),
  Connectivity:
      External Connection Points (described via CP Descriptors, CPD).
      Internal Virtual Links (described via VL Descriptors, VLD)
      Internal Connection Points (described via CP Descriptors, CPD)
  LCM behavior (e.g. scaling, instantiation), operations, and configuration
  References to SW images, LCM scripts and other files located or referred in VNF package
  Affinity / anti-affinity and other policy rules
  Deployment flavours (size-bounded deployment configurations, e.g. related to capacity).
The VNFD is the main input to VNF instances lifecycle management
VNFD
Deployment Flavour
Internal VLD
External CPD
VDU
Compute
Storage
Internal CPD
SW image Descr
References:
ETSI GS NFV-IFA 011
ETSI GS NFV-SOL 001
© ETSI 2017. All rights reserved

## Slide 14: Mapping VNFD Info Model elements to TOSCA constructs (In progress)
A VNFD represents as one or multiple TOSCA service templates, including:
  Node templates: VDU, VL, CP
  Policies: anti/Affinity
  Interface: LCM operation
  Capabilities: VirtualBindable, Metric, VirtualLinkable, VirtualCompute
ETSI NFV Element [IFA011] | TOSCA VNFD [TOSCA-Simple-Profile-NFV-v1.0] | Derived from
VNF | tosca.nodes.nfv.VNF | tosca.nodes.Root
VDU | tosca.nodes.nfv.VDU | tosca.nodes.Root
Cpd (Connection Point) | tosca.nodes.nfv.Cpd | tosca.nodes.Root
VduCpd (internal connection point) | tosca.nodes.nfv.VduCpd | tosca.nodes.nfv.Cpd
VnfVirtualLinkDesc (Virtual Link) | tosca.nodes.nfv.VnfVirtualLinkDesc | tosca.nodes.Root
VnfExtCpd (External Connection Point) | tosca.nodes.nfv.VnfExtCpd | tosca.nodes.Root
Virtual Storage |  | 
Virtual Compute | tosca.capabilities.nfv.VirtualCompute | tosca.capabilities.Root
Software Image | tosca.artifacts.nfv.SwImage | tosca.artifacts.Deployment.Image
Deployment Flavour | tosca.capabilities.nfv.DeploymentFlavour | tosca.capabilities.Root
Scaling Aspect | tosca.datatypes.nfv.ScalingAspect | tosca.datatypes.Root
Element Group | tosca.groups.nfv.ElementGroup | tosca.groups.Root
Instantiation Level | tosca.datatypes.nfv.InstantiationLevel | tosca.datatypes.Root

## Slide 15: VNFD TOSCA Service Template - Example

## Slide 16
More information:
NFV Technology Page (information) http://www.etsi.org/nfv
NFV Portal (working area) http://portal.etsi.org/nfv
NFV Proofs of Concept (information) http://www.etsi.org/nfv-poc
NFV Plugtest (information & registration) http://www.etsi.org/nfvplugtest
Open Area:
  Drafts http://docbox.etsi.org/ISG/NFV/Open/Drafts/
  Issue tracker http://nfvwiki.etsi.org/index.php?title=NFV_Issue_Tracker