## Slide 1: Simplified CRAN/HeNB/eNB/gNB management PoC
02/21/2018

## Slide 2: [a] GET Device Information
The following attributes provide details of the device:
Device.DeviceInfo. | object | -
Manufacturer | string­(64) | -
ManufacturerOUI | string­(6:6) | -
ModelName | string­(64) | -
Description | string­(256) | -
ProductClass | string­(64) | -
SerialNumber | string­(64) | -
HardwareVersion | string­(64) | -
SoftwareVersion | string­(64) | -
AdditionalHardwareVersion | string­(64) | -
AdditionalSoftwareVersion | string­(64) | -
UpTime | unsignedInt | -
FirstUseDate | dateTime | -

## Slide 3: [b] Configure the device for service (with PCI Range)
The following attributes are required at minimum for service :
FAPService.{i}.CellConfig.LTE.RAN.RF. | object | -
DLBandwidth | string | W
ULBandwidth | string | W
PhyCellID (configure a RANGE) | string­(64) | W
EARFCNDL | string­(128) | W
EARFCNUL | string­(128) | W
FAPService.{i}.CellConfig.LTE.RAN.PHY.PRACH. | object | -
RootSequenceIndex | unsignedInt­[0:837] | W
FAPService.{i}.CellConfig.LTE.RAN.Common. | object | -
CellIdentity | unsignedInt­[0:268435455] | W
FAPService.{i}.CellConfig.LTE.EPC.PLMNList.{i}. | object | W
PLMNID | string­(6) | W
IsPrimary | boolean | W
FAPService.{i}.FAPControl.LTE.Gateway. | object | -
S1SigLinkServerList | string­(256) | W
Device.Time. | object | -
LocalTimeZone | string­(256) | W
FAPService.{i}.CellConfig.LTE.EPC. | object | -
TAC | unsignedInt­[0:65535] | W
FAPService.{i}.FAPControl.LTE. | object | -
OpState | boolean | -
AdminState | boolean | W

## Slide 4: [c] Perform REM (Automatic PCI selection (SON))
FAPService.{i}.REM.LTE. | object | -
EUTRACarrierARFCNDLList | string­(64) | W
ScanTimeout | unsignedInt | W
ScanStatus | string | -
LastScanTime | dateTime | -
The following attributes are required for REM :
REMBandList | string | W
ScanOnBoot | boolean | W

## Slide 5: [d] View REM Result
FAPService.{i}.REM.LTE.Cell.{i}.RF. | object | -
EUTRACarrierARFCN | unsignedInt­[0:65535] | -
PhyCellID | unsignedInt­[0:503] | -
RSRP | int­[-140:-44] | -
RSRQ | int­[-240:0] | -
RSSI | int­[-110:-19] | -
FAPService.{i}.REM.LTE.Cell.{i}.BCCH. | object | -
DLBandwidth | unsignedInt­[6, 15, 25, 50, 75, 100] | -
ULBandwidth | unsignedInt­[6, 15, 25, 50, 75, 100] | -
RSTxPower | int­[-60:50] | -
TAC | unsignedInt­[:65535] | -
CellID | unsignedInt­[:268435455] | -
CellBarred | boolean | -
CSGIndication | boolean | -
CSGIdentity | unsignedInt­[0:134217727] | -
FAPService.{i}.REM.LTE.Cell.{i}.BCCH.PLMNList.{i}. | object | -
PLMNID | string­(6) | -
The following attributes are required to view REM Results:

## Slide 6: [e] ONAP – Device communication
Device supports TR069 protocol for management
Netconf-TR069 translator at ONAP
Basic BBF TR181 + TR196 data model implemented in YANG
View device information in ONAP
Configure device with minimum attributes required for service and PCI selection (SON)
View REM Result

## Slide 7: [f] Connect to the device
The following attributes are required to contact the device:
ConnectionRequestURL | string­(256) | -
ConnectionRequestUsername | string­(256) | W
ConnectionRequestPassword | string­(256) | W
Device.ManagementServer. | object | -