## Slide 1: ONAP Beijing Architecture (v2.0.0) For TSC Approval
Chris Donley

## Slide 2: ONAP Amsterdam Architecture (for reference)
Policy Creation & Validation
VNF SDK
Portal Framework, U-UI, ONAP CLI
Resource Onboarding
Service & Product Design
Recipe/Eng Rules & Policy Distribution
ONAP Operations Manager (OOM)
Dashboard OA&M (VID)
A&AI/ESR
External API Framework
Micro Services Bus (MSB)
DMaaP
AAF
DCAE
Correlation Engine
(Holmes)
Logging
Policy Framework
SDN-C
(L0-L3 Controller)
Multi-VIM/Cloud
Infrastructure Adaptation Layer
CCSDK
External Systems
Network Function Layer
Hypervisor / OS Layer
OpenStack
Commercial VIM
Public Cloud
…
3rd Party Controller
sVNFM
EMS
VNFs
PNFs
…
Service Orchestration
Private
Edge Cloud
Private
DC Cloud
IP
MPLS
Managed Environment
Application Controller
(L4-L7)
Virtual Function Controller
(ETSI-aligned)
CLAMP
Catalog
DESIGN-TIME (SDC)
RUN-TIME
Public
Cloud
Common Services
Notes: Key points:
Unified framework for design-time & run-time
  Common platform for service design and netops to drive collaboration
Simultaneous orchestration of physical and virtual networks
  Vendor-agnostic orchestration can only happen in open source context
Real-time analytics and closed-loop automation
  Easy re-use of service concepts
  Iterative service improvements based on network feedback

## Slide 3: ONAP Beijing Architecture (High-Level View with Projects)
Integration
VNF Requirements
Modeling (Utilities)
VNF Validation Program

## Slide 4: Changes in Beijing Architecture
Since the Beijing release is focusing on Platform Maturity, the ARC has minimized changes to the functional architecture
  New projects approved by the TSC
  Formatting updates to provide clarity
As a foundation for the long-term target architecture, ONAP will strive for model-driven, microservices-based, modular architecture, and enable integration with other systems via MSB/proxy
  Enable secure communication between internal and external components
  Improve APIs for better consistency between components
  Align with models from Modeling subcommittee and external SDOs (as appropriate)
  Use OOM for instantiation and register with Microservices Bus

## Slide 5: ONAP Beijing Architecture Recommendations

## Slide 6: Recommendations for Beijing Release
Achievable Recommendations for Beijing to begin aligning with target architecture
  Key Architecture Principles: Modular, Microservices, Model-driven
  Modular:
    Improve APIs between components. Document them using Swagger.
    Align interfaces with industry standards, where available/appropriate (for example, ETSI SOL-003, SOL-005, MEF Interlude, Legato, etc.)
  Microservices-based
    Use OOM for onboarding, instantiation (support MSB natively), scalability
    Register with MSB
    Use microservices best practices (e.g., separate data from the component, use common KV stores/databases, for KV stores – prefer Consul, etc.)
  Model-driven
    Align with info/data models from the Modeling Subcommittee (to be published Feb 2018)
    Explore ways to use model-driven principles inside each component as well as across various components (SDC, SO, VFC, APPC, ..)
Release Theme is Platform Maturity/S3P
  S3P (see Jason Hunt 1/4 TSC presentation for list of projects providing support for S3P)
    Adhere to cloud-native principles (see https://martinfowler.com/, https://12factor.net/)
    Use common libraries/SDKs/common services where possible to improve overall system resiliency/reliability
    More focus on common services (where possible) also to help reduce testing
    MUSIC for managing various ONAP components states, DB replication in a consistent manner
    Enhanced AAF to support credential management for certificates
    Support Image Management service to enhance security, virus checking, etc.

## Slide 7: Functional Description of Beijing Project Components Note – The detailed description of features/capabilities/interfaces for each component planned for the Beijing release will be provided by respective projects.

## Slide 8: Orchestration (1/2)
Orchestration
Definition:
Provides functionality for the execution of specified process and automated sequencing of activities, task, rules and policies needed for creation, modification, removal of network application, infrastructure services or resources.
Supports different specializations with specific orchestration scopes.
Specialization scopes include, but are not limited to, network service LCM (i.e., NFVO specialization), network slice specialization, domain specific specialization (beyond Beijing).
Provided Interfaces:
Service Management Interface
  Provides the interface to manage the services that orchestration provides.
Network Service LCM interface
  Provides the specific network service LCM interface.
Actuation Request Interface
  Provides support of actuation requests towards the services.
Service Management Interface
Network Service LCM Interface
Actuation Request Interface
Service Definition Reception interface
Service Management Interface
VNF LCM Interface
NF Config Interface
Optimization request Interface
Inventory Service Interface
Transport Service Interface
Network Service LCM interface

## Slide 9: Orchestration (2/2)
Orchestration
Consumed interface Interfaces:
Service Management Interface, from: Orchestration
VNF LCM Interface, from: Generic NF controller
Optimization Request Interface, from: Optimization Framework
NF Config Interface, from: Generic NF controller
Inventory Service Interface, from: Available and Active Inventory
Transport Service Interface, from: SDN Controller.
Network Service LCM interface, from: Orchestrator
Service Distribution interface, from: Service Design and Creation
Consumed Models:
Network Service Descriptor
Service Management Interface
Network Service LCM Interface
Actuation Request Interface
Service Definition Reception Interface
Service Management Interface
VNF LCM Interface
NF Config Interface
Optimization request Interface
Inventory Service Interface
Transport Service Interface
Network Service LCM interface

## Slide 10: Data Collection, Analytics, and Events
Data Collection, Analytics, and Events
Definition:
DCAE is the ONAP subsystem that supports closed loop control and higher-level correlation for business and operations activities. DCAE collects performance, usage, and configuration data; provides computation of analytics; aids in trouble-shooting and management; and publishes event, data, and analytics to the rest of the ONAP system for FCAPS functionality.
Provided Interfaces:
Interface 1: Data collection interface (used by VNFs and others from which data is collected)
  Interface for various FCAPS data entering DCAE/ONAP.
Interface 2: Deployment interface (used by CLAMP)
  Interface for triggering the deployment and changes of a control loop
Consumed interface Interfaces:
Interface 1: Data movement platform interface (provided by DMaaP)
  Interface for data transportation between DCAE subcomponents and between DCAE and other ONAP components
  This interface can also be used for publishing events to other ONAP components.
Interface 2: Data enrichment interface (provided by A&AI)
  Interface used by DCAE for enriching collected raw data by adding information not contained in original data, e.g. identifying the VNF type from VNF identity by querying this interface.
Interface 2: Service model change interface (Provided by SDC)
  Interface for fetching control loop models and updates.
Interface 4: Policy interface (Provided by Policy)
  Interface for fetching configuration and operation policies on control loop and control loop components into DCAE for application.
Consumed Models: TOSCA models descripting control loop construction (e.g. collection and analytics apparatus)
Interface 1
Interface N

## Slide 11: Active & Available Inventory, External Registry
Active & Available Inventory, External Registry
Definition:
AAI maintains a live view of services and resources in the network, providing the state and relationships of the service components
Maintains the view of the managed systems services and resources, as well as information of the external systems that ONAP will connect to.
It provides real-time views of a managed systems resources, services and relationships with each other.
AAI provides a GUI to provide users the ability to find and inspect inventory data. This includes a free-text search, inspection of specific entities and their relationships, and aggregated views of data.
Provided Interfaces:
Inventory Service Interfaces:
  AAI Resources REST API - Provides the ability to store, read, update inventory information
  Gizmo: a low-level REST CRUD API that provides targeted and simple access to entities, relationships, and their properties. Gizmo also provides lightweight collections, and transactional bulk write support
Complex Query Interface: AAI Traversal REST API – Provides the ability to perform complex traversals of the AAI Graph
External Register interface
  Provides the ability to provision and read external system information
Consumed interface Interfaces:
DMaaP
SDC
Multivim
Consumed Models: TOSCA Service and Resource Models
Inventory Service Interface
External Register Interface
Interface N

## Slide 12: AAF Functional Description
The purpose of AAF (Application Authorization Framework) is to organize software authorizations so that applications, tools and services can match the access needed to perform job functions. This is a critical function for Cloud environments, as Services need to be able to be installed and running in a very short time, and should not be encumbered with local configurations of Users, Permissions and Passwords.
To be effective during a computer transaction, Security must not only be secure, but very fast. Given that each transaction must be checked and validated for Authorization and Authentication, it is critical that all elements on this path perform optimally.
AAF contains some elements of Role Based Authorization, but includes Attribute Based Authorization elements as well.
Essential Functional Components:
The core component to deliver this Enterprise Access is a RESTful service, with runtime instances backed by a resilient Datastore (Cassandra as of release 1.3)
The Data is managed by RESTful API, with Admin functions supplemented by Character Based User interface and certain GUI elements.
The Service accessible by provided Caching Clients and by specialized plugins
CADI (A Framework for providing Enterprise Class Authentication and Authorization with minimal configuration to Containers and Standalone Services)
Cassandra (GRID Core)

## Slide 13: AAF Functional Description
CADI stands for Code, Access, Data and Identity, This Framework addresses the Runtime Elements of Access and Identity.
Many other tools address elements of this vision. For instance, Sonar and Fortify evaluate code for maintainability and security problems, while Voltage provides encryption for Data at Rest.
However, CADI Framework contributes to these for runtime applications by:
Code - CADI provides reusable Security Client code, and ties in with appropriate Security Interfaces (i.e. J2EE Standard Filters)
Access - CADI provides links to Authorization tool(s) (AAF) for Fine-grained Authorization. Also, data from Identity servers is also made available to Coders easily. For instance, CADI provides a clean API to read the Course Grained Authorization information available within the CSP Cookie.
Data - CADI provides simple setup for certificates needed for TLS connectivity, so that barriers to using HTTPS are greatly reduced. It also ensures that no one using CADI uses clear-text passwords in Configuration files.
Identity - CADI Framework obtains the Identity of any callers by delegating to CSO approved Identity servers on behalf of the client, so that Applications can be assured of who is talking to them.

## Slide 14: AAF Functional Description
Entities within AAF
Namespaces
A Namespace, in AAF, is the ensemble of Roles, Permissions and Identities controllable within the domain assigned to a member of the Organization's chain-of-command.
Namespaces are known by domain, in dot-delimited form. ex: com.att.aaf or com.att.wfa, and they are hierarchically managed.
People in Namespaces
Owner (Responsible)
A key feature of how AAF works for an Enterprise is by supporting federated responsibility. This responsibility is clearly delineated by the owner entry. Organizations (i.e. companies) may establish their own policies
Roles
I) "Roles" is a bit of an overloaded term in Security software. It has unfortunately been typically used as a flat, unscoped Group, known only to the Application.
Typical examples such as "user" and "admin" have no meaning outside the immediate context of the application. "admin"??? "admin" of what? What are the behaviors allowed for "admin"? Is the "admin" of Application A, the same as Application B? (answer, no!)
Permissions
Permissions are the other side of the decoupled Authorization equation. Permissions represent some resource that needs to be protected by the Application in question. examples:
A GUI Admin page should be available to only those who job function is to administer this app.
SPI Data that this App accesses should only be accessible to those who are allowed to see SPI data.
Full data reporting dumps should only be accessible to Audit teams.

## Slide 15: AAF Object Model

## Slide 16: DMaaP Functional Description
Data movement as a platform(DMaaP) is a premier platform for high performing and cost effective data movement services that transports and processes data from any source to any target with the format, quality, security, and concurrency required to serve the business and customer needs.
DMaaP consists of three major functional areas:
  Data Filtering - the data preprocessing at the edge via data analytics and compression to reduce the data size needed to be processed.
  Data Transport - the transport of data intra & inter data centers. The transport will support both file based and event based data movement. The Data Transport process needs to provide the ability to move data from any system to any system with minimal latency, guaranteed delivery and highly available solution that supports a self-subscription model that lowers initial cost and improves time to market.
  Data Processing - the low latency and high throughput data transformation, aggregation, and analysis. The processing will be elastically scalable and fault-tolerant across data centers. The Data processing needs to provide the ability to process both batch and near real-time data.
This service is build using Apache Kafka and Restful API is created for message publishing, subscribing and admin activities

## Slide 17: APPC (1/2)
APPC
Definition:
Application Controller (APPC) performs the functions to manage the lifecycle of VNFs and their components.
It provides a comprehensive set of controller actions such as Configure, Modify Configuration, Start, Stop, Migrate, Restart, Rebuild, and so on. Consult readthedocs documentation for the full set of APIs offered/supported.
It supports a set of standard VNF interfaces (Netconf, Chef, Ansible.), and
Is designed to be self-service using a model driven architecture that provides a layer of abstraction making APPC completely service, VNF, and site agnostic.
Information about the APPC architecture and provided APIs can be found in the APPC User Guide and LCM & OAM API Guides on readthedocs
.
Provided Interfaces: (refer to APPC User Guide for details)

## Slide 18: APPC (2/2)
APPC
Consumed Interfaces
Consumed Models:
TOSCA Dependency Model
APP-C also support a variety of models, most of which are created by the APPC Configuration Design Tool (CDT). Examples are:
  Reference Data Model (json)
  VNF Capabilities Model (json)
  Template Model (json or xml)
  Parameter Definition Model (yaml)

## Slide 19: CLAMP (1/2)
CLAMP
Definition:
CLAMP is a platform for designing and managing control loops.
It is used to design a control loop, configure it with specific parameters for a particular network service,
then It interacts with other systems to deploy/undeploy and execute the control loop.
Information about the CLAMP architecture and provided APIs can be found in the CLAMP User Guide and LCM & OAM API Guides on readthedocs
Provided Interfaces: (CLAMP doesn’t expose functional relates API’s except the one below, refer to CLAMP documentation for more details)
Interfaces Service Purpose/Comments
HealthCheck REST Health Check of CLAMP instance

## Slide 20: CLAMP (2/2)
CLAMP
Consumed Models: (No specific models were used in the above interface except for Policy(json))
Consumed Interfaces:
Interfaces Service Purpose/Comments
SDC REST Distribution of service to DCAE
DCAE REST Common Controller Framework
Policy REST(JSON data) Create Configuration and Operational policy

## Slide 21: Use-case UI
Usecase UI
Definition:
Provides portal for service life cycle management
Provides portal for VNF alarm and performance
Provides portal for VM alarm and performance
Provided Interfaces:
None
Note: Can be more than one page
None
Catalog Synchronization Interface
Service Orchestrator Interface
Inventory Service Interface
NS/VNF Onboard Interface
Service Registration Interface
Data Subscription Interface

## Slide 22: Use-case UI
Usecase UI
Consumed Interfaces:
Catalog Synchronization Interface, from: SDC
Service Orchestrator Interface, from: SO
Inventory Service Interface, from: Available and Active Inventory
NS/VNF Onboard Interface, from: VF-C
Service Registration Interface, from: MSB
Data Subscription Interface, from: DMaaP
Note: Can be more than one page
None
Catalog Synchronization Interface
Service Orchestrator Interface
Inventory Service Interface
NS/VNF Onboard Interface
Service Registration Interface
Data Subscription Interface
Consumed Models:
Network Service Descriptor
VNF Descriptor

## Slide 23: ONAP CLI
ONAP CLI
Definition:
Provides Open CLI Platform (OCLIP) – Industry first Model-driven command line interface platform
Provides commands for performing end-end service on-boarding and life cycle management
Provides command console for Linux and web platforms.
Provided Interfaces:
micro-service discovery
  Provides commands for micro service discovery and registration
external system and VNF cloud on-boarding
  Provides commands for registering/unregistering VIM, VNFM, EMS and SDNC
customer and subscription management
  Provides commands for subscription and service-type life cycle management
resource on-boarding
  Provides commands for adding VNF modules
Product and service management
  Provides commands for design time creation and management of VF and NS
network service life-cycle management
  Provides commands for creating and managing Network services (NS)
Consumed interface Interfaces:
REST API from SDC, SO, AAI, MSB.
micro-service discovery Interface (MSB)
external system and VNF cloud on-boarding interface (AAI)
customer and subscription management interface (AAI)
resource on-boarding interface (SDC)
Product and service management interface (SDC)
network service life-cycle management interface (SO)
micro-service discovery commands
external system and VNF cloud on-boarding commands
customer and subscription management commands
resource on-boarding commands
Product and service management commands
network service life-cycle management commands
Consumed Models:
- Open Command Specification (OCS) 1.0

## Slide 24: Microservices Bus (1/2)
Micro Services Bus / Data Movement
Definition:
Provides a reliable, resilient and scalable communication and governance infrastructure to support ONAP Microservice Architecture(OMSA).
Provides RESTFul API for service registration/discovery
Provides JAVA SDK for service registration and access
Provides a transparent service registration proxy with OOM-Kube2MSB
Provides a transparent service communication proxy which handles service discovery, load balancing, routing, failure handling, and visibility-Internal API Gateway(Implemented) and Mesh Sidecar(WIP)
Provides an External API Gateway to expose ONAP services to the outside world
Service Registration REST Interface
Service Discovery RES Interface
JAVA SDK for Service Registration/Access
Interface N

## Slide 25: Microservices Bus (2/2)
Micro Services Bus / Data Movement
Consumed interface Interfaces: (None)
Consumed Models:
Swagger for RESTFul APIs definition
Service definition in kubernetes config files for Kube2MSB service registration
Service Registration REST Interface
Service Discovery RES Interface
JAVA SDK for Service Registration/Access
Interface N
Provided Interfaces:
Service Registration REST Interface
  Provides the RESTFul interface to register ONAP services.
Service Discovery REST Interface
  Provides the RESTFul interface to discover ONAP services.
JAVA SDK
  Provides JAVA SDK to register ONAP services.
  Provides JAVA SDK to access ONAP services.
  Note: ONAP components don' t need interfaces to leverage the transparent service registration proxy and communication proxy.

## Slide 26: Microservices Bus Updated With Swagger SDK(1/2)
Micro Services Bus / Data Movement
Definition:
Provides a reliable, resilient and scalable communication and governance infrastructure to support ONAP Microservice Architecture(OMSA).
Provides RESTFul API for service registration/discovery
Provides JAVA SDK for service registration and access
Provides a transparent service registration proxy with OOM-Kube2MSB
Provides a transparent service communication proxy which handles service discovery, load balancing, routing, failure handling, and visibility-Internal API Gateway(Implemented) and Mesh Sidecar(WIP)
Provides an External API Gateway to expose ONAP services to the outside world
Swagger SDK for auto-generate the client SDK in different languages for every micro-services in ONAP. Also it deploys the generated SDK into the nexus.
Service Registration REST Interface
Service Discovery RES Interface
JAVA SDK for Service Registration/Access
Swagger SDK
Interface N

## Slide 27: Microservices Bus Updated With Swagger SDK(2/2)
Micro Services Bus / Data Movement
Consumed interface Interfaces: (None)
Consumed Models:
Swagger for RESTFul APIs definition
Service definition in kubernetes config files for Kube2MSB service registration
Service Registration REST Interface
Service Discovery RES Interface
JAVA SDK for Service Registration/Access
Swagger SDK
Interface N
Provided Interfaces:
Service Registration REST Interface
  Provides the RESTFul interface to register ONAP services.
Service Discovery REST Interface
  Provides the RESTFul interface to discover ONAP services.
JAVA SDK
  Provides JAVA SDK to register ONAP services.
  Provides JAVA SDK to access ONAP services.
  Note: ONAP components don' t need interfaces to leverage the transparent service registration proxy and communication proxy.
Swagger SDK
  provides Mvn plug-in settings for (JAVA)client sdk generation

## Slide 28: Optimization Framework - R2 (1/4)
Optimization Framework (OOF)
Definition:
ONAP Optimization Framework (OOF) provides functionality for creating and running optimization applications by leveraging a policy-driven, declarative approach.
Supports different specializations (applications) with specific domain and optimization needs.
Initial specialization scopes include, but are not limited to, VNF placement support via Homing and Allocation Service (HAS) with different use cases, and change management scheduling service.
  For R2, the OOF will support vCPE use case (as a MVP).
  For R2, the OOF will demonstrate an example of Change Management Scheduling Optimization using the OOF design framework with simple, representative constraints.
Service Orchestrator (SO)
Change Management Portal
Policy Interface
Inventory Service Interface
Service/Policy Models Interface
Infrastructure Metrics Interface
Provided Interfaces:
Placement Optimization Interface
  Provides functionality for the Service Orchestrator to specify placement services [vCPE use case]
Change Management Portal Interface
  Provides functionality for calculating schedules that satisfy time constraints and conflicts [R2 focus on a demonstration of the design framework; alignment with Change Management scheduling use case]
Consumed Models:
Policy Models (constraints) and License Models from: SDC
Infrastructure Metrics Models, from: Multi Cloud
Consumed Interfaces:
Policy Interface, from: Policy
Inventory Service Interface, from: Available and Active Inventory
Service/Policy Models Interface, from: SDC
Infrastructure Metrics Interface, from: Multi Cloud

## Slide 29: Optimization Framework - R3+ (2/4)
Optimization Framework (OOF)
Additional Provided Interfaces for R3 and beyond:
Placement Optimization Interface
  For R2, the focus is on supporting vCPE use case;
  for R3 and beyond, the OOF will also support VoLTE, VNF/Service scale-in/out (higher order control loop), and RAN-5G.
Change Management Portal Interface
  For R2, the focus is on a demonstration of OOF with simple, representative constraints; this effort will be aligned with the Change Management scheduling use case (for R3 and beyond)
Service Orchestrator (SO)
Change Management Portal
Policy Interface
Inventory Service Interface
Service/Policy Models Interface
Infrastructure Metrics Interface
R3 and Beyond
Application Metrics Interface
Additional Consumed Interfaces for R3 and Beyond:
Application Metrics Interface, from: DCAE [R3 and Beyond]
These are in addition to Policy, Inventory, SDC Models, and Infrastructure metrics from R2
Additional Consumed Models for R3 and beyond:
Application Metrics Models, from: DCAE
Additional Definitions for R3 and beyond:
For R3 and beyond, the OOF will focus on supporting multiple R3 and beyond use case (along with R2 use cases) [supporting VoLTE, VNF/Service scale-in/out (higher order control loop), and RAN-5G].
Synchronization with Change Management Scheduling use case.
Providing additional sample/example optimization applications as documentation.
Proving initial Knowledge Base on OOF (building blocks and recipes for creating complex applications).
Further alignment with S3P objectives.
Note on Functionality for R3 and beyond:
While the items listed below are not part of MVP for R2, the OOF team is initiating discussions and collaborations on these during the R2 time frame, so that the OOF is aligned with the use cases that will mature in R3 and beyond.

## Slide 30: Optimization Framework - Interface Definitions (3/4)
Optimization Request Interface | 
Provided Service | Homing Service API (HAS-API)
Supplementary Information | The OOF will provide a list of possible candidates for placement, which the service orchestrator can use to instantiate the service
Interface Provider(s) | Optimization Framework
Provided Capabilities | Optimization Information Request

## Slide 31: Optimization Framework - Interface Definitions (4/4)
Scheduling Optimization Request Interface | 
Provided Service | Change Management Scheduling API (CMSO API)
Supplementary Information | The OOF will provide a possible schedule of VNF actions (e.g. upgrades) that satisfy the constraints on availability periods and constraints related to conflicts
Interface Provider(s) | Optimization Framework
Provided Capabilities | Optimization Information Request

## Slide 32: VNF SDK (VNF package validation) (1/2)
VNF SDK Marketplace
Definition:
Provides functionality to upload, verify, and download VNFs
VNF Vendors upload VNFs through the Marketplace portal
Marketplace runs package validation tests
VNFs are made available for Onboarding
Marketplace API:
Upload/Re-upload VNF
  Upload VNFs to the Marketplace
Download VNF
  Download VNFs
Query VNF
  Query VNFs by CSAR ID or conditions (name, version, type, provider)
Delete VNF
  Delete VNF from the Marketplace
Consumed Models: SOL-004 (Beijing)
Marketplace API
Note: Can be more than one page
Here we put the services provided

## Slide 33: VNF SDK - Interface Definitions (2/2)
Marketplace API | 
Provided Service | Upload, Download, Query, Delete
Supplementary Information | The VNFSDK APIs are documented on the ONAP Wiki: https://wiki.onap.org/display/DW/API+Documentation
Interface Provider(s) | VNF SDK Marketplace
Provided Capabilities | VNF Pre-onboarding upload/download/validation/query/delete

## Slide 34: VF-C Components
NFVO
NFVI&VIM
VNF Package ( VNFD)
NS Package ( NSD)
NFVO Functions
Support NS Lifecycle Management including NS instantiate, scale, heal, operate (query /update/…)and terminate. In R1, most of NSLCM interfaces align with SOL005 Os-Ma-nfvo reference point
Support integration with multi VNFMs via drivers which include vendors VNFM and generic VNFM. The interfaces between NFVO and driver comply with Or-Vnfm reference point.
Support integration with multi VIM via Multi-Cloud
In R1, NFVO also supports integration with vendor EMS via driver
Instantiate
Scale
Heal
Terminate
SVNFM
Driver
Multi-Cloud
Operate
GVNFM
Vi-Vnfm
Vi-Vnfm
Vi-Vnfm
Or- Vnfm
Or- Vnfm
Or-Vi
EMS
Driver
SO
Policy
UUI
Os-Ma-nfvo

## Slide 35: VF-C – NFVO (1/2)
NFVO
Definition:
Provides reference implementation of NFVO in ETSI MANO architecture
Provides Network service life cycle management
Provides NS/VNF layer’s FCAPS management
Provided Interfaces:
Network Service LCM interface
  Provides Network Service LCM interface
  (NS create/instantiate/scale/heal/terminate/delete/query)
VNF Operation Granting interface
  Provides VNF Operation Granting interface and make granting decision
NS package management interface
  Provides runtime NS package management interface
VNF package management interface
  Provides runtime VNF package management interface
Network Service LCM Interface
VNF Operation Granting Interface
NS package management Interface
VNF package management interface
Note: Can be more than one page
VNF LCM Interface
Inventory Service Interface
Catalog Synchronization interface
Generic VIM Interface
Date report interface
Tosca parser interface
Optimization Request Interface

## Slide 36: VF-C – NFVO (2/2)
NFVO
Consumed Interfaces:
VNF LCM Interface, from: Generic NF controller, SVNFM
Inventory Service Interface, from: Available and Active Inventory
Catalog Synchronization Interface, from: SDC
Generic VIM Interface, From: Multi-cloud
Data report Interface, From: DCAE
Tosca parser Interface, From: Modeling
Service registration and discovery, From: MSB
Optimization Request Interface, from: Optimization Framework -TBD
Consumed Models:
Network Service Descriptor
VNF Descriptor
VES data format
Bpmn Workflow
Network Service LCM Interface
VNF Operation Granting Interface
NS package management interface
VNF package management interface
Note: Can be more than one page
VNF LCM Interface
Inventory Service Interface
Catalog Synchronization interface
Generic VIM Interface
Data report interface
Tosca parser interface
Optimization Request Interface

## Slide 37: VF-C - GVNFM
GVNFM
Definition:
Provides the Generic VNFM
Provides the VNF life cycle management
Supports NFVO to implement Network service LCM management
Provided Interfaces:
VNF LCM interface
  Provides the VNF LCM interface(VNF instantiate/scale/terminate/query)
VNF Package Management interface
  Provides runtime VNF Package management interface
Consumed interface Interfaces:
Catalog and notification Interface, from: NFVO
Inventory Interface, from: A&AI
Tosca parser Interface, From: Modeling
Generic VIM Interface, From: Multi-cloud
Service registration and discovery, From: MSB
VNF Config interface: from VNF -TBD
:
Consumed Models
VNFD
Note: Can be more than one page
VNF LCM Interface
VNF Package management interface
Catalog and notification Interface
Inventory Interface
Tosca parser Interface
Generic VIM Interface
VNF config interface

## Slide 38
38
ONAP Portal
ONAP Portal
Definition:
Portal is a platform that provides the ability to integrate different ONAP applications into a centralized Portal Core.
It allows decentralized applications to run within their own infrastructure while providing common management services and connectivity.
It provides capabilities including application onboarding & user management, and hosted application widgets.
Using the provided SDK, application developers can leverage the built-in capabilities (Services / API / UI controls) along with bundled tools and technologies.
Provided Interfaces:
Portal Admin Interfaces
  Onboarding and User management
SDK Module
  SDK will be used as a base for any ONAP application being built.
  Components using SDK jars: Policy, VID, AAI, and SDC
  SDK bundles together a host of different tools, technologies, and standards that will assist the teams during the development phase.
  SDK includes reusable UI components, authentication & authorization components, visualization & reporting engine, collaborative services, workflow manager, GIS / Map, web component, and widget development framework.
Consumed interface Interfaces:
Restful APIs for fetching available roles to portal’s onboarded application users. from: AAF
Portal Admin Interfaces
SDK Jars (Policy, VID, AAI, and SDC)
AAF

## Slide 39: Logging-analytics (1/2)
Logging-analytics
Definition:
Provides ELK stack where logs are streamed from filebeat sidecar containers per component
Provided Interfaces:
Kibana UI:
  dashboard for indexed logs
Logstash:
  Consumes logs pushed by filebeat containers into elasticsearch indexer
Consumed interface Interfaces:
Filebeat container per microservice exposing logs through a Kubernetes PV:
Consumed Models: none
Kibana
filebeat

## Slide 40
Logging-analytics Interface | 
Provided Service | Kibana dashboard, search service on top of elaticsearch index of ONAP logs – via filebeat
Supplementary Information | 
Interface Provider(s) | AA&I, APPC, SO, Policy, Portal, SDC, SDNC, VID
Provided Capabilities | Search logs using lucene search format Dashboard of configurable search views of logs
Logging-analytics (2/2)

## Slide 41: Multi-Cloud Adaptation (1/2)
Multi-Cloud adaptation
Definition:
enable ONAP to deploy and run on multiple infrastructure environments, including OpenStack and its different distributions, public and private clouds, and micro services containers, etc.
provide a Cloud Mediation Layer supporting multiple infrastructures and network backends so as to effectively prevents vendor lock-in.
decouple the evolution of ONAP platform from the evolution of underlying cloud infrastructure, and minimizes the impact on the deployed ONAP while upgrading the underlying cloud infrastructures independently.
Provided Interfaces:
Resource LCM interface
    Support VNF instantiation/termination
    (Resource create/delete/update/query)
VIM registry/un-registry Interface
  Support registry/un-registry of multiple clouds
  (VIM create/delete/update)
VIM FCAPS management Interface
  Support FCAPS required data collection, event/alert/metrics federation functions
  (message pub/sub)
  VIM capacity/capability query
    Support placement and scheduling purpose
    (capacity/capability query/report)
Resource LCM Interface
VIM registry/un-registry Interface
VIM FCAPS management Interface
  VIM capacity/capability query
ONAP Interface
  Inventory Service Interface
  DMAAP interface
  Logging interface
The third party Cloud interface
  OpenStack Interface
  VMware VIO interface
  Wind River Titanium Interface

## Slide 42: Multi-Cloud Adaptation (2/2)
Multi-Cloud adaptation
Consumed Interfaces:
ONAP
  Inventory Service Interface from Available and Active Inventory
  Message pub/sub interface from DMAAP
  Logging interface from Logging project
The third party Cloud API
    OpenStack Interface
      Ocata
      Mitaka
    VMware VIO interface (Ocata)
    Wind River Titanium Interface (Mitaka)
Consumed Models:
Existing
  VES data format
Underworking
  Hierarchical Infrastructure Resource Information Model
  FCAPS Data Model
ONAP Interface
  Inventory Service Interface
  DMAAP interface
  Logging interface
The third party Cloud interface
  OpenStack Interface
  VMware VIO interface
  Wind River Titanium Interface
Resource LCM Interface
VIM registry/un-registry Interface
VIM FCAPS management Interface
  VIM capacity/capability query

## Slide 43: ONAP Operations Manager (OOM)
ONAP Operations Manager
Definition: OOM is the life cycle manager of the ONAP platform (i.e. SDC, SO, SDNC, etc.). OOM uses the Kubernetes container management system and Consul to provide the following functionality:
  Deployment - with built-in component dependency management (including multiple clusters, federated deployments across sites, and anti-affinity rules)
  Configuration - unified configuration across all ONAP components
  Monitoring - real-time health monitoring feeding to a Consul GUI and Kubernetes
  Restart - failed ONAP components are restarted automatically
  Clustering and Scaling - cluster ONAP services to enable seamless scaling
  Upgrade - change-out containers or configuration with little or no service impact
  Deletion - cleanup individual containers or entire deployments
OOM supports a wide variety of cloud infrastructures to suit your individual requirements.
Provided Interfaces: Consul GUI for health monitoring, Kubernetes CLI for platform management
Consumed interface Interfaces: None
Consumed Models: ONAP Deployment Specifications, ONAP Component Configuration Artifacts
Interface 1
Interface N

## Slide 44: Policy Framework (1/2)
Policy Framework
Definition:
Provides a logically centralized environment for the creation and management of modifiable configurations, rules, assertions and/or conditions to provide real-time decision making on conditions and events that underlie ONAP’s control, orchestration, and management functions
Supports specification, decomposition, distribution and enforcement for various types of policies such as microservice configuration policy, operational policy, decision policy, guard policy, etc.
Policy scopes include, but are not limited to, infrastructure/network management, products and services, operation automation, and security.
Provided Interfaces:
Policy CRUD interface:
  Provide UI and API options to create/query/update/delete configuration, decision and operational policies
Policy deployment interface:
  - Provide UI and API options to deploy configuration, decision and operational policies
Policy model CRUD interface:
  Provide UI and API options to create, query, update and delete policy models
Policy CRUD interface
Policy deployment interface
Policy model CRUD interface
Message Router Pub/Sub Service Interface
Service Registration/Discovery Interface
VNF/VM LCM Interface
NF Config Interface
Inventory Service Interface
Network Service LCM Interface
Service Distribution Interface

## Slide 45: Policy Framework (2/2)
Policy Framework
Consumed interface Interfaces:
Message Router Pub/Sub Service Interface, from: Data Movement as a Platform
Service Registration/Discovery Interface, from: Microservices Bus
VNF/VM LCM Interface, from: Generic NF controller
NF Config Interface, from: Generic NF controller
Inventory Service Interface, from: Available and Active Inventory
Network Service LCM Interface, from: Service Orchestrator
Network Service LCM Interface, from: Virtual Controllers (APPC and VFC)
Service Distribution Interface, from: Service Design & Creation
Consumed Models
Operational policy model
Configuration policy model
Resource model in the catalog
Service model in the catalog
Message Router Pub/Sub Service Interface
Service Registration/Discovery Interface
VNF/VM LCM Interface
NF Config Interface
Inventory Service Interface
Network Service LCM Interface
Service Distribution Interface
Policy CRUD interface
Policy deployment interface
Policy model CRUD interface