## Slide 1: Orchestration for Edge-Computing (WIP) - Background work to identify gaps
For more information
Edge-Automation group in ONAP
Contact: Srinivasa.r.addepalli@intel.com on this presentation

## Slide 2: Network E2E (5G – An Edge computing enabler)
Device Edge
CPE
(White box)
RU
CU-UP/UPF
SMF
CU-CP
Value Added Services – MEC Apps (contextual)
Central Orchestration, Analytics and Closed loop control (ONAP)
Value Added Services
POP
BRAS, PE
Value Added Services
Apps
Network Edge
Edge Cloud
(tens of thousands)
Core Cloud (EPC)
AMF
UDM
AUSF
UPF
PCF
AF
Clouds (Global)
Value Added Services
IaaS
CaaS
DU
Notes: RU – Remote Radio Unit
DU – Distributed Unit (5G Base Unit)
CU-UP – Centralized User Plane
CU-CP – Centralized Control Plane (low and high)
UPF – User Plane Function
SMF – Session Management Function
UDM – Unified Data Management Function
AUSF – Authentication Service Function
Drivers
5G - High throughput, Low latency and low jitter need
New revenue streams from New services
Making sense of enormous data generation at device layer

## Slide 3: Why Edge?
Massive Data from/to Devices – Data Reduction to Clouds
(Upstream : Data from Drones, Autonomous vehicles, factories
Downstream : 4K Streaming, AR/VR, Sports Casting, Live Gaming )
Real time and Ultra real time performance
(Closed loop control in case of IOT, On-demand compute for AR/VR, Live Gaming etc…)
Contextual Services
(User based Services, Location based Services)

## Slide 4: Edge Requirements (to ONAP)
Scalability
(Ability to address large number of Edge Clouds, switches at Edges, Support various edge controller technologies)
Security
(Infrastructure verifications, Securing secrets/keys)
Regulations
(Keep data local, GDPR – Encrypt all user data at storage/memory/on-wire)
Performance in Constrained Environment
(Very low latency, High performance, Performance determinism, data reduction, Lesser utilization of resources)
Edge App provisioning
(Traffic Redirection, Providing contextual information, slice aware)
Zero touch provisioning
(Faster bring up of Edge Clouds, Easy upgrades)

## Slide 5: ONAP Enhancements to support Edges – Summary (Green in Started in R3, Red – start in R4 and rest later)
Edge Requirement | ONAP Changes (WIP)
Scalability | Optimization needed to address large number of edge-clouds – ONAPEdge Workloads - Parent-Child ONAP (Distributed/Delegated – domain orchestration, analytics), Fabric Control, Closed loop
Security | Mutual TLS with Edges, Secrets/keys protection (HSM/DHSM), Hardware rooted security, Verification of Edge stack (Attestation), Centralized security for FaaS.
Regulations | GDPR – Symmetric keys protection, KMS at ONAP Placement decisions based geography location.
Performance | Containerized VNFs (ONAP talking to K8S based Edge Clouds) SRIOV-NIC, FPGA-NIC support (HPA++) – Enhancements needed in ONAP, Fabric Control
Edge App provisioning (MEC or others) | ONAP to expose API for Application providers – to create MEC Service, instantiate MEC Service, provide MEC status, MEC analytics etc… Integration with MEC Platform by creating MEC EMS in ONAP. Use NEV SDK as MEC platform (as VNF – Container/VM)
Zero Touch provisioning (Install/Update) | Ability for ZTP systems to interact with ONAP to provide information about Edge inventory. Edge connectivity (using private IP addresses) (IPV6)
Network Slicing/PNF provisioning (5G use case requirements), Optimization constraints support, SON integration | Being addressed in 5G use case group.
Container & VM & FaaS deployments | Unified networking (OVN/Contiv CNI) support from ONAP Support for FaaS platforms (OpenWhisk, OpenFaaS, Kubeless, Fn etc…) Modeling enhancements to support container and FaaS workloads
Analytics | Aggregation of statistics & network analytics (including ML/DL) for various edge deployments and provide infrastructure information to application providers.

## Slide 6
Scalability – Hierarchical Federation

## Slide 7: Edge Deployment Architecture – ONAP for Service Orchestration
ONAP
Multi Cloud Service
(OS and K8S support)
Edge
(With K8S for both VMs and Containers)
Edge
(With Openstack VIM)
Edge (*)
(Two logical edges – Openstack for VMs and K8S for containers)
APP Orchestrators
OSS
BSS
SDNC
(Fabric Control)
Support for both Openstack based Edges and K8S based Edges.
Support for K8S based Edges that do both VM and Container VNF management
Fabric Control to manage switch (Manage Stratum, dNOS based switches)
Challenges
  Can it handle large number of edges?
  --
  Automation Offload Platform at different sites.

## Slide 8: Edge Deployment Architecture – ONAP + Akraino
Central Orchestration, Analytics and Closed loop control (ONAP)
Regional Sites
VNFs, Edge Applications – As VMs/containers
Automation Offload Platform (AOP)
Offload I/F
Edges with OpenStack VIM
Edges with Kubernetes (K8S)
HW
HW
Edge (e.g Core networks)
HW
Automation Offload Platform (AOP) – Scale-out support to address hundreds of edges
AOP from Akraino can be used to deploy in Edge site itself or in a regional site.
Big Edges
HW
AOP
Notes: Colors matching the wiki page picture
Infrastructure profile….
Storage requirements
Network infrastructure…
Table…

## Slide 9: ONAP - Edge scalability
ONAP and Edge-Scalability (Addressing 1000s of Edge Clouds)_
Support for various VIMs (eg. Akraino, Openstack, K8S, VIO, Titanium, Azure, AWS etc..)
Tune/Enhance – for performance Hierarchical Federation: Site-level orchestration, Fabric control, Gateway control, Analytics, Topology discovery and capability distribution Placement decisions across thousands of Edges (eg. OOF, Multi-Cloud) Discovery of Edges and edge capabilities Fault/Alarm/Statistics collection agents Service scale-out Database limitations
Usability/Simplicity Auto registration : Avoid manual addition & Deletion of each Edge (Collaboration between ONAP and Akraino)
Fabric Control (Controlling L2/L3 physical switches for VLAN/VXLAN/QoS/Policies, mainly for SRIOV-NIC VNFs) Collaboration between ONAP and Akraino. Take advantage of Stratum project and avoid new plugins in AOP & ONAP
Fault/Alarm/Statistics Collection Collaboration between ONAP and Akraino to define Data models and protocols, RESP

## Slide 10: Edge Deployment Architecture – Offload Interface points
AOP
ONAP Central
SO/VFC
Offload i/f
APPC
Offload i/f
SDNC
Offload i/f
DCAE
VNF LCM Offload
Fabric Control for VLs
PNF LCM Offload
Gateway Control Offload
Prometheus
Policy
Duplicate I/f
Closed loop-local
Optimization - Local
Collectd
extension
Topology
AAI
K8S based Orchestration of ONAP offload services
ISTIO Service mesh, Vault, fluentd, Opentrace
Multi-Cloud Broker/Service with plugins
L4-L7 & App Configurator
Predictive Analytics
VES proxy
Notes: RU – Remote Radio Unit
DU – Distributed Unit (5G Base Unit)
CU-UP – Centralized User Plane
CU-CP – Centralized Control Plane (low and high)
UPF – User Plane Function
SMF – Session Management Function
UDM – Unified Data Management Function
AUSF – Authentication Service Function
Drivers
5G - High throughput, Low latency and low jitter need
New revenue streams from New services
Making sense of enormous data generation at device layer

## Slide 11: Hierarchical Federation – Site registration
ONAP Central
Sites
1. Add Site
2. Register Edge
Sites with AOP
Edges
Edges
3. Get Edge Info
4. Topology discovery
5. Add Edge to the site
Sites are added to Central ONAP by administrator
AOP adds information about edges to the Central ONAP
Edges with AOP
AOP collects information about Edges
  HPA information
  Fabric topology and Fabric element capacity
Projects: A&AI
AOP Topology Project – Leverage A&AI software

## Slide 12: Hierarchical Federation – VNF LCM
ONAP Central
Sites
AOP
Edges
Edges
SO
OOF
APPC
A&AI
1
2
AOP – VNF
LCM
AOP – MC
3
Service instantiation request (SO decomposes NSD)
For each VNFD, SO requests OOF to get the best sites to place VNF and get the edges that can host VNF. Modifies VNFD and VLs with the information from OOF. Also sends any artifacts related to VNF LCM such as initial configuration data
SO finds the Site that controls Edge and sends modified VNFD and VLs (in TOSCA) to AOP
AOP-VNFLCM decomposes VNFD & VLs from TOSCA and uses AIOP-MC to bring up workloads and Fabric control to program the switches in the edge. Also via L4-L7 configurator, it configures VNF applications.
APPC sends any configuration update to AIOP
AOP also does monitoring, Healing, Scale-out, migration on existing VNFCs
AOP informs SO if it can’t do any part of LCM
Fabric Control
4
Projects: SO, APPC
L4-L7 Configurator
5

## Slide 13: Networking – Fabric Control
Compute Servers – Hardware (CPU/Memory/SRIOV-NIC/FPGA/GPU) etc…
NFVI/VMM
Network1 (VLAN/VXLAN/GENEVE)
Network N (VLAN/VXLAN/GENEVE)
SRIOV networking
vSwitch (e.g OVSDPDK) networking
VM
VM
C
C
POD
C
POD
Site (edge/cloud)
K8S Master/OS
Network Controller
ONT
ONT
Edge Router
POD
DVR among local networks in case of OVS based vSwitch
ToR/Spine switch routing in case of SRIOV networking among local networks
Switching (L2/L3) fabric
WAN Routing/bridging via Edge Router VNF
AOP
Fabric control
L4-L7 Configurator
ONAP

## Slide 14: Scalability - Casablanca
Fix any scalability issues in ONAP – Ongoing
  Benchmarking (with at least 100 Edge Clouds)
  Fix any gaps/issues
Define ONAP-AOP Interfaces
Define architecture of AOP.
  Identify common components.
  Identify new components to be developed.
Stretch Goal:
  VNF LCM

## Slide 15
Security

## Slide 16: Security – ONAP Enhancements
Security requirements & ONAP enhancements
Mutual TLS on every communication between ONAP and Edges Enhancements at Multi-Cloud layer & DCAE
Certificate Enrollment CA Instance that provides certificates for Edges Auto Certificate enrollment (Ability for CA to verify the Edges)
Certificate Private key protection using PKCS11 at Edge nodes ONAP CA to wrap the certificate private key using public key of Edge TEE(eg. TPM) – Joint initiative/project between ONAP and Akraino
ONAP supplied Secret/Passwords protection at Edge nodes ONAP to provide a way to wrap passwords using public key of Edge TEE – Joint initiative/project between ONAP and Akraino
Software tamper detection of Edges and blacklisting edges Software/firmware/hardware attestation at the ONAP – Joint project between ONAP and Akraino
Security analytics – Joint project between ONAP/Akraino

## Slide 17
Regulations

## Slide 18: Regulations – ONAP Enhancements
Regulation requirements & ONAP enhancements
GDPR – Need for securing the data at Edges. Encryption of data requires keys and keys should not be in storage. Key Management Service at the ONAP to provide keys on demand basis
Data placement restrictions/regulations Enhance OOF with policies that specify data placement regulations ONAP SO to to place VNFs accordingly.

## Slide 19
Performance

## Slide 20: Performance – ONAP Enhancements
Performance requirements & ONAP enhancements
Containerized VNFs ONAP to control K8S based Edge-Clouds. ONAP to use K8S for both VMs and container placement. ONAP to allow specification of VNF (TOSCA) with both VMs and containers
Support SRIOV Networking for performance determinism for highly real time applications
Unified networking between VMs and ONAP (possible choices : OVN or Contiv)
Multiple interfaces – Device tagging support in ONAP

## Slide 21
Zero Touch Provisioning

## Slide 22: Zero Touch Provisioning – ONAP Enhancements
Zero Touch Provisioning & ONAP enhancements
Auto Edge registration to ONAP – ZTP to help?

## Slide 23
Edge App Provisioning

## Slide 24: MEC Architecture
MEC Specifications
    GS MEC 009: General Principles for Mobile Edge Service APIs
    GS MEC 012: Radio Network Information API
    GS MEC 013: Location API
    GS MEC 014: UE Identity API
    GS MEC 015: Bandwidth Management API
    GS MEC 016: UE Application Interface
    GS MEC 010: System, Host and Platform Management
    GS MEC 011: Mobile Edge Platform Application Enablement
  Virtualization & Containers
    MEC027 – Container study
    MEC020 - NFV Study
Reference: http://www.etsi.org/deliver/etsi_gs/MEC/001_099/003/01.01.01_60/gs_MEC003v010101p.pdf

## Slide 25: MEC Architecture – Challenges (in 4G)
APP
APP
APP
MEC Edge Platform
Packet DeMux
API
API
API
API
Packets
Proprietary (in 4G)
MEC has decent RESTful API definition to provide contextual information
4G challenges
No standard way to provide contextual information to MEC edge platform.
No standard way to De multiplex the UL traffic and aggregate DL traffic.

## Slide 26: 5G and MEC
APP
APP
APP
MEC Edge Platform
API
API
API
API
Packets
UPF
UL Classifier
AMF
SMF
NEF
AF
UE
5G is defining standard way to redirect the traffic (SMF and UPF).
5G is also defining standard way to get hold of contextual information (AMF and SMF with NEF).
Mobile Edge Platform VNF can be a translator between 5G exposed information to APPs that use MEC API to get contextual information.
PCF
Traffic rules

## Slide 27: MEC Application Provider and ONAP deployments – Choice 1 (ONAP-Managed Edge App provisioning)
App provider 1
(May be based on MobileEdgeX)
App provider m
(Based on XYZ)
Operator 1
Operator n
Edge/
Core
Edge
Edge
Edge
Edge
Edge
ONAP- Central
OSS/BSS
ONAP-Central
OSS/BSS
End user application 1 that requires compute offload in edges
End user application m that requires compute offload in edges
ONAP-Edge for scaling (Delegation)
Does not exist today – Optional to deploy
Public Cloud
Public Cloud
focus

## Slide 28: Edge Application use case – Compute offload by User Entity
Device Edge
RU/DU
UPF (App Routing)
NEF
ONAP
POP
BRAS, PE
Network Edge
Core Cloud (EPC)
UPF
Application Functions (e.g in AWS, Azure)
AF1
AF2
AF3
Dyn
APP
Dyn
APP
Dyn
APP
UE APP
UE APP
UE APP
SMF
1
4
2
5
6
3
DN
UE APP requests AF to create compute for it (e.g. AR/VR, Gaming offload). UE provides information such as ‘coordinates’, ‘max cost’, ‘max latency’, etc…
AF requests ONAP to create DynApp (can be a VNF too) in closest edge that satisfies UE requirements (ONAP figures out the best region out of thousands of clouds).
ONAP brings up DynApp/VNFs on the Edge Cloud using VIM API
AF informs NEF/SMF to create traffic rule (to enable redirection of UE APP traffic to newly-created VNFs).
SMF informs UPF in the edge cloud (i.e., programs UE classifier of UPF).
Traffic from a UE app is directed to the correct edge cloud app.
AMF
UDM
AUSF
PCF
Edge Cloud
Static APPs (e.g. Caching, CDN, Security)
Local DN
Notes: UE APP requests AF to create compute for it (Eg. AR/VR, Gaming offload). UE provides information such as ‘coordinates’, ‘max cost’, ‘max latency’ etc…
AF requests ONAP to create VNFs in edge that is closer to UE that satisfies UE request(ONAP figures out the best region out of thousands of clouds)
ONAP brings up VNFs on the Edge Cloud using VIM API
AF informs NEF/SMF to create traffic rule (to enable redirection of UE APP traffic to new VNFs created).
SMF informs UPF in the edge cloud (Programs UE classifier of UPF).
When the traffic comes from UE APP, right application in the edge cloud receives the traffic.

## Slide 29: Network E2E with Edge Apps – MEC Apps & Contextual information
Device Edge
RU/DU
UPF
NEF
ONAP
Value Added Services
POP
BRAS, PE
Network Edge
Edge Cloud
(tens of thousands)
Core Cloud (EPC)
AMF
UDM
AUSF
UPF
PCF
Application Providers (eg. In AWS, Azure)
AF1
AF2
AF3
Dyn
APP
Static APPs (eg. Caching, CDN, Security)
UE APP
UE APP
UE APP
SMF
DN
Local DN
Dyn Apps get contextual information from AFs.
Legacy MEC Applications can be supported.
AF can get the information from SMF and AMF (location, Subscriber ID and others) and make it available to “MEC Edge Platform”. MEC Edge Platform can in turn expose this information via ETSI MEC API
Question: Do we see MEC Edge platform by each application provider? Or one platform for entire edge by operator? Or support both cases?
OOF
MC
DCAE
MEC APP
MEC APP
MEC Edge Platform
1
Notes: RU – Remote Radio Unit
DU – Distributed Unit (5G Base Unit)
CU-UP – Centralized User Plane
CU-CP – Centralized Control Plane (low and high)
UPF – User Plane Function
SMF – Session Management Function
UDM – Unified Data Management Function
AUSF – Authentication Service Function
Drivers
5G - High throughput, Low latency and low jitter need
New revenue streams from New services
Making sense of enormous data generation at device layer

## Slide 30: MEC Application Provider and ONAP deployments – Choice 2 (ONAP-unaware Edge App provisioning)
App provider 1
App provider m
(Based on XYZ)
Operator 1
Edge
ONAP
OSS/BSS
End user application 1 that requires compute offload in edges
End user application m that requires compute offload in edges
Edge Domain Orchestrator
Public Cloud
Edge
Edge Domain Orchestrator
Edge
Edge
Edge
Non-edge (Core)
Operator 1
Edge
ONAP
OSS/BSS
Edge Domain Orchestrator
Edge
Edge Domain Orchestrator
Edge
Edge
Edge
Non-edge (Core)

## Slide 31: Comparison between ONAP-Managed vs ONAP-unaware Edge App provisioning
ONAP Managed Edge App provisioning:
App providers only see the ONAP interface to provision applications in any edges managed by ONAP. (ONAP is the entry point for any application provisioning)
ONAP is used for both telecom VNFs and VNFs & Apps from App providers.
For scaling with large number of edges, ONAP-Edge (to be developed) will take care of virtualization life cycle management. ONAP-Edge can be instantiated across regional sites.
Pros:
One interface point per operator to application providers.
ONAP as an orchestrator for edge apps -> More use cases for ONAP.
Cons:
ONAP scope change as it deployed third party VNFs/Apps.
ONAP-unaware App provisioning:
New project – Edge domain Orchestrator. (May be Akraino project or may be MobileEdgeX project or something else)
App providers communicate with the Edge Domain Orchestrators. ONAP is also considered as one of the consumers of Edge Domain Orchestrators.
ONAP is only used to on-board & instantiate only telecom VNFs.
For scaling with large number of edges, Edge Domain Orchestrators will have its own scaling methods.
Pros:
ONAP scope is unchanged.
ONAP can be made consumer of Edge Domain orchestrator slowly in future.
Cons:
Some Edge Domain Orchestrator functionality overlaps with ONAP functionality such as placement decisions, VNF/service onboarding etc…

## Slide 32: Edge App Provisioning – ONAP Enhancements (for Choice1)
Edge App provisioning
ONAP External API (Study and find the gaps) Registration of Application providers (AFs) Dynamic onboarding of NSDs (Services with DynApps/VNFs) Authenticate/authorization of Application providers (Token/Cert based), Mutual TLS Providing information about NEF Manager reachability information (for AF to look for events), DynAPP reachability information to help in creating traffic rules Auto-scaling notifications.
Traffic rule (steering) creation In UPF via NEF/SMF (ONAP to talk to NEF management systems?). Inter-VNF SFC enhancements in ONAP (DynApp might consists of multiple workloads and may need SFC.
PNF on boarding ( If UPF is PNF ) – Existing feature
ONAP to provide a way to select the best region to place dynamic apps (using UE coordinates, cost and other parameters) – Already existing, more enhancements?
ONAP to act as Service registry? Or leave it to AF vendors (Leave it to AF vendors to have service registry as workload)
AF interaction related enhancements in ONAP Network Slicing Controller
MEC Edge Platform Manager as EMS by Application Providers – ONAP to provide right information to EMS (when Apps come up, App instances go down, etc…) - Should ONAP provide its own MEC platform Manager?

## Slide 33: BACKUP

## Slide 34: What changes required in ONAP
Edge Requirement | ONAP Changes (To be filled)
Scalability | 
Security | 
Regulations | 
Performance & Constrained environment | 
Edge App provisioning (MEC or others) | 
Zero Touch provisioning (Install/Update) | 
Network Slicing | 
Container & VM VNF deployments | 
Analytics | 

## Slide 35: Edge Deployment Architecture – Various Edge Groups
ONAP
Multi Cloud Service
Regional Controller
K8S API Server
K8S Scheduler
CNI (OVN) Controller
K8S Controllers
Zero Touch Provisioning
(install, Update)
Storage Node
Ceph Cluster
SAN
Local Drives
Compute nodes
Real time OS
OVS DPDK
SRIOV
Network
CNI agent
Docker
Kubelet
VM
EdgeX Containers
Container
Virtlet
Logging
(fluentd)
Monitoring (Prometheus)
Service mesh, (istio)
Security (Auth, Secrets, HSM)
Agents
Etcd, kafka
Akraino
Openstack (Alternative)
Openstack Edge-computing
Open Edge Compute (QEMU changes, Openstack++ for faster VNF migration)
EdgeXFoundry (IOT infrastructure)
ETSI MEC for contextual applications
5G – NEF/NRF/UPF-5G Classifier for Edge Apps
OpenFog – Edge Architecture