## Slide 1: ONAP SDN-R Managing Network Notifications and Data Persistence in support of 4G & 5G RAN (draft) Aymen Saidi as963q@att.com
May 23rd, 2018

## Slide 2: Introduction
© 2017 AT&T Intellectual Property. All rights reserved. AT&T and the AT&T logo are trademarks of AT&T Intellectual Property.
.
  Option 1: Continuously Read from the Network
    ONAP Controller Acts as a proxy
    Increase OAM bandwidth requirements at Southbound
    NF can reduce the amount of data by providing a delta service. However this would add a high level of complexity
    Upper layer responsible
  Option 2: Notifications/Subscription based services
    Read the network once then receives deltas
    Only receive network changes
    Requires data persistence, a copy of the network must exist somewhere
Opportunity that SDN-R must address to truly be useful
Notes:   In option 2, one can think of a having notification/subscriptions services at the upper layer. In this case, all complexity is moved to the Network.

## Slide 3: Radio Network Characteristics, Behavior and Evolution
Characteristics & Behaviors
Probabilistic
Dynamic
Adaptable
The environment constantly changes
Self-Optimized
A large amount of network changes
© 2017 AT&T Intellectual Property. All rights reserved. AT&T and the AT&T logo are trademarks of AT&T Intellectual Property.
.
Chart: Trends - Daily Network Changes per Cells
| 2G | 3G | 4G | 5G
Actual | 1.23 | 38.5 | 600
In 2G, the radio network is static
In 3G, the radio network is relatively static
In 4G, the radio network is dynamic
In 5G, the radio network will be extremely dynamic.
  Beamforming
  Increased SON use cases
  Refinement of decision granularity
Notes: Note:
Data averaged daily over a period of 1 year for 2G/3G while 4G data is a daily average from January to April 2018. It’s limited to configuration changes events (Ex: Parameter X goes from Value A to Value B)
It reads X changes per individual Cell.

## Slide 4: Possible Architectures
© 2017 AT&T Intellectual Property. All rights reserved. AT&T and the AT&T logo are trademarks of AT&T Intellectual Property.
.
  Distributed
  Centralized
Multiple collectors/controllers
Centralized Network Copy
Centralized REST API
Resources centric
Simple architecture
Limited Data Categorization Opportunity
Distributed Collector + Collection Manager
Support Data Model Slicing
Centralized REST API
De-centralized Resources requirement
Complex architecture
Data Categorization Opportunity
Notes: Note:
Architecture not defined. This to highlight opportunity for datastore supporting radio characteristics.
Area represent a geographical area.
Partial copy represent a slice of the network. In both option, it’s expected that the “network copy” is a complete copy of the network. Such copy need to be synchronized in real-time
SDNRc: SDNR Controller
SDNRd: SDNR Distributed Controller

## Slide 5: Ways Forward / Opportunities
Predict 5G network management information gain (paper opportunity)
Distributed vs centralized SDN-R architecture
Data “noise” reduction and categorization for distributed SDN-R architecture (paper opportunity)
© 2017 AT&T Intellectual Property. All rights reserved. AT&T and the AT&T logo are trademarks of AT&T Intellectual Property.
.