## Slide 1: OOF-PCI items deferred to Dublin Release
Onboard PCI Handler MS to DCAE, and include in SDC Catalog
SDN-R use cases moved from Casablanca to Dublin
  SDNC-430: Modify RAN informational model and yang model for RAN
  SDNC-431: Implement config DB and REST API (SDN-R / OOF interface)
  SDNC-432: Interfacing SDN-R with Policy
    Receive DMaaP message in CL format from Policy (Modify Config message using existing LCM API), send netconf message changing PCI value to cellID as specified, update config DB, and publish change on DMaaP (DMaaP client is available and can be called)
  SDNC-432: Receive netconf notification from RAN, update configDB, and publish change on DMaaP

## Slide 2: OOF-PCI items deferred to Dublin Release
Complete the data flows for PCI use case
Include FM/PM input for SON:
  Send FM/PM data from RAN to DCAE Collector (e.g. PCI confusion alarm)
  Enhance PCI Handler MS to receive FM/PM data from DMaaP
Include New Cell Addition as input for SON:
  Include SDC, SO, A&AI flow for new cell addition
  Enhance PCI Handler MS to receive request for PCI allocation for new cell

## Slide 3: 5G Configuration Management: SDN-R Enhancements for Dublin Release
Common RAN Information Model
  Build on Casablanca RAN Information Model, and target consensus among vendors for complete common RAN information model
SDN-C/SDN-R Controller enhancements
  Implement both Configuration Database and Operational Database as per ODL industry practice, leveraging Casablanca POC work on ConfigDB database
  Configuration Database – values needed to perform / initiate configuration
  Operational Database – dynamically changing network parameters relevant to ONAP and SDN-C/SDN-R
  Support history of config state as needed for Change Management
  Support both reactive and predictive network change actions
Inventory & Configuration Management synchronization
  Develop models and relationship between A&AI Database and SDN-C Configuration Database and Operational Database
  A&AI is primary reference for inventory and id of VNF, PNF, elements

## Slide 4: Policy Enhancement for Dublin for SON Coordination
Enhance the Policy functionality for Control Loop Coordination (CLC) – build on basic functionality in Casablanca
POC to implement two Control Loops (one could be PCI-SON) and demonstrate coordination using CLC

## Slide 5: OOF Enhancement for Dublin Release
Add optimization for ANR (Automated Neighbor Relations) SON functionality, which is closely couple to PCI SON
Changes to: ANR Handler MS, Policy, SDN-R, RAN Simulator
Add RAN Simulator functionality to provide data
  Add metrics for neighboring cell pairs needed for ANR, e.g. handover KPIs
  Implement messages between SDN-R and RAN Simulator to support ANR function (e.g. cell relationship table, neighbor add and delete actions)