## Slide 1: Simplified CRAN/HeNB management PoC
02/21/2018

## Slide 2: [a] GET Device Information
The following attributes provide details of the device:
Device.DeviceInfo. | object | -
Manufacturer | string­(64) | -
ManufacturerOUI | string­(6:6) | -
ModelName | string­(64) | -
Description | string­(256) | -
ProductClass | string­(64) | -
SerialNumber | string­(64) | -
HardwareVersion | string­(64) | -
SoftwareVersion | string­(64) | -
AdditionalHardwareVersion | string­(64) | -
AdditionalSoftwareVersion | string­(64) | -
UpTime | unsignedInt | -
FirstUseDate | dateTime | -

## Slide 3: [b] Configure the device for service (with PCI Range)
The following attributes are required at minimum for service :
FAPService.{i}.CellConfig.LTE.RAN.RF. | object | -
DLBandwidth | string | W
ULBandwidth | string | W
PhyCellID (configure a RANGE) | string­(64) | W
EARFCNDL | string­(128) | W
EARFCNUL | string­(128) | W
FAPService.{i}.CellConfig.LTE.RAN.PHY.PRACH. | object | -
RootSequenceIndex | unsignedInt­[0:837] | W
FAPService.{i}.CellConfig.LTE.RAN.Common. | object | -
CellIdentity | unsignedInt­[0:268435455] | W
FAPService.{i}.CellConfig.LTE.EPC.PLMNList.{i}. | object | W
PLMNID | string­(6) | W
IsPrimary | boolean | W
FAPService.{i}.FAPControl.LTE.Gateway. | object | -
S1SigLinkServerList | string­(256) | W
Device.Time. | object | -
LocalTimeZone | string­(256) | W
FAPService.{i}.CellConfig.LTE.EPC. | object | -
TAC | unsignedInt­[0:65535] | W
FAPService.{i}.FAPControl.LTE. | object | -
OpState | boolean | -
AdminState | boolean | W

## Slide 4: [c] Perform REM (Automatic PCI selection (SON))
FAPService.{i}.REM.LTE. | object | -
EUTRACarrierARFCNDLList | string­(64) | W
ScanTimeout | unsignedInt | W
ScanStatus | string | -
LastScanTime | dateTime | -
The following attributes are required for REM :
REMBandList | string | W
ScanOnBoot | boolean | W

## Slide 5: [d] View REM Result
FAPService.{i}.REM.LTE.Cell.{i}.RF. | object | -
EUTRACarrierARFCN | unsignedInt­[0:65535] | -
PhyCellID | unsignedInt­[0:503] | -
RSRP | int­[-140:-44] | -
RSRQ | int­[-240:0] | -
RSSI | int­[-110:-19] | -
FAPService.{i}.REM.LTE.Cell.{i}.BCCH. | object | -
DLBandwidth | unsignedInt­[6, 15, 25, 50, 75, 100] | -
ULBandwidth | unsignedInt­[6, 15, 25, 50, 75, 100] | -
RSTxPower | int­[-60:50] | -
TAC | unsignedInt­[:65535] | -
CellID | unsignedInt­[:268435455] | -
CellBarred | boolean | -
CSGIndication | boolean | -
CSGIdentity | unsignedInt­[0:134217727] | -
FAPService.{i}.REM.LTE.Cell.{i}.BCCH.PLMNList.{i}. | object | -
PLMNID | string­(6) | -
The following attributes are required to view REM Results:

## Slide 6: [e] ONAP – Device communication
Device supports the proposed basic data model
Implement this basic data model in YANG
View device information in ONAP
Device connects to ONAP
ONAP configures device with minimum attributes required for service and PCI selection (SON)
View REM Result from device

## Slide 7: [f] Connect to the device
The following attributes are required to contact the device:
ConnectionRequestURL | string­(256) | -
ConnectionRequestUsername | string­(256) | W
ConnectionRequestPassword | string­(256) | W
Device.ManagementServer. | object | -