## Slide 1: Casablanca Platform Enhancements to Support 5G Use Case Architecture Review
5G Use Case Team
June 26, 2018

## Slide 2: Contributors:
Supporting Companies
And Others

## Slide 3: 5G Network Architecture & Casablanca Scope
5G
Application
Ecosystem
UE/CPE
RU
DU
CU-UP
Internet
Edge Cloud
Macro Radio
& Small Cell
Antennas
External Content
CU-CP
RU – Remote Radio Unit DU – Distributed Unit (5G Base Unit)
CU-UP – Centralized User Plane CU-CP – Centralized Control Plane
UPF – User Plane Function SMF – Session Management Function
UDM – Unified Data Management Function AUSF – Authentication Service Function
Mid Haul
Back Haul
Centralized
Cloud
Disaggregated Core
UPF
SMF
UDM
AUSF
Casablanca Scope
Front Haul

## Slide 4: 5G Network Architecture & Casablanca Scope
DU
CU-UP
Edge Cloud
CU-CP
Mid Haul
Front Haul
DESIGN-TIME
Policy Creation & Validation
Analytic Application Design
VNF / PNF Certification & Onboarding
Resource Onboarding
Service Design
Catalog
ONAP Operations Manager
Dashboard OA&M
Common
Services
Application
Authorization
Framework
Logging
Policy Framework
Active & Available Inventory
External Registry
App-C
Data Collection, Analytics, and Events
Event Correlation
ONAP Optimization Framework
SDN Controller (SDN-C)
Orchestration
Micro Services Bus / Data Movement
Others
Closed Loop Design
Change Management Design
Adaptation Layer
Design Test & Certification
Common Controller SDK
RUN-TIME
Common Services
Multi-Cloud
Adaptation
(Data Center & Edge Cloud)
Adaptation Layer
Configuration & Life Cycle Management
Configuration & Life Cycle Management

## Slide 5: Casablanca Enhancement Summary:
  Enhance ONAP Platform to deploy hybrid 5G Radio Network (PNFs & VNFs)
    Expand Packaging standards to include PNFs
    Enhance VNFDSK to support PNF packages as well (depends on 1)
    Enhance SDC to support PNF onboarding and hybrid network design (using PNF / VNF)
    Need a way to model in SDC the “Service Instantiation” sequencing relationships that SO must enforce for PNF service instantiation.
    Add PNF Plug-n-Play to auto register newly installed PNF
    Enhance SO to support decomposition of Services that include VNFs and PNFs
    Support for Edge deployment (e.g. CUs) – Edge Cloud Automation
    Expand ONAP controllers by adding wireless service yang models, network yang models and service logic to ONAP.
    Add common reusable logic to CCSDK to support wireless
    Support a single controller persona (SDN-C) to support L1-7 network configuration and lifecycle management for 5G network elements
    Integrated controller configuration design tool to capture L1-7 configuration data for radio network elements
    Enhance DCAE for near real-time (order of seconds) streaming performance data collection
    Enhance DCAE for Bulk performance data collection
    Introduce Real-time streaming analytic platform
  OOF enhancements for optimal placement of edge resources & Framework Enhancements to implement selected network optimization (e.g. PCI assignment)

## Slide 6: PNF PnP Enhancements
TOPIC | DESCRIPTION
PNF Registration Handler (PRH) enhancements | Define a New VES Event Domain for PNF registration with the corresponding support in DCAE VES Collector, DMaaP and PRH
SDC Enhancements | Enhance SDC to support PNF onboarding and hybrid network design (using PNF / VNF) with generic workflow to instantiate PNF (i.e. put it in service)
SO Workflow enhancements | Enhance SO to support model driven dedicated workflow for PNF elements
Service Configuration Enhancements | Add needed artifacts in CCSDK to support Radio / Microwave configuration, PNF discovery and registration support
Security enhancements | Authentication and Certificate support for PNF, including registration event and data collection (fault and performance)
Modeling enhancements | Enhance ONAP information and data model to fully support 5G PNF elements, including inheritance and PNF sharing characteristic
PNF onboarding and packaging | Define PNF Package, PNF package validation and onboarding enhancements

## Slide 7: Service Configuration Enhancements
TOPIC | DESCRIPTION
Enhance CDT tool to support 5G and integrate into SDC | Integrate App-C focused CDT tool into SDC and enhance it to support 5G network elements configuration design
Capture and Verify PNF Software version | Enhance ONAP controller (SDN-C) to capture and verify PNF software version, Enhance A&AI to store PNF Software version
PNF & CU Application Level Configuration (Controller Enhancements) | Generate a single ONAP controller persona (SDN-C) from CCSDK to support various 5G network elements (Layer 1 through 7 configuration and management)
Lifecycle management Support | Enhance change management support 5G PNF / VNFs (e.g. software upgrade)

## Slide 8: PERFORMANCE ANALYSIS & OPTIMIZATION
TOPIC | DESCRIPTION
Bulk performance measurement (PM) data collection | Enhance DCAE VES collection layer to support periodic (e.g. every 5 to 15 minutes) bulk data collection from VNFs and PNFs. Support both file-based collection and mapping to VES Events for chosen file content
High Volume and Near Real-time streamed data collection of Performance measurements | Enhance DCAE performance measurement (PM) data collection to support near real-time (order of seconds) data. Introduce a high-volume VES collector using a persistent connection (TCP socket), support a new data encoding (GPB). Distribute DCAE collection at the cloud edge (for scalability)

## Slide 9: Optimization Framework Enhancements
TOPIC | DESCRIPTION
Optimal placement of vNF | Placement of Mobility Virtual Network Elements (CUs) across the highly distributed edge clouds is a fundamental requirement. Service Providers must also optimize the performance of the 5G RAN in real-time.
Optimization problem formulation | Ability to model the problem as a constrained optimization problem, that is driven by policies – Potential use case examples: formulation of optimization problems at various levels: Customer (e.g. provisioning), Service (e.g. slice optimization ), Network (e.g. Routing, problems at the network planning level), Infrastructure (e.g. Placement) & Resource (e.g. License)
Optimization problem solving | Ability to use and deploy appropriate analytics, algorithms and solvers to solve the problem in acceptable time frames at various levels: Customer, Service (e.g. Slice Optimization Analytics), Network (e.g. SON network planning analytics), Infrastructure (e.g. Placement) & Resource

## Slide 10: Overview of SDN-R work:
Goal of SDN-R team is to develop extensions/models for OpenDaylight based SDN-C controller to support wireless transport network
Team is focused on contributing code in SDN-C in the following areas:
  License & Spectrum Management Logic
  RAN and Wireless Management Logic
SDN-R team is also defining a shared data model for wireless transport
In addition to wireless transport, 5G use case requires application level (L4-7) parameter management for disaggregated 5G elements like DU, CU-UP, CU-CP, etc.
Key Architecture Guiding Principle for 5G Controller Design Are:
  There should be only one ONAP controller persona for all Mobility functions (e.g. LTE, 5G, RAN, Wireless, Core)
  All 5G RAN and Core elements (e.g. DU, CU, UPF) should be controlled by the same ONAP controller persona, due to cross-dependencies (e.g. CU-UP and UPF can be combined into one NE)
  The same ONAP controller persona should support OA&M lifecycle management (config, change, reset, suspend, resume etc.), and include all interfaces needed (e.g. Netconf, Chef, Ansible)

## Slide 11: ONAP Project Repos & Executables: Casablanca
Executable Images
SDN-C
App-C
Repos
SDN-C
CCSDK
ccsdk-parent
ccsdk-sli-core
ccsdk-sli-plugins
ccsdk-sli-adapters
ccsdk-distribution
Common microservices
Common health checks
Common APIs
Common logging
Common model management
Common resource management
sdnc-logic
App-C
appc-northbound
appc-logic
appc-adapters
5G element adapters
New
Northbound APIs
  VNF-API
  GEN-RESOURCE
  DMaaP
  LCM
  Wireless Services
New
spectrum-logic
wireless-logic
ran-logic
SDN-R Team Contribution

## Slide 12
Thank You!