## Slide 1
ROADMAP FOR SECURITY ENHANCEMENTS
FOR 5G USE CASE
5G Use Case A : Deployment
5G Use Case C : Optimization
Aug 23, 2018

## Slide 2
DCAE Authentication of NF
Security Function | Release | Impacted Projects | Comments
HTTP authentication with username/password, no TLS | Casablanca | DCAE VES Collectors | Already supported. NF sends username & password in VES event as base-64 encoded string. VES Collector (VC) authenticates username & password with Basic Authentication as described in the VES Specification. SECCOM does not recommend this option due to the risk of sending passwords in the clear. Operators are able to configure DCAE to prohibit HTTP w/o TLS (close port 80).
HTTP authentication with username/password, TLS enabled, one-way TLS server authentication (NF doesn’t have a cert) | Casablanca | DCAE VES Collectors | Already supported. NF and VC establish a server authenticated TLS session (NF authenticates VC using VC certificate. NF needs VC signing chain). NF sends username & password for HTTP. VC authenticates HTTP username & password with Basic Auth. SECCOM does not recommend this option due to concerns about managing and securing M2M pwds.
HTTP authentication with username/password, TLS enabled, mutual TLS authentication (NF has a certificate) | Casablanca | DCAE VES Collectors | Already supported. NF and VC establish a mutually authenticated TLS session (NF authenticates VC using VC certificate; VC authenticates NF using NF certificate). NF sends username & password for HTTP because DCAE requires it. VC authenticates HTTP username & password with Basic Auth. SECCOM does not recommend this option due to concerns about managing and securing M2M pwds.
HTTP authentication via TLS, TLS enabled, mutual TLS auth, no HTTP username/pwd sent | Dublin | DCAE VES Collectors NF Reqts | SECCOM recommendation. NF and VC establish a mutually authenticated TLS session. NF does not send HTTP username & pwd. HTTP is authenticated via TLS authentication. Until supported, username & password must be sent for HTTP with or without TLS enabled because DCAE requires it.

## Slide 3
DCAE Authorization of NF
Security Function | Release | Impacted Projects | Comments
NF role and permissions created at NF Design Time | Dublin | AAF | When the YAML Event artifact is distributed for a NF Type at Design Time, AAF automatically creates a role for the NF Type and assigns permissions based on the events in the YAML file. Until supported, a human user with the proper permissions can use the AAF GUI to manually create a role and permissions. Alternately, authentication equals authorization, meaning no separate authorization is performed and all valid events are accepted.
NF instance assigned to NF role during VNF instantiation or PNF PnP | Dublin | SO | SO calls AAF (existing API) to assign the NF instance to the NF Role during VNF Instantiation or PNF PnP. Until supported, a human user with the proper permissions can use the AAF GUI to manually add the NF instance to the role after instantiation/PnP. Alternately, authentication equals authorization, meaning no separate authorization is performed and all valid events are accepted.
DCAE VES Collector authorizes NF when VC receives an event from NF | Dublin | DCAE VES Collectors | When DCAE VES Collectors (VC) receives an event from an NF, VC retrieves the role and permissions from AAF for that NF. VC checks if the event is allowed for that NF and either accepts or rejects the event. Until supported, authentication equals authorization, meaning no separate authorization is performed and all valid events are accepted. Alternately, DCAE may have its own local role DB. In this case, it is of no use to manually create a role in AAF or add the NF instance to the role in AAF. Instead, the role and NF instance must be added to the local DCAE role DB.

## Slide 4
CA/RA Functionality
Security Function | Release | Impacted Projects | Comments
Vendor or Service Provider (SP) CA certificate chain provisioned in ONAP | Casablanca | AAF Cert Manager | Already supported. ONAP user is able to manually provision the necessary CA certificate chain into ONAP to allow TLS certificate authentication; either the Vendor or SP chain.
ONAP supports at least 3 levels of cert chaining; CA, RA, end-entity | Casablanca | AAF Cert Manager | Already supported.
ONAP provides CA services to ONAP components. | Casablanca | AAF Cert Manager | Already supported. ONAP components can get certificates from AAF CertMan. CMPv2 is not required.
AAF CertMan acts as an RA when a commercial Service Provider (SP) CA is used. | Casablanca | AAF Cert Manager | Already supported. During deployment of ONAP, AAF CertMan is provisioned to be an online, near real time RA for the SP CA to provide IAK/RV to NF for initial certificate enrollment. It is not necessary to support key renewal because NF goes directly to SP CA for these services. Until supported, NFs must obtain IAK/RV to NF for initial certificate enrollment outside of ONAP, possibly directly with the SP CA.
ONAP provides CA services to NFs via CMPv2 when in an ONAP development environment. | Dublin | AAF Cert Manager | AAF CertMan acts as the CA for NFs in a development environment and supports NF certificate enrollment via CMPv2. It is not necessary to support key renewal for dev env. Until supported, NFs must obtain certificates for TLS in a out-of-band way and manually install on the NF. Alternately, do not use TLS until supported.

## Slide 5
ONAP Requirements for VNF Certificate Enrollment
Security Function | Release | Impacted Projects | Comments
Controller SSH username, public key and FQDN are obtained for the VNF during instantiation. | Dublin | SO, AAI | SO retrieves the Controller SSH username and public key and FQDN for the Controller that is managing the VNF and populates this in the VNF AAI entry. Until supported, Controller SSH username, public key and FQDN must be manually configured (e.g. in the HEAT template). Open point: how SO knows which Controller (APPC vs SDNC vs VFC) and which Controller instance manages this VNF instance (there may be multiple SDNC instances, for example at different geographic locations, DC vs Edge Cloud). For now, SO workflow hard-codes the controller.
Controller information available to SO | Dublin | APPC, SDNC, VFC | Controller FQDN, SSH username and SSH public key are available for SO to retrieve for the VNFs. This can be in AAI or some other appropriate data storage location or obtained via a Controller API.
IAK/RV is obtained for the VNF from the CA during instantiation. | Dublin | SO, AAF CertMan | SO triggers AAF to get IAK and RV for the VNF. AAF CertMan requests the IAK/RV from the CA using CMPv2. AAF returns IAK, RV, CA URL and CA Root Certificate to SO. SO keeps this in memory to pass to Controller at a later step. Until supported, IAK/RV must be obtained in an out-of-band way from the SP CA and manually installed on the NF. Alternately, do not use TLS until supported.

## Slide 6
ONAP Requirements for VNF Certificate Enrollment
Security Function | Release | Impacted Projects | Comments
HEAT template updated with Controller SSH username, public key and CA root certificate | Dublin | SO | SO updates HEAT template with Controller SSH username, public key and CA root certificate. Until supported, HEAT template must be manually updated before instantiation.
IP address and FQDN are assigned to the VNF during instantiation. | Dublin | SO, AAI | SO triggers OpenStack to assign VNF IP address and VNF FQDN and update DNS. SO updates AAI with VNF FQDN and IP address. Until supported, FQDN must be manually assigned before the VNF performs certificate enrollment and DNS must be manually provisioned.

## Slide 7
VNF Requirements for VNF Certificate Enrollment
Security Function | Release | Impacted Projects | Comments
VNF accepts and processes security data passed during instantiation. | Dublin | VNF Reqts | VNFs must accept the instantiation security data (Controller SSH key and CA Root Certificate) during instantiation and process it; e.g. store it in the proper locations.
VNF performs certificate enrollment automatically after activation. | Dublin | VNF Reqts | If the CA URL is configured, VNF automatically performs certificate enrollment via CMPv2 using the IAK and RV during activation of the service configuration. Until supported, certificate enrollment must be triggered on the VNF manually.

## Slide 8
PNF Requirements for PNF Certificate Enrollment
Security Function | Release | Impacted Projects | Comments
PNF Vendor Certificate | Casablanca | PNF Reqts | PNF comes with a vendor certificate that can be used to obtain a SP/ONAP certificate and/or can be used for TLS. Until supported, PNF would need to be manually provisioned with end-entity certificate or with a IAK/RV so PNF can perform certificate enrollment or alternately do not TLS.
PNF Certificate Enrollment | Casablanca | PNF Reqts | PNF is able to perform certificate enrollment with a SP/ONAP CA/RA. 3GPP devices use CMPv2 but this is not required as long as the CA/RA supports the protocol and procedure that the PNF uses. Until supported, PNF would need to be manually provisioned with an end-entity certificate or alternately do not use TLS.
Provision PNF with CA/RA information | Casablanca | PNF Reqts | PNF is provisioned with the necessary CA/RA information (e.g. CA URL, CA name) by the Initial Element Manager (EM) during Plug-n-Play (PnP). EM and PNF must support the PnP procedure. Until supported, PNF would need to be manually provisioned with CA/RA information or alternately, do not use TLS.
Update PNF Registration workflow to assign PNF instance to PNF role created at onboarding | Dublin | SO | SO calls AAF (existing API) to assign the PNF instance to the NF Role during PNF Registration. Until supported, a human user with the proper permissions can use the AAF GUI to manually add the PNF instance to the role after PNF Registration. Alternately, authentication equals authorization, meaning no separate authorization is performed and all valid events are accepted.

## Slide 9
Controller CM Requirements
Security Function | Release | Impacted Projects | Comments
Support for NetConf/TLS | Dublin | APPC, SDNC, VFC | Controller support for NetConf over TLS as an option for Configuration Management (CM) of the NF. Until supported, one of the other supported CM protocols could be used (Ansible/SSH, Chef/SSH, NetConf/SSH) or alternately, delay CM from ONAP until NetConf/TLS is supported.
Controller determines which CM protocol to use for an NF. | Dublin | APPC, SDNC, VFC, maybe SDC, AAI, modeling | Open point: how the Controller knows which CM protocol to use for a particular NF (Ansible/SSH, Chef/SSH, NetConf/SSH or NetConf/TLS). No agreement has been reached. Some options were discussed; add it to the model, add it to the NF package, populate it in AAI, try the CM protocols in a priority order, APPC uses Directed Graphs and Config Templates. Until agreed and supported, Controllers hard-code which protocol to use.
SO triggers Controller to perform service configuration, including passing security data | Dublin | SO, APPC, SDNC, VFC | SO triggers Controller to configure VNF, passing Controller FQDN, VNF FQDN, IAK, RV and CA URL as configuration data.

## Slide 10
HTTP Security Bootstrapping Data
Security Function | Release | Impacted Projects | Comments
HTTP username and password created in DCAE VES Collector | Casablanca | DCAE VES Collector | HTTP account (with username and password) has been created in ONAP to be used by NFs when sending VES events to the DCAE VES Collector.
HTTP username and password provisioned in NF | Casablanca | NF Reqts | HTTP username and password for DCAE VES Collector is provided to NF out-of-band according to operator security procedures. For PNFs, this must be provided before PNF can send the pnfRegistration VES event.
Note that starting in Dublin, HTTP username and password is no longer needed.

## Slide 11
SSH Security Bootstrapping Data
Security Function | Release | Impacted Projects | Comments
Controller creates RSA key pair for NF SSH access | Casablanca | APPC, SDNC, VFC | Controller creates its SSH RSA key pair at ONAP deployment. Assume one key per Controller for all NFs for Casablanca.
Controller SSH username and public key provisioned in PNF | Casablanca | PNF Reqts | Controller username and public SSH key are provided to PNF out-of-band according to operator security procedures. PNF creates an SSH account for the username and stores the public key in the authorized_keys file. Note that for PNFs, this must be provided before PNF can receive the service configuration during PnP.
Controller SSH username and public key provisioned in VNF | Casablanca | VNF Reqts | Controller username and public SSH key are provided to VNF during instantiation. VNF creates an SSH account for the username and stores the public key in the authorized_keys file.
SSH key renewal process | El Alto | APPC, SDNC, VFC | Operators need a procedure to renew SSH keys due to (1) key has “expired” and (2) key has been compromised. Controllers need to be integrated into this process.
Note that SSH username and public key is not needed if CM uses Netconf/TLS and if instantiation uses a REST interface with TLS instead of Ansible/SSH.

## Slide 12
SFTP Security Bootstrapping Data
Security Function | Release | Impacted Projects | Comments
File Collector supports FTPeS for file upload | Casablanca | DCAE File Collector | Approved for R3. File Collector supports FTPeS client for file upload with certificate authentication.
File Collector supports SFTP for file upload | Casablanca | DCAE File Collector | Approved for R3. File Collector supports SFTP client for file upload with public key authentication.
NF supports FTPeS or SFTP for file upload | Casablanca | NF Reqts | NF supports either FTPeS server or SFTP server for file upload by File Collector.
File Collector creates RSA key pair for NF SFTP access | Casablanca | DCAE File Collector | Approved for R3. File Collector creates its SFTP RSA key pair at ONAP deployment. Assume one key per FC for all NFs for Casablanca.
File Collector SFTP username and public key provisioned in NF | Casablanca | NF Reqts | File Collector SFTP username and public key is configured in NF during NF service configuration. NF creates an SFTP account for the username and stores the public key in the authorized_keys file.
Note that SFTP username and public key is not needed if File Upload used FTPeS.