## Slide 1
SECURITY ENHANCEMENTS
FOR 5G USE CASE
5G Use Case A : Deployment
5G Use Case C : Optimization
Meeting Minutes Jul 26, 2018

## Slide 2
Casablanca 5G Use Cases with Security Impacts
5G Use Case A Deployment :
PNF Plug and Play (PnP) Registration
JSON encoded asynchronous PNF Registration event sent via HTTP/TLS from PNF to DCAE.
Configuration Management (CM)
SSH and possibly TLS from ONAP Controller to NF for CM and from ONAP M-VIM for LCM.
Ansible/SSH required for VNF Life Cycle Management (instantiation for example).
Ansible/SSH or NetConf/SSH or NetConf/TLS or Chef/SSH required for CM.
5G Use Case C Optimization :
Bulk Performance Measurements (PM)
JSON encoded asynchronous File Ready event sent via HTTP/TLS from NF to DCAE.
SFTP or FTPeS from ONAP File Collector to NF for Bulk PM file transfer.
Real Time Performance Measurements (RTPM)
GPB encoded asynchronous RTPM event streamed via TLS/TCP from NF to DCAE.
Fault Management (FM)
JSON encoded asynchronous Fault event sent via HTTP/TLS from NF to DCAE.

## Slide 3
Security capabilities needed in ONAP for Casablanca
HTTP
Recommend that ONAP eliminate username and password for HTTPS.
TLS
DCAE is able to authenticate Vendor or Service Provider X.509v3 certificate for TLS connection.
ONAP User is able to install Vendor Root CA certificate as trust anchor in ONAP.
ONAP supports 3 level chain; Root CA, Sub CA (RA) and End-Entity certificates.
Vendor is able to install Root CA certificate chain as trust anchor on NF for mutual TLS authentication.
CA
Provide CA services to NFs in ONAP for development and testing; PKCS#12, IAK/RV.
Support CMPv2 for NF for certificate enrollment in ONAP for development and testing.
Support integration with Service Provider CA/PKI in ONAP.
SSH/SFTP
Create RSA public/private key pair for ONAP Controllers for SSH access into the NF for CM and for File Collector for SFTP access into the NF for PM.
Provision SSH username/public key on NF for Ansible or NetConf or Chef access from ONAP Controllers for CM and SFTP from ONAP File Collector for Bulk PM.
Recommend that client should not accept username and password for SSH/SFTP authentication.
Impacted ONAP Projects: AAF, DCAE, Controllers, NF Requirements

## Slide 4
Meeting Minutes – May 17, 2018
Attendees
Pierre Close (AT&T)
Gunner Forssell (Ericsson)
Jonathan Gathman (AT&T)
Marge Hillis (Nokia)
Linda Horn (Nokia)
Samuli Kuusela (Ericsson)
Vesa Lehtovirta (Ericsson)
Zygmunt Lozinski (IBM)
Natacha Mach (Orange)
Gervais-Martial Ngueko (AT&T)
Pawel Pawlak (Orange)
Alex Salvarani (Nokia)
Randy Stricklin
Stephen Terrill (Ericsson)
Amy Zwarico (AT&T)
Apologies to those I missed or misspelled. Let me know and I can update the list.

## Slide 5
Discussion Points – May 17, 2018
General
Goal for these meetings is to identify:
  Assumptions that impact ONAP security capabilities and NF requirements
  Recommendations for the Security Subcommittee
  Requirements for ONAP and NFs
  Project impacts for Casablanca
HTTP
Agreed to the following Recommendations:
  ONAP shall not support username and password authentication for HTTPS; certificate authentication only.
  ONAP components and NFs shall support TLS for security of HTTP connections.
  ONAP shall not support HTTP for communications between ONAP components or between NFs and ONAP components, except for NF certificate enrollment over CMPv2.
CMPv2 uses HTTP and must be allowed for certificate enrollment.
Performance is no longer an issue and is not a valid excuse for not using TLS.
Project impacts: VNF Requirements, VES Listener document, DCAE

## Slide 6
Discussion Points – May 17, 2018
TLS
NF Authentication
  DCAE must be able to authenticate NF’s Vendor or Service Provider X.509v3 certificate for TLS connection.
    DCAE needs its own end-entity X.509v3 certificate.
    DCAE needs to use CADI to authentication the NF certificate.
    AI: Determine if DCAE already supports this or if there is work needed in Casablanca for this item. Status: In Progress Email sent to DCAE. DCAE is assessing impacts.
  Root CA certificate for the NF end-entity certificate must be installed in the DCAE trust store.
    This can be done manually if the Root CA certificate is not already part of the trust store.
    CADI can be used to manually install the Root CA certificate, but is not required.
    Instructions for installing Root CA certificates in the trust store must be provided. Some instructions are already available on the wiki.
    No work needed in Casablanca for this item.
  Sub CA certificate is not required in DCAE trust store.
    However, some Service Providers may choose to require this extra level of security in their own commercial deployments of ONAP, depending on their security policies. This topic is not for Casablanca.
    No work needed in Casablanca for this item.

## Slide 7
Discussion Points – May 17, 2018
TLS
NF Authorization
  CADI can be used for authorization after certificate is authenticated.
    A list of valid Sub CA Subject names can be provisioned in the DCAE trust store and CADI can verify that the NF end-entity certificate was signed by a valid Sub CA. This is optional.
  CADI may be too much overhead for NF authorization; it is not scalable to provision every NF instance and its permissions into CADI.
  Authorization of NF can be achieved via NF onboarding and service instantiation processes.
    This provides a list of VES events that the NF emits, NF instance ID, NF IP address and other information that is stored in AAI and can be used by DCAE to verify that the NF is authorized to send certain asynchronous events to DCAE. Are there DCAE impacts for this?
DCAE Authentication by NF
  NF must be able to authenticate the DCAE certificate for mutual TLS authentication.
  ONAP Root CA certificate must be installed as trust anchor on NF when the DCAE end-entity certificate is signed by ONAP CA.
    Root CA certificate can be manually pre-provisioned in NF before any TLS connection is set up.
    NF could accept the Root CA certificate one time the first time the TLS connection was set up; for example during Plug and Play of a PNF when the PNF Registration event is sent from the NF to DCAE. What happens when NF sends the PNF Registration event a second time?
  NF can configure TLS to accept a Root CA certificate the first time or not. Choice is left to the vendor and/or service provider, depending on its security policies.

## Slide 8
Discussion Points – May 17, 2018
CA
Assumptions
  ONAP CA is used to sign DCAE and NF end-entity certificates during development and testing.
  For commercial deployment, it is expected that each Service Provider has its own CA/PKI and the Service Provider Root CA/Sub CA is used to sign DCAE and NF end-entity certificates.
  3GPP compliant NFs use CMPv2 for certificate management; enrollment, key renewal.
SSH/SFTP
Authorization of ONAP access in NF
  How does the NF authorize the ONAP components (e.g. Controller) to ensure that the access is limited to allowed operations, directories, etc. inside the NF; for example, will LDAP be supported?
  Needs further discussion in a future meeting.

## Slide 9
Meeting Minutes – May 21, 2018
Attendees
Olaf Burdziakowski (Nokia)
Gunner Forssell (Ericsson)
Marge Hillis (Nokia)
Linda Horn (Nokia)
Thomas Ingemarsson (Ericsson)
Samuli Kuusela (Ericsson)
Alexander Pantus (Ericsson)
Alex Salvarani (Nokia)
Stephen Terrill (Ericsson)
Maciej Wejs (Nokia)
Amy Zwarico (AT&T)
Apologies to those I missed or misspelled. Let me know and I can update the list.

## Slide 10
Discussion Points – May 21, 2018
TLS
NF Authorization
  NF Authorization can be achieved via NF onboarding and service instantiation processes.
    A list of VES events that the NF emits is provided, NF instance ID, NF IP address and other information that is stored in AAI and can be used by DCAE to verify that the NF is authorized to send certain asynchronous events to DCAE.
  The typical way for DCAE to authorize ONAP users and components is via CADI.
    There is some concern that it is not scalable to manually provision every NF instance and its roles and permissions into CADI prior to the first NF TLS connection into ONAP.
    Can we provision NF roles, permissions and instances into AAF automatically at onboarding and service instantiation time?
      At onboarding, NF provides artifacts with list of events the NF emits. A role could be created in AAF per NF Type with permissions that include sending these VES events to DCAE. What projects are impacted for this; SDC, AAF?
      At instantiation, the unique NF instance ID becomes known. This “user” could be added to AAF and assigned to the role created at onboarding. SO workflow and/or DCAE would need to include updating AAF. What projects are impacted for this; AAF, SO, DCAE?
      What is the “user” for a NF? UUID? NF Name in AAI? Choice determines when CADI must be updated; e.g. instantiation, restart, SW upgrade.
    AI: AAF team to identify what information is needed for CADI to authorize a NF and what can be automated. Status: Closed Jul 12 Jonathan and Amy developed a proposal, available in slide deck on wiki. Further details still to be worked.

## Slide 11
Discussion Points – May 21, 2018
TLS
NF Authorization (continued)
  Could we use Pluggable Authentication to authorize NFs instead of CADI?
    CADI would be configured to point back to DCAE for authorization.
  Need to consider the complexity of the authorization solution to:
    DCAE
    Onboarding process
    Instantiation process
    Service Provider
  Need to consider the automation of the solution:
    We can not have manual steps at run time (during instantiation) and that is the first time ONAP knows the NF instance ID (user)
    We could tolerate manual steps at design time.
  Need to consider how we could phase the final “ideal” solution over time if it can’t all be completed in Casablanca.
    Identify some steps that make sense.

## Slide 12
Discussion Points – May 21, 2018
TLS
DCAE Authentication by NF
  NF must be able to authenticate the DCAE certificate for mutual TLS authentication.
  If DCAE and NF certificate are signed by the same CA (ONAP or Service Provider (SP) CA) then there is no problem.
  If NF certificate is signed by Vendor Factory CA and DCAE certificate is signed by ONAP/SP CA, then ONAP/SP Root CA certificate must be in NF trust store.
    ONAP/SP Root CA certificate can be manually pre-provisioned in NF before any TLS connection is set up. But this does not work for Plug and Play (PnP) of PNFs.
    NF could accept the Root CA certificate one time the first time the TLS connection was set up; for example during PNF PnP when the PNF Registration event is sent from the NF to DCAE.
      What happens when NF sends the PNF Registration event a second time? Is the Root CA certificate still valid?
      NF can configure TLS to accept a Root CA certificate the first time or not. Choice is left to the vendor and/or service provider, depending on its security policies.
  To avoid this situation, ONAP could require that NFs perform operator certificate enrollment before the first TLS connection.
  AI: Check SOL002 and SOL004 to see if this problem has already been solved. Status: Closed May 24 SOL002 and SOL004 do not address these kind of certificate issues.

## Slide 13
Discussion Points – May 21, 2018
SSH/SFTP
Authorization of ONAP access in NF
  How does the NF authorize the ONAP components (e.g. Controller) to ensure that the access is limited to allowed operations, directories, etc. inside the NF?
  LDAP is the 3GPP standard according to TS 33.310.
    Many Service Providers have LDAP systems in place.
  However, LDAP is difficult to manage and the world is moving away from it to simpler protocols.
    Consider HTTP Server as an alternative.
    3GPP standard needs to be updated and/or softened with regard to LDAP.
  VNF Requirements do not specify what protocols must be supported for Identity and Access Management (IDAM).
    AI: Propose protocols for IDAM to Amy Zwarico. Status: Closed May 24 LDAP and HTTP recommended. See details in May 24 meeting minutes.
    Consider what vendors and service providers currently support as well as where the industry is heading.
    LDAP should be one of the supported protocols to support legacy systems.

## Slide 14
Discussion Points – May 21, 2018
Certificate chaining
Recommend that ONAP components and NFs support 3 levels of certificate chaining; Root CA, Sub CA, End-entity. This is already supported in ONAP.
No work needed in Casablanca for this item.
VNF Certificates
Need a scenario specified for how and when VNFs get their certificates.
  Must happen before the first TLS connection.
  What is used as the CN? Choice of CN determines when a new certificate is needed.
    If it is UUID, then a new certificate is needed every time VNF is restarted or SW upgraded. Certificate enrollment must be part of instantiation.
    If it is VNF Name, then the certificate must be persistently stored over VNF restart and SW upgrade.

## Slide 15
Meeting Minutes – May 24, 2018
Attendees
Masoud Asadi (Ericsson)
Pierre Close (AT&T)
Gunner Forssell (Ericsson)
Jonathan Gathman (AT&T)
Marge Hillis (Nokia)
Linda Horn (Nokia)
Thomas Ingemarsson (Ericsson)
Samuli Kuusela (Ericsson)
Natacha Mach (Orange)
Jonathan Olsson (Ericsson)
Alex Salvarani (Nokia)
Kazi Wali Ullah (Ericsson)
Maciej Wejs (Nokia)
Amy Zwarico (AT&T)
Apologies to those I missed or misspelled. Let me know and I can update the list.

## Slide 16
Discussion Points – May 24, 2018
Recommended Protocols in NF for Identity and Access Management (IDAM).
  When certificates are used, LDAPv3 shall be supported as the primary method of authorization of a NF in ONAP.
  When certificates are used, HTTP shall be used as an alternative method of authorization of an NF when LDAP is not available.
  LDAPv3 format or HTTP format shall be used to access file repositories of TLS certificates.
  LDAPv3 and HTTP formats shall be supported for checking the revocation status of TLS certificates.
LDAP
  PROS
    3GPP standard according to TS 33.310
    Supported by all PKI products today
    Flexible
    Scalable
  CONS
    Complex
HTTP
  PROS
    Simple
    Low cost and maintenance
  CONS
    Not supported by all PKI products, although widely supported

## Slide 17
Discussion Points – May 24, 2018
Other Protocols to consider for Identity and Access Management (IDAM).
Should TACAS, TACAS+, DIAMETER, RADIUS protocols be considered?
  If authorization of ONAP Controller in NF uses the Controller certificate (e.g. TLS), these protocols are not an alternative to LDAP or HTTP because they don’t handle certificate functions such as revocation.
    Certificates optionally have Distribution Points (DPs) where an authenticator can check if a certificate has been revoked. DPs support LDAP and HTTP formats.
  If authorization of ONAP Controller in NF does not use Controller certificate (e.g. SSH), these protocols may be useful.
Provisioning SSH Public Keys in NF
Recommendations for SSH authentication:
  When SSH/SFTP is used, public key authentication shall be supported by NF to authenticate ONAP access; password authentication shall not be supported for SSH/SFTP access into the NF.
SSH is used for Configuration Management (CM) and Life Cycle Management (LCM) with NetConf, Ansible or Chef.
  For VNFs, SSH public keys are passed during instantiation.
  For PNFs, how are SSH public keys provisioned? There is a bootstrapping problem if SSH is used as the Configuration Management transport protocol. Possible provisioning options :
    Pass it during PnP in the DHCP response
    Provision it during PnP from the Initial EM (PnP Server)
    Provision it manually on-site during installation

## Slide 18
Discussion Points – May 24, 2018
Recommendations for NetConf transport protocol – TLS or SSH
  ONAP shall support both TLS and SSH as the transport protocol for NetConf.
  TLS shall be the preferred transport protocol for NetConf.
  How would the Controller know which to use for a NF? Recommendations:
    It shall be possible to specify the configuration management protocol supported by a NF at design time (NetConf/TLS, Netconf/SSH, Ansible/SSH or Chef/SSH).
    If a configuration management protocol is not specified for a NF, ONAP shall try NetConf/TLS first as the default.
      This is so Service Providers do not have to configure things which are default.
    As an option, ONAP Controllers could also try other CM protocols in some priority order if NetConf/TLS fails. This is left to the Controller designers to decide.
NetConf/TLS
  PROS
    Uses certificates for authentication; don’t need to provision SSH public key for CM; eliminates the bootstrapping problem.
  CONS
    Not widely used with NetConf now; may have trouble finding a third party NetConf product that supports TLS.
    Still have to solve the SSH public key provisioning problem for Ansible for LCM; but can use NetConf/TLS to configure the SSH public key for Ansible so no bootstrapping problem.

## Slide 19
Discussion Points – May 24, 2018
VNF Certificates
Need a scenario specified for how and when VNFs get their certificates.
  Must happen before the first TLS connection.
  Recommend that VNF certificate enrollment happens automatically as part of instantiation.
VNF Certificate Enrollment Options
  VNF SW image comes with a default certificate to use for enrollment. Rejected as not secure.
  Check SOL005. It has standards for generating keys and certificates for VNFs.
  One time password for VNF to use during enrollment. AI: Ericsson to present a proposal for this option on May 31. Status: Closed Ericsson presented on May 31 and presentation is posted to wiki.
  ONAP (potentially SO with the help of CertMan) generates a key pair, performs enrollment and installs a PKCS#12 bundle on the VNF. AI: AT&T to present a proposal for this option. Status: Closed Presentations given by AT&T (Amy) and Nokia (Linda) on Jun 7, 14, 28 and Jul 12. Further details still to be worked. Presentation available on wiki.
    Does SO have the authority to generate a key pair and perform cert enrollment for the VNF?
    How is the PKCS#12 installation done; what component, protocol, API is used?
What is used as the CN for a VNF? Choice of CN determines when a new certificate is needed.
    If it is UUID or some identity that changes for each instantiation, then a new certificate is needed every time VNF is restarted or SW upgraded. Certificate enrollment must be part of instantiation. This is ideal - simple.
    If it is VNF Name or some identity that is persistent when a VNF is re-instantiated, then the certificate must be persistently stored over VNF restart and SW upgrade. Not ideal - complex.

## Slide 20
Discussion Points – May 24, 2018
NF Authorization
  DCAE must ensure that NF is authorized to send VES events to DCAE. It is not enough to authenticate the NF certificate for the TLS connection.
  The typical way for DCAE to authorize ONAP users and components is via CADI.
    Recommend that NF roles, permissions and instances are provisioned into AAF automatically at onboarding and service instantiation time.
      At onboarding, NF provides artifacts with list of events the NF emits. A role could be created in AAF per NF Type with permissions that include sending these VES events to DCAE. What projects are impacted for this; SDC, AAF?
      At instantiation, the unique NF instance ID becomes known. This “user” could be added to AAF and assigned to the role created at onboarding. SO workflow and/or DCAE would need to include integration with AAF. What projects are impacted for this; AAF, SO, DCAE?
    What is the “user” for a NF? UUID? NF Name in AAI?
      Choice determines when AAF must be updated; e.g. instantiation, restart, SW upgrade.
      At each instantiation, create user and potentially roles and permissions.
      At each termination, remove user and potentially roles and permissions.
  AI: AT&T (Amy and Jonathan) to present a proposal at a future meeting. Closed Jul 12 Proposal presented on Jul 12. Further details to be worked. Presentation available on wiki.

## Slide 21
Meeting Minutes – May 31, 2018
Attendees
Masoud Asadi (Ericsson)
Pierre Close (AT&T)
Marge Hillis (Nokia)
Linda Horn (Nokia)
Thomas Ingemarsson (Ericsson)
Samuli Kuusela (Ericsson)
Vesa Lehtovirta (Ericsson)
Zygmunt Lozinski (IBM)
Henry Thorpe (AT&T)
Amy Zwarico (AT&T)
Apologies to those I missed or misspelled. Let me know and I can update the list.
Next Meeting Thu Jun 7, 2018 at UTC 13:00, Eastern 8:00

## Slide 22
Discussion Points – May 31, 2018
Ericsson presented a proposal for PNF and VNF certificate enrollment. See the presentation posted to the wiki for details. Next 2 slides contain a brief summary of the discussions.
PNF Certificate Enrollment
  Occurs during Plug and Play (PnP) and follows 3GPP TS 32.508.
  PNF uses its vendor certificate for identity, authentication and authorization to the CA. Vendor Root certificate must be pre-provisioned in the CA. This procedure is outside of ONAP (unless the CA is the ONAP CA used for development and testing).
  Should scenarios that occur outside of ONAP, but are needed for NF operation, be documented somewhere in ONAP? Examples: PNF PnP, certificate operations (enrollment, renewal, CRL)
ONAP CA certificate functions
  ONAP CA is only used for development and test; Service Provider CA is used for production.
  3GPP devices use CMPv2 for certificate operations to a CA.
  What certificate functions/protocols does the ONAP CA need to perform for NFs in the dev/test environment?
    enrollment via CMPv2 – would be nice to have
    CRL and renewal – maybe not necessary

## Slide 23
Discussion Points – May 31, 2018
VNF Certificate
  VNF Certificate Enrollment follows ETSI standards: SOL002, SOL003, SOL005, IFA006, IFA007.
  Two options supported.
  Option 1: PKCS#12 container can be installed on the VNF at instantiation time
    Out-of-band pre-provisioning with the CA is necessary to generate the PKCS#12 bundle before the VNF is instantiated.
    What is used as the identity in the certificate?
  Option 2: VNF can perform certificate enrollment with a One Time Password (OTP):
    The OTP, which is a Pre-Shared Key (PSK), is generated by the CA, along with a Reference Number (REFNUM) and provisioned on the VNF at instantiation.
    After instantiation, VNF performs certificate enrollment via CMPv2; VNF includes the REFNUM in the Certificate Signing Request (CSR); PSK is used to sign the CSR. See RFC4210 Appendix D.4.
    UUID can be used as the VNF identity in the certificate.
    Out-of-band pre-provisioning with the CA is necessary to generate the PSK and REFNUM before the VNF is instantiated. This is just one part of the larger network planning exercise that must be completed before a gNB is deployed.
Secure Boot
  3GPP NFs validate the SW running on the HW during startup.
  A trusted anchor, including the public key, is used to validate the signed SW.
  Only validated SW is allowed to run.
  Initial boot SW and all subsequent SW upgrades are validated.

## Slide 24
Meeting Minutes – Jun 7, 2018
Attendees
Masoud Asadi (Ericsson)
Olaf Burdziakowski (Nokia)
Pierre Close (AT&T)
Gunnar Forssell (Ericsson)
Jonathan Gathman (AT&T)
Linda Horn (Nokia)
Thomas Ingemarsson (Ericsson)
Tomasz Kaminski (Nokia)
Samuli Kuusela (Ericsson)
Donald Levy (AT&T)
Natacha Mach (Orange)
Alexander Pantus (Ericsson)
Pawel Pawlak (Orange)
Timo Perala (Nokia)
Stephen Terrill (Ericsson)
Henry Thorpe (AT&T)
Kazi Wali Ullah (Ericsson)
Jakub Zieba (Nokia)
Amy Zwarico (AT&T)
Apologies to those I missed or misspelled. Let me know and I can update the list.
Next Meeting Thu Jun 14, 2018 at UTC 13:00, Eastern 8:00

## Slide 25
Discussion Points – Jun 7, 2018
VNF Requirements
  The new security recommendations will generate new requirements on VNFs and PNFs and so the VNF Requirements document must be updated accordingly.
AAF Cert Man (see presentation on wiki)
  Phase 1 Set up authorization to request certificates
    Done ahead of time; perhaps during NF onboarding or during network planning.
    Done once per VNF Type.
  Phase 2 Request a certificate
    Done at VNF instantiation time.
    Done once per VNF Instance.
    Option 1 Slide 23: PKCS#12 file is created and installed in the VNF during instantiation.
    Option 2 Slide 23: Could also update CertMan to generate the PSK and REFNUM and install that during VNF instantiation. Then VNF would perform certificate enrollment with CA via CMPv2 after instantiation.
  Certificate Renewal
    CertMan runs a cron job to renew certificates. This is not necessary for RAN VNFs. They will autonomously trigger certificate renewal with the Service Provider CA via CMPv2.
  Next meeting – Amy Zwarico and Linda Horn to create a flow to show initial certificate enrollment for a VNF.

## Slide 26
Meeting Minutes – Jun 14, 2018
Attendees
Masoud Asadi (Ericsson)
Pasquale Borgonovo (Ericsson)
Olaf Burdziakowski (Nokia)
Youssef Chawki (Orange)
Pierre Close (AT&T)
Gunnar Forssell (Ericsson)
Jonathan Gathman (AT&T)
Linda Horn (Nokia)
Thomas Ingemarsson (Ericsson)
Tomasz Kaminski (Nokia)
Samuli Kuusela (Ericsson)
Donald Levy (AT&T)
Alexander Pantus (Ericsson)
Pawel Pawlak (Orange)
Kazi Wali Ullah (Ericsson)
Jakub Zieba (Nokia)
Amy Zwarico (AT&T)
Apologies to those I missed or misspelled. Let me know and I can update the list.
Next Meeting Thu Jun 28, 2018 at UTC 13:00, Eastern 8:00

## Slide 27
Discussion Points – Jun 14, 2018
There was a presentation on Initial Certificate Enrollment for VNFs given by Amy Zwarico (AT&T) and Linda Horn (Nokia). Presentation is called VNF Initial Certificate Enrollment v1 and is on the Secure Communications to Network Functions wiki page.
Discussion and comments:
  Why are we supporting Scenarios 1 and 2? We should only support Scenarios 3 and 4.
  What protocol/interface is used by M-VIM to pass security data to VNF during instantiation?
  PKCS#12 Creation, Slide 5, Step B9.8, VNF Authorizations
    This step to automatically create the authorizations for the VNF to send events to DCAE should be removed from the slide and a new slide should be created. This step is not related to certificate enrollment and so it is confusing to include it here. How the authorization is automatically created from the YAML file needs to be explicitly described in its own slide.
  Certificate Pool Creation, Slide 9:
    What identity is used for the certificates? How is this identity associated with the VNF when the certificate is allocated to the VNF? Does this become the VNF identity in AAI? Can UUIDs be created during this time for use in the certificates and then assigned during instantiation?
    When certificate pool is almost depleted, more certificates need to be obtained. How is this triggered? Who does it?
    There are a lot of issues associated with creating a certificate pool in advance, both logistical and security. Perhaps this option should not be supported. Instead, if the CA is not near real-time, the VNF receives a IAK and RV at instantiation and performs its own certificate enrollment after activation – Scenario 4. Scenario 4 needs to be developed. There is still the precondition to obtain a pool of IAK and RV from the CA in advance to pass to VNFs during instantiation.

## Slide 28
Discussion Points – Jun 14, 2018
Impacts to Projects (shown in red in the presentation) Reference is v1 of the slides.
Slide, Step | Description | Projects Impacted
3, Precondition 8, Precondition | AAF gets IAK and RV from CA | AAF
3, A1 8, A1 | VNF Controller is specified at Design Time | SDC
4, B4 10, B4 | SO populates Controller SSH key in VNF AAI entry | SO
4, B8 | SO triggers AAF to create security data | SO, AAF
5, B9 all | AAF obtains PKCS#12 bundle for VNF | AAF
5, B10 10, B10 | Security data is returned to SO | SO, AAF
6, B11 11, B11 | SO passes security data to M-VIM | SO, M-VIM
6, B12 | M-VIM passes security data to VNF at instantiation | M-VIM
6, B16 11, B16 | VNF installs PKCS#12 bundle | VNF Requirements
8, A2a | SDC triggers creation of certificate pool | SDC
9, A2a all | AAF creates certificate pool | AAF
9, A2a1, A2a10 | SDC triggers certificate pool creation and receives response when done | SDC, AAF
10, B8 | SO asks AAF for security data | SO, AAF
10, B9 | AAF retrieves certificate from secrets vault | AAF

## Slide 29
Meeting Minutes – Jun 28, 2018
Attendees
Masoud Asadi (Ericsson)
Olaf Burdziakowski (Nokia)
Youssef Chawki (Orange)
Pierre Close (AT&T)
Jonathan Gathman (AT&T)
Linda Horn (Nokia)
Samuli Kuusela (Ericsson)
Zygmunt Lozinski (IBM)
Kazi Wali Ullah (Ericsson)
Jing Ping (Nokia)
Ole Reinartz (Nokia)
Jakub Zieba (Nokia)
Amy Zwarico (AT&T)
Apologies to those I missed or misspelled. Let me know and I can update the list.
Next Meeting Thu Jul 12, 2018 at UTC 13:00, Eastern 8:00

## Slide 30
Discussion Points – Jun 28, 2018
We continued to discuss the presentation on Initial Certificate Enrollment for VNFs from Amy Zwarico (AT&T) and Linda Horn (Nokia).
Discussion and comments:
  We discussed Scenarios 3 and 4 where an Initial Authentication Key (IAK) and a Reference Value (RV) are used by the VNF for initial certificate enrollment.
  IAK is a one time use key. It is issued by the CA along with a RV which identifies the IAK to the CA when it is used.
  IAK is also sometimes called Pre-Shared Key (PSK) or One Time Password (OTP).
  During ONAP deployment, AAF should get its own certificate from the Operator CA so that is it able to act as a proxy for the VNFs to request PKCS#12 bundles and IAK/RV pairs during instantiation.
  The next two slides contain the problem statement and the ONAP options for initial VNF certificate enrollment . These slides were added to the presentation as an introduction.
An updated presentation called VNF Initial Certificate Enrollment v2 is on the Secure Communications to Network Functions wiki page. It has been updated based discussions during the meeting and to add some details to Scenarios 3 and 4 (however they are not yet complete).
At the next meeting, we will review Scenarios 3 and 4.

## Slide 31
When a VNF is instantiated, it needs a way to obtain a certificate from the operator’s CA that allows it to communicate with DCAE (via HTTP/TLS).
PNFs generally come with vendor certificates issued by the vendor’s factory CA that uses its serial number or MAC address as the identity. This allows an operator to pre-provision the vendor’s factory root certificate into its CA and even pre-provision the PNF identity to authorize the PNF to request a certificate.
This pre-provisioning is not possible for a VNF. A VNF has no vendor certificate and no fixed identity.
Two options are supported by 3GPP for VNFs using CMPv2 as described in RFC 4210.
Option 1: PKCS#12 bundle is installed on the VNF at instantiation time.
  A proxy entity performs Certificate Enrollment with the CA on behalf of the VNF to request a PKCS#12 bundle from the CA and this is installed in the VNF during or after instantiation.
Option 2: VNF performs certificate enrollment with a one time use Initial Authentication Key (IAK)
  A proxy entity requests an IAK and Reference Value (RV) from the CA on behalf of the VNF. The IAK and RV are provisioned on the VNF during or after instantiation.
  After instantiation and activation, VNF performs certificate enrollment with the CA via CMPv2 using the IAK to sign the Certificate Signing Request (CSR). The RV identifies the IAK to the CA.
In ONAP, AAF Cert Manager acts as the proxy for the VNF. As part of ONAP deployment, AAF Cert Manager obtains a certificate from the Operator CA which allows it to execute CMPv2 requests for VNFs.
In ONAP, VNF UUID can be used as the identity in the VNF certificate.
Current thinking is that ONAP should support both Options. Need to determine how ONAP knows which option a VNF supports.
Problem Statement

## Slide 32
There are 2 scenarios for each Option, depending on whether the Operator CA is near real-time or not.
Option#1: PKCS#12 bundle is installed on the VNF at instantiation time.
  Scenario #1: CA responds in near real-time to CMPv2 request from AAF Cert Mgr for PKCS#12.
    AAF Cert Mgr requests PKCS#12 bundle during the VNF instantiation process.
  Scenario #2: CA does not respond in near real-time to CMPv2 request from AAF Cert Mgr for PKCS#12.
    AAF Cert Mgr requests a pool of PKCS#12 bundles ahead of time and provides them to VNFs during the VNF instantiation process.
    Note: This is not a viable solution due to issues with VNF Identity. At the time when the PKCS#12 bundle is requested, we do not have the VNF identity (UUID). If we create a pool of UUIDs at that time, it is problematic to later associate these UUIDs with the VNF at instantiation.
Option 2: VNF performs certificate enrollment with a one time use Initial Authentication Key (IAK).
  Scenario #3: CA responds in near real-time to CMPv2 request from AAF Cert Mgr for IAK/RV.
    AAF Cert Mgr requests IAK/RV during the VNF instantiation process.
  Scenario #4: CA does not respond in near real-time to CMPv2 request from AAF Cert Mgr for IAK/RV.
    AAF Cert Mgr requests a pool of IAK/RV pairs ahead of time and provides them to VNFs during the VNF instantiation process. Storing and protecting these keys is a security concern.
Discussion is on-going about whether we should say that ONAP requires a near real-time CA, to avoid storing a pool of security data and for simplicity. In this case, only Scenarios #1 and #3 are supported.
Scenario #3 is preferred as it is the most secure.
ONAP Options for VNF Initial Certificate Enrollment

## Slide 33
Meeting Minutes – Jul 12, 2018
Attendees
Pasquale Borgonovo (Ericsson)
Olaf Burdziakowski (Nokia)
Pierre Close (AT&T)
Jonathan Gathman (AT&T)
Marge Hillis (Nokia)
Linda Horn (Nokia)
Tomasz Kaminski (Nokia)
Pawel Kasperkiewicz (Nokia)
Alexander Pantus (Ericsson)
Jing Ping (Nokia)
Kazi Wali Ullah (Ericsson)
Jakub Zieba (Nokia)
Amy Zwarico (AT&T)
Apologies to those I missed or misspelled. Let me know and I can update the list.
Next Meeting Thu Jul 19, 2018 at UTC 13:00, Eastern 8:00

## Slide 34
Option 2: VNF performs certificate enrollment with a one time use Initial Authentication Key (IAK).
  Scenario #3: CA responds in near real-time to CMPv2 request from AAF Cert Mgr for IAK/RV.
Proposal discussed AAF CertMan acting as the Registration Authority (RA) for the Operator CA.
  During ONAP deployment, AAF CertMan becomes RA to Operator CA. Impacts: AAF.
  During VNF instantiation, SO triggers AAF CertMan to request a IAK/RV on behalf of the VNF in near-real time. Impacts: SO, AAF.
  AI: Does CertMan have to support CMPv2 for this initial certificate enrollment or can it use a simpler protocol?
  AI: Will CertMan continue to act as RA during VNF normal operation? If so, what other CMPv2 operations need to be supported; e.g. key update, CRL?
Proposal also discussed AAF creating a role and permissions for each VNF Type at onboarding.
  During Design Time, SDC publishes a YAML artifact of NF Events to DMaaP (existing functionality). AAF subscribes. AAF creates a Role and Permissions for the VNF Type for the events in the YAML file. Impacts: AAF.
  During VNF Instantiation, SO populates VNF AAI entry with Controller SSH key and triggers AAF to add the VNF instance to the Role created at Design Time. Impacts: SO. AAF already has an API for this.
  During Run Time, when DCAE receives an event from a VNF, DCAE calls CADI to determine if the VNF is authorized to send the event. Impacts: DCAE. CADI already already has an API for this. DCAE is assessing integrating with CADI for Casablanca. DCAE uses Python and CDAI API is JAVA.
Discussion Points – Jul 12, 2018

## Slide 35
Notes:
  Public CAs like DigiCert can have an auto authentication portal set up to enable the real-time issuing of certs. This eliminates the need for Scenario #4 which is good news. Scenario #3 is the preferred option.
  CMPv2 will be added to the Microsoft CA that so many organizations use to create a private CA. This is also good news. Less work for ONAP developers to support 3GPP RAN VNFs.
  There is nothing in the PKI standards that requires that a subject name be associated with an IP address, so we can use UUID as the VNF subject.
    AI: TLS authentication may require an IP address or Host Name as Subject Name or Subject Alternative Name. TBD.
Discussion Points – Jul 12, 2018

## Slide 36
Meeting Minutes – Jul 19, 2018
Attendees
Pierre Close (AT&T)
Lukasz Grech (Nokia)
Tony Hansen (AT&T)
Linda Horn (Nokia)
Piotr Karas (Nokia)
Pawel Kasperkiewicz (Nokia)
Marek Kukulski (Nokia)
Donald Levy (AT&T)
Zygmunt Lozinski (IBM)
Jing Ping (Nokia)
Kazi Wali Ullah (Ericsson)
Jakub Zieba (Nokia)
Amy Zwarico (AT&T)
Apologies to those I missed or misspelled. Let me know and I can update the list.
Next Meeting Thu Jul 26, 2018 at UTC 13:00, Eastern 8:00

## Slide 37
We continued to discuss Scenario #3: CA responds in near real-time to CMPv2 request from AAF Cert Mgr for IAK/RV
  We walked through the scenario and made several refinements. Amy Zwarico will update the slide deck and post to the wiki. We will review this again at the next meeting.
  A Secure VNF Bootstrapping Protocol is specified in NFV-SEC 013 (section 7.6.4). We should compare the ONAP VNF instantiation procedure against this.
We briefly discussed the Common Name (CN) in the Subject of the certificate and the Subject Alternate Name (SAN).
  RFC 6125 recommends using a host name (FQDN) as the Subject Alternative Name for TLS authentication.
  We agreed to use FQDN for CN and SAN, instead of UUID as was initially proposed.
  We began discussions on how ONAP will know the FQDN to use for a VNF as it is configured by the Service Provider.
  FQDN can often be derived from the domain and other information known to ONAP. Currently DCAE uses the Designate Service from Openstack to assign a FQDN during deployment.
  For VNFs, we proposed that SDN-C could be the component that obtains the FQDN because it is the entity that assigns the IP address and this assignment happens before the VNF is instantiated, which is important for our scenario.
  FQDN must be provisioned in a DNS Server. We need to determine how/when this will occur.
  We should also discuss DNSSEC and whether this should be a recommendation to the Security Subcommittee.
Discussion Points – Jul 19, 2018

## Slide 38
Meeting Minutes – Jul 26, 2018
Attendees
Pierre Close (AT&T)
Anael Closson (AT&T)
Gunnar Forssell (Ericsson)
Linda Horn (Nokia)
Thomas Ingemarsson (Ericsson)
Pawel Kasperkiewicz (Nokia)
Tomasz Kaminski (Nokia)
Zygmunt Lozinski (IBM)
Natacha Mach (Orange)
Seshu Kumar Mudiganti (Huawei)
Pawel Pawlak (Nokia)
Maciej Wejs (Nokia)
Amy Zwarico (AT&T)
Apologies to those I missed or misspelled. Let me know and I can update the list.
Next Meeting Thu Aug 2, 2018 at UTC 13:00, Eastern 8:00

## Slide 39
We continued to discuss Scenario #3: CA responds in near real-time to CMPv2 request from AAF Cert Mgr for IAK/RV
  We walked through the scenario and made several refinements. Amy Zwarico will update the slide deck and post to the wiki. We will review this again at the next meeting.
Refinements
  We clarified the security data that should be passed to a VNF during instantiation: VNF IP address, VNF FQDN, Controller FQDN, Controller SSH Public Key, IAK, RV, CA Signing Chain, CA URL.
  We clarified where M-VIM gets the security data:
    Retrieved from AAI: VNF IP address, VNF FQDN, Controller FQDN, Controller SSH Public Key
    Passed by SO: IAK, RV, CA Signing Chain, CA URL
  Since IAK and RV are a one-time use, there is no reason to store it. Just keep in memory.
  VNF needs FQDN of Controller and CA signing chain at VNF instantiation to be able to authenticate the Controller certificate.
    This is needed if NetConf/TLS is used at the Service Configuration step.
    Controller can not authenticate the VNF certificate at this step because the VNF does not yet have a certificate. Authentication is one-way during VNF instantiation but that is OK.
Discussion Points – Jul 26, 2018