## Slide 1: 5G- RTPM For USE CASE Discussion July 16

## Slide 2: Real Time Performance Management Data Delivery to ONAP
Event driven high volume data delivery from xNF to ONAP/DCAE. A new VES-HV Collector will support GPB over TLS/TCP(committed). xNF will generate hvMeas events containing real time PM data. These events will be GPB encoded and transmitted over TLS/TCP. A new collector is needed as the existing collector supports REST/JSON only.
The collected events will be published to DMaaP and sent directly to the Kafka Cluster (not planning to use the DMaaP-MR.
PRESENTATIONS
PDF File Real Time PM--HV Event proposal to DCAE 5G Use Case Presentation.pdf June 13, 2018 by Marge Hillis
PDF File Optimization Use Case .pdf April 20 2018 by Marge Hillis

## Slide 3: Development Status Jira Tasks
Project | PTL | JIRA | Description
DCAE | Lusheng Ji | DCAEGEN2_565 | Enhance DCAE performance measurement (PM) data collection to support near real-time (order of seconds) data. Introduce a high-volume VES collector using a persistent connection (TCP socket), support a new data encoding (GPB).
 |  | DCAEGEN2-564 | Support VES Version 6.0 specification and new hvMeas domain (Dependency for us to finalize)
DMaaP | Ram Koya | DMAAP-525 | KAFKA AAF integration--dependency not part of our delivery (under investigation, not committed)
DMaaP |  | Discussing with DMaaP team 16 July | Publication of data directly from HV-VES collector to Kafka without using DMaaP message router (under investigation, whether we need a task or not---not committed?)
VNFRQTS | Steven Wright | VNFRQTS-268 | xNF requirements to support Real Time Performance Measurement collection from RAN NF using streaming connection (if needed)

## Slide 4
Kafka
High Volume flow and TC
DCAE HV
VES
Collector
Data Validation Simulator
PNF
VNF
4
Authenticate connection
1
Verify that data available in the Kafka topic can be decoded using the GPB and PM Dictionary and is equivalent to what the NF sent
Topic content validation
DCAE authenticates new TLS connection using functionality provided by AAF----DONE ONLY ONCE
NF sends PM data in real time—high volume data to DCAE HVES Collector TCP GPB for performance TLS for security if needed
Publish Event
DCAE sends event to DMaaP
DMaaP publishes data to topic
NF sends Real Time PM event and HV-VES Collector validates Event
NF initiates initial VES event and establishes connection. DCAE authenticates connection—connection is persistent so this is only done once. (TC: Verifying the connection can be established using TCP—assume that the AAF integration of security enhancements is covered by the Jira item doing this integration)
NF sends hvMeas Event to VES collector. Real Time PM sent with GPB schema. DCAE validates the VES event using the VES_Event.proto file (TC Verify that VES Collector can receive and validate the hvMeas event—success—event header and field population agrees with GPB and failure event does not agree with GPB specification) NOTE PAYLOAD DOES NOT HAVE TO BE DECODED FOR THIS TEST TO SUCCEED.
DCAE sends the event to DMaaP for publication. DMaaP publishes the data to a Kafka topic directly. (TC Verify that direct publication is done successfully to Kafka)
Retrieve data from Kafka topic decode and display measurements sent in the event. Use the VES_Event.proto file, the HvMeasFields.proto file and the PM Content Metadata to process the data. (TC : using PM Dictionary/e.g. PM Content Meta Data and proto file generated code to manually decode data.)
Additional recommended TCs: test multiple events reported to a HV-Collector in a short window—are there performance metrics that will indicate scale out needed?
TCP
TCP
Repeat for each event
2
3

## Slide 5: Test Cases
Flow Step | Test Case Description | Status | Comments
Authenticate Connection | Verifying the connection can be established using TCP | Not Tested | 
NF sends Real Time PM event and HV-VES Collector validates Event | Verify that VES Collector can receive and validate the hvMeas event—a) success—event header and field population agrees with GPB and b) failure event does not agree with GPB specification | Not Tested | 
Publish Event | Verify that direct publication is done successfully to Kafka) | Not Tested | 
Topic Content Validation | Using a simple analytics program subscribe to the RTPM topic and using PM Dictionary/e.g. PM Content Meta Data and proto file generated code decode the data and display | Not Tested | Displayed data should be compared to the original data the NF put in the event
Additional Test Case for Performance | Send Events rapidly to HV-VES Collector to assess any bottlenecks/areas needing scaling (HV-VES, Kafka etc) | Not Tested |