## Slide 1: ONAP – PNF Modeling Summary lixiang (China Mobile) Bianhongliang (China telecom) zhangmaopeng (ZTE), wangyaoguang (Huawei), Lishitao (Huawei)

## Slide 2: PNF model in R3
PNFD will use the existing definition in SDC AID
  Generic PNF: org.openecomp.resource.abstract.nodes.PNF
    nf_type: New generic type with the generic PNF properties. The properties in the generic PNF are.
    nf_role: String property defining a generic type (like category) of the PNF
    nf_function:String property for short code that defines a Network function that the Vendor Software or PNF is providing. E.g. vCE, vARM
Agreed to add SW version list in the PNF node type definition
Only for 5G use case

## Slide 3: Target model in ONAP (align with ETSI NFV)
PNFD Definition in ETSI-NFV-IFA014v243
Attribute | Qualifier | Cardinality | Content | Description
pnfdId | M | 1 | Identifier | Identifier of this Pnfd information element. It uniquely identifies the PNFD.
functionDescription | M | 1 | String | Describes the PNF function
provider | M | 1 | String | Identifies the provider of the PNFD.
version | M | 1 | Version | Identifies the version of the PNFD.
pnfdInvariantId | M | 1 | Identifier | Identifies a PNFD in a version independent manner. This attribute is invariant across versions of PNFD.
name | M | 1 | String | Provides the human readable name of the PNFD.
pnfExtCp | M | 1..N | PnfExtCpd | Specifies the characteristics of one or more connection points where to connect the PNF to a VL. See clause 6.6.4.
security | M | 0..1 | SecurityParameters | Provides a signature to prevent tampering.
geographicalLocationInfo | M | 0..1 | Not specified | It provides information about the geographical location (e.g. geographic coordinates or address of the building, etc.) of the PNF. The cardinality 0 is used when the location is unknown.
NOTE: The provider of the PNFD might be different from the provider of the PNF. |  |  |  | 
Table 6.6.2.2-1: Attributes of the Pnfd information element
PNF management in ETSI-NFV-IFA013v303
Attribute | Qualifier | Cardinality | Content | Description
pnfId | M | 1 | Identifier | Identifier of the PNF. Assigned by OSS and provided to NFVO.
pnfName | M | 1 | String | Human readable name of the PNF.
pnfdId | M | 1 | Identifier (Reference to Pnfd) | Identifier of (reference to) the PNFD related to this PNF.
pnfProfileId | M | 1 | Identifier (Reference to PnfProfile) | Identifier of (reference to) the PNF Profile to be used for this PNF.
cpData | M | 0..N | PnfExtCpData | Information on the external CP of the PNF.
Table 8.3.4.32.2-1: Attributes of the AddPnfData information element
AddPnfData is used when instantiating a NS
Contains the address (e.g. IP address) information of the CP.

## Slide 4: Future (R4+) work for PNF modeling
How to differentiate between PNFD and PNF
PNFD
PNF
1:1 or 1: many
PNF and VNF derived from the same parent NF node type
Main criteria:
1,Whether use of geographical parameter is described
2, vendor information
3, PNF instance registration and mapping procedure between PNFD and PND
Proposal from SDC (ATT),
Potential scenario: When Designing a NF used in a service, the NF can be whether VNF or PNF
Effect: ETSI NFV procedure

## Slide 5: Future (R4+) work for PNF modeling
PNF Package
  What will be included in the PNF package,
  Alarm information
PNF instantiation
  How to map PnfdId with PNF instance, two options:
  In PNF instantiation request, it contains the PnfdId
  From PNF registration
VES VS REST API
  Does PNF registration to DCAE is required
Controller selection
  Model driven
  Policy driven
  Hard-coded (Table driven)