## Slide 1: Enhancing ONAP Management for 5G RAN
CMCC-GCRC

## Slide 2
5G RAN side Management Planning based on ONAP
Research on the of O-RAN management with ONAP
  Research on the A1 data collection. Define the structure and content of the measurement data handled by VES. Define 5G RAN measurement data collection mechanism in DCAE
  Research on the Non-RT-RIC deployment in DCAE Analytic Platform
  Research on the end-to-end data processing procedure in ONAP. Define relevant Topic for Non-RT-RIC data. Analyze the affected blocks in ONAP. Define the data processing workflow
  Research on the enhancement of VF-C/APP-C/SDN-R. Enhance ONAP VF-C/APP-C/SDN-R for supporting Non-RT-RIC management. Define relevant IOC in VF-C/APP-C/SDN-R for Non-RT-RIC configuration
  Research on distributed ONAP deployment. Analyze the distributed ONAP architecture
Research on the 5G RAN sub-Network Slice management over RAN.
Introduce accelerator description in 5G RAN VNF template
Enhance the capability of ONAP to orchestrate and manage 5G RAN VNFs/PNFs

## Slide 3
Deploy O-RAN Intelligent Analysis Module in ONAP
O-RAN introduce the AI and Big Data tech in to TMN, realizing the intelligent RAN management
A large number of measurement data collected from every part of RAN, e.g. CU, DU, each interface and so on, and needed to be handled in management entity
O-RAN could take the advantage of ONAP to collect the measurement data and deploy analysis micro service in some specific ONAP components
Rationale
Non-RT RIC Deployed in ONAP
Non-Real Time RIC as the intelligent controller management the O-RAN
A1: btw RIC near-RT and RIC non-RT, ONAP
F1
NGFI-I/eCPRI
RAN DU: RLC/MAC/PHY-high
RAN RRU: PHY-low/RF
NFVI Platform: Virtualization layer and COTS platform
Orchestration & Automation (e.g. ONAP): MANO, NMS
Design
Inventory
Policy
Configuration
RAN Intelligent Controller (RIC) non-RT
E2 :btw RIC near-RT and CU/DU
CU-UP
CU-CP
SDAP
PDCP-U
RRC
PDCP-C
E1
Multi-RAT CU Protocol Stack
E2
Radio-Network Information Base
Applications Layer
Radio Connection Mgmt
Mobility
Mgmt
QoS
Mgmt.
Interference
Mgmt
3rd party APP
Trained Model
RAN Intelligent Controller (RIC) near-RT

## Slide 4
Deploy O-RAN Intelligent Analysis Module in ONAP
DCAE VES Controller collects PM/FM data/alarm from 5G RAN, and distributes Topic to Non-RT RIC
The Non-RT RIC handles the relevant Topic and may distribute a Topic for the specific configuration
5G RAN VF-C/APP-C/SDN-R handles the Topic about the Non-RT RIC, and configures the 5G RAN
Rationale
Non-RT RIC Deployed in ONAP
DU
CU
Analysis Plat form
VES Collector
DMaaP Bus Controller
Non-RT-RIC
DCAE
DMaaP
VF-C/APP-C/SDN-R
Non-RT-RIC Handler
Handle Non-RT-RIC configurations, management for 5G RAN
EM
A potential Non-RT RIC deployment solution
SDN-C
SDN-R
VF-C/APP-C
PNF Controller
1
2

## Slide 5
ONAP deployed near RAN side
To guarantee the end user service experience and improving the 5G RAN performance
To manage distributed 5G RAN equipment, ONAP needs a distributed deployment
Some of the ONAP components could be deployed near RAN side
Rationale
…
DMaaP
DCAE
VF-C/APP-C/SDN-R
Edge ONAP Components
CN
CU
DU
Backhaul
Fronthaul II
Fronthaul I
Intelligent App
e.g. N-RIC in O-RAN
DU
CU-CP, CU-UP
Provide an entire integration Orchestration & Management
solution for Distributed RAN
Deploy O-RAN Intelligent Analysis Module in ONAP
ONAP component e.g. DCAE, VF-C/APP-C/SDN-R … deployed near the RAN side for fine granularity management
User deploy MS for RAN PM optimization in edge DCAE
The edge DCAE interact with edge VF-C/APP-C/SDN-R through the edge DMaaP
The edge ONAP VF-C/APP-C/SDN-R manage the 5G RAN

## Slide 6
Enhancement for 5G RAN VNF and PNF Management
Management service exposed to ONAP
With the 5G TMN evolution, the concept of Management service could be introduced into ONAP
Management service producer could expose management capability to management service consumers
ONAP as a management service consumer could make use of the new concept to simplify the TMN Arch
To realize 5G RAN fine management by using the management service mechanism, the potential modules to be enhanced as follows:
. NE Modeling
. VF-C/APP-C/SDN-R
Function layer modeling
Resource layer modeling
The exposed Management Service could be consumed by ONAP
NF Management function
FM svc
CM svc
PM svc
NF Management function
FM svc
CM svc
PM svc
Management Service Exposure governance (e.g. encapsulation, filter etc)
NE
NE
ONAP DCAE (Analysis the FM/PM data)
SO Manage 5G RAN based on Policy
ONAP VF-C/APP-C/SDN-R consumes the MS exposed by 5G RAN
Enhanced 5G RAN Model
Rationale

## Slide 7
Virtualized 5G RAN Accelerator Management
Accelerator Management:
Modeling kinds of accelerators, e.g. vendor ID, Type, role number, supported algorithms
Programming and LCM for accelerators
Specified network transmission, such as lookaside and inline mode
In order to render the 5G RAN VNF energy efficiency, introducing accelerator is an effective solution
The abstraction of accelerator resources, accelerator modeling and the TOSCA are important contents of accelerator management research
In ONAP, the mature accelerator management solution will speed up the 5G RAN achievement
Rationale
QAT 8970
Netro nome
Smart NIC
FPGA
Hardware
Virtio-crypto
Hypervisor
VIRTIO ACC_LA
BackEndE
QAT plug-in
QAT driver
Openstack
GPU mgt
cyborg
Netronome mgt
QAT
mgt
ONAP
Accelerator Management with ONAP
To develop the accelerator adaptor layer, promoting NFV energy efficiency
VNF
VNF
MC
OPAE
NIC Driver
ZUC
1role
1role
FPGA API
VNF
FrontEnd

## Slide 8
5G RAN sub-Network Slice Management
5G RAN sub-Network Slice Management
Follow the progress of 3GPP for Network Slice definition, clearify the orchestration method for 5G RAN sub-Network Slice
Define 5G RAN sub-Network Slice model at ONAP, enhance 5G RAN equipment capability description and exposure to ONAP for orchestration
Real-time monitoring of the service quality on 5G RAN sub-Network Slicing, and improving the performance dynamically
Rationale
Configurable New Radios to meet specific RAT coverage demands
Explicit geographic coverage, Transmission and Reception points
Radio resource assignment, includes frequent, bandwidth, latency and etc
TRP
TRP
TRP
TRP
TRP
TRP
TRP
TRP
TRP
TRP
TRP
TRP
TRP
TRP
TRP
TRP
TRP
TRP
TRP
CU1
CU2
CU3
5G RAN sub Slice B
5G RAN sub Slice A
ONAP should satisfy such network slice requirements

## Slide 9
5G RAN Contributions to ONAP Casablanca
PNF Plug and Play
Change management
ONAP User/Service designer decides the targeted PNF software version to deploy a PNF with specific network function
PNF Software Version 1
PNF Software version2……n
5GDU
4GBBU
Multi-RAT Change scenario
SDC
Portal
Upgrade
PNFID, Target sw ver, RuleNameMap, Params
Onboard
PNF
SO
Operator
(e.g. VID, Timer)
APP-C
EM
Onboard
Change workflow
Rules, for each stage
Upgrade
PNFID, sw upgrade object
Target sw version, new sw version
RuleNameMap, specify rule name for each stage
Params, stage-related params for corresponding Rule (vendor specific)

## Slide 10
Vision of RAN orchestration with ONAP
CU
Vision of ONAP In RAN Orchestration
Adequate information models for RAN at ONAP, fulfill on-demand orchestration and intelligent management at RAN side
A complete Network Slice model definition at ONAP, Flexible orchestration management of RAN sub-Network Slice
Diversified deployment solutions and intelligent functionality integrating in ONAP, satisfying the management requirements for RAN
…
DCAE
VF-C/APP-C/SDN-R
DMaaP
ONAP Components
…
DCAE
VF-C/APP-C/SDN-R
DMaaP
ONAP Components
Edge

## Slide 11
Thank You!