## Slide 1
5G Use Cases for R4/Dublin
5G Use Case Subcommittee
Virtual Face to Face (December 10-12, 2018)
Dec 10, 2018 version 8
Benjamin Cheung, Vimal Begwani, et al

## Slide 2
PNF PRE-ONBOARDING/ONBOARDING U/C OVERVIEW
PNF
Descriptor
NF
Registration
Informational
Artifacts
Configuration
Files
Ansible
Playbook
SDC
Catalog
Onboarding
PNF
Onboarding
Package
+VENDOR
META DATA
SDC
Package
creation
xNF
SDK
Distribute
SO, AAI,
DCAE etc.
CSAR
Package
Dublin Priority
Dublin Priority
Package Delivery
Onboarding
Design Time
Run Time
Onboarding Package
NF Descriptor
Platform Model
NF Instance
1. PNF Package Delivery: Vendor creates & delivers PNF Package with PNF artifacts
1
3. PNF Onboarding package: Package loaded
3
2. PNF Pre-Onboarding: PNF-SDK ( ) to (create) PNF Onboarding Package & validates of PNF onboarding package
2
4. SDC: NF OB Package > SDC catalog
5. ONAP RT Components:
Ingest and use CSAR package
4
5
PM Dictionary
Schema (YAML)

## Slide 3
PNF PRE-ONBOARDING/ONBOARDING U/C IMPACTS
https://wiki.onap.org/pages/viewpage.action?pageId=45303641
RT COMPONENT | IMPACT | PTL
SDC | PNF package format Onboarding PNF package to internal PNF package mapping Onboarding PNFD to internal PNFD mapping Artifact management | Yes
Modelling | Definition of Platform Info & Data model | Yes
Resource Data Model | Onboarding PNFD to Platform PNFD mapping | Yes
VNF-SDK / PNF-SDK | Update to xNF-SDK and (create), parse, validation, of PNF Onboarding Package | TBR (to be reviewed)
SO, AAI, DCAE, Controller | Updates to RT components for proper ingestion of CSAR | TBR
PNF Onboarding Package | Vendor provided PNF onboarding package w/ PNF Registration and PNF-Descriptor. And ETSI SOL 001-007 Alignment | TBR
VNF Requirements | PNF requirements (in the VNF requirements projects) for PNF onboarding. (1) NF requirements updated to cover PNF package, descriptor and artifacts (2) VNF requirements could be reviewed. | TBR
This Use Case will introduce the support for PNF pre-onboarding (PNF Package, PNF descriptor support) and PNF onboarding (SDC, Design Time, PNF-SDK).
PNF Package delivery by vendor (during Pre-onboarding activities) and PNF Onboarding via SDC in Dublin.
U/C DESCRIPTION
Wiki
ONAP RT COMPONENT IMPACTS

## Slide 4
PNF Plug and Play U/C Overview
PNF
Contacts ONAP
PNF connects to ONAP via a Registration Event
PNF Registration Handler (PRH) processes the event
PNF
Activation
Connection points configured
Second part of PNF service instantiation
PNF configured and ready to provide service
PNF
Boot-strapping
PNF Powers up and Boot-straps
PNF performs a “Plug and Play” procedure
Equipment vendor proprietary steps
3
4
5
PNF Modeling
1
Run-Time (Instances)
PNF Instance
Declaration
2
Design Time
Resources Definition/Services Definition
SDC: PNF (physical element) Modeling
Distribution of types
18
17
20
19
22
21
16
15
26
25
28
27
30
29
31
36
35
37
39
40
41
42
34
38
PNF Infrastructure Service Declaration
First part of PNF instantiation
PNF A&AI Entry created

## Slide 5
PNF Plug and Play enhancements for R4 Dublin
https://wiki.onap.org/pages/viewpage.action?pageId=40206485
RT COMPONENT | IMPACT | PTL INVOLVEMENT
Controller to NF Type Association | Association of Controller to NF Type, so that SO knows which controller to use for a particular NF instance | TBR(to be reviewed)
AAF, DCAE (Collectors) | Security enhancements to use Certificates & TLS | TBR
Controller (VF-C, SDN-C/R) | Service configuration to PNF by controller (Step 37). SDN-C already supports DG & Ansible. NetConf introduction (separate U/C) | TBR
VID | VID enhancements for PNF PnP. Supporting Work Order. Supported with service specific applications. | TBR
A&AI | PNF Indexing using pnf-id (instead of pnf-name) | TBR
SO | Support of SO for an already existing PNF (active) A&AI Entry | TBR
ESR | Association to External Controller (EMS/NMS). | TBR
PRH | updates for A&AI adaptations & A&AI Entry < pnfRegistration | Reviewed
This Use Case will continue PNF Plug and Play development started in R3 Casablanca. Functionality that was started but not completed, and introduce some enhancements to improve Plug and Play operation.
U/C DESCRIPTION
Wiki
ONAP RT COMPONENT IMPACTS

## Slide 6
PNF S/W Upgrade

## Slide 7
PNF S/W Upgrade for R4 Dublin
https://wiki.onap.org/pages/viewpage.action?pageId=40206485
RT COMPONENT | IMPACT | PTL INVOLVEMENT
PNF Reporting | PNF sends information regarding its Software Version directly to ONAP through a VES event. | TBR
Design Time Components | PNF software update workflow design, artifact onboarding upgrade rule list, utility of software version list. | TBR
PNF Package Update | A software update may require a change in the PNF Package before the software update or post update or both. | TBR (to be reviewed)
Software Update Coverage Analysis | Find out what services, control loops, etc. are impacted during and post software update before the PNF software update | TBR
Post/Pre PNF SW Update Event Workflows | Deregistration, re-registration | TBR
VNF & PNF in-place software upgrade processes alignment | Unifying PNF and VNF entries in A&AI | TBR
VID support | Execute the E2E run time software upgrade workflow. | TBR
PNF Software upgrade is one aspect of Software Management. The purpose is to modify the software running on the PNF. This could be used to update the PNF software to a newer or older version of software.
U/C DESCRIPTION
Wiki
ONAP RT COMPONENT IMPACTS

## Slide 8
Perf3gpp Event Generation Overview
Bulk PM File Upload and Performance Event Generation
Network Function (NF) establishes a HTTP/TLS connection to the DCAE VES Collector.
NF sends FileReady notification Event to DCAE VES Collector. Event is encoded in JSON and sent via HTTP/TLS. HTTP/TLS connection is set up and torn down every time a FileReady notification event is sent.
DCAE VES Collector publishes the event to on DMaaP Message Router (MR).
DCAE File Collector retrieves the FileReady notification event from DMaaP MR.
File Collector uploads PM File from NF using a secure file transfer protocol; FTPES supported in Casablanca. NF authenticates the connection.
File Collector publishes PM Data to DMaaP Data Router (DR).
PM Mapper retrieves PM Data from DR and generates Perf3gpp events as configured by PM Mapper File.
PM Mapper publishes Perf3gpp events to MR.
Analytics Applications (AA) retrieve the Perf3gpp events of interest from MR. AA analyze the data to produce statistics and KPIs and optimization recommendations.
Bulk PM File Upload and Perf3gpp Event Generation
Data
Router
VES
Collector
Authenticate connection
HTTP/TLS
Upload PM file
Publish Event
HTTP/TLS
Send FileReady event
7
FTPES
Retrieve PM Data +metadata
Retrieve Event
Publish PM Data + metadata
Message
Router
VES
Collector
VNF
PNF
6
5
4
3
2
1
Publish Perf3gpp Event
Retrieve Perf3gpp Event
8
9
7
6
2
3
4
5
8
9
PM
Mapper
File
Collector
Analytics
Application
1

## Slide 9
Bulk PM Enhancements for Dublin R4
https://wiki.onap.org/pages/viewpage.action?pageId=40206494
RT COMPONENT | IMPACT | PTL INVOLVEMENT
DCAE | UC1 Perf3gpp event creation from PM XML file: implement 3GPP PM Mapper microservice, configure PM Mapper, subscribe to PM XML file and metadata from Data Router, generate Perf3gpp events, publish to Message Router | TBR
DCAE, Policy, Controller | UC2 Closed loop support using PM data: Analytics Applications subscribe to Perf3gpp event of interest or Bulk PM XML file, analyze the data, notify Policy of desired CM change, Policy triggers CM update to Controller. (Stretch Goal) | TBR
Data File Collector (DFC) | DFC robustness enhancements: FileReady for all files on the node, DFC retry handling. | TBR
DMaaP Data Router (DR) | DR enhanced handling of PM feeds: enhancements for DFC metadata, optional DR consumer specified feed encoding, high availability and scaling support. | TBR
Support the following work items for Bulk PM for 5G xNFs:
UC1: Perf3gpp event creation by 3GPP PM Mapper from Bulk PM XML file
UC2: Closed Loop support using 3GPP PM data (stretch goal)
Additional Requirements: DFC robustness enhancements, DMaaP DR enhancements
U/C DESCRIPTION
Wiki
ONAP RT COMPONENT IMPACTS

## Slide 10
FM Meta Data
SDC
Catalog
Onboarding
Policy
Designer
Add
Policies
DESIGN-TIME (SDC)
NF
Onboarding Package
Policy
Database
CSAR
Package
CLAMP
Designer
Add Control
Loops
DCAE
Design Studio
Define
Templates
P
P
Descriptor
YML Registration
Dublin (R4) Goal is to be able to view the onboarded FM Meta-Data (from the PNF onboarding package) in a GUI (either Policy Designer, CLAMP, DCAE DS).

## Slide 11
FM Meta Data
https://wiki.onap.org/pages/viewpage.action?pageId=40206485
RT COMPONENT | IMPACT | PTL INVOLVEMENT
VES Specifications | Review and finalize VES Event Listener Specification v7.1 and VES Event Registration Specification v3.2 | Yes
GUI Display of FM Meta Data | Display the FM Meta data in a GUI (either DCAE-DS, Policy GUI and/or SDC GUI) to allow an ONAP User to create Policies for handling alarms | TBR
VNF Requirements | Update to VNF requirements for FM Dictionary metadata artifact creation | TBR
Support the following work items for FM Meta Data for 5G xNFs:
Review and finalize VES Event Listener Specification v7.1 and VES Event Registration Specification v3.2 which contains the FM metadata format and content.
Onboard the FM metadata for an xNF as part of the VES Event Registration YAML file. Note: Processing of the FM meta data is covered the PNF Pre-onboarding & onboarding Use Case
Display the FM metadata in a GUI to allow an ONAP User to create Policies for handling alarms.
Update VNF Requirements for FM metadata artifact.
U/C DESCRIPTION
Wiki
ONAP RT COMPONENT IMPACTS

## Slide 12
PM Dictionary
SDC
Catalog
Onboarding
DESIGN-TIME (SDC)
PNF
Onboarding
Package
CSAR
Package
DCAE
Design Studio
Define
Templates
Descriptor
PM Dictionary (YAML)
Measurement
& Schema
Dublin (R4) Goal is to be able to view the onboarded PM Dictionary (from the PNF onboarding package) in a GUI (either SDC Service Designer or DCAE-DS).
Service
Designer
Define
Services

## Slide 13
PM Dictionary
https://wiki.onap.org/pages/viewpage.action?pageId=40206485
RT COMPONENT | IMPACT | PTL INVOLVEMENT
VES Specifications | Review and finalize VES Event Listener Specification v7.1 and VES Event Registration Specification v3.2 | Yes
GUI display of PM dictionary | Display the PM Dictionary in a GUI (either DCAE-DS or SDC-DS GUI) to allow an ONAP User to create PM Mapper configuration files for Perf3gpp event generation | TBR
VNF Requirements | Update to VNF requirements for PM Dictionary artifact creation | TBR
Support the following work items for PM Dictionary for 5G xNFs:
Review and finalize VES Event Listener Specification v7.1 and VES Event Registration Specification v3.2 which contains the PM Dictionary format and content.
Onboard the PM Dictionary for an xNF as a PM Dictionary YAML file. Note: Onboarding of the PM Dictionary artifact is covered under the PNF Onboarding Use Case.
Display the PM Dictionary in a GUI to allow an ONAP User to create PM Mapper configuration files for Perf3gpp event generation.
Update VNF Requirements for PM Dictionary artifact.
U/C DESCRIPTION
Wiki
ONAP RT COMPONENT IMPACTS

## Slide 14
Configuration with NetConf
NETCONF
Transport
Client
Server
- Authentication - Data integrity - Confidentiality
- Replay protection
Authenticated client identity passed to NETCONF layer for access control
NETCONF assumes that security is provided by the chosen transport protocol
NETCONF over SSH (RFC6242) is mandatory but other options have also been standardized
  NETCONF over TLS with mutual X.509 authentication (RFC7589)
ONAP security sub-committee has recommended use of NETCONF over TLS: Secure Communication to Network Functions

## Slide 15
Configuration with NetConf
https://wiki.onap.org/display/DW/5G+-+Configuration+with+NETCONF
RT COMPONENT | IMPACT | PTL INVOLVEMENT
APPC, SDN-C, CCSDK | Controller north-bound APIs and implementation GR API or LCM API, PNF support Self-service support for APIs in the configuration use cases: Possible to specify NETCONF/TLS in blueprint & YANG XML template Controller south-bound adapter NETCONF/TLS support, YANG 1.1 support, ODL-based? | TBR
SO, Policy | Investigate how to trigger configuration action | TBR
AAF | Investigate AAF impact for NETCONF over TLS Also discuss in SECCOM meeting | TBR (to be reviewed)
VNF Requirements | Update applicable xNF requirements | 
Proposed UC to focus on in Dublin for configuration with NETCONF:
Post-instantiation (triggered by SO), Including final configuration step (36/37) in the PNF PnP UC
Configuration modification (e g triggered by Policy)
Specific requirements on NETCONF support in ONAP:
Officially support both PNFs and VNFs for north-bound controller APIs in the use cases
Support for NETCONF over TLS (RFC7589), Support for YANG 1.1 (RFC7950) modules in addition to YANG 1.0
U/C DESCRIPTION
Wiki
ONAP RT COMPONENT IMPACTS

## Slide 16
OOF & PCI
DCAE
DCAE
PCI Handler MS
OOF
SDN-C*
Policy
Simulated RAN
~2000 Cells
Nbr_list, PCI values
2
5
6
1b
1c
Config Value
Change Notifn
(Netconf/Yang)
9
1d
1a
8
10
(*SDN-C work done
in SDN-R team)
4b
4a
Config Value Change
11
DMaaP Message
REST API
3a
7
ConfigDB
3b
FM/PM KPIs
SO
4c
DCAE Collector
(VES)
DCAE Database
FM/PM
1e
4d
PCI enhancements
ANR function
FM/PM Collector and Database
FM/PM Data
Query to allocate PCI for new cell (optional)

## Slide 17
OOF & PCI
https://wiki.onap.org/display/DW/OOF-PCI+Use+Case+-+Dublin+Release
RT COMPONENT | IMPACT | PTL INVOLVEMENT
OOF | SON Coordination, Optimization for ANR ANR Handler MS, RAN Simulator | Yes
SDN-R | Configuration Database Operational Database Configuration History | Yes
DCAE | Onboard PCI Handler MS to DCAE | ?
POLICY | Enhance the Policy functionality for Control Loop Coordination Implement 2 control loops for POC | Yes
AAI | Models & relationship between Config, Operational DB & AAI | ?
Carry-over Items From Casablanca:
Onboard PCI Handler MS to DCAE, and include in SDC Catalog
SDN-R use cases moved from Casablanca to Dublin
  SDNC-430: Modify RAN informational model and yang model for RAN
  SDNC-431: Implement config DB and REST API (SDN-R / OOF interface)
  SDNC-432: Interfacing SDN-R with Policy
  SDNC-432: Receive netconf notification from RAN, update configDB, and publish change on DMaaP
Enhancements:
Common RAN Information Model, Configuration Management, Controller Enhancements, SON Coordination
Optimization for ANR (closely coupled with PCI)
U/C DESCRIPTION
Wiki
ONAP RT COMPONENT IMPACTS

## Slide 18
Network Slicing
Design Time
Configuration templates are designed and distributed.
Service templates are designed and distributed
Run Time
Create E2E service instance
Determine VNF placement
Build required input for lower level service
Create resource service instance
Create networks
Instantiate VNF(s), applying Day-0 configuration
Configure instantiate VNF(s) with Day-1 configuration
Configure dependent PNF(s) &/ VNF(s) with Day-1 configuration
1
10
9
7
6
5
4
3
2
8

## Slide 19
Network Slicing
https://wiki.onap.org/pages/viewpage.action?pageId=38119661
RT COMPONENT | IMPACT | PTL INVOLVEMENT
SDC | Support the design and distribution of configuration templates Support the design of nested service templates (see ONAP Network Slice Modelling) Support the distribution of service templates | TBR
SO | Support orchestration of nested service templates Support integration with common functions for VNF placement decisions Support parameterization of configuration templates | TBR
A&AI | Evolve model to support NW Slicing aspects | TBR
Controllers | Support VNF Day-1 configuration Support VNF&PNF Day-n configuration | TBR
VID | Provide view of all available templates Provide means to trigger and monitor service instance creation and deletion Provide view of service instances and their dependencies | TBR
..Based on identified Use Cases for NW Slicing in Dublin Release.
First proposal outlines the scope of the identified use cases with ambition levels for each.
Use Case Scope and Ambition Levels
Following proposal focuses on flows for Use case 1, Ambition level 1.
Use Case 1 Ambition level 1
U/C DESCRIPTION
Wiki
ONAP RT COMPONENT IMPACTS

## Slide 20: Impact Matrix (Preliminary)
PNF Pre-onboarding & Onboarding |  |  |  |  |  |  |  |  |  |  |  | 
PNF Plug and Play |  |  |  |  |  |  |  |  |  |  |  | 
PNF SW Upgrade |  |  |  |  |  |  |  |  |  |  |  | 
Bulk PM |  |  |  |  |  |  |  |  |  |  |  | 
PM Dictionary |  |  |  |  |  |  |  |  |  |  |  | 
FM Meta Data |  |  |  |  |  |  |  |  |  |  |  | 
Configuration with NETCONF |  |  |  |  |  |  |  |  |  |  |  | 
OOF & PCI |  |  |  |  |  |  |  |  |  |  |  | 
Network Slicing |  |  |  |  |  |  |  |  |  |  |  | 
Policy/CLAMP
SDC
VID/Portal
SO
Controllers
DCAE
DMaaP
AAF
VNF SDK
VNF Reqs & VES Spec
AAI/ESR
Likely
Possible
OOF

## Slide 21: Controller Impacts and Questions
Background
  Several 5G sub-cases involve ONAP controllers and may require enhancements in R4/Dublin
  There are also some questions since Casablanca about role of the different controllers
Design-time
  Need tool alignment: CDT -> CDS? When?
  Blueprint format improvements: per service blueprints, PNF support, additional device protocols (e g NETCONF/TLS), follow API additions
Controller personas and instances
  Which personas will be defined in Dublin, how will clients like SO and Policy known which controller instance to use
Controller (north-bound) APIs
  Existing APIs (GR and LCM) don’t recognize PNF as valid target
  New model-driven “self-service API” also being added in Dublin (CCSDK)
  Config DB API for PCI
  Need to recommend APIs for some use cases: day 1/N configuration, Policy
Implementation features
  Configurable behavior (onboarded or self-service) supporting multiple protocols (Ansible and NETCONF), different vendors, VNFs and PNFs
  Common NETCONF south-bound adapter supporting NETCONF/TLS, YANG 1.1
  Configuration database
  Operational database