## Slide 1: FM Meta Data Content Proposal Nokia November 15, 2018

## Slide 2: Overview
Fault Events carry key information about a fault that is occurring
Additional Meta Data about the fault needs to be provided to help explain the fault and determine subsequent actions
  In legacy RAN products a fault dictionary or fault meta data file was provided by RAN vendors to fill this need
  Fields that described the meta data were not necessarily commonly defined across providers
In this proposal we identify the fields that a NF could provide and that the YAML registration event can include if the are not already provided in the fault event.
  Agree upon a common name for the fields and definition for the fields
  Identify which fields are mandatory and which are optional
Providing the information in the fault registration record obviates the need for a separate dictionary artifact to be provided

## Slide 3
FM Meta Data ALARM FIELDS
DEFINITION FIELD | Mandatory/Optional | DESCRIPTION
Alarm Id | O | Gives the Identifier for the alarm. This is also the Identifier that is used in the VES event so it can be used to associate the event with the definition entry.
Alarm Name | M | Alarm Name which will be used in the Event Name. Note this maps to the alarmCondition in the VES Fault Event in faultevent fields.
Event Type | O | Indicates the type of alarm. The types are: Communications Alarm, Processing Error Alarm, Environmental Alarm, Quality of Service Alarm, Equipment Alarm, Integrity Violation, Operational Violation, Physical Violation, Security Service or Mechanism Violation, or Time Domain Violation. Note this maps to the eventCategtory in the VES Fault Event in faultevent fields. (Mandatory in 3GPP)
Meaning of Alarm | M | Provides a descriptive meaning of the alarm condition. This is intended to be read by an operator to give an idea of what happened.
Effect of Alarm | M | Provides a description of the consequence of the alarm condition. When this alarm condition occurs. This is intended to be read by an operator to give a sense of the effects, consequences, and other impacted areas of the system.
Managed Object(s) | M | Managed object (MO) associated with this Alarm. Note this maps to the eventSourceType in the VES Fault Event in faultevent fields.
Probable Cause | O | Provides the probable cause qualifier for the alarm. Probable causes are found in 3GPP TS 32.111 Annex B drawn from ITU-T M.3100 and from ITU-T Recommendation X.721, X.733, and X.736
Probable Cause Number | O | Probable Cause Number the numeric value associated with the Probable Cause
Proposed Repair Actions | M | It indicates instructions for proposed repair actions. These are defined in ITU-T Recommendation X.733 clause 8.1.2.12. This is required already in the YAML registration record for a fault event.
Clearing Type | M | Indicates whether the alarm is automatically or manually cleared
Additional Text | O | This field contain further information on the alarm.
Associated Fault(s) | O | Indicates the associated faults that triggered this alarm. List of fault(s) associated with the alarm cross indexed against a vendor provided fault information.

## Slide 4
FM Meta Data--FAULT FIELDS
DEFINITION FIELD | Mandatory Optional | DESCRIPTION
Fault Id | O | Gives the Identifier for the alarm. This is also the Identifier that is used in the VES event so it can be used to associate the event with the definition entry.
Fault Name | O | Alarm Name which will be used in the Event Name. Note this maps to the probable cause in the VES Fault Event in faultevent fields.
Fault Description | O | Provides a descriptive meaning of the alarm condition. This is intended to be read by an operator to give an idea of what happened.
Managed Object(s) | O | Managed object (MO) associated with this Alarm. Note this maps to the eventSourceType in the VES Fault Event in faultevent fields.
Effect of Fault | O | Provides a description of the consequence of the alarm condition. When this alarm condition occurs. This is intended to be read by an operator to give a sense of the effects, consequences, and other impacted areas of the system.
Associated Alarm(s) | O | Indicates the associated faults that triggered this alarm. List of fault(s) associated with the alarm cross indexed against a vendor provided fault information.
Proposed Repair Actions | O | It indicates instructions for proposed repair actions. These are defined in ITU-T Recommendation X.733 clause 8.1.2.12.
Additional Text | O | This field contain further information on the alarm.
NOTE: Fault fields are optional as not all NF providers differentiate between faults and alarms. If a NF can raise an alarm due to multiple fault conditions then information on which fault caused the alarm must be provided.

## Slide 5: YAML Registration Proposal
NFs provide separate YAML registration records for each of the Fault Events they emit.
FM Meta Data particular to the specific event proposed to be included in the registration record
  Provides all of the meta data for the fault so separate fault/alarm dictionaries do not have to be provided by the NF provider
  YAML Registration provides a comment capability which the Registration processing can use to extract the meta data information for Policy creation.
  Example file follows

## Slide 6: YAML Registration Proposal
  # registration for Fault_Nokia_5gBTS_baseStationSynchronizationProblem
  # Constants: the values of version, domain, eventName, faultFieldsVersion,
  # Variables (to be supplied at runtime) include: eventId, eventSourceType faultId, lastEpochMicrosec,
  # reportingEntityName, sequence, sourceId, sourceName, startEpochMicrosec, eventSeverity,
  # specificProblem, timeZoneOffset, vfStatus, instructions, effect, btsName, cellName
  # Comments: information that is not required, that is constant for this alarm, that the NF WILL NOT
  # SEND IN THE EVENT AND CAN BE POPULATED PERMANENTLY FOR THE EVENT,
  # includes: alarmId, meaning, eventCategory - These are commented at the event level and can be used
  # to construct an alarm dictionary. Fault specific information is in the additional information fields,
  # mimicking the structure used in the measurement registration.
  event: {presence: required, action: {any, any, AlarmID 71xx RECO-contact Nokia technical support }, comment: “
  MEANING OF ALARM = A fault has occurred in the base station synchronization. For example: the base station reference clock signal is lost or is unstable/inaccurate, ….,
  EFFECT OF ALARM = The effect of the fault on the functioning of the network element depends on the fault id raised. See fault effect below in registration YAML,
  CLEARING TYPE = automatic
  ”,
  structure: {
  commonEventHeader: {presence: required, structure: {
  version: {presence: required, value: 3.0},
  domain: {presence: required, value: fault},
  eventName: {presence: required, value: Fault_5gBts_Nokia_baseStationSynchronizationProblem},
  eventId: {presence: required),
  sourceName: {presence: required},
  reportingEntityName: {presence: required
  priority: {presence: required},
  startEpochMicrosec: {presence: required},
  lastEpochMicrosec: {presence: required},
  timeZoneOffset: {presence: requiredl},
  sequence: {presence: required}
  }},
Provides capability to provide meta data at the event level

## Slide 7: YAML Registration Proposal
  faultFields: {presence: required, structure: {
  faultFieldsVersion: {presence: required, value: 3.0},
  eventCategory: {presence: optional, comment: “Quality of service”},
  alarmCondition: {presence: required, value: 'baseStationSynchronizationProblem'},
  eventSourceType: {presence: required},
  alarminterfaceA: {presence: required},
  specificProblem: {presence: required},
  eventSeverity: {presence: required},
  nfStatus: {default: Active},
  alarmAdditionalInformation: {presence: required, array: {
  keyValuePair: {presence: required, structure: {
  key: {presence: required, value: 'Fault ID'},
  value: {presence: required}},
  comment: “
  FAULT ID = 9,
  FAULT NAME = ‘BTS time not corrected’,
  FAULT DESCRIPTION = ‘The reference frequency that the BTS master clock receives has changed by about 200 ppb or more (which equals the change magnitude of 204 DAC steps or more (with 12bit DAC)) during the measurement period, compared to the BTS master clock frequency.
  Causes can be:
  1. The reference frequency …..
  2. The reference frequency fluctuates …’,
  EFFECT OF FAULT = ‘This fault does not immediately affect the operations of the BTS, but it is a notification …’,
  PROPOSED REPAIR ACTIONS = ‘access the ….follow the instructions below:
  1. In case of a fault in the transmission network synchronization, …
  2. If the basic accuracy of the signal used for synch is correct…
  3. In case of a BTS equipment fault, the location might be:
  4. After the fault situation has been cleared, ….’,
Provides capability to allow NF to provide meta data about each fault that raises an alarm where applicable.
Provides capability to set a default for an optional field

## Slide 8: YAML Registration Proposal
  FAULT ID= 1818,
  FAULT NAME = ‘BTS master clock tuning failure’,
  FAULT DESCRIPTON = ‘Master clock frequency is tuned to within 5% of its minimum or maximum tuning limit.’,
  EFFECT OF FAULT = ‘The BTS can operate properly for months ….
  Effects in Frequency Synchronization mode: …
  Effects in Phase Synchronization mode: ….’,
  PROPOSED REPAIR ACTIONS = ‘Perform the steps below in the listed order until the fault disappears.
  Not tracking satellites:
  1. The most common reason ….
  2. There might be a malfunction in the GPS receiver. Perform a (remote) power reset for the GPS receiver.
  3. There might be a HW fault in the GPS receiver. Check the operation and change the GPS module, if needed.’
  ”,
  keyValuePair: {presence: required, structure: {
  key: {presence: required, value: ' Identifying application additional information fields’},
  value: {presence: optional}
  keyValuePair: {presence: required, structure: {
  key: {presence: required, value: 'application additional information fields’},
  value: {presence: optional}
  }},
  additionalFields: {presence: required, keyValuePairString: {|, =, keyValuePairs: [
  keyValuePair: {presence: required, structure: {
  key: {presence: required, value: 'BTS name'},
  value: {presence: required}
  }},
  keyValuePair: {presence: optional, structure: {
  key: {presence: required, value: 'Cell name'},
  value: {presence: required}
  }}
  ]}}
  }}
  }}

## Slide 9
Backup

## Slide 10
Fault Event Example Common Header Content
Field | Type | Required | Description
version | string | Yes | Version of the event header (currently: 4.0.1) 4.0.1
eventName | string | Yes | Fault_nfType_NFVendor_AlarmName, where nfType is defined by the NF provider e.g. 5gCu, 5gBts etc. and AlarmName is the name of the Nokia alarm being raised.--example Fault_gnb-Nokia_BaseStationSynchronizationProblem
domain | enum | Yes | Event domain enumeration: ‘fault’, ‘heartbeat’, ‘measurement’, ‘mobileFlow’, ‘other’, ‘pnfRegistration’, ‘sipSignaling’, ‘stateChange’, syslog’, thresholdCrossingAlert’, voiceQuality, ’fault’
eventId | string | Yes | Event key that is unique to the event source faultyyyyyy where fault is the domain and we increment the eventid for each unique occurrence of an alarm—helps ONAP determine if a fault event is missed. Do NOT INCREMENT THE FAULT ID for subsequent reporting of the same fault or even for the clearing of the fault—only increment if there is a new occurrence. If nf reboots go back to 0 so the first fault is fault000001
eventType | string | No | Not used
nfcNamingCode | string | No | Network function component type: 3 characters (aligned with vfc naming standards) Not used
nfNamingCode | string | No | Network function type: 4 characters (aligned with vnf naming standards) Not used
sourceId | bytes | No | UUID identifying the entity experiencing the event issue (note: the AT&T internal enrichment process shall ensure that this field is populated) Not used
sourceName | string | Yes | Name of the entity experiencing the event issue NF Name(pnf-name or vnf-name ) as entered in A&AI uniquely identifying this instance of the NF Nokserial number of the pnf for example--TBD
reportingEntityId | bytes | No | UUID identifying the entity reporting the event, for example an OAM VM (note: the AT&T internal enrichment process shall ensure that this field is populated) Not Used
reportingEntityName | string | Yes | Name of the entity reporting the event, for example, an EMS name. May be the same as the sourceName. For synthetic events generated by DCAE, it is the name of the app generating the event. NF name (pnf-name or vnf-name in A&AI ) TBD
priority | enum | Yes | Processing priority enumeration: is High, Medium, Normal, Low’ Priority is based on alarmSeverity-Critical is High, major is Medium, Cleared is Normal, Minor/Warning is Low Medium
startEpochMicrosec | number (uint64) | Yes | the earliest unix time aka epoch time associated with the event from any component--as microseconds elapsed since 1 Jan 1970 not including leap seconds This is always the same value and that is the first observation time that was reported until alarm is cleared. 13172659790000000
lastEpochMicrosec | number (uint64) | Yes | the latest unix time aka epoch time associated with the event from any component--as microseconds elapsed since 1 Jan 1970 not including leap seconds When raised set to same time as startEpochMicrosec, if this is raised multiple times or periodically it’s the current time, if its cleared it’s the time it was cleared. 13172659790000000
timeZoneOffset | string | No | Offset to GMT to indicate local time zone for device +06:00
sequence | number (uint32) | Yes | Ordering of events communicated by an event source instance (or 0 if not needed) 1 when initially occurs Integer incremented when same fault occurrence reported until a clear is sent. The clear will be the last occurrence to increment the sequence number. After a clear the sequence number is reset to 1. 1
vesEventListenerVersion | String | Yes | Version of the VesEvent Listener 7.0.1
fault event input in red

## Slide 11
fault Event faultFields example
Field Name | Rqd | Format | Format Example | Field Description
faultFieldsVersion | M | number | 4.0 | version of the faultFields block
additionalFields | O | hashMap | btsName BTS5gNokiaBts2018 | Additional Information
eventSeverity | M | String | MAJOR | Event severity or priority. NORMAL severity reflects the event condition is back to Normal, or has Cleared.
eventSourceType | M | string | ASIK | Managed Object raising the alarm
eventCategory | O | string | qualityofServiceAlarm | Event category, for example: ‘license’, ‘link’, ‘routing’, ‘security’, ‘signaling’
alarmCondition | M | string | baseStationSynchronizationProblem | Short name of the alarm/problem, like trap name. Could be of SPECIFIC_PROBLEM list: (x733_SpecificProblems). Should be string to avoid duplicate dictionary translation. This should be a one word.
specificProblem | M | string | ppsReferenceMissing | Indicates the Alarm Condition as reported by the device, Should be string to avoid duplicate dictionary translation. This would be a fault description.
nfStatus | M | string | Active | Used to report on VF status, both to indicate success/failure of start/stop/prepare to terminate events, but also to allow VF to request termination after unrecoverable errors. Enumeration; valid values are - Idle - Active - Preparing to terminate '- Ready to terminate - Requesting termination

## Slide 12
fault Event faultFields example continued
Field Name | Req/Opt | Format | Format Example | Field Description
alarmInterfaceA | O | String Field [ ] | RAP-1/ASIK-1 | Provide port or channel or interface information when alarm is related with interface faults. Could be card/port, or channel, or interface name. -could reflect ManagedObject data
alarmAdditionalInformation | O | String Field [ ] | faultId, 18xx; alarmId, 71xx | Additional Information related to Alarm, such as Repair Action, Remedy code….May by serialized alarm payload: varbind list, original syslog message, notification parameters, etc. when event is generated via other means, should provide raw detail out of element. -