## Slide 1: Allotted Resources, Nested/Recursive Service Orchestration, and 5G Slicing
Gil Bullard – AT&T
Seshu Kumar - Huawei
October 30, 2018

## Slide 2: Allotted Resources
The Allotted Resource (a.k.a., Allotted Network Function, or ANF) is a useful construct for ONAP support of many Services, including vCPE and MPLS VPN.
In addition, the current thinking is that ONAP support of 5G “Slicing” could best be realized using the Allotted Resource construct in its modeling
Therefore, in order for ONAP to support 5G Slicing (and many other Services) in a model-driven manner, ONAP must support ANFs in a model-driven manner
An ANF is “instantiated” through applying application level configuration data to an underlying “multi-tenant” VNF/PNF. Thus, an ANF “descriptor” would capture the application configuration pattern that ONAP must apply to a “multi-tenant” VNF/PNF.
Therefore, in order to support ANFs in a model-driven manner, ONAP must support VNF/PNF configuration in a model driven manner

## Slide 3: Network Functions as a Service Versus Allotment Thereof
Service_X
Service_A
Service_Z
Service Used as a Network Function
Allotment of a Service Used as a Network Function
In this case, an instance of Service_A consumes an entire instance of Service_X. Instances of VNFs A1, A2, etc are chained with instances of VNFs X1 and X2 directly.
Service_A instantiation results in instantiation of Service_X in the same manner as if Service_X were instantiated through VID
VNF A1
VNF A2
Service_B
VNF B1
VNF B2
VNF X1
VNF X2
VNF Z1
VNF Z2
In this case, an instance of Service_B needs ONAP to instantiate (what appears to Service_B as) a Network Function (ANF) provided by a Service_Z instance, resulting in ONAP Service_Z processing to apply the appropriate configuration to VNFs Z1 and Z2.
Instances of VNFs B1, B2, etc are chained with this “Network Function” collectively offered by VNFs Z1 and Z2.
Service_B instantiation results in instantiation of this ANF NF provided by Service_Z. This is different from instantiation of Service_Z itself.
A single instance of Service_Z can support many instances of Service_B, as well as other Services that use this same NF type (ANF_Z).
ONAP Client
Service_X Instantiation
Is Comprised Of
Service_Z Instantiation
AllottedNetworkFunction_Z Instantiation
ANF_Z
Service_A Instantiation
Service_B Instantiation
ONAP Client
Service_X Instantiation

## Slide 4: Need to Advance ONAP Capabilities with Respect to ANFs
Allotted Resources are not a new concept to ONAP, in fact they were used in Amsterdam as part of the vCPE use case
However, whereas ONAP instantiation orchestration of Services comprised of VNFs and PNFs is “generic” and model driven in Casablanca (except for “configuration”), for ANFs custom sub-flows are needed
Given its criticality for ONAP support of many key Services including 5G Slicing, we should start working on ONAP model-driven support of ANFs in the ONAP Dublin timeframe
VNF
PNF
ANF
Network Function

## Slide 5: Nested Services and 5G Slicing
3GPP documentation assumes that 5G Slices will be administered as shared “Slice Segments” that can be “chained” together into end to end “Slices”
By “shared” it is meant that a single “Slice Segment” instance can serve multiple end to end “Slice” instances
This can be understood as each end to end “Slice” instance believes it is getting its own Network Function from some underlying “Slice Segment” instance
In modeling terms, the end to end “Slice” (modeled as a Service) has a Network Function (an ANF) “provided by” an underlying “Slice Segment” (also modeled as a Service)
Thus, the current thinking is that ONAP support for 5G slicing will require ONAP support of “Nested” Services

## Slide 6: 5G Slicing Nested Services
DU_Infra_Slice (ANF)
DU (PNF)
CU-CP
(VNF)
CU_Infra_Slice (ANF)
Video_RAN_NSS Service
Build
DU_Slice_Capability
CU_Slice_Capability
Create Slice (Purple Thing)
Build
DU_Infra Svc
CU-CP_Infra Svc
Build
Create Slice (Purple Thing)
Build
Build
Create Slice (Purple Thing)
Telemedicine_NS_Service
Build
Create Slice (Purple Thing)
Video_RAN_NSS_Slice (ANF)
DU_Slice_Capability
Build
Video_Core_NSS Service
Build
Create Slice (Purple Thing)
Video_Core_NSS_Slice (ANF)
DU_Slice_Capability
Build
Core Infra Services, VNFs and ANFs
In the target it is possible that ONAP will instantiate some “shared” (infrastructure) core VNFs “on demand” as needed during instantiation of specific Network Slices and/or Network Slice Segments.

## Slide 7: Prioritized Major Work Activities Proposed for Dublin
In order to start building model-driven runtime behavior in ONAP, we need a stable model to build on. So the modeling team should immediately begin working on finalizing the model of ANFs so that it is ready for the Component teams to start building on in the Dublin timeframe.
Because an ANF is instantiated through applying an application-level configuration pattern to an underlying Service’s VNF/PNF, the most critical ONAP runtime functionality needed is to support model-driven configuration of VNFs and PNFs.
The various ONAP components should use the above foundation to build out their model-driven ANF instantiation functionality. In this timeframe, the ONAP components can make simplifying assumptions such that ONAP will support instantiation of ANFs only if :
  The “Providing Service” of the ANF is comprised of:
    Only a single Network Function that is
    Either a VNF or a PNF
  ONAP finds an existing “Providing Service” instance that has capacity to meet the requirements of this instantiation.

## Slide 8: Extensions in El Alto and Frankfurt
El Alto
Relax the Dublin simplifying assumption such that ONAP will support instantiation of ANFs even if the “Providing Service” of the ANF is comprised of:
  Multiple Network Functions that can be any combination of
  VNF, PNF or ANF
Frankfurt
Relax the Dublin and El Alto simplifying assumption such that, if ONAP does not find an existing “Providing Service” instance, that it can now instantiate a “Providing Service” instance “on demand” (policy driven).