## Slide 1: ONAP TOSCA Driven Orchestration

## Slide 2: Terminology

## Slide 3: Terminology

## Slide 4: Orchestrator Functional Internal View
Key
OE-x
OI-x
SO External API
SO Internal API
APIs labeled on slide relative to SO for reference only.
SO-SO communication across ONAP instances looks like an External API.
OE-8
Orch Execution Engine (BPMN/TOSCA)
Data Store
Request DB
Multi-Cloud
Orch Service & Resource
Catalog
Request
Handler
Store
Request
Select Recipe
Track
Requests
BPMN DB
SDN Controller
Generic NF Controller
Map Request Data to Recipe & Invoke BPEL Execution
Resource
Models
Service Models
Orchestrator
Resource/Controller Adapters
API Handler
Infrastructure/Network Adapter
Select Adapter Template
Map Data to Template
Execute Transaction
Controller Adapter
Service Level
OE-2
OE-1
OE-3
OE-5
OE-6
OE-7
OE-9
OE-10a
OE-10b
OI-11
OI-12
OI-5
OI-6
Micro Services Bus / Data Movement
Dashboard OA&M
OE-4
OE-11
External API
Service Design & Creation
Micro Services Bus / Data Movement
OI-7
OI-8
OI-2
OI-3
OI-10
SDC Distribution Client
OI-1
Active & Available Inventory
External Registry
ONAP Optimization Framework
Data Collection, Analytics, and Events
Event Correlation
SO-SO communication within a single ONAP instance is via Micro Services Bus.
Controller functions common to both SDN-C and Generic NF Controller (OE-10a for LCM, OE-10b for App Configuration). Note that these may actually be separate APIs for SDNC and GenNFC
Allotted Resources case
Complex Services case
Controller functions specific only to SDN-C. E.g., “Assign Network Resources” for the VNFs in a L4+ Service.
OI-9
OI-4
OI-13
OI-14
Resource Level Orch
Asgn
Actv
SDNC
Common
Scale
OI-15
OI-16
LCM

## Slide 5: Layers of TOSCA Orchestration (Original Approach)
Service Level Orchestration
Instantiate
Service_Request
Resource Level Orchestration
Cloud Workload Level Orchestration
MultiVIM
Service Service Template
Build
VF Module Service Template
Assign
Request
Build
ANF Service Template
Build
PNF Service Template
Build
Network Service Template
Build
VNF Service Template
Build
SO

## Slide 6: High Level TOSCA Organization (Original Approach)
Service Service Template
Build (inputs)
VNF
Network
VF Module
Build (inputs)
Service Template
PNF
Build (inputs)
Service Template
Allotted Resource
Build (inputs)
Service Template
Build (Inputs)
Service Template
Assign (inputs)
Request (inputs)
Build (inputs)
Service Template

## Slide 7: Major TOSCA Orchestration Gaps - (Original Approach)
Conversion from onboarding to runtime model needs work
The sequencing of Node Templates within a Topology Template is not based on Requirements/Capabilities between the Nodes, but rather based on hard-coded heuristics or properties. Need to fix this.
Lifecycle operations should be modeled in TOSCA, including the inputs and outputs of those operations.
The inventorying of object instance attributes should be driven from TOSCA attributes

## Slide 8: Level of Abstraction in VNF Model that Drives ONAP “Assign”
vVNF
“vVNF” VNF Model
VM1
VM2
VMA
“Base VDU”
extdataplane_net_id
extoam_net_id
VMBn
VMBn+1
“Add-On VDU”
intdataplane_net_id
extoam_net_id
0..8
Each vVNF instance is comprised of 2-18 VMB backend server VNFs.
“Reachability” requirements, such as L2/L3, Dynamic address assignment, SRIOV, etc. are captured as attributes of the connections.
Virtual Host requirements, such as NUMA, Rack Level Anti-Affinity/Affinity Grouping, etc. are captured as attributes of the VMs.
Attributes:
Bandwidth=200mbps

## Slide 9: VF Module Modeling (Original and Current Approach)
Topology Template
Node Types
Relationship Types
Plans
VF Module Service Template
NodeType: Standard “tosca.nodes”
  Properties
    Standard TOSCA properties
  Interfaces
    Standard “tosca.interfaces”
RelationshipType: Standard “tosca.relationships”
  Properties
    Standard TOSCA properties
  Interfaces
    Standard “tosca.interfaces”
Each Node in the VF Module Topology Template is of a standard TOSCA node type. The relationships between these Nodes are standard TOSCA relationships. ONAP would be the Orchestrator for the “Assign” and “Request” Plans. “Assign” would cause the Orchestrator to call SDNC to make assignments, “Request” would cause Orchestrator to retrieve those assignments and map into the input params of the Service Template to send to MultiVIM.
The Orchestrator for the other Plans (such as the “Build” Plan) can be a standard off-the-shelf TOSCA orchestrator. However, this orchestrator should be within the “separation of concerns” space of the Cloud Provider, and not the responsibility of ONAP. However, ONAP would be responsible for providing the Input parameter values to the Cloud Provider with the Plan request (e.g., Build).
Inputs:
The inputs to a VF Module Topology Template would be comprised of basically the same sort of parameters that one would expect to find in a HEAT ENV.
Assign_VFMod
Request_VFMod
Other, standard TOSCA Plans (e.g., Build)

## Slide 10: VNF Modeling (Original Approach)
Topology Template
Node Types
Relationship Types
Plans
VNF Service Template
NodeType: VF Module
  Properties
    ScalingAspect
    MaxScaleLevel
Depends On
Each Node in the VNF Topology Template is of Node Type “VF Module”. These VF Modules have “Depends On” relationships between them. The Orchestrator determines the order in which to Request VF Modules based on the relationships, and not based upon any specific “Base” versus “Add-On” property. Because a VNF can have different “scaling aspects”, these relationships may need to be “scaling aspect” specific. (Not if we assume each VF Module appears in only a single “scaling aspect”.)
VF Module Service Template
Assign
Request
Need to work through how to model a “Scaling Level”.
Inputs:
The inputs to a VNF Topology Template are those required for the VNF-level Orchestration Plans.
Build_VNF

## Slide 11: Service Modeling (Original Approach)
Topology Template
Node Types
Relationship Types
Plans
Service Service Template
NodeType: VNF
  Properties
    InitialScaleLevel
NodeType: PNF
NodeType: AllottedResource
NodeType: Network
Depends On
Each Node in the Service Topology Template is of Node Type “VNF”, “PNF”, “AllottedResource”, or “Network”. These Nodes have “Depends On” relationships between them. The Orchestrator determines the order in which to deploy a Node based on the relationships. Because the sequencing of the Node “Assign” may need to be different than Node “Create”, these relationships may need to be Plan specific.
Build_Svc
Inputs:
The inputs to a Service Topology Template are those required for the Service-level Orchestration Plans.
VNF Service Template
Build
PNF Service Template
Build
AllottedResource Service Template
Build
Network Service Template
Build

## Slide 12: Service Level TOSCA Orchestration: “Build Plan” (Original Approach)
Create service-instance object in A&AI, orchestration-status = Inventoried
Call SDN-C Assign (the mapping of input data should be from TOSCA)
Update service-instance object in A&AI, orchestration-status = Assigned
Decompose
Instantiate
Service_Request
Decompose Service
Service Level Flow
Home
OOF
Loop Thru Resources
Determine Sequencing
VNF
Service Template
Build
Does not support decomposition of Services comprised of Allotted Resources and PNFs.
Assign Svc
Instance
Assign Service Instance
Activate Svc
Instance
Activate Service Instance
Update service-instance object in A&AI, orchestration-status = Active
Create
ANF
Service Template
Build
PNF
Service Template
Build
Network
Service Template
Build
Config Svc
Instance
TBD
The mapping of “Build” input data from the “service context” of the Service needs to be TOSCA model driven.
The sequencing is currently hard coded based on Resource Type, but should rather be determined from TOSCA dependencies between the Node Templates.

## Slide 13: VNF Level TOSCA Orchestration: “Build Plan” (Original Approach)
“Build”
VNF Request
VNF Level Flow
Loop Thru VF Modules
Assign VNF
Instance
Assign VNF
Activate VNF
Instance
Activate VNF
Call Controller Configure
Update generic-vnf object in A&AI, orchestration-status = Configured
Call Controller Activate
Update generic-vnf object in A&AI, orchestration-status = Active
Create generic-vnf object in A&AI, orchestration-status = Inventoried
Call SDN-C Assign (the mapping of input data should be from TOSCA)
Update generic-vnf object in A&AI, orchestration-status = Assigned
Config VNF
Instance
TBD
Assign VF Module
Request VF Module
Create vf-module object in A&AI, orchestration-status = Inventoried
Call SDN-C Assign (the mapping of input data should be from TOSCA)
Update volume-group object in A&AI, orchestration-status = Assigned
Call SDN-C to get vf-module assignments
Generate Heat parameters and call Heat to create object in cloud
Update vf-module object in A&AI, orchestration-status = Created
Determine Sequencing
The sequencing is currently hard coded based on Resource Type, but should rather be determined from TOSCA dependencies between the Node Templates.
Assign VF Mod
Instance
Request VF Mod
Instance

## Slide 14: vCPE Example (Original Approach)
Topology Template
Node Types
Relationship Types
Plans
vCpeResCust Service Service Template
NodeType: VNF
  Properties
NodeType: PNF
  Properties
NodeType: AllottedResource
  Properties
  NodeType: Service
Depends On
Requirement/Capability
Build_Svc
TunnelXConn
(ANF)
BRG
(PNF)
vG
(VNF)
(assign)
(assign)
(activate)
vGMux
(Service)
(requirement/
capability)

## Slide 15: vCPE Example (Original Approach)
Topology Template
Node Types
Relationship Types
Plans
vG VNF Service Template
NodeType: VF Module
  Properties
    Requirements: TunnelXConnCapability
Depends On
Build_Vnf
base_vcpe_vgw
(VF Module)

## Slide 16: vCPE Example (Original Approach)
Topology Template
Node Types
Relationship Types
Plans
base_vcpe_vgw VF Module Service Template
NodeType: Neutron Port
  Properties
NodeType: Nova Server
  Properties
Depends On
Assign
Request
Build (not executed by ONAP)
vgw_private_0_port
(Neutron Port)
vgw_private_1_port
(Neutron Port)
vgw_private_2_port
(Neutron Port)
vgw_0
(Nova Server)

## Slide 17: vCPE Example (Original Approach)
Topology Template
Node Types
Relationship Types
Plans
vGMux Infra Service Service Template
NodeType: Service
  Properties
    Capabilities: TunnelXConnCapability
Depends On
Build_Svc
BNG_MUX
(Network)
vBNG
(VNF)
BRG_BNG
(Network)
(assign,
activate)
(assign,
activate)

## Slide 18: vCPE Example (Original Approach)
Topology Template
Node Types
Relationship Types
Plans
vBNG Infra Service Service Template
NodeType: VNF
  Properties
NodeType: Network
  Properties
Depends On
Build_Svc
BNG_MUX
(Network)
vBNG
(VNF)
BRG_BNG
(Network)
(assign,
activate)
(assign,
activate)

## Slide 19: New Requirement
Service A – Service Template
VNF A.1
VNF A.2
VNF A.3
Original Approach:
Build Service A:
  Build VNF A.1
    Assign VNF A.1
    Create VNF A.1
    Activate VNF A.1
  Build VNF A.2
    Assign VNF A.2
    Create VNF A.2
    Activate VNF A.2
  Build VNF A.3
    Assign VNF A.3
    Create VNF A.3
    Activate VNF A.3
New Requirement Approach:
Assign Service A:
  Assign VNF A.1
  Assign VNF A.2
  Assign VNF A.3
Create Service A:
  Create VNF A.1
  Create VNF A.2
  Create VNF A.3
Activate Service A:
  Activate VNF A.1
  Activate
  Activate VNF A.3

## Slide 20: High Level TOSCA Organization (New Approach)
Service Service Template
Assign (inputs)
Create (inputs)
Configure (inputs)
Activate (inputs)
Assign (inputs)
Create (inputs)
Configure (inputs)
Activate (inputs)
VNF Service Template
Assign (inputs)
Request (inputs)
VF Module Service Template
PNF Service Template
Assign
Configure
Activate
AllottedResource Service Template
Assign
Create/Config
Activate
????
Build (inputs)
Still exists

## Slide 21: VNF Modeling (New Approach)
Topology Template
Node Types
Relationship Types
Plans
VNF Service Template
NodeType: VF Module
  Properties
    ScalingAspect
    MaxScaleLevel
Depends On
Each Node in the VNF Topology Template is of Node Type “VF Module”. These VF Modules have “Depends On” relationships between them. The Orchestrator determines the order in which to Request VF Modules based on the relationships, and not based upon any specific “Base” versus “Add-On” property. Because a VNF can have different “scaling aspects”, these relationships may need to be “scaling aspect” specific. (Not if we assume each VF Module appears in only a single “scaling aspect”.)
VF Module Service Template
Assign
Request
Need to work through how to model a “Scaling Level”. Is that a separate TOSCA Service Template per Scale Level? Or what?
“Assign” and “Create” Plans orchestrate the “Assign” and “Request” interfaces of the VF Module Nodes based upon the relationships in the Topology Template. The “Configure” and “Activate” Plans do not call VF Module Node interfaces at all, but rather call VNF-level interface exposed by a Controller. How do you model VNF-level interfaces in a VNF Service Template?
Inputs:
The inputs to a VNF Topology Template are those required for the VNF-level Orchestration Plans.
Build_VNF
Assign_VNF
Create_VNF
Configure_VNF
Activate_VNF

## Slide 22: Service Modeling (New Approach)
Topology Template
Node Types
Relationship Types
Plans
Service Service Template
NodeType: VNF
  Properties
    InitialScaleLevel
NodeType: PNF
NodeType: AllottedResource
NodeType: Network
Depends On
Each Node in the Service Topology Template is of Node Type “VNF”, “PNF”, “AllottedResource”, or “Network”. These Nodes have “Depends On” relationships between them. The Orchestrator determines the order in which to deploy a Node based on the relationships. Because the sequencing of the Node “Assign” may need to be different than Node “Create”, these relationships may need to be Plan specific.
Build_Svc
Assign_Svc
Create_Svc
Configure_Svc
Activate_Svc
The “Build” Plan orchestrates the “Assign”, “Create”, “Configure”, and “Activate” interfaces of the Resource-level Nodes based upon the relationships in the Topology Template. The other Plans orchestrate just the respective interface of the Resource-level Nodes.
Inputs:
The inputs to a Service Topology Template are those required for the Service-level Orchestration Plans.
VNF Service Template
Assign
Create
Configure
Activate
PNF Service Template
Assign
Configure
Activate
AllottedResource Service Template
Assign
Create/Config
Activate

## Slide 23: Service Level TOSCA Orchestration: “Build (and other) Plan(s)” (New Approach)
Instantiate
Service_Request
Service Level Flow
Assign Service Instance
Assign
Resources
Loop Thru Resources
NF
Service Template
Assign
Create Service Instance
Create
Resources
Loop Thru Resources
VNF, PNF, Ntw
Service Template
Create
Create Service_Instance
Assign Service
Create Service
Home
Decompose
Decompose Service
OOF
Assign Service_Instance
Configure Service Instance
Configure
Resources
Loop Thru Resources
NF
Service Template
Configure
Configure Service_Instance
Configure
Activate Service Instance
Activate Resources
Loop Thru Resources
NF
Service Template
Activate
Activate Service_Instance
Activate
Service Service Template
Assign
Create
Configure
Activate
Build
Assign Svc
Instance
Assign Service Instance

## Slide 24: VNF Level TOSCA Orchestration: “Build Plan” (Original Implementation)
Assign VNF Instance
Assign VF Module
Loop Thru VF Modules
Assign Vf Module
Create vf-module object in A&AI, orchestration-status = Inventoried
Call SDN-C Assign
Update volume-group object in A&AI, orchestration-status = Assigned
Request VNF Instance
Loop Thru VF Modules
Create VF Module
Activate VF Module
Assign VNF
Instance
Assign Vnf
Create generic-vnf object in A&AI, orchestration-status = Inventoried
Call SDN-C Assign
Update generic-vnf object in A&AI, orchestration-status = Assigned
Request Vf Module Create
Call SDN-C to get vf-module assignments
Generate VF Module Template (or HEAT) input parameter instance values (e.g., ENV) and call Cloud Orchestrator (e.g., OpenStack HEAT) to create object in cloud
Update vf-module object in A&AI, orchestration-status = Created
Send an VF-Module activate request to SND-C (REALLY??? WHY??)
Update the vf-module object in A&AI, orchestration-status = Active
Activate Vf Module