## Slide 1: Casablanca Release Highlights
Oct , 2018

## Slide 2: ONAP Casablanca Architecture (High-Level View with Projects)
Integration
Benchmark / Container Images
VNF Requirements
Modeling (Utilities)
VNF Validation Program
Version 3.0.3 7/31/2018
Notes: rop L0-3 for SDNC and 4-7 for APPC.

## Slide 3: Two New USE CASES

## Slide 4: CCVPN(Cross Domain and Cross Layer VPN) USE CASE
CCVPN by ONAP Peering Orchestration Between SPs
CCVPN use case is to realize connections between different ONAPs.
The Joint CCVPN PoC demo was demonstrated at ONS-EU in Sep 2018.
Internet
vCPE
vCPE
CPE
uCPE
ONAP (CMCC)
ONAP (VDF)
SOTN Controller
SD-WAN
Controller
SOTN Controller
SD-WAN
Controller
Connection（ E-Line）
UNI
UNI
Connection（ E-Line）
UNI
UNI
Site
Site
Site
Site
11

## Slide 5: 5G USE CASE
  Deployment of the hybrid 5G Radio Network (PNFs & VNFs)
    Complete PNF Support
    Platform Enhancements to Deploy Edge PNF & Virtual Radio Network Functions (e.g. CU)
      PNF PlugNplay, Configuration Enhancements, Performance Analysis & Optimization
  Optimization of the deployed 5G network
    OOF enhancements for optimal placement of edge resources
    Edge Analytics to Support 5G Network Optimization

## Slide 6: PROJECT Summary

## Slide 7: AAI
Upgrade HBase and Titan to Cassandra & Janus Graph Upgrade and add RethinkDB
Add SR-IOV to the AAI data-model
Historical View – see when ONAP data changed
Note: AAI Historial Data backend is available, but the UI is pending.
Notes: Note:

## Slide 8: APPC
Add support for new LCM Action Reboot and enhancement existing LCM actions
  Add Reboot support to APP-C Client Library as well as support to enable payloads in the response for Healthcheck, UpgradePrecheck, and UpgradePostcheck
  Support OpenStack actions Start, Stop, Reboot and Restart at the VNF levels
  Add feature in Design Services to support Reboot LCM command
  Enhance Ansible support by enabling granular parsing of response messages
  Support HealthCheck response with Payload which contains detailed status coming from VNF
  Support UpgradePreCheck and UpgradePostCheck responses with Payload which contain detailed status coming from VNF
  DistributeTraffic for migration of traffic from source to destination with appropriate input parameters. The payload would then be passed to the downstream Ansible server to take appropriate actions.

## Slide 9: CCSDK
Controller Design Studio
  common design tool to support both SDNC and Generic L4-7 NFs (APPC, VFC) Controller integrated with SDC
Upgrade to ODL ‘Oxygen’
Controller Framework (CCSDK)
RUN TIME
Templates
Resource Resolution Bundle
Data Sources
A&AI
MD-SAL
Database
Etc..
Data Sources
mS Naming
mS IP Assign
mS VLAN Tag
mS MAC Address
Etc..
Template Meshing mS
East/West API
SDNC *
Network Controller
Generic L4-7 NF
API
API
Cloud Sites (many edge sites)
VNFs
VNFs
Application Adapters
Network Adapters
VNFs
VNFs
Legend:
Platform components contributed POST Casablanca
Existing Run Time Application Instance in ONAP
Runtime
Catalog
DESIGN TIME
Controller
Design Center
(Backend)
SDC Integrated User Experience
SDC Design Catalog
Common Data
Dictionary
mS
Controller
Design
Center GUI
Generate Templates
Populate Data Dictionary
Create Controller Service Models aka blueprint
Controller
Design Artifacts

## Slide 10: CLAMP
Control Loop Dashboard
  View DMaaP events exchange during runtime Control Operations(DCAE/Policy/APPC/…).
  Filter/Slice/Dice through Control Loop Events.
Work
in
Progress

## Slide 11: DCAE
PNDA
  Introduce PNDA (http://pnda.io) as the analytics engine
  Enables a wide variety of big data technologies
HV VES
  Enhance DCAE performance measurement (PM) data collection to support near real-time (order of seconds) data. Introduce a high-volume VES collector using a persistent connection (TCP socket), support a new data encoding (GPB).
VES 7.0 upgrade
PRH Microservice
  Introduce PNF Registrator Handler (PRH) services for listening on the PNF Ready VES notification and updating A&AI and SO.
SNMP Trap Collector
  Generic SNMP trap collector added into DCAE collector suite. This can be used for legacy xNF event collector through standard SNMP interfaces.
DataFile Collector Service
  New mS provides collection of 3GPP bulk PM files and publishes to DMaaP Data Router ‘3GPP PM’ feed. Suitable for non real-time data collection, e.g. PM data files, logs, etc.
Notes: Develop new PM-Mapper MS to receive the data file collected and published into DMAAP-DR and transform that into VES for further processing with analytics/correlation systems in DCAE

## Slide 12: Documentation
New look
Easier to read via the web and mobile devices
‘Report Issue’ link allows reader to open a Jira bug report

## Slide 13: External API
Support for MEF Legato & Interlude APIs, e.g.:
  TMF 633 Service Catalog
  TMF 641 Service Order
  TMF 638 Service Inventory
Legato Operations
(North):
Query service catalog
Query serviceability
Create Service
Modify Service
Delete Service
Service Inventory operations
Interlude Operations
(East-West):
Query service catalog
Create Service
Modify Service
Delete Service
Service Inventory operations

## Slide 14: HOLMES
Provided a GUI to ease rule management
Improved flexibility for new scenarios by making Holmes more scripts-based
Added support for CCVPN alarm correlation

## Slide 15: Integration
CI/CD with Daily Summary
  functional tests + health checks
Container Optimization
  define Docker best practices
  minimize container size
Offline Deployment
  deploy ONAP without direct internet access
Work
in
Progress

## Slide 16: Multi-Cloud
plugin for k8s
plugin for azure
plugin for Titanium Cloud
Multi-Cloud
Functional Enhancement
    Integration with SO:
      Enables centralized representation of Cloud Regions
      Offloads workload template updating from SO to specific MultiCloud plugin
    Upgrade API version from v0 to v1
      Enables consistent ID of a cloud region
Expansion of infrastructure supports
    OpenStack Ocata, Pike
    Wind River Titanium Cloud R5
      Automate the onboarding of multiple edge clouds
    VMware VIO 5.0
    (PoC) Azure
    (PoC) Kubernetes
Infra workload
VNF Resource LCM
FCAPS
Provider Registry
broker
plugin for openstack
plugin for VIO
OOF
VES
APPC
VF-C
AAI
SO
Work
in
Progress
Work
in
Progress
Note: The K8s and Azure plugins are not integrated with other ONAP components in this release.

## Slide 17: MSB
Stability and Reliability
    Timeout & Retries
    Circuit breaker
Security
    Secured communication with TLS
Performance
    Latency aware load balancing with warm cache
Observability
    Metrics measurement
    Distributed tracing without instrumenting application
Manageability
    Routing rule
    Rate limiting enforcement
Testability
    Fault injection to test resilience of the services
Istio Service Mesh Proof of Concept to manage ONAP microservices. Istio Service Mesh is a dedicated infrastructure layer to connect, manage and secure microservices, which brings the below benefits to facilitate the ONAP S3P goals:

## Slide 18: OOM
Chart Repository
  ONAP provides a central chart repository avoiding the need to build local Helm repositories
Persistent Storage / Storage Classes
  pluggable persistent storage technologies to expand beyond static host path configuration + NFS backend
  provide support for GlusterFS as the first storage class provisioner
Resource Limits
  CPU and Memory limits to Helm Charts in order to improve Pod placement based on resources available in a Kubernetes Cluster
Common "shared" Helm Charts
  mariadb-galera cluster, postgres cluster, & cassandra
Platform Resiliency
  backup and restore of entire K8s deployment – Heptio Ark
  Node Selectors for Pod placement (place components on specified nodes)

## Slide 19: Policy
Support the Auto Scale Out functional requirements
Support HPA
Added a new Policy Lifecycle API
  Provide validation of model content when creating policies via API
Flexible control loop coordination facility.
Provide way to import spreadsheet for blacklist servers

## Slide 20: POMBA (Post Orchestration Model Based Audit)
An event-driven auditing platform that tests the data integrity across NFV orchestration environment and NFV infrastructure using model driven approach and reports on any data integrity issues found.
POMBA Architecture
New
Project

## Slide 21: SDC
3 New Design Studios
  DCAE Design Studio
  Workflow Designer (shown)
  Controller Design Studio
On-board ETSI NFV-SOL 004 TOSCA YAML Cloud Service Archive (CSAR) files
  enable use of standard TOSCA defined VNFs (in addition to OpenStack Heat Orchestration Templates)
SDC
ActivitySpec Catalog
CreateVNF
DeleteVNF
ConfigureVNF
StopVNF
StartVNF
LockVNF
UnlockVNF
StopTraffic
DrainTraffic
ResumeTraffic
HealthCheck
createSnapshot
copySnapshot
CreateTicket
NotifyUser
1. Activity are Developed by developer & ActivitySpec is On-boarded to Catalog
2. Workflow Designed in SDC using Workflow Editor and BPMN Artifact is generated
Firewall VNF
Instantiate
Upgrade
Operations
3. Workflow Associated to VNF Operations
SO
5. Deploy Workflows
SDC
VID
6. Initiate VNF Operation
SO
7. Execute Workflow Associated to Operation
4. Distribute
Workflow Designer

## Slide 22: SDNC
Site Failure Resiliency via Geo-graphic Redundancy with auto-failover
  Active / Standby model
  CoreDNS resolves requests to the current primary ODL server
active
standby
Notifications send via DMaaP
  Site Health Issue detected
  Site Health Issue cleared
  Site Switch initiated
  Site Switch (catastrophic failure) initiated

## Slide 23: SO
New internal mServices architecture (shown)
PNF Orchestration Support
New Scale Out Functionality
Hardware Platform Awareness (HPA)
  HPA aware SO Homing requests to OOF
  e.g. Deployment of VNF requiring SR-IOV (as specified in a TOSCA VNFD) is supported as Multi-Cloud and AAI extract hardware capabilities and OOF matches request to infrastructure
SO-Monitoring component allows a user to have a detailed monitoring view of the Camunda BPMN workflows that have run, or are running
child pods
SO
so-vfc-adapter
so-request-db-adapter
so-sdnc-adapter
so-catalog-db-adapter
api-handler-infra
so-bpmn-infra
so-openstack-adapter
so-mariadb
service
pod
pod
pod
pod
pod
pod
pod
pod
nodeport
so-sdc-controller
pod

## Slide 24: VF-C
Functional Enhancement
    NS Orchestration Supports PNF
      NSLCM supports NSD, composed of VNF, PNF, and VL
      Catalog supports PNFD and updates NSD DM
      Hardware Platform Awareness (HPA) Support
      integrate with OOF, and VF-C sending HPA homing requests to OOF and OOF return homing decision to VF-C.
      VF-C can parse R2+ TOSCA MODEL which includes HPA feature
Standard Alignment
    SOL003 Alignment
      GVNFM support SOL003 API, including
    Create/Instantiate/Operate/Terminate/Delete/Query VNF Instance
    VNF LCM Operation subscriptions and notification.
      Catalog support SOL003 related API, including
    VNF Package content upload/Download
    Create/Delete/Get VNF Package
    Maturity Enhancement
    Standalone DB Microservice
    Separate databases from VF-C components and provide standalone database microservices
SVNFM
SDC
Catalog
Driver
Drivers
DB
UUI
SO
Multivim
OOF
ESR/AAI
EMS
NSLCM
GVNFM
Note1: components listed here don’t contain all VF-C components, only used to highlight Casablanca work .