## Slide 1: PM Dictionary Proposal for ONAP Common Schema for 3GPP Compliant NFs Nokia Proposal for Dublin November 12, 2018

## Slide 2
Agenda
Topics Covered:
Overview of Bulk PM File Upload and Performance Event Generation
Overview of Real Time PM
PM Dictionary Usage in ONAP
PM Dictionary Requirements for ONAP
PM Dictionary Content for 3GPP Compliant Network Functions
Common PM Dictionary for ONAP
Progress to Date
Next Steps

## Slide 3: Bulk PM File Upload and Performance Event Generation

## Slide 4
Bulk PM File Upload and Performance Event Generation
Network Function (NF) establishes a HTTP/TLS connection to the DCAE VES Collector. DCAE authenticates the NF certificate for TLS.
NF sends FileReady notification Event to DCAE VES Collector. Event is encoded in JSON and sent via HTTP/TLS. HTTP/TLS connection is set up and torn down every time a FileReady notification event is sent.
DCAE VES Collector publishes the event to appropriate topic in DMaaP Message Router (MR).
DCAE File Collector retrieves the FileReady notification event from DMaaP MR.
File Collector uploads PM File from NF using a secure file transfer protocol FTPeS. NF authenticates the connection with the File Collector certificate.
File Collector publishes PM File to DMaaP Data Router (DR).
PM Mapper retrieves PM file from DR and generates perf3gpp events as configured by PM Mapper File.
PM Mapper publishes perf3gpp events to MR.
Analytics Applications (AA) retrieve the perf3gpp events of interest from MR. AA analyze the data to produce statistics and KPIs and optimization recommendations.
Bulk PM File Upload and Performance Event Generation
PM
Mapper
Data
Router
VES
Collector
Authenticate connection
HTTP/TLS
Upload PM file
Publish Event
HTTP/TLS
Send FileReady event
7
FTPeS
Retrieve PM File
File
Collector
Retrieve Event
Publish File
Message
Router
VES
Collector
VNF
PNF
6
5
4
3
2
1
Analytics
Application
Publish perf3gpp Event
Retrieve perf3gpp Event
8
9
1
7
6
2
3
4
5
8
9

## Slide 5
Performance Event Generation by PM Mapper
Proposal
Provide the ONAP Operator with the ability to define flexible, customizable perf3gpp events.
Events are generated from PM XML File and targeted for analytics applications in ONAP.
Define Perf3gpp Events
ONAP displays list of available measurements for a NF Type.
ONAP Operator selects the desired measurements from the list of measurements.
A PM Mapping File is generated so the PM Mapper knows how to create the events.
Create Perf3gpp Events
NF notifies DCAE that a PM file is available for upload.
File Collector uploads PM Files from NF and stores them in Data Router.
PM Mapper creates custom perf3gpp events from the PM File data according to PM Mapping File.
Analytics Applications use these perf3gpp events for targeted analysis of network operations.
PM Dictionary is needed to display the list of available measurements for this NF Type (future goal).
PM Dictionary may be needed by AA to understand the measurements it receives so that it can automatically and dynamically process them (future goal).

## Slide 6: Real Time Performance Measurements (RTPM)

## Slide 7
Real Time PM High Volume Measurement Events
Real Time PM Flow
Real Time PM High Volume Event Scenario
Network Function (NF) establishes a TCP connection to the DCAE High Volume (HV) VES Collector. If TLS is used, DCAE authenticates the NF certificate. Connection is persistent as long as Real Time PM (RTPM) is enabled so this is only done once.
For each event:
NF sends perf3gpp Event containing RTPM data to DCAE HV VES collector. Event is binary encoded with Google Protocol Buffer (GPB). Some string fields (measType) may be converted to numeric values (iMeasType) for efficiency.
DCAE validates the perf3gpp Event using the VesEvent.proto (which contains the schema for the Common Header and an opaque event field). DCAE publishes the event to DMaaP.
Analytics Application retrieves data. To decode and process the data, AA uses the VesEvent.proto, Perf3gppFields.proto (which contains the schema for the per3gpp specific fields) and MeasDataCollection.proto (which contains the schema for the RTPM measurements themselves), and the PM Dictionary.
DMaaP
DCAE HV
VES
Collector
Analytics
Application
PNF
VNF
4
Authenticate connection
1
AA retrieves data
Publish perf3gpp Event
NF sends RTPM perf3gpp event
TLS(optional)/TCP
Repeat for each event
2
3
TLS(optional)/TCP
PM Dictionary may be needed by AA to map the numeric IDs to names and also to understand how to process the measurements (future goal) .

## Slide 8: PM Dictionary Usage and Requirements

## Slide 9
PM Dictionary Usage for Analytics Applications
PM Dictionary is used by Analytics Applications to retrieve information about the measurements in the perf3gpp events and in the Bulk PM XML File.
PM Dictionary provides detailed information about each Measurement that a NF produces, including Measurement Name, Measurement Family, Measured Object Class, Description, Collection Method, Value Ranges, Unit of Measure, Triggering Conditions and other information.
A very important value of the PM dictionary is to separate the meta data from the actual data so that new measurements can be defined/deleted/updated anytime without requiring any change to the transport framework, since all the data is sent using the same format and structure. As such, use of the data requires the dictionary so that the data can be properly interpreted.
Initially,
  PM Dictionary is used by the Analytics Application developers to update the Analytics Application code as needed to process the measurements.
  PM Dictionary may be used by the Analytics Applications to translate a numeric measurement identifier (iMeasType) in a RTPM event into a measurement name (measType). Alternately, AA may use the numeric values directly. This depends on how the AA code is written.
Ultimately,
  Goal is for the Analytics Applications to use the PM Dictionary directly to be able to dynamically process new measurements based on the information in the PM Dictionary.

## Slide 10
PM Dictionary Usage for Measurement Change Management
The set of PM Measurements produced by a NF changes with each new NF SW Release.
PM Dictionary is used by ONAP operators to determine the PM changes associated with a new NF SW release so they can update perf3gpp events, associated PM Mapper Files and impacted Analytics Applications if needed.
PM Dictionary contains a Last Change indicator for each measurement.
    Identifies the PM Dictionary version for the last time each measurement changed. For example, measLastChange=“5G18A_1807_003” or measLastChange=“5G19_1906_002”.
    Makes it possible to easily identify per3gpp events and analytics applications that are candidates for update due to a changed measurement in the new SW release.
At onboarding, ONAP Operator filters the PM Dictionary for the current version.
  Cross check against PM Mapper event definitions.
  Events that use measurements that were modified or deleted in the current version of the PM Dictionary need to be analyzed to see if they are still applicable and if the event definition and/or the Analytics Application needs to be updated.
  Measurements that were added in the current version need to be analyzed to see if they should be included in a new or existing PM Mapper event definition and if an Analytics Application needs to be updated to process them.

## Slide 11
PM Dictionary Usage for Event Specification
PM Dictionary is used by ONAP components (for example, SDC, CLAMP, Policy) to display the set of measurements supported by a particular NF.
ONAP Operator can:
  select the desired measurements for PM Mapper perf3gpp events (future goal)
  configure the NF to generate RTPM perf3gpp events (future goal).
For PM Mapper events, ONAP creates:
  a PM Mapping File so the PM Mapper knows how to create the perf3gpp events. Format and content of PM Mapping File is TDB (future goal).
PM Dictionary is versioned. For example, pmDefVsn=“5G19_1906_002”.
  Allows ONAP components to associate the PM Mapper perf3gpp events, RTPM perf3gpp events and Bulk PM XML Files with the appropriate PM Dictionary version based on the NF instance that emitted the event.
  Each NF package has one PM Dictionary version onboarded with it.
  ONAP must keep track of the association between PM Dictionary version and NF Package version and NF Instance.

## Slide 12
PM Dictionary Requirements for ONAP
PM Dictionary requirements:
  Provides detailed information about each Measurement that a NF produces.
  Delivered as part of the NF package at onboarding.
  Updated whenever a PM is added, deleted or modified.
  Delivered in a machine-readable format.
  Formatted according to a common PM Dictionary schema.
  Contains “last change” indicators for each measurement to make it easy for an Operator to know what has changed.
  Aligns with a NF package version. There is a PM Dictionary version (pmDefVsn) that describes the set of PM measurements supported by the NF in that NF package version.
  Is the same artifact for Bulk PM and Real Time PM.
  Nokia is proposing a common PM Dictionary for ONAP.

## Slide 13: PM Dictionary Content for 3GPP Compliant NFs

## Slide 14
PM Dictionary Contents for 3GPP Compliant NFs
Field | Description | M or O | Example
pmDefVsn | Version of the PM Dictionary. Version is vendor defined. | M | 5G19_1906_002
pmDefSchemaVsn | Version of the PM Dictionary Schema used for this PM Dictionary. Schema versions are specified in the VES Specifications. | M | 1.0
nfType | NF type to whom this PM Dictionary applies. nfType is vendor defined and should match the string used in eventName. | M | gnb
vendor | Vendor of the NF type to whom this PM Dictionary applies. | M | Nokia
4G NFs comply with the following 3GPP standards for Performance Measurements:
  3GPP TS 32.425 Performance Measurements
  3GPP TS 32.432 PM File Naming
  3GPP TS 32.435 PM XML File Format Definition
5G NFs comply with the following 3GPP standards for Performance Measurements:
  3GPP TS 28.550 5G PM Management and File Format Definition
  3GPP TS 28.552 5G Performance Measurements
  3GPP TS 28.554 5G Key Performance Indicators

## Slide 15
PM Dictionary Contents for 3GPP Compliant NFs
Field | Description | M/O | Example
measType | Measurement name used in PM file, in 3GPP format where specified, else vendor defined. Names for 3GPP-defined 4G measurements are specified in 3GPP TS 32.425 item e). Names for 3GPP-defined 5G measurements are specified in 3GPP TS 28.552 item e). Vendor defined names are preceded with VS. | M | RRC.ConnMean
iMeasType | Vendor defined integer identifier for measType for efficiency in GPB. | O | 2
sMeasType | Vendor defined string identifier for measType; could be the same as measType or it could be a shortened version for efficiency in GPB. | O | RRC.ConnMean
measInfoId | Name for a group of related measurements, in 3GPP format where specified, else vendor defined. Family names for 3GPP-defined 4G measurements are specified in 3GPP TS 32.425 Section 3.1. Family names for 3GPP-defined 5G measurements are specified in 3GPP TS 28.552 Section 3.4. | O | Radio Resource Control
iMeasInfoId | Vendor defined integer identifier for measInfoId for efficiency in GPB. | O | 2024
sMeasInfoId | Vendor defined string identifier for measInfoId; could be the same as measInfoId or shortened version like measFamily for efficiency in GPB. | O | RRC
measFamily | Abbreviation for a family of measurements, in 3GPP format where specified, else vendor defined. Family name abbreviations for 3GPP-defined 4G measurements are specified in 3GPP TS 32.425 Section 3.1. Family name abbreviations for 3GPP-defined 5G measurements are specified in 3GPP TS 28.552 Section 3.4. | O | RRC

## Slide 16
PM Dictionary Contents for 3GPP Compliant NFs
Field | Description | M/O | Example
measDescription | Text description of the purpose of the measurement, what information does the measurement provide. Descriptions for 3GPP-defined 4G measurements are specified in 3GPP TS 32.425 item a). Descriptions for 3GPP-defined 5G measurements are specified in 3GPP TS 28.552 item a). Vendors are free to augment or modify the 3GPP-provided descriptions to more accurately describe their measurements as needed. | M | This measurement provides the mean number of users in RRC connected mode during each granularity period.
measCondition | Text description of the condition that causes the measurement to be updated. Conditions for 3GPP-defined 4G measurements are specified in 3GPP TS 32.425 item c). Conditions for 3GPP-defined 5G measurements are specified in 3GPP TS 28.552 item c). Vendors are free to augment or modify the 3GPP-provided conditions to more accurately describe their measurements as needed. | M | This measurement is obtained by sampling at a pre-defined interval, the number of users in RRC connected mode for each NR cell and then taking the arithmetic mean.
measLastChange | PM Dictionary version the last time this measurement was changed, added or deleted. | M | 5G18A_1807_003
measChangeType | For the measLastChange, indicates the type of change made for this measurement. Valid values are added, modified or deleted. Deleted measurements may be kept in the PM Dictionary for one release or more or permanently for historical purposes, if desired. | M | added
measObjClass | Measurement Object Class. Object classes for 3GPP-defined 4G measurements are specified in 3GPP TS 32.425 item f). Object classes for 3GPP-defined 5G measurements are specified in 3GPP TS 28.552 item f). The measObjClass values supported by a vendor are specified in the PM Dictionary YAML using the “value” attribute and may include vendor-defined objects not specified by 3GPP; for example IPSEC. | M | NRCellCU

## Slide 17
PM Dictionary Contents for 3GPP Compliant NFs
Field | Description | M/O | Example
measResultType | Data type of the measurement result. Result data types for 3GPP-defined 4G measurements are specified in 3GPP TS 32.425 item d). Result data types for 3GPP-defined 5G measurements are specified in 3GPP TS 28.552 item d). The measResultType values supported by a vendor are specified in the PM Dictionary YAML using the “value” attribute and may include vendor-defined data types not specified by 3GPP; for example boolean. | M | integer
measResultRange | Range for the measurement result. The range is specified as a comma separated list of discrete values or a range of values specified as minimum value-maximum value with no spaces. Result ranges for 3GPP-defined 4G measurements are specified in 3GPP TS 32.425 item d) if applicable. Result ranges for 3GPP-defined 5G measurements are specified in 3GPP TS 28.552 item d) if applicable. | O | 0,128-4096
measResultUnits | Unit of measure for the result; e.g. milliseconds, bytes, kilobytes, packets, number. Unit of measure for 3GPP-defined 4G measurements are specified in 3GPP TS 32.425 item d) if applicable. Unit of measure for 3GPP-defined 5G measurements are specified in 3GPP TS 28.552 item d) if applicable. The measResultsUnits values supported by a vendor are specified in the PM Dictionary YAML using the “value” attribute and may include vendor-defined units of measure not specified by 3GPP; for example ethernet frames. | O | number

## Slide 18
PM Dictionary Contents for 3GPP Compliant NFs
Field | Description | M/O | Example
measCollectionMethod | Collection Method for the measurement. 3GPP-defined collection methods are CC, SI, DER and Gauge. Collection Methods for 3GPP-defined 4G measurements are specified in 3GPP TS 32.425 item b). Collection Methods for 3GPP-defined 5G measurements are specified in 3GPP TS 28.552 item c). The measCollectionMethod values supported by a vendor are specified in the PM Dictionary YAML using the “value” attribute and may include vendor-defined collection methods not specified by 3GPP; for example Average. | M | SI
measAdditionalFields | Hashmap of vendor specific PM Dictionary fields in key value pair format | O | measAggregationLevels

## Slide 19: Common PM Dictionary for 3GPP Compliant NFs

## Slide 20
PM Dictionary Format
There are two logical choices for PM Dictionary format:
  YAML
    This is the preferred format for the PM Dictionary because all other ONAP artifacts are in YAML format.
    See PM Dictionary YAML Example below. Ideally, this type of YAML document would be included in the vendor’s event registration YAML file. This example contains the vendor-specific, NF-specific YAML registration for the PM Dictionary that specifies, for example, the fields in the PM Dictionary relevant to this NF, whether they are mandatory or optional for this NF and the values supported for the fields by this NF. This is similar to the event registration YAML that specifies the vendor-specific, NF-specific YAML registration for events. The YAML registration is followed by the actual PM Dictionary contents.
  XML
    3GPP PM files are in XML format so Analytics Applications can more easily handle a XML format for the PM Dictionary. But ONAP does not process XML artifacts and so this makes XML a less desirable choice.