## Slide 1
VES Universal Mapper
High level Solution Design

## Slide 2
PROBLEM
Different VNF vendors generates event and telemetry data in different formats. Out of the box all VNF vendors may not support ONAP VES format.
SOLUTION
BUSINESS BENEFIT
A generic adapter which can convert different formats of event and telemetry data to VES format which is needed by ONAP.
VES Universal Mapper makes all VNF’s ONAP compatible which will enable rapid VNF onboarding and reduced time to market leading to increased revenue generation.
VES Universal Mapper

## Slide 3
All SNMP traps received by the SNMP Trap receiver are coverted to json and pushed to DMaaP by trap receiver.
The Universal VES Adapter micro service will subscribe to the SNMP traps topic from DMaaP queue.
Each SNMP trap processor micro service will parse the system object id , generic and specific tarp id’s present in the SNMP Trap and if they match the id’s they are processing, it will further process the trap else drop the trap.
The Universal VES Adapter will then pick up the corresponding mapping file from repository for each trap by using the system object id as identifier.
The Universal VES Adapter will use the mappings from the mapping file and creates the VES object for the corresponding trap.
For SNMP Traps for which no mapping file is identified, a default mapping file is used with generic mappings to create the VES object.
The VES formatted Event will be then publish to the specific DMaaP topic.
Universal VES Mapper
DMaaP
Cache DB
Persistent DB
Trap Parser
Identify the mapping file
Create VES JSON
Push To DMaap
SNMP Trap Receiver
VES Listener REST Service
Trap Parser
Identify the mapping file
Create VES JSON
Push To DMaap
1
2
3
4
5
DMaaP

## Slide 4
Run Time SNMP Processing(Beijing Release)
VNF
Sends SNMP Trap to SNMP Trap Collector
SNMP Trap Collector
Trap collector pushes received traps to DMaaP
DMaaP SNMP Trap Queue
Trap Processer subscribes SNMP Traps DMaaP Topic.
Universal VES Adapter
Mapping files
Trap Processer picks the correct mapping file using sys obj ID.
Trap Processer creates VES event and push the ves formatted traps to dmaap queue.
DMAAP

## Slide 5
Demo

## Slide 6
DMaap
VES collector
SNMP collector
VES Mapper
File Collector
VNF
E/// VNF
SNMP Trap
SNMP JSON
format
SNMP JSON
format
VES JSON
format
1
2
3
4
Option 1
FTP/SCP
File contain in
JSON format
1
2
MR
MR

## Slide 7
DMaap
VES collector
SNMP collector
VES Mapper
VNF
E/// VNF
SNMP Trap
SNMP JSON
format
SNMP JSON
format
VES JSON
format
1
2
3
4
Option 2
1
File contain in
JSON format
MR
MR

## Slide 8
Thank You