## Slide 1: DCAE Security enhancement in VES Collectors
Nov 29, 2018

## Slide 2: DCEA Casablanca security status
HTTP authentication with username/password, no TLS
HTTP authentication with username/password, TLS enabled, one-way TLS server authentication (NF doesn’t have a cert)
HTTP authentication with username/password, TLS enabled, mutual TLS authentication (NF has a certificate)
username/password stored on VESCollector host, can be compromise by obtaining access to environment

## Slide 3: DCAE enhancements
Replace storage of passwords with storage of hashes (e.g., PBKDF2, Bcrypt or Scrypt
Separate credentials storage from other configuration storage.

## Slide 4: SECCOM recomendation.
Security Subcommittee is proposing security enhancements for Dublin to improve secure communications between Network Functions (NFs) and ONAP.
One of it concerning DCAE is:
Eliminating the need for username/password for the HTTP/TLS connection from NF to DCAE.
  Use NF certificate and standard PKI validation for HTTP/TLS authentication instead of Basic authentication with username and password.
ref. https://wiki.onap.org/display/DW/Secure+Communication+to+Network+Functions

## Slide 5
Authentication of HTTP/TLS Connection from NF to DCAE

## Slide 6: DCAE enhancements – target with TLS
DCAE VES Collector
NF Sends VES Event to DCAE
NF
NF sends VES event to DCAE
NF sends an asynchronous VES event to DCAE VES Collector via HTTP/TLS.
VES Collector authenticates the HTTP/TLS connection using the NF certificate and standard PKI validation. No Basic HTTP Authentication with username and password is necessary.
VES Collector publishes the event to the appropriate DMaaP topic.
The appropriate Analytics Application subscribes to the event and processes it.
DMaaP
E2
NF sends event to VES Collector
E1
E4
AA subscribes to event to process
E3
E4
VES authenticates NF using NF certificate
E1
E2
VES Collector publishes event to DMaaP topic
E3
AA
HTTP/TLS

## Slide 7: DCAE enhancements
Accept event
Drop event
User, pass valid?
Has Basic Auth
Is Identity known?
Has valid PKI?
NF event
Yes
No
Yes
Internal DCAE storage
No
No
Yes
Yes
New
Internal DCAE storage

## Slide 8: DCAE enhancements
VES collectors verifies identity of NF (from certificate) against internal list of authorized entities
  substitute (but doesn`t completely replace) Basic Auth user/pass verification
  internal list can be replaced with verification in AAF or any other source in future
  fall-back to Basic Auth if identity unknown – backward compatibility

## Slide 9: DCAE enhancements
Development plan (ONAP/Dublin):
VES Basic Auth enhancement (non-breakable)
  Implement password hashing
VES TLS certificate as identity source support (non-breakable)
  Add certificate support - check against a list of known identities
Externalize Authentication Library to dcaegen2/services/sdk (n-b)
  Externalize the authentication module, and place in services/sdk
  This will allow to use the same mechanism in other TLS based collectors
Integrate the TLS certificate support with AAF (breakable)
  Replace the "list of known identities" with an appropriate AAF interface call.
  Possibly implement a cache of recent known identities