## Slide 1: Details of Targeted Service Template & SDC Enhancement
Lin Meng

## Slide 2: Background
In Casablanca release,
  The CCVPN service consisted of 3 abstracted nodes: Site, SOTN infra, SD-WAN infra.
  The current SDC doesn’t support multiple sets of inputs in one service template.
Goal of Dublin release
  The CCVPN service should be able to design in one template.
  Service template should support multiple instances inputs, so we can design all resources into one service
List type input will be rational solution.
https://wiki.onap.org/display/DW/CCVPN+DM+Requirement

## Slide 3: SD-WAN Model
device
site
WAN
site resource
vpn
LAN
vpn resource
1..UNBOUNDED
1
1-4
1
1-2
1..UNBOUNDED
1..UNBOUNDED
SD-WAN
Service
One SD-WAN Service:
There are more then one sites. And also based on these sites, enterprise can have more than one VPNs.
One Site Resource:
In one site, there are 1-2 devices(main-standby mode), for each device , there can be 1 or 2 wan port(mpls and internet), so each site can have 1-4 wan port.
One VPN Resource:
In each vpn , there can have 1 vpn definition, and there are 1-unbounded site wans in this vpn

## Slide 4
Sdwanvpnresource
[type=list]
sdwansiteresource
[type=list]
VPN[0]
CCVPN Service Example
Inputs
Inputs Example
…
Site[2]
Site[0]
Site[1]
Site[0]. Sdwansite_***
Site[0]. sdwansitewan_list
Site[0]. Sdwandevice_list
CCVPN Service Example
sdwansiteresouce_list:
- [0].sdwansite_***=
.sdwansitewan_list=
.sdwandevice_list=
- [1] .sdwansite_***=
.sdwansitewan_list=
.sdwandevice_list=
- [2].sdwansite_***=
.sdwansitewan_list=
.sdwandevice_list=
This inputs are given in the Run-time.
Site[1]. Sdwansite_***
Site[1]. sdwansitewan_list
Site[1]. Sdwandevice_list
Site[2]. Sdwansite_***
Site[2]. sdwansitewan_list
Site[2]. Sdwandevice_list
sdwanvpnresource_list:
-[0].sdwanvpn_topology
-[0].sdwanvpn_name
-[0].sdwansitelan_list
VPN[0].sdwanvpn_topology
VPN[0].sdwanvpn_name
VPN[0].sdwansitelan_list

## Slide 5: TOSCA Service Template Sample
tosca_definitions_version: tosca_simple_yaml_1_1
description: Enhance_Service
data_types:
org.openecomp.datatypes.vf.sdwanvpnresource:
properties:
sdwanvpn_topology:
type: string
required: true
sdwanvpn_name:
type: string
required: true
sdwansitelan_list:
type: list
entry_schema: org.openecomp.datatypes.vfc.sdwansitelan
required: true
org.openecomp.datatypes.vf.sdwansiteresource:
properties:
…
sdwansitewan_list:
type: list
entry_schema: org.openecomp.datatypes.vfc.sdwansitewan
required: true
sdwandevice_list:
type: list
entry_schema: org.openecomp.datatypes.vfc.sdwandevice
required: true
topology_template:
inputs:
sdwanvpnresource_list:
type: list
entry_schema: org.openecomp.datatypes.vf.sdwanvpnresource
required: true
sdwansiteresource_list:
type: list
entry_schema: org.openecomp.datatypes.vf.sdwansiteresource
required: true
node_templates:
sdwanvpnresource:
type: org.openecomp.resource.vf.Sdwanvpnresource
properties:
availability_zone_max_count: 1
min_instances: 1
sdwanvpn_topology:
get_input: [sdwanvpnresource_list, INDEX, sdwanvpn_topology]
sdwanvpn_name:
get_input: [sdwanvpnresource_list, INDEX, sdwanvpn_name]
sdwansitelan_list:
get_input: [sdwanvpnresource_list, INDEX, sdwansitelan_list]
Define Data Type of each resource
Declare new list input
Get each property