## Slide 1: HLD - Cross-domain E-LINE Services with OTN NNI
CMCC, Huawei

## Slide 2: Use Case Description
Changes Description:
  NNI handover between 2 OTN domain.
  E2E OTN tunnel across multiple domains
  E2E E-LINE service
Transport Domain
SOTN Controller
SOTN Controller
100G+ Grey OTN
100G+ Grey OTN
RESTCONF protocol +
Standard transport NBI (e.g. IETF ACTN, T-API)
OTN topology YANG
OTN tunnel YANG
Client service YANG
Path computation YANG
CPE
CPE
Ethernet
OTN/DWDM
Ethernet
Transport Domain
Portal
API
SDN-C
SDC
A&AI
SO
OTN/DWDM
NNI
UNI
UNI
End-to-end VPN service
E-LINE
OTN Tunnel
Changes

## Slide 3: ONAP SOTN
Topology Discovery
Service Design
Service Provisioning

## Slide 4: Topology Discovery
CPE
CPE
SOTN Controller
SOTN Controller
Transport Domain
Transport Domain
Standard NBI
Ethernet (topo)
OTN (topo, tunnel)
OTN NNI
ETH
ETH
ONAP Topology
OTN NNI
Standard NBI
Ethernet (topo)
OTN (topo, tunnel)
CPE
CPE
SOTN Controller
SOTN Controller
Transport Domain
Transport Domain
Standard NBI
Ethernet (topo)
OTN NNI
ETH
ETH
ONAP Topology
OTN NNI
Standard NBI
Ethernet (topo)
Abstract Ethernet Node1
Abstract Ethernet Node2
ETH topology 1
ETH topology 2
OTN topology 1
OTN topology 2
Current
Required

## Slide 5: Topology Resources
TP
TP
TP
TP
TP
TP
TP
TTP
inter-layer-lock-id
inter-layer-lock-id
ETH Link
ETH Link
ETH Link
ETH Node
ETH Node
OTN Node
OTN Node
ETH Topology
OTN Link
OTN Topology
TP
TTP
LLCL
LLCL
AAI needs to have two layers (Eth and OTN) of topology.
Need to add Tunnel Termination Point (TTP) attribute to Topology Node.
TP in upper layer node (ETH Node) are associated with TTP in lower layer node (OTN Node) by inter-layer lock ID

## Slide 6: Topology Resources in AAI
TP
(P-Intf)
TP
(P-Intf)
TP
(P-Intf)
TP
(P-Intf)
Node (PNF)
Node (PNF)
Ethernet Topology
Network-Resource
Link
(Logical-Link)
Ethernet Topology could be either comprised of abstract Ethernet nodes, or native Ethernet Nodes, or mix of both. For this we add an addition parameter “isAbstract” in Ethernet Node.
Logical link could be intra optical domain or inter optical domain or inter operator domain for this we add a new attribute
“LinkType” in Logical Link.
TP to have a new attribute “inter-layer-lock-id” to associate with OTN topology.
Note:
If network-resource can’t be extended, use a new type.
Also define a new type for TP if TP can’t be extended.

## Slide 7: Topology Resources in AAI
TP
(P-Intf)
TP
(P-Intf)
TP
(P-Intf)
TP
(P-Intf)
Node (PNF)
Node (PNF)
OTN Topology
Network-Resource
Link
(Logical-Link)
Re-use network-resource and add a new attribute “NetworkType” to differentiate whether it’s a Ethernet topology of OTN topology
Re-use PNF as a OTN node & P-Intf as TP.
A new TTP node type is required in AAI. It should have OneToMany relation with TP
Also PNF needs to have OneToMany relation with TTP
Note:
If network-resource can’t be extended, use a new type.
Also define a new type for TP if TP can’t be extended.
TTP
TTP
TP
(P-Intf)
Ethernet Topology

## Slide 8: Service Design
CCVPN service
Site Service
SOTN Infra Service
Site Service
service
Site
SOTNVPN Attachment
Site Service
SD-WAN VPN Attachment
Device
WAN
LAN
Internet Cloud Access
SPPartner
service
SOTN Connectivity
SOTN VPN_Infra
SPPartner
subnet
subvpn
tnp
site
device
site NS
sdwan vpn resource
site resource
*
1
*
*
1
1-4
1-2
CCVPN Service
1
l2vpn
sotn vpn resource
1
*
subnet
subvpn
tnp
site
device
site NS
sdwan vpn resource
*
1
*
*
1
1-4
1-2
CCVPN Service
1
Beijing Approach
Dublin Approach
Requirement
site resource

## Slide 9: Service Design
SOTNConnectivity
Name
Description
tenantId
vpnType
startTime
endTime
COS
Reroute
SLS
dualLink
Cir
Eir
Cbs
ebs
colorAware
couplingFlag
Site
siteId
name
Description
location
clientSignal
CVLAN
sotnVpnAttachment
vpnName
tpId
CVLAN
SOTNConnectivity
Name
Description
tenantId
vpnType
startTime
endTime
COS
Reroute
SLS
dualLink
Cir
Eir
Cbs
ebs
colorAware
couplingFlag
Site
siteId
name
Description
location
clientSignal
Beijing
Change
Whether CVLAN needs to be specified
by user?

## Slide 10: Service Provisioning
SDNC resumes the responsibility of a super controller. SDNC retrieves both the OTN and the ETH topology from the NCE.
SDNC converts OTN and ETH topology from ACTN to AAI format and writes them to AAI
For E-Line service creation, SDNC sends down the OTN tunnel creation request to NCE, and then sends the E-Line service creation request.
UUI
SO
SDNC
UUI to adapt the new model and make request to SO accordingly.
AAI changes as depicted in next page
OOF changes for OTN path computation, Ethernet path computation?
SO only test efforts.
AAI
OOF
Involved & Impacted Components

## Slide 11: Service Provisioning Flow - Flow & APIs
API Details
UUI-SO:
/onap/so/infra/serviceInstantiation/e2eServiceInstances/v3
SO-SDNC:
Service Creation
/operations/GENERIC-RESOURCE-API:service-topology-operation
VNF Creation
/operations/GENERIC-RESOURCE-API:vnf-topology-operation
VF-Module Creation
/operations/GENERIC-RESOURCE-API:vf-module-topology-operation
SO-OOF:
/api/oof/v1/route

## Slide 12: Service Provisioning – SB Request

## Slide 13: Service Provisioning – E2E AAI View?
L2VPN (SOTN-Connectivity)
vpn-resource
TP
(P-Intf)
TP
(P-Intf)
TP
(P-Intf)
TP
(P-Intf)
Node (PNF)
Node (PNF)
Link
(Logical-Link)
Intra Domain Link
vpn-resource
TP
(P-Intf)
TP
(P-Intf)
Node (PNF)
Link
(Logical-Link)
Inter Domain Link
Created by SDNC
No Change
SOTN VPN (Generic-VNF)
CCVPN Service
Site (Generic-VNF)
Site (Generic-VNF)
Site-Resource
Site-Resource

## Slide 14: Project Changes
Project | Code Change | Change Description
A&AI | Yes | OTN resources & Native Ethernet topology
SDC | No | SOTN based on new CCVPN Dublin model
UUI | Yes | Change in UUI Backend to adapt new template. UUI Frontend from VDF JIS can be re-used
SO | No | Ideally only Test efforts
SDN-C | Yes | OTN Topology discovery, Native Ethernet Topology discovery, Service provisioning based on NNI
OOF | Yes | OTN Path computation
Remark: Closed loop is kept out of current scope. Not a priority currently.
To be discussed further based on resource availability and interest from partners.

## Slide 15
Thanks

## Slide 16: Reference: IETF ACTN YANG Models as Standard
Network Topology Model
RFC 8345
Topology Models
OTN TE Topology Model
draft-ietf-ccamp-otn-topo-yang
WSON TE Topology Model
draft-ietf-ccamp-wson-yang
Tunnel Models
YANG Data Model for TE Tunnel
draft-ietf-teas-yang-te
OTN TE Tunnel Model
draft-ietf-ccamp-otn-tunnel-model
WSON TE Tunnel Model
draft-ietf-ccamp-wson-tunnel-model
Client Service Model (ETH, client service)
draft-ietf-ccamp-client-signal-yang
Reference
Augmentation
Generic Models
Generic Scheduling Model
draft-liu-netmod-yang-schedule
Generic Notification Model
draft-ietf-netconf-restconf-noti
Transport Client Service Model
Ethernet TE Topology Model
draft-zheng-ccamp-client-topo-yang
ETH TE Tunnel Model
draft-zheng-ccamp-client-tunnel-yang
YANG Alarm Module
draft-ietf-ccamp-alarm-module
OAM
RFC
WG
WG
ID
WG
WG
ID
WG
WG
WG
WG
ACTN Information Model
draft-ietf-teas-actn-info-model
RFC
ACTN Framework
draft-ietf-teas-actn-framework
RFC
ACTN Requirements
draft-ietf-teas-actn-requirements
RFC
YANG Data Model for TE Topologies
draft-ietf-teas-yang-te-topo
RFC*
WG
These models are deployed between ONAP SDN-C and transport SDN controller
SDN-C internal models for the modeling for PNF and abstract topologies are aligned with the IETF YANG models