## Slide 1: Support for Shared IP addresses – USE CASES
Arturo Martin de Nicolas ( Ericsson )
NFVIFA(19)000288r1

## Slide 2: Problem statement and motivation (1/2)
VNFs may need to share an IP address among two or more VduCps, e.g.
  To ensure high availability of a service
  For load balancing purposes
This has been recognized by ONAP:
  https://wiki.onap.org/display/DW/Potential+Feedback+to+ETSI+IFA011+v2.5.1
vnfReservedCpd | VduCpd | 0..* | Reserved IP Address for VNF which is not bounded to any specific VNFC, but assigned manually from outside and potentially shared as a floating IP among VNFCs.
allowedAddressData Note: Ongoing discussion is proposing to move this out of Cpd (into VNFD) as it is specified to VNFD. | AddressData | 0..N | For specifying floating IP(s) to be shared among Cpds, which are reserved for vnfReservedCpd described in the VNFD.

## Slide 3: Problem statement and motivation (2/2)
In OpenStack this relies on “allowed-address-pair”
VNFC_A (instance 1)
VduCp
IpAddress: 192.168.100.154
Shared IpAddress: 200.10.100.104
VNFC_A (instance 2)
VduCp
IpAddress: 192.168.100.155
Shared IpAddress: 200.10.100.104
$ neutron port-create --name VduCp1 --allowed-address-pair 200.10.100.104
$ neutron port-create --name VduCp2 --allowed-address-pair 200.10.100.104

## Slide 4: Background: Use of shared IP addresses (1/3)
There are multiple ways to use shared address, e.g.
  a) Load balancing with ECMP
Edge router
ECMP
Dest: 200.10.100.104
Dest: 200.10.100.104
Dest: 200.10.100.104 Dest MAC: mac_add1
VNFC_A (instance 1)
Dest: 200.10.100.104 Dest MAC: mac_add2
VNFC_A (instance 2)
Next hop alternatives

## Slide 5: Background: Use of shared IP addresses (2/3)
  b) High availability:
    shared IP address is bound to only one port at a time (instance 1 or instance 2), but the binding can change over time (e.g. in case of VM failure)
Edge router
VNFC_A (instance 1)
VNFC_A (instance 2)
Gratuitous ARP (MAC: mac_add1,
IPadd: 200.10.100.104)
1)
Edge router
VNFC_A (instance 1)
VNFC_A (instance 2)
Gratuitous ARP (MAC: mac_add2,
IPadd: 200.10.100.104)
2)
VM Failure

## Slide 6: Background: Use of shared IP addresses (3/3)
  c) DNAT based load balancing :
  Note: above case does not require to enable OpenStack “allowed-address-pair”
The different usages result on different ways of configuring routing tables
DNAT load balancing
Dest: 200.10.100.104
Dest: 200.10.100.104
Dest: 192.168.100.154
VNFC_A (instance 1)
Dest: 192.168.100.155
VNFC_A (instance 2)
Next hop alternatives

## Slide 7: Next steps
ONAP feedback expected by 15.04.2019
ETSI NFV will start developing a solution based on the feedback, targeting Release 2 ed271 maintenance cycle.