## Slide 1: End User Advisory Group CCVPN - L0/L1 Optical Networks Carriers Interconnection
Olivier Augizeau, Brian Freeman
18th June 2019

## Slide 2: Fujitsu proposal supported by Orange and AT&T
CCVPN
L0/L1 Optical Networks
Carriers Interconnection

## Slide 3: Overview
Background
  In order to offer service to customers with geographically diverse locations, service providers often lease resources in networks where they do not have a presence (“off net”). This allows them to provide end-to-end service to their customers, but requires a manual and complex negotiation between providers that includes both the business arrangement and the actual service design and activation.
  Operators may also be structured such that they operate multiple networks independently and require similar transactions among their own networks and business units in order to provide an end-to-end service.
Objective
  Automate the service activation and operations (service assurance, monitoring, …) resulting from a service request exchanged between or among service providers or independent operational units within a service provider.

## Slide 4: Cross Carriers L1 Service – MEF based.
Emulated BSS
ONAP(SP1)
ONAP(SP2)
Domain Controller
Domain Controller
Subscriber
L1 Service
SP1 Access L1 Service
SP2 Access L1 Service
OTU4 L1 ENNI
A
BSS (SP1)
Open Standard Network APIs
ONF T-API
Optical Domain 1
Optical Domain 2
Optical Domain 3
Open ROADM service API
Open Standard Network APIs Open ROADM
L1 UNI (eg. 10GE)
L1 UNI (eg. 10GE)
MEF / Interlude
BSS (SP2)
MEF / LEGATO
MEF / LEGATO
Proprietary
OpenDaylight Optical controller
Transport-PCE
Open Standard Network APIs
ONF T-API
Z

## Slide 5: L1 Interconnect
Layer 0/1 Carrier Interconnect Service
 | Milestone | Baseline | Actual | RAG
1 | Architecture / Design | TBD | TBD | 
2 | Define PoC scope |  |  | 
3 | Identify Platform Requirements |  |  | 
4 | L0/L1 Model(s) and APIs defined |  |  | 
5 | Controller architecture |  |  | 
6 | Development |  |  | 
7 | Test plan / testing complete |  |  | 
8 |  |  |  | 
Key Enhancements Proposed / Delivered
 | Description | Status
A | TransportPCE support for OTN | TBD
B | MEF L1 service Order support for inter-carrier interactions | TBD
Key Milestones
Activities
Status
Description
Design and activation of global optical services that require interconnection between or among service providers.
Proposed as a CCVPN sub use case. First step could be Frankfurt and focused on service provisioning.
Service insurance and monitoring are scheduled for a 2nd step.
Architecture in progress
Proposed L0/L1 extension to CCVPN
Enhancements to SDN-C and A&AI implemented to support topology exposed from external controllers.
Identified L1 service use case reviewed with AT&T and Orange
ODL/T-PCE integration to ONAP
https://wiki.onap.org/display/DW/Multi-domain+Optical+Network+Services
ONAP wiki resources:

## Slide 6: Thank you