## Slide 1: Optical Service (L0/L1) Orchestration Use-case
Fujitsu Network Business Group (NBG)

## Slide 2: Problem Statement / Overview
Project Description
  Goal of this use case is to provide end to end multi-operator L1 service orchestration based on MEF L1 Subscriber and Operator service definitions across multiple optical transport domains
    Harmonize with proposal on incorporating MEF Interlude APIs
    https://wiki.onap.org/display/DW/Draft+Dublin+Interlude+High+Level+Requirement
  Each of the optical transport domains can be managed to create intra domain L0/L1 access service which are used in the over-all end to end L1 service
    Direct management via standard APIs such as OpenROADM, OpenConfig, etc
    Indirect management through a local domain controller via standard network and service models such as ONF T-API and OpenROADM
  The Optical service created above could then be adopted/embedded to provide optical transport for other blueprints like 5G Network slice across FH and MH/BH domains
Notes: Multi-domain/multi-layer

## Slide 3: Multi-Operator L1 Service
ONAP(SP1)
ONAP(SP2)
Domain Controller (TAPI)
Domain Controller (Open ROADM)
Subscriber
L1 Service
SP1 Access L1 Service
SP2 Access L1 Service
OTU4 L1 ENNI
A
Z
OSS/BSS
Open Standard Network APIs
ONF T-API
Optical Domain 1
Optical Domain 2
Optical Domain 1
Direct management via standard Device APIs such as OpenROADM, OpenConfig etc.
Open Standard Network APIs OpenROADM
L1 UNI (eg. 10GE)
L1 UNI (eg. 10GE)
INTERLUDE
x
y
a
z
Notes: Multi-domain/multi-layer

## Slide 4: Break down of a Multi Operator L1 Service:
Customer requests a 10GB pipe between location A and Z where location A is under service provider-1 who will be the primary provider and location Z is under a different service provider-2 who will be the partner
A to Z subscriber L1 service will comprise of two separate Access L1 services from SP-1 and SP-2. These will then be interconnected using OTU4 L1 ENNI
Access L1 service which is part of a SP network may in-turn comprise of one or more L0/L1 service over different optical domains. These services are interconnected using inter domain manual links
A to Z subscriber link has
  A to a Access L1 service provided by SP-1
  z to Z Access L1 service provided by SP-2
  OTU4 L1 ENNI connecting a to z and managed by SP-1
A to a Access L1 service provided by SP-1 can in-turn have
  A to x L0/L1 service over a optical domain-1(say based on T-API)
  y to a L0/L1 service over another optical domain-2 (say based on Open ROADM)
  x and y are inter connected using inter domain manual links managed by SP-1
Notes: Multi-domain/multi-layer

## Slide 5: Onboarding of External Domain controllers
SDN-C
CDS
Blue Print Processor
A&AI
CDS
FE & BE
Design Time
Run Time
DG Plug-in(s)
Ext-Domain Controller1
Ext-Domain Controller2
Add Ext-Controllers, Inter domain & Inter SP Links
Open Standard Network APIs
ONF T-API
Open Standard Network APIs OpenROADM
DMAP
1
3
5
6
7
8
INTERLUDE
4
SDC
Resource Catalog
2
9

## Slide 6: Domain Controller Onboarding
Register the Tosca template that defines the workflow to add external controller. Also add all the external SDN domain controllers and all the required Inter domain manual links and OTU4 ENNI Inter SP links.
Workflow and the resources gets stored in the SDC catalog using SDC plug-in API
Run time component of CDS which is the blue print processor in SDN-C will then get triggered, invoking the on-boarding workflow for each of the controllers
As per the workflow it calls REST API of ESR component of A&AI to onboard external SDN controllers. It will also call REST-API’s of A&AI to add all manual Inter domain and inter SP OTU4 ENNI links
A&AI sends out a message to DMAAP for each of the on boarded external Controller
SDNC receives this message and acts on each of the message and identify the actual DG to retrieve the Topology
SDNC Invokes DG mapped to Domain controller-1 REST API to get the T-API based Topology
SDNC Invokes DG mapped to Domain controller-2 REST API to get the Open ROADM based Topology
SDN-C then maps the retrieved topology from each of the controller and maps them to A&AI schema and stores them at A&AI

## Slide 7: Optical Service Design & Instantiation – Phase1
SDC
SDN-C
CDS
Blue Print Processor
Ext API / NBI
A&AI
Design Time
Service & Resource Catalog
Run Time
DG Plug-in(s)
Ext-Domain Controller1
Ext-Domain Controller2
Open Standard Network APIs
ONF T-API
Open Standard Network APIs OpenROADM
Register Intra domain Service definitions & End-To-End Inter service provider Service definition
1
2
3
6
8
9
5
INTERLUDE
SO
4
10
11
7

## Slide 8: Service Design & Instantiation Workflow
Onboard all the artifacts that define the end to end Subscriber L1 service across operators. Also Onboard the templates that will be used to create Access L1 service which may involve the nested L0/L1 service across multiple Domains like T-API/Open ROADM networks. On-boarded services get stored in service & resource catalog of SDC and will generate North bound Ext-APIs which can later be used by OSS/BSS to instantiate these services
OSS/BSS invokes the Ext-API to create an end to end L1 subscriber service between A to Z locations
NBI component invokes SO to create the end to end L1 subscriber service
SO interacts with SDC and based on the on-boarded service definition it will deduce that the A to Z service will consist of SP1 and SP2 Access L1 service and SP1 Access L1 service will in-turn have 2 inter domain L0/L1 services
SO will then communicates with partner ONAP through the Ext-API via MEF Interlude interface to trigger the creation of SP2 Access L1 service on the partner side
SO then interacts with CDS blue print processor to create the local side(SP1) Access L1 service
CDS blue print processor interacts with SDC catalog to understand the nested inter domain service definitions that are required to create the local side of Access L1 service
CDS blue print processor will then interact with A&AI to identify the end points for each of the multi domain services that are required to create the Access L1 service
CDS blue print processor will use the endpoints from A&AI and service definition defined in SDC catalog and then invoke the corresponding DG which calls the REST-API of Ext-Domain controller1 to create first part of L0/L1 service
CDS blue print processor will use the endpoints from A&AI and service definition defined in SDC catalog and then invoke the corresponding DG which calls the REST-API of Ext-Domain controller2 to create second part of L0/L1 service

## Slide 9: Optical Service Design & Instantiation – Phase2
SDC
SDN-C
CDS
Blue Print Processor
POLICY
Ext API / NBI
OOF
A&AI
Design Time
Service & Resource Catalog
Run Time
DG Plug-in(s)
Ext-Domain Controller1
Ext-Domain Controller2
Open Standard Network APIs
ONF T-API
Open Standard Network APIs OpenROADM
Register Intra domain Service definitions & End-To-End Inter service provider Service definition
10
13
14
16
17
18
19
20
15
INTERLUDE
SO
11
21
22
12

## Slide 10: References and Useful URLs
CDS Controller Design Studio Documentation
https://wiki.onap.org/display/DW/Controller+Design+Studio+%5BCDS%5D+Documentation
https://wiki.onap.org/display/DW/2019+Silicon+Valley+Meeting+Proposals?preview=/53248195/60889399/CDS%20-%20ONS%20NA%202019_v2.pptx
Proposed definitions for Allotted Network functions and Hierarchical Orchestration for 5G slice which we can use as reference for defining our service
https://wiki.onap.org/display/DW/2019+Silicon+Valley+Meeting+Proposals?preview=/53248195/60889445/Allotted%20Network%20Function%20Presentation%20-%202019%2004%2001.pptx
https://wiki.onap.org/display/DW/2019+Silicon+Valley+Meeting+Proposals?preview=/53248195/60889706/Hierarchical%20Orchestration%20Presentation%20-%202019%2004%2002.pptx