## Slide 1: Optical Service (L0/L1) Orchestration Use-case
Fujitsu Network Business Group (NBG)

## Slide 2: Problem Statement / Overview
Project Description
  Goal of this use case is to provide end to end multi-operator L1 service orchestration based on MEF L1 Subscriber and Operator service definitions across multiple optical transport domains
    Harmonize with proposal on incorporating MEF Interlude APIs
    https://wiki.onap.org/display/DW/Draft+Dublin+Interlude+High+Level+Requirement
  Each of the optical transport domains can be managed to create intra domain L0/L1 access service which are used in the over-all end to end L1 service
    Direct management via standard APIs such as OpenROADM, OpenConfig, etc
    Indirect management through a local domain controller via standard network and service models such as ONF T-API and OpenROADM
  The Optical service created above could then be adopted/embedded to provide optical transport for other blueprints like 5G Network slice across FH and MH/BH domains
Notes: Multi-domain/multi-layer

## Slide 3: Multi-Operator L1 Service
ONAP(SP1)
ONAP(SP2)
Domain Controller
Domain Controller
Subscriber
L1 Service
SP1 Access L1 Service
SP2 Access L1 Service
OTU4 L1 ENNI
A
Z
OSS/BSS
Open Standard Network APIs
ONF T-API
Optical Domain 1
Optical Domain 2
Optical Domain 1
Direct management via standard Device APIs such as OpenROADM, OpenConfig etc.
Open Standard Network APIs OpenROADM
L1 UNI (eg. 10GE)
L1 UNI (eg. 10GE)
Notes: Multi-domain/multi-layer

## Slide 4: Preliminary ONAP Workflow
SP1-ONAP
SDN-C
SP2-ONAP
SDN-C
SO
SO
Ext API / NBI
SDC
1
2
3a
4
5a
3
6
Ext API / NBI
5b
3b
A&AI
1d
4
A&AI
6
1c
1d
SDC
1b
1
1a
API Plug-in(s)
1c
6
Domain Controller
Domain Controller
Optical Domain 1 L0/L1
Optical Domain 2 L0/L1
Optical Domain 1 L0/L1
Optical Extensions
(e.g. Transport PCE)
ONF T-API
OpenROADM
Open, Standard Device APIs
(e.g. OpenROADM or Open Config etc)
INTERLUDE
1a
1b

## Slide 5: High Level ONAP Workflow
1. On-board the modeled end to end nested L1 Service into SDC of Service provider SP-ONAP and also to the Partner ONAP
1a. On-board on to both ONAPs SDC the required CSAR packages that are needed to create Access L1 service within the individual Operator domain
1b. Register the External controller/Network resource into A&AI component of both ONAPs ESR registry
1c. Based on registered network resources SDN-C will invoke the respective directed graph which will invoke the corresponding REST API to retrieve the network topology
1d. Map & save network topology to the A&AI schema
2. SP-ONAP gets a nested service Order from BSS to create a 10G pipe which spans across operator domains.
3. Ext-API/NBI component of ONAP-SP decomposes this nested request and communicates to partner ONAP via Interlude to create Access L1 service at Partner side
3a. NBI on ONAP-SP side invokes SO for creating provider side of Access L1 service
3b. NBI on ONAP-partner side invokes SO for creating partner side of Access L1 service
4. SO on both ONAP references Run Time SDC design and playbooks
5a. SO of ONAP-SP instantiates the provider side L1 service by invoking SDN-C
5b. SO of Provider ONAP instantiates the partner side L1 service by invoking SDN-C
6. SDN-C interacts with the respective external domain controller/devices to implement the respective service