## Slide 1: PNF software version in PNF upgrade in Frankfurt release
Fei Zhang (Ericsson)
09, Sep. 2019

## Slide 2: Up to date Status of PNF SW version in ONAP
5G Use Case in Frankurt, ONAP shall support PNF software upgrade in R6 Frankfurt
To support PNF software upgrade in R6 Frankfurt, it requires PNF software version in onboarding package. The backgroud and proposal was presented on ONAP R4 Resource IM Call 2019-6-17 (PNF software version)
The conclusion: non-MANO artifact is preferred and call a poll
  next step: copy the wiki page (ONAP R4+ Onboarding PNF package format, non-MANO artifacts set definition and PNF package mapping) to create a R6 version of non-MANO artifact; describe the detailed solutions on the new wiki page and ask for a poll on modeling subcommittee call
  ONAP R6+ Onboarding VNF/PNF package format, non-MANO artifacts set definition

## Slide 3: Dublin PNF onboarding package example
CSAR file
ROOT
MainServiceTemplate.mf
MainServiceTemplate.yaml
TOSCA-Metadata
Definitions
TOSCA.meta
Artifacts
Note:
This is an example of the package.
The files listed in the folder is example only. And not all files are listed here.
Folder / file name in blue is requested by SOL004v2.6.1.
Folder / file name in purple is requested by ONAP
Text in black is example only. It can be changed if there is a need
TOSCA-Meta-File-Version: 1.0
CSAR-Version: 1.1
Created-By: Ericsson (Zu Qiang 2018-12-03)
Entry-Definitions: Definitions/MainServiceTemplate.yaml
ETSI-Entry-Manifest: MainServiceTemplate.mf
ETSI-Entry-Change-Log: Artifacts/ChangLog.txt
Other
ChangeLog.txt
scripts
Yang_module
Measurements
Events
Informational
etsi_nfv_sol001_pnfd_2_5_1_types.yaml
etsi_nfv_sol001_vnfd_2_5_1_types.yaml
metadata:
pnfd_name: gNB
pnfd_provider: Ericsson
pnfd_archive_version:1.0
pnfd_release_date_time:2018-12-03T08:44:00-05:00
source: Definitions/MainServiceTemplate.yaml
source: Definitions/etsi_nfv_sol001_vnfd_2_5_1_types.yaml
source: Definitions/etsi_nfv_sol001_pnfd_2_5_1_types.yaml
non_mano_artifact_sets:
onap_ves_events:
source: Artifacts/Events/VES_registration.yaml
onap_pm_dictionary:
source: Artifacts/Measurements/PM_Dictionary.yaml
onap_yang_module:
source: Artifacts/Yang_module/Yang_module.yaml
onap_ansible_playbooks:
source: Artifacts/Playbooks/playbook.yml
onap_pnf_sw_information:
source:Artifacts/ pnf_sw_information /pnf_sw_information.yaml
onap_others:
source: Artifacts/scripts/install.sh
source: Artifacts/Informational/user_guide.txt
source: Artifacts/Other/installation_guide.txt
source: Artifacts/Other/review_log.txt
pnf_sw_information
    pnf_sw_information.yaml
description: "pnf software information"
provider: Ericsson
version: "1.0"
pnf_ software_infomation:
- description: "software version of PNF"
pnf_software_version: ”5gDUv18.05.201”
Notes: https://wiki.onap.org/display/DW/Csar+Structure

## Slide 4: Use Case
UC1:
  One more step to support PNF SW version in E2E Automation solution. Currently, SDC GUI (Resource composition GUI) allow operator manually to define the list of software versions by using SDC GUI. But no ONAP compoments use it today
UC2:
  To support Scenario 2 in PNF software upgrade in R6 Frankfurt, it requires PNF software version in onboarding package AND then can be used (Modelling/SDC/AAI/PNF).
Portal
VID
SDC
SO
ONAP Controller (SDNC/APPC)
PNF
AAI
CDS
distribution
SDC Resource Composition and
AID DM in SDC internal datamodel
Generic_PNF.yml
node_types:
org.openecomp.resource.abstract.nodes.PNF:
derived_from: tosca.nodes.Root
properties:
software_versions
type: list
VES specification: 5G PnP Registration Event
(PnfRegistration) on ONAP R5+ Common IM Clean
Attribute: softwareVersion  active SW
A&AI, PNF DataStructure: two attributes
element name="software-version
element name="sw-version"
-- Reserved for PNF SW UP UC, no
components use it in Dublin
-- For on-bording PNF package, no software_versions escriptor because it is fully complied with ETSI(no software_versions in PNFD in ETSI).
PNF on-boarding DM(TOSCA node types of PNFD)
Notes: Netconf connection setup (how to setup over TLS)

## Slide 5: Proposal of identifier of PNF SW version in the PNF non-mano artifact
NON-MANO Artifact Set Identifier name
  onap_pnf_sw_information
Proposal PNF SW version file:
  a specific onap_pnf_sw_information directory.
  .yaml format for pnf software version like pnf_sw_information.yaml
File Example
  pnf_sw_information.yaml
    description: "pnf software information"
    provider: Ericsson
    version: "1.0"
    pnf_ software_infomation:
    - description: "software version of PNF"
    pnf_software_version: ”5gDUv18.05.201”
During the on-boarding procedure, SDC shall transform pnf_sw_version into AID module(software_versions property of PNF)

## Slide 6: Next Step
  Get approved for key word
    onap_pnf_sw_information for non-MANO artifact Registered in ETSI&IANA
    .yaml format
    Key words in .yaml file
      pnf_ software_infomation:
      - pnf_software_version: ”5gDUv18.05.201”
  Update ONAP Non-MANO Artifacts Set Identifiers
  Update ONAP R6+ Onboarding VNF/PNF package format, non-MANO artifacts set definition
  Note: It is prerequisite for Code Commit in Frankfurt Release in PNF software upgrade in R6 Frankfurt.