## Slide 1: SW version intro in ONAP PNF package
Ericsson

## Slide 2: Background
PNFD is introduced in ETSI SOL001/IFA014
ONAP continue to develop 5G UCs PNF PnP and PNF on-boarding package and PNF SW UP on Dublin and forward
In current Dublin status, existed software_version(SW) (used or un-used) in below ONAP components
Portal
VID
SDC
SO
ONAP Controller (SDNC/APPC)
PNF
AAI
CDS
distribution
SDC Resource Composition and
AID DM in SDC internal datamodel
Generic_PNF.yml
node_types:
org.openecomp.resource.abstract.nodes.PNF:
derived_from: tosca.nodes.Root
properties:
software_versions
type: list
VES specification: 5G PnP Registration Event
(PnfRegistration) on ONAP R5+ Common IM Clean
Attribute: softwareVersion  active SW
A&AI, PNF DataStructure: two attributes
element name="software-version
element name="sw-version"
-- Reserved for PNF SW UP UC, no
components use it in Dublin
-- For on-bording PNF package, no software_versions escriptor because it is fully complied with ETSI(no software_versions in PNFD in ETSI).
PNF Common IM (Agreed PNFD Model )
PNF on-boarding DM(TOSCA node types of PNFD)
-- SDC GUI (Resource composition GUI) allow operator manually to define the list of software versions by using SDC GUI. But no ONAP compoments use it today
-- PNF Common IM does not include
the sw version today.
Notes: Netconf connection setup (how to setup over TLS)

## Slide 3: NEED OF PNF Software version
An unique identifier is needed in multiple steps during the Sw Upgrade
  If PNF needs download Software image, it needs identifier to find out correct image
  Package deliver using a unique identifier to identify the delivered function/product
  Upgrade GUI: unique identifier is needed to identify source software version and target software version
  PNF registration: report a unique identifier to indicate which function is enabled in the box.
  Schema/artifact update in different PNF sw versions, needs distinguishing target package and included artifacts/schema to be updated to support new upgraded box
More useful for vendor/operator to get running software version from OSS for troubleshooting, auto-upgrade informaction collecting at so on.
Current related identifier for PNFD in ETSI and ONAP. In both ETSI and ONAP, no human readable identifier for PNF box
  ETSI
    descriptor_id, indescriptor_invariant_id, version(for descriptor) in ETSI PNFD, not identifier of PNF
    functionDescription property in ETSI PNFD is description/string, but not an identifier/integer
  ONAP
    Descriptor ID, resource UUID / invariantUUID in ONAP are all unique. However it is meaningless for human who initiating a LCM procedure. Besides, there is no way to find it’s identifier in the PNF box.
  Note: Unique Identifier either Sw_version or product_version ? It really does not matter.
Operator
Portal
VID
SDC
SO
ONAP Controller (SDNC)
PNF
2
3
4
5
6
7
AAI
Vendor
SFTP Server
CDS
distribution
3
4
6
1
1
Notes: Netconf connection setup (how to setup over TLS)

## Slide 4: Introduction of PNF sw version in the onboarded package:
Onboarding CSAR
Artifacts
Info
Changlog.txt
Events
VES_registration.yaml
Measurements
PM_Dictionary.yaml
Yang_module
yang_modile.yang
Root
TOSCA-Metadata
TOSCA.meta
MainServiceTemplate.mf
Definitions
etsi_nfv_sol004_pnfd_2_5_1_types.yml
etsi_nfv_sol004_vnfd_2_5_1_types.yml
ManiServiceTemplate.yaml
pnf_sw_information
pnf_sw_information.yaml
Option 1: additional non-mano artifact introduced in the xNF package containing the PNF sw version parameter onap_pnf_sw_information
Option 2: additional properties in ETSI PNFD
Properties:
software_version: 5gDUv18.05.201
    pnf_sw_information.yaml
description: "pnf software information"
provider: Ericsson
version: "1.0"
pnf_ software_infomation:
- description: "software version of PNF"
pnf_software_version: ”5gDUv18.05.201”
metadata:
pnfd_name: gNB
pnfd_provider: Ericsson
pnfd_archive_version:1.0
pnfd_release_date_time:2018-12-03T08:44:00-05:00
source: Definitions/MainServiceTemplate.yaml
source: Definitions/etsi_nfv_sol001_vnfd_2_5_1_types.yaml
source: Definitions/etsi_nfv_sol001_pnfd_2_5_1_types.yaml
non_mano_artifact_sets:
onap_ves_events:
source: Artifacts/Events/VES_registration.yaml
onap_pm_dictionary:
source: Artifacts/Measurements/PM_Dictionary.yaml
onap_yang_module:
source: Artifacts/Yang_module/Yang_module.yaml
onap_ansible_playbooks:
source: Artifacts/Playbooks/playbook.yml
onap_others:
source: Artifacts/scripts/install.sh
sousource: Artifacts/Informational/user_guide.txt
source: Artifacts/Other/installation_guide.txt
source: Artifacts/Other/review_log.txt
onap_pnf_sw_information:
source:Artifacts/pnf_sw_information/pnf_sw_information.yaml

## Slide 5: OPTIONs COMPARISON
OPTIONs | ETSI impacts | ONAP impacts | Comments/Preferred options
Option 1: additional non-mano artifact | No | SDC on-boarding with new artifact SDC mapping to AID model (SO , AAI, Portal, VID as part of the PNF sw upgrade) | First preferred option ONAP can extend it in the future for other purpose
Option 2: additional property in ETSI PNFD | Yes, new property | SDC on-boarding with new PNFD SDC mapping to AID model (SO , AAI, Portal, VID as part of the PNF sw upgrade) | Alternative in case more companies can sustain this option in ETSI Pros: ETSI extension, alignment to VNFD, various Usecases...