## Slide 1: model-driven DMaaP Agent
by SDN-R team
2019 August

## Slide 2: µService communication to NetConf device – Summer 2019
In the current architecture each µService can use the on-the-fly autogenerated RestConf interfaces of ODL to communicate with NetConf controlled devices.
Perfect!!! ;)
… but,
Experience showed that the independent µServices are not aligned (and should not be aligned), which leads to repeated GET requests to the devices.
It also happened the concurrent configurations by the µServices lead to errors and misbehavior (e.g. Device is locked, …)
µServices needs to know which SDN-C instance is “responsible” for a certain NetConf session to the device.
Idea:
ONAP components usually communication via the message bus DMaaP.
How to use DMaaP in this scenario?
µService #1
ODL/CCSDK/SDN-C
µService #2
µService #3
NetConf device
NetConf Server
NetConf Client
RestConf Server
RestConf Client
RestConf Client
RestConf Client
NetConf/Yang
RestConf/Yang
Controller NBIs and SBIs are defined by the same YANG modules. ODL automatically provides RestConf and NetConf interfaces based on exposed YANG modules by devices.

## Slide 3: µService communication to NetConf device – 2020
Using a message bus by µServices gives the advantages, that the communication to a certain NetConf device can be done
avoiding that data is requested from the devices twice (in a short time period – e.g. re-connect), µService x can subscribe for responses of µService y.
without knowing the master controller of the NetConf connection for this device.
The previous RestConf commination is not affected.
All NetConf/RestConf operations should be supported.
ODL/CCSDK/SDN-C
NetConf device#A
NetConf Server
NetConf Client
RestConf Server
NetConf/Yang
md-DMaaP
µService #1
ODL/CCSDK/SDN-C
µService #2
µService #3
NetConf device#1
NetConf Server
NetConf Client
RestConf Server
RestConf Client
DMaaP Agent
DMaaP Agent
NetConf/Yang
RestConf/Yang
md-DMaaP
DMaaP

## Slide 4: Thank you very much!
Martin Skorupski
highstreet technologies System Architect
ONAP: https://wiki.onap.org/display/~demx8as6
Skype: martin.skorupski
WhatsApp: +49 172 317 04 88
E-Mail: martin.skorupski@highstreet-technologies.com
Web: https://www.highstreet-technologies.com