## Slide 1: ONAP/3GPP & ORAN Alignment use case August 19, 2019 Marge Hillis, Vimal Begwani

## Slide 2: O-RAN Target Architecture for Disaggregated Radio Network
NFVI Platform: Virtualization layer and COTS platform
E2
A1
E2
CU-UP
CU-CP
RAN RRU: PHY-low/RF
Radio-Network Information Base
Applications Layer
SDAP
PDCP-U
RRC
PDCP-C
3GPP E1
Orchestration
VNF
Mgmt
VIM
A1: RAN Intelligent Controller (RIC) near -RT
CU HW
Orchestration & Automation (e.g. ONAP/MANO), NMS
Policy
Inventory
Design
Configuration
RAN Analytics, model training & control
(RIC non-RT)
Multi-RAT CU Protocol Stack
RAN DU: RLC/MAC/PHY-high
NGFI-I
Radio Connection Mgmt
Mobility
Mgmt
QoS
Mgmt.
Interference
Mgmt
3rd party APP
Trained Model
Modular CU SW
3GPP F1
O1
O1

## Slide 3: O-RAN O1 & A1 Specifications:
O-RAN Alliance has defined OA&M specifications (called O1) for disaggregated Radio Access Network.
  It leverages 3GPP as much as possible
  Specifications are management frame neutral
  It covers FCAP functions (Fault, Configuration, Performance, etc.)
  O1 specifications also cover software upgrade
O-RAN also introduce a new interface called A1.
  A1 interface is an open logical interface between non-RT RIC functionality in the Orchestration/management platform and near-RT RIC functionality in RAN of O-RAN architecture.
  A1 interface should enable a multi-vendor environment, and is independent of specific implementation of the Orchestration/management platform, non-RT RIC, and near-RT RIC.
  A1 interface should enable policy-based guidance of radio resource management and control functions or applications that are internal to the near-RT RIC.

## Slide 4: OA&M Architecture for Disaggregated RAN
Near-Real Time RAN Intelligent Controller (RIC)
O-CU-CP
O-CU-UP
O-DU
O-RU
Non-Real Time RIC
Infrastructure – COTS / White Box / Peripheral Hardware & Virtualization layer
Infrastructure Management Framework
O1
VIM
O1*
Whitebox H/W
Virt
~NfVi
O1
O1
O1
O1
Open Fronthaul Interface
F1-c
A1
F1-u
E1
E2
Service Management & Orchestration (e.g. ONAP)

## Slide 5: ONAP/3GPP & O-RAN Alignment Work
Provisioning Management
  Three New CM VES notifications notifyMOICreation, notifyMOIDeletion, notifyMOIAttributeValueChange.
Fault Supervision
  Align existing VES fault event or create new VES fault3gpp event to support harmonization work in TS 28.532.
Performance Assurance/File Management
  Modify the changeIdentifier field name of the fileReady event to filetype indicating the type of file that is ready for upload (call trace, log, certificate, beamforming etc.) or add a new field fileType for this purpose

## Slide 6: ONAP/3GPP & O-RAN Alignment Work
PNF Registration
  ONAP modifications to support the addressing of MEs behind a NAT
  Potential modification of pnfRegistration event when 3GPP completes harmonization activity.
PNF SW Management
  Ensure O-RAN PNF Software Management can be supported in ONAP
    O1 PNF Software Management specifies the order, behavior, input and output for each step.
    O-RAN needs ONAP to support workflow order, events, and steps specified in the O1.
      Order and behavior of steps is different in ONAP proposals in Frankfurt; e.g. pre-check, update AAI, post-check.
  Definition of additional Notifications (VES events)
    resetReason Notification
    softwareActivate Notification
    downloadFile Notification

## Slide 7: ONAP/3GPP & O-RAN Alignment Work
A1 Interface introduction
  A1 interface between Non-Real Time RIC and the Near Real Time RIC to transmit Policy and optimization information to the Near Real Time RIC and carry responses (e.g. policy applied, couldn’t be applied etc)
  A1 interface to be defined by WG2 in O-RAN in September.
  Evaluation of impact to follow

## Slide 8: Status
Evaluating Project impacts for the work items
Prioritizing work items to be addressed in Frankfurt

## Slide 9: Goals for Frankfurt
A1 Interface Introduction
Fault Assurance alignment of fault event to fault3gpp
fileReady field name change or the addition of a new field to specify the fileType.
CM notification events defined in VES, supported in DCAE and DMaaP