## Slide 1: ONAP/3GPP & ORAN Alignment use case August 14, 2019 Marge Hillis, Vimal Begwani

## Slide 2: ONAP/3GPP & O-RAN Alignment Work
Provisioning Management
  Three New CM VES notifications notifyMOICreation, notifyMOIDeletion, notifyMOIAttributeValueChange.
Fault Supervision
  Align existing VES fault event or create new VES fault3gpp event to support harmonization work in TS 28.532.
Performance Assurance/File Management
  Modify the changeIdentifier field name of the fileReady event to filetype indicating the type of file that is ready for upload (call trace, log, certificate, beamforming etc) or add a new field fileType for this purpose

## Slide 3: ONAP/3GPP & O-RAN Alignment Work
PNF Registration
  ONAP modifications to support the addressing of MEs behind a NAT
  Potential modification of pnfRegistration event when 3GPP completes harmonization activity.
PNF SW Management
  Ensure O-RAN PNF Software Management can be supported in ONAP
    O1 PNF Software Management specifies the order, behavior, input and output for each step.
    O-RAN needs ONAP to support workflow order, events, and steps specified in the O1.
      Order and behavior of steps is different in ONAP proposals in Frankfurt; e.g. pre-check, update AAI, post-check.
  Definition of additional Notifications (VES events)
    resetReason Notification
    softwareActivate Notification
    downloadFile Notification

## Slide 4: ONAP/3GPP & O-RAN Alignment Work
A1 Interface introduction
  A1 interface between Non-Real Time RIC and the Near Real Time RIC to transmit Policy and optimization information to the Near Real Time RIC and carry responses (e.g. policy applied, couldn’t be applied etc)
  A1 interface to be defined by WG2 in O-RAN in September.
  Evaluation of impact to follow

## Slide 5: Status
Evaluating Project impacts for the work items
Prioritizing work items to be addressed in Frankfurt

## Slide 6: Goals for Frankfurt
A1 Interface Introduction
Fault Assurance alignment of fault event to fault3gpp
fileReady field name change or the addition of a new field to specify the fileType.
CM notification events defined in VES, supported in DCAE and DMaaP