## Slide 1: PNFD Model Mapping ETSI DM  SDC AID / AAI schema Ericsson
2019-08-05

## Slide 2: PNF(D) comparison

## Slide 3: PNFD in ETSI NFV IFA014 v2.5.1 (base for Resource IM)
Attribute | Qualifier | Cardinality | Content | Description
pnfdId | M | 1 | Identifier | Identifier of this Pnfd information element. It uniquely identifies the PNFD.
functionDescription | M | 1 | String | Describes the PNF function
provider | M | 1 | String | Identifies the provider of the PNFD. (NOTE: The provider of the PNFD might be different from the provider of the PNF.)
version | M | 1 | Version | Identifies the version of the PNFD.
pnfdInvariantId | M | 1 | Identifier | Identifies a PNFD in a version independent manner. This attribute is invariant across versions of PNFD.
name | M | 1 | String | Provides the human readable name of the PNFD.
pnfExtCp | M | 1..N | PnfExtCpd | Specifies the characteristics of one or more connection points where to connect the PNF to a VL. See clause 6.6.4.
security | M | 0..1 | SecurityParameters | Provides a signature to prevent tampering.
geographicalLocationInfo | M | 0..1 | Not specified | It provides information about the geographical location (e.g. geographic coordinates or address of the building, etc.) of the PNF. The cardinality 0 is used when the location is unknown.

## Slide 4: PNF in ETSI NFV SOL001 v2.5.1 (used in PNF package)
Property name | Required | Type | Constraints | Description
descriptor_id | yes | string | (UUID format) | Identifier of this PNFD information element. It uniquely identifies the PNFD.
function_description | yes | string |  | Describes the PNF function.
provider | yes | string |  | Identifies the provider of the PNFD.
version | yes | string |  | Identifies the version of the PNFD.
descriptor_invariant_id | yes | string | (UUID format) | Identifier of this PNFD in a version independent manner. This attribute is invariant across versions of PNFD.
name | yes | string |  | Name to identify the PNFD.
geographical_location_info | no | tosca.datatype.nfv.LocationInfo |  | Provides information about the geographical location (e.g. geographic coordinates or address of the building, ...) of the PNF.
Requirement name | Required | Type | Constraints | Description
virtual_link | yes | tosca.nodes.nfv.VnfVirtualLink |  | Describes the requirements for linking to virtual link
Requirements:
Properties:

## Slide 5: PNF in ONAP R3 SDC AID data model org.openecomp.resource.abstract.nodes.PNF, derived_from: tosca.nodes.Root
Name | Required | Type | Description | Specified in | Value currently set by
invariantUUID | Yes | string | Constant identifier of the resource model. Ex.: AA97B177-9383-4934-8543-0F91A7A02836 | SDC DM, Node Type Metadata | SDC sets internally at resource creation
uuid | Yes | string | Versioned identifier of the resource model (this uuid is changed for every major version of the resource) Ex.: b8ff69ca-786d-479e-9f9c-217a90ee0ebc | SDC DM, Node Type Metadata | SDC sets internally at resource creation
customizationUUID | Yes | string | Identifier of the resource instance (uuid of the specific use of the resource model in this service). This identifier is regenerated whenever a user makes a change on the resource instance. Ex.: 38e5fb81-5e8c-479b-9140-38786db19967 | SDC DM, Node Type Metadata | SDC sets internally at resource creation
version | Yes | string | The resource version in SDC catalog. Two digit blocks separated by a dot (“.”). Ex. : “2.0” | SDC DM, Node Type Metadata | SDC sets internally at resource creation
type | Yes | string (enum) | The type of resource. Resource type can be either VF, VFC, VFCMT, CP or VL. Ex. “VF” | SDC DM, Node Type Metadata | SDC sets internally to “PNF” at resource creation (enum hardcoded)
name | Yes | string | The name of the resource. Ex. “vMME” | SDC DM, Node Type Metadata | Using SDC UI, at PNF resource def.
description | Yes | string | Description of the resource | SDC DM, Node Type Metadata | Using SDC UI, at PNF resource def.
resourceVendor | Yes | string | String value that specifies the vendor providing this asset | SDC DM, Node Type Metadata | Using SDC UI, at PNF resource def.
resourceVendorRelease | Yes | string | String value that specifies the release version given by the vendor (no exact correlation to the version of the asset in the SDC catalog) | SDC DM, Node Type Metadata | Using SDC UI, at PNF resource def.
resourceVendorModelNumber | No | string | The value for this field is the part number defined by the vendor, e.g. “MX960” | SDC DM, Node Type Metadata | Using SDC UI, at PNF resource def.
category | Yes | string (enum) | Category of the resource. Ex. “Application L4+” | SDC DM, Node Type Metadata | Using SDC UI, at PNF resource def. (enum also managed in SDC UI)
subcategory | Yes | string (enum) | Sub-category of the resource. Ex. “Load Balancer” | SDC DM, Node Type Metadata | Using SDC UI, at PNF resource def. (enum also managed in SDC UI)
nf_function | No | string | String property defining a generic type (like category) of the PNF. | PNF node type and VF | Using SDC UI, at service definition
nf_role | No | string | String property for short code that defines a Network function that the Vendor Software or PNF is providing. E.g. vCE, vARM | PNF node type and VF | Using SDC UI, at service definition
nf_type | No | string | String property that provides English description of the functionality of the PNF in the Service context | PNF node type and VF | Using SDC UI, at service definition
software_versions | No | list of string | ? | PNF node type (but not in the AIM Word doc!) | Using SDC UI, at service definition
Notes: Ref: https://wiki.onap.org/display/DW/ONAP+SDC+AID+Data+Model

## Slide 6: Mapping: SOL001 PNFD vs. ONAP R3 SDC AID DM PNF
Current PNFD, SOL001 | Current PNF, AID DM | Handling
provider | resourceVendor | SDC can be populated with initial value from PNFD
name | name | SDC can be populated with initial value from PNFD
function_description | description | SDC can be populated with initial value from PNFD
descriptor_id | uuid | Needs to be generated by SDC to be unique. Updated by SDC when the PNFD is updated by user.
descriptor_invariant_id | invariantUUID | Needs to be generated by SDC to be unique. Populated when the CSAR file is imported, and then value is constant.
version | - | No equivalent in SDC, needs to be added
geographical_location_info | - | Not in R4
- | customizationUUID | ID of resource instance, set internally by SDC  not from vendor PNFD. Updated by SDC when the PNFD is updated by user.
- | version | Resource version in SDC catalog, set internally by SDC  not from vendor PNFD. Updated by SDC when the PNFD is updated by user.
- | type | Hardcoded to PNF based on TOSCA node type in PNFD
- | category | Local to SDC UI, needs to be entered in SDC
- | subcategory | Local to SDC UI, needs to be entered in SDC
- | resourceVendorRelease | Add to SOL001?
- | resourceVendorModelNumber | Add to SOL001?
- | nf_function | Specified as part of service def  not from vendor PNFD
- | nf_role | Specified as part of service def  not from vendor PNFD
- | nf_type | Specified as part of service def  not from vendor PNFD
- | software_versions | Specified as part of service def  not from vendor PNFD

## Slide 7: PNF in AAI schema v.16 (1/2)
Attribute name | Type | minOccurs | Metadata | Description
pnf-name | xs:string | 0 | isKey=true | unique name of Physical Network Function.
pnf-name2 | xs:string | 0 |  | name of Physical Network Function.
selflink | xs:string | 0 |  | URL to endpoint where AAI can get more details.
pnf-name2-source | xs:string | 0 |  | source of name2
pnf-id | xs:string | 0 |  | id of pnf
equip-type | xs:string | 0 |  | Equipment type. Source of truth should define valid values.
equip-vendor | xs:string | 0 |  | Equipment vendor. Source of truth should define valid values.
equip-model | xs:string | 0 |  | Equipment model. Source of truth should define valid values.
management-option | xs:string | 0 |  | identifier of managed by ATT or customer
orchestration-status | xs:string | 0 |  | Orchestration status of this pnf
ipaddress-v4-oam | xs:string | 0 |  | ipv4-oam-address with new naming convention for IP addresses
sw-version | xs:string | 0 |  | sw-version is the version of SW for the hosted application on the PNF.
in-maint | xs:boolean | 0 | defaultValue="false" | Used to indicate whether or not this object is in maintenance mode (maintenance mode = true). This field (in conjunction with prov-status) is used to suppress alarms and vSCL on VNFs/VMs.
frame-id | xs:string | 0 |  | ID of the physical frame (relay rack) where pnf is installed.
serial-number | xs:string | 0 |  | Serial number of the device
ipaddress-v4-loopback-0 | xs:string | 0 |  | IPV4 Loopback 0 address
ipaddress-v6-loopback-0 | xs:string | 0 |  | IPV6 Loopback 0 address
ipaddress-v4-aim | xs:string | 0 |  | IPV4 AIM address
ipaddress-v6-aim | xs:string | 0 |  | IPV6 AIM address
ipaddress-v6-oam | xs:string | 0 |  | IPV6 OAM address
inv-status | xs:string | 0 |  | CANOPI's inventory status. Only set with values exactly as defined by CANOPI.
resource-version | xs:string | 0 |  | Used for optimistic concurrency. Must be empty on create, valid on update and delete.
prov-status | xs:string | 0 |  | Prov Status of this device (not under canopi control) Valid values [PREPROV/NVTPROV/PROV]
nf-role | xs:string | 0 |  | Nf Role is the role performed by this instance in the network.
admin-status | xs:string | 0 |  | admin Status of this PNF
operational-status | xs:string | 0 |  | Store the operational-status for this object.
Cont…

## Slide 8: PNF in AAI schema v.16 (2/2)
Attribute name | Type | minOccurs | Metadata | Description
model-customization-id | xs:string | 0 |  | Store the model-customization-id for this object.
model-invariant-id | xs:string | 0 | visibility="deployment", requires="model-version-id", dbAlias="model-invariant-id-local" | The ASDC model id for this resource model.
model-version-id | xs:string | 0 | visibility="deployment", requires="model-invariant-id", dbAlias="model-version-id-local", privateEdge="service-design-and-creation/models/model/{model-invariant-id}/model-vers/model-ver/{model-version-id}" | The ASDC model version for this resource model.
pnf-ipv4-address | xs:string | 0 |  | This is the IP address (IPv4) for the PNF itself. This is the IPv4 address that the PNF iself can be accessed at.
pnf-ipv6-address | xs:string | 0 |  | This is the IP address (IPv6) for the PNF itself. This is the IPv6 address that the PNF iself can be accessed at.
(containment ref) | tns:software-versions | 0 |  | 
(containment ref) | tns:relationship-list | 0 |  | 
(containment ref) | tns:p-interfaces | 0 |  | 
(containment ref) | tns:lag-interfaces | 0 |  | 
(containment ref) | tns:vrfs | 0 |  | 

## Slide 9: Agreed Resource IM PNFD  AAI schema v.16 PNF
Resource IM attribute name | Type | Multiplicity | Description | AAI class/attribute name | Description
version | Version | 1 | Identifies the version of the PNFD | PnfType: modelVersionId | The ASDC model version for this resource model.
security | SecurityParameters | 0..1 | Provides a signature to prevent tampering. |  | 
provider | String | 1 | Identifies the provider of the PNFD. NOTE: The provider of the PNFD might be different from the provider of the PNF. | PnfType: equipVendor ? | Equipment vendor. Source of truth should define valid values.
pnfdInvariantId | Identifier | 1 | Identifies a PNFD in a version independent manner. This attribute is invariant across versions of PNFD. | PnfType: model-invariant-id | The ASDC model id for this resource model.
pnfdId | Identifier | 1 | Identifier of this Pnfd class. It uniquely identifies the PNFD. |  | 
name | String | 1 | Provides the human readable name of the PNFD. | PnfType: pnfName/pnfName2 ? | name of Physical Network Function
functionDescription | String | 1 | Describes the PNF function. |  | 
_pnfExtCpd | PnfExtCpd | 1..* | Specifies the characteristics of one or more connection points where to connect the PNF to a VL. | PInterfaceType/LagInterfaceType | 
Notes: Ref: https://wiki.onap.org/display/DW/Agreed+PNFD+Model

## Slide 10: PnfCp(D) comparison

## Slide 11: PnfExtCpd in ETSI NFV IFA014 v2.5.1
All attributes are inherited from Cpd as defined in IFA014 (NOTE! Not aligned with the IFA011 definition used by VNF):
Attribute | Qualifier | Cardinality | Content | Description
cpdId | M | 1 | Identifier | Identifier of this Cpd information element.
layerProtocol | M | 1..N | Enum | Identifies a protocol that the connection points corresponding to the CPD support for connectivity purposes (e.g. Ethernet, MPLS,ODU2, IPV4, IPV6, Pseudo-Wire, etc.). (This information determines, amongst other things, which type of address to assign to the connection point at instantiation time.)
cpRole | M | 0..1 | String | Identifies the role of the connection points corresponding to the CPD in the context of the traffic flow patterns in the VNF, PNF or NS. For example an NS with a tree flow pattern within the NS will have legal cpRoles of ROOT and LEAF.
description | M | 0..1 | String | Provides human-readable information on the purpose of the connection point (e.g.connection point for control plane traffic).
trunkMode | M | 0..1 | Boolean | Information about whether the Cp instantiated from this CPD is in Trunk mode (802.1Q or other). When operating in "trunk mode", the Cp is capable of carrying traffic for several VLANs. A cardinality of 0 implies that trunkMode is not configured for the Cp i.e. It is equivalent to Boolean value "false".

## Slide 12: PnfExtCp in ETSI NFV SOL001 v2.5.1
Requirement name | Required | Type | Constraints | Description
external_virtual_link | no | tosca.capabilities.nfv.VirtualLinkable |  | Specifies that CP instances require to be connected to a node that has a VirtualLinkable capability.
All properties of PnfExtCp node type are derived from Cp node type, which has a common definition with VNF in ETSI:
Property name | Required | Type | Constraints | Description
layer_protocols | yes | list of string | Valid values: ethernet, mpls, odu2, ipv4, ipv6, pseudo-wire | Identifies which protocol the connection point uses for connectivity purposes.
role | no | string | valid values: root, leaf | Identifies the role of the port in the context of the traffic flow patterns in the VNF or parent NS. For example a VNF with a tree flow pattern within the VNF will have legal cpRoles of ROOT and LEAF.
description | no | string |  | Provides human-readable information on the purpose of the connection point (e.g. connection point for control plane traffic).
protocol | no | list of tosca.datatypes.nfv.CpProtocolData |  | Provides information on the addresses to be assigned to the connection point(s) instantiated from this Connection Point Descriptor.
trunk_mode | no | boolean |  | Information about whether the CP instantiated from this Cp is in Trunk mode (802.1Q or other). When operating in "trunk mode", the Cp is capable of carrying traffic for several VLANs. Absence of this property implies that trunkMode is not configured for the Cp i.e. It is equivalent to boolean value "false".
Requirements:

## Slide 13: PnfExtCp datatypes CpProtocolData & AddressData in ETSI NFV SOL001 v2.5.1
Property name | Required | Type | Constraints | Description
address_type | yes | string | Valid values: mac_address ip_address. | Describes the type of the address to be assigned to a connection point The content type shall be aligned with the address type supported by the layerProtocol property of the connection point.
l2_address_data | no | tosca.datatypes.nfv.L2AddressData | Shall be present when the address_type is mac_address. | Provides the information on the MAC addresses to be assigned to a connection point.
l3_address_data | no | tosca.datatypes.nfv.L3AddressData | Shall be present when the address_type is ip_address. | Provides the information on the IP addresses to be assigned to a connection point.
tosca.datatypes.nfv.CpProtocolData (common definition with VNF in ETSI):
Property name | Required | Type | Constraints | Description
associated_layer_protocol | yes | string | Valid values: ethernet, mpls, odu2, ipv4, ipv6, pseudo-wire | One of the values of the property layer_protocols of the CP.
address_data | no | list of tosca.datatypes.nfv.AddressData |  | Provides information on the addresses to be assigned to the CP.
tosca.datatypes.nfv.AddressData (common definition with VNF in ETSI):

## Slide 14: extCp in ONAP R3 SDC AID data model (1/2) org.openecomp.resource.cp.v2.extCP, derived_from: org.openecomp.resource.cp.nodes.network.Port
Name | Required | Type | Description | Specified in | Value currently set by
invariantUUID | Yes | string | Constant identifier of the resource model. Ex.: AA97B177-9383-4934-8543-0F91A7A02836 | SDC DM, Node Type Metadata | SDC sets internally at resource creation
uuid | Yes | string | Versioned identifier of the resource model (this uuid is changed for every major version of the resource) Ex.: b8ff69ca-786d-479e-9f9c-217a90ee0ebc | SDC DM, Node Type Metadata | SDC sets internally at resource creation
customizationUUID | Yes | string | Identifier of the resource instance (uuid of the specific use of the resource model in this service). This identifier is regenerated whenever a user makes a change on the resource instance. Ex.: 38e5fb81-5e8c-479b-9140-38786db19967 | SDC DM, Node Type Metadata | SDC sets internally at resource creation
version | Yes | string | The resource version in SDC catalog. Two digit blocks separated by a dot (“.”). Ex. : “2.0” | SDC DM, Node Type Metadata | SDC sets internally at resource creation
type | Yes | string (enum) | The type of resource. Resource type can be either VF, VFC, VFCMT, CP or VL. Ex. “VF” | SDC DM, Node Type Metadata | SDC sets internally to “CP” at resource creation (enum hardcoded)
name | Yes | string | The name of the resource. Ex. “vMME” | SDC DM, Node Type Metadata | Using SDC UI, at CP resource def.
description | Yes | string | Description of the resource | SDC DM, Node Type Metadata | Using SDC UI, at CP resource def.
resourceVendor | Yes | string | String value that specifies the vendor providing this asset | SDC DM, Node Type Metadata | Using SDC UI, at CP resource def.
resourceVendorRelease | Yes | string | String value that specifies the release version given by the vendor (no exact correlation to the version of the asset in the SDC catalog) | SDC DM, Node Type Metadata | Using SDC UI, at CP resource def.
resourceVendorModelNumber | No | string | The value for this field is the part number defined by the vendor, e.g. “MX960” | SDC DM, Node Type Metadata | Using SDC UI, at CP resource def.
category | Yes | string (enum) | Category of the resource. Ex. “Application L4+” | SDC DM, Node Type Metadata | Using SDC UI, at CP resource def.
subcategory | Yes | string (enum) | Sub-category of the resource. Ex. “Load Balancer” | SDC DM, Node Type Metadata | Using SDC UI, at CP resource def.
network_role | Yes | string | identical to VL network_role | Property inherited from Port | Using SDC UI(?)
order | Yes | integer | The order of the CP on the compute instance (e.g. eth2). | Property inherited from Port | Using SDC UI(?)
network_role_tag | Yes | string | Must correlate to the set of defined “network-role” tag identifiers from the associated HEAT template | Property inherited from Port | Using SDC UI(?)
Cont…
Notes: Ref: https://wiki.onap.org/display/DW/ONAP+SDC+AID+Data+Model

## Slide 15: extCp in ONAP R3 SDC AID data model (2/2) org.openecomp.resource.cp.v2.extCP, derived_from: org.openecomp.resource.cp.nodes.network.Port
Name | Required | Type | Description | Specified in | Value currently set by
mac_requirements | No | org.openecomp.datatypes.network.MacRequirements | identifies MAC address assignments to the CP | Property inherited from Port | Using SDC UI(?)
vlan_requirements | No | list, entry_schema: type: org.openecomp.datatypes.network.VlanRequirements | identifies vlan address assignments to the CP | Property inherited from Port | Using SDC UI(?)
ip_requirements | Yes | list, entry_schema: type: org.openecomp.datatypes.network.IpRequirements | identifies IP requirements to the CP | Property inherited from Port | Using SDC UI(?)
exCP_naming | No? | org.openecomp.datatypes.Naming |  | Property inherited from Port | Using SDC UI(?)
subnetpoolid | No? | string |  | Property inherited from Port | Using SDC UI(?)
subinterface_indicator | No | boolean | identifies if Port is having Sub Interface | Property inherited from Port | Using SDC UI(?)
related_networks | No | list, entry_schema: type: org.openecomp.datatypes.network.RelatedNetworksAssignments | Related Networks List. | Property inherited from Port | Using SDC UI(?)
org.openecomp.datatypes.network.IpRequirements, derived_from: org.openecomp.datatypes.Root:
Property name | Required | Type | Constraints | Description
ip_version | Yes | integer | valid_values: 4, 6 | 
ip_count | No | integer |  | identifies the number of ip address to assign to the CP from the plan
floating_ip_count | No | integer |  | 
subnet_role | No | string |  | 
assingment_method | Yes | string | valid_values: fixed, dhcp | 
dhcp_enabled | No | boolean |  | 
ip_count_required | No | org.openecomp.datatypes.AssignmentRequirements |  | identifies the number of ip address to assign to the CP from the plan
floating_ip_count_required | No | org.openecomp.datatypes.AssignmentRequirements |  | 
ip_address_plan_name | No | string |  | 
vrf_name | No | string |  | 
Notes: Ref: https://wiki.onap.org/display/DW/ONAP+SDC+AID+Data+Model

## Slide 16: Transform tosca.nodes.nfv.PnfExtCp to org.openecomp.resource.cp.v2.extCP in Dublin
The node instance name “MyExtCP-1” : ETSI node instance name can be used when creating SDC AID node instance.
The same number of node instance can be created in SDC AID
The ‘metadata’ has to be generated by SDC.
The capabilities / requirements are added under substitution_mappings by SDC.
The ‘properties’ mapping from ETSI tosca.nodes.nfv.Cp can follow the following rules:
  If tosca.nodes.nfv.Cp.layer_protocols = ‘ipv4’ or ‘ipv6’, then org.openecomp.resource.cp.v2.extCP. ip_requirements [ IpRequirements: ip_version {4, 6}, assingment_method {dhcp or fixed} ]
  A default value can be assigned to assingment_method.
Open issues
  Some proprieties are mandatory in SDC AID org.openecomp.resource.cp.v2.extCP, including network_role, order, network_role_tag, and ip_requirements. However in it does not appear in the SDC generated PNF csar. AP on Ofir to check if there is any updates in SDC AID model.

## Slide 17: Location comparison

## Slide 18: PNF datatypes LocationInfo & CivicAddressElement in ETSI NFV SOL001 v2.5.1
Name | Required | Type | Constraints | Description
country_code | yes | string |  | Shall be a two-letter ISO 3166 country code in capital letters.
civic_address_element | no | list of tosca.datatypes.nfv.CivicAddressElement |  | Elements composing the civic address where the PNF is deployed.
tosca.datatypes.nfv.LocationInfo: geographical information on the location where a PNF is deployed
Name | Required | Type | Constraints | Description
ca_type | yes | string |  | Describe the content type of caValue. The value of caType shall comply with Section 3.4 of IETF RFC 4776.  A one-octet descriptor of the data civic address value. (NB: effectively an enum, see following slide)
ca_value | yes | string |  | Content of civic address element corresponding to the caType. The format caValue shall comply with section 3.4 of IETF RFC 4776  The civic address value, as described in detail in IETF RFC 4776.
tosca.datatypes.nfv.CivicAddressElement: an element of a civic location as specified in IETF

## Slide 19: IETF RFC 4776 definition of CAtype
CAtype | label/ NENA/PIDF | description | examples
1 | A1 | national subdivisions (state, canton, region, province, prefecture) | 
2 | A2 | county, parish, gun (JP), district (IN) | 
3 | A3 | city, township, shi (JP) | 
4 | A4 | city division, borough, city district, ward, chou (JP) | 
5 | A5 | neighborhood, block | 
6 | A6 | group of streets below the neighborhood level | 
16 | PRD | leading street direction | N
17 | POD | trailing street suffix | SW
18 | STS | street suffix or type | Ave, Platz
19 | HNO | house number | 123
20 | HNS | house number suffix | A, 1/2
21 | LMK | landmark or vanity address | Columbia University
22 | LOC | additional location information | South Wing
23 | NAM | name (residence and office occupant) | Joe’s Barbershop
24 | ZIP/PC | postal/zip code | 10027-1234
25 |  | building (structure) | Low Library
CAtype | label/ NENA/PIDF | description | examples
26 |  | unit (apartment, suite) | Apt 42
27 | FLR | floor | 4
28 |  | room | 450F
29 |  | type of place | office
30 | PCN | postal community name | Leonia
31 |  | post office box (P.O. Box) | 12345
32 |  | additional code | 13203000003
33 | SEAT | seat (desk, cubicle, workstation) | WS 181
34 |  | primary road name | Broadway
35 |  | road section | 14
36 |  | branch road name | Lane 7
37 |  | sub-branch road name | Alley 8
38 |  | street name pre-modifier | Old
39 |  | street name post-modifier | Service
0 |  | language | 
128 |  | script | Latn
255 |  | reserved | 
“NENA” correspond to items from the National Emergency Number Assocation, "NENA Recommended Formats and Protocols For ALI Data Exchange, ALI Response and GIS Mapping", NENA NENA-02-010, January 2002.
“PIDF” indicates the element name from Peterson, J., "A Presence-based GEOPRIV Location Object Format", RFC 4119, December 2005.
This document specifies a Dynamic Host Configuration Protocol (DHCPv4 and DHCPv6) option containing the civic location of the client or the DHCP server.
  Civic information is useful since it often provides additional, human-usable information, particularly within buildings.

## Slide 20: Current AAI Complex datatype
Name | Required | Type | Constraints | Description
physical-location-id | no | string | key | Unique identifier for physical location, e.g., CLLI
data-center-code | no | string |  | Data center code which can be an alternate way to identify a complex
complex-name | no | string |  | Gamma complex name for LCP instance.
identity-url | no | string |  | URL of the keystone identity service
resource-version | no | string |  | Used for optimistic concurrency. Must be empty on create, valid on update and delete.
physical-location-type | no | string |  | Type, e.g., central office, data center.
street1 | no | string |  | 
street2 | no | string |  | 
city | no | string |  | 
state | no | string |  | 
postal-code | no | string |  | 
country | no | string |  | 
region | no | string |  | 
latitude | no | string |  | 
longitude | no | string |  | 
elevation | no | string |  | 
lata | no | string |  | 
tns:ctag-pools |  |  |  | 
tns:relationship-list |  |  |  | 
Description: Collection of physical locations that can house cloud-regions.

## Slide 21: ETSI SOL001 PNFD LocationInfo vs. AAI Complex (1/3)
ETSI SOL001 PNFD LocationInfo | description | AAI Complex | Handling
country_code | Shall be a two-letter ISO 3166 [10] country code in capital letters. | country | Convert from ISO 3166 code to string?
civic_address_element.ca_value, where ca_type=1 | national subdivisions (state, canton, region, province, prefecture) | state | Copy from PNFD
civic_address_element.ca_value, where ca_type=2 | county, parish, gun (JP), district (IN) | region | Copy from PNFD
civic_address_element.ca_value, where ca_type=3 | city, township, shi (JP) | city | Copy from PNFD
civic_address_element.ca_value, where ca_type=4 | city division, borough, city district, ward, chou (JP) | - | Add to AAI? Or include in ”city”?
civic_address_element.ca_value, where ca_type=5 | neighborhood, block | - | Add to AAI? Or include in ”city”?
civic_address_element.ca_value, where ca_type=6 | group of streets below the neighborhood level | - | Add to AAI? Or include in ”city”?
civic_address_element.ca_value, where ca_type=16 | leading street direction | street1/street2 | Need to define in which order to copy fields from PNFD
civic_address_element.ca_value, where ca_type=17 | trailing street suffix | street1/street2 | Need to define in which order to copy fields from PNFD
civic_address_element.ca_value, where ca_type=18 | street suffix or type | street1/street2 | Need to define in which order to copy fields from PNFD
civic_address_element.ca_value, where ca_type=19 | house number | street1/street2 | Need to define in which order to copy fields from PNFD
civic_address_element.ca_value, where ca_type=20 | house number suffix | street1/street2 | Need to define in which order to copy fields from PNFD
civic_address_element.ca_value, where ca_type=21 | landmark or vanity address | street1/street2 | Need to define in which order to copy fields from PNFD
civic_address_element.ca_value, where ca_type=22 | additional location information | - | ?
civic_address_element.ca_value, where ca_type=23 | name (residence and office occupant) | - | New for PNFs, add to AAI?
civic_address_element.ca_value, where ca_type=24 | postal/zip code | postal-code | Copy from PNFD
civic_address_element.ca_value, where ca_type=25 | building (structure) | street1/street2 | Need to define in which order to copy fields from PNFD
Cont…

## Slide 22: ETSI SOL001 PNFD LocationInfo vs. AAI Complex (2/3)
ETSI SOL001 PNFD LocationInfo | description | AAI Complex | Handling
civic_address_element.ca_value, where ca_type=26 | unit (apartment, suite) | - | New for PNFs, add to AAI?
civic_address_element.ca_value, where ca_type=27 | floor | - | New for PNFs, add to AAI?
civic_address_element.ca_value, where ca_type=28 | room | - | New for PNFs, add to AAI?
civic_address_element.ca_value, where ca_type=29 | type of place | physical-location-type | Copy from PNFD
civic_address_element.ca_value, where ca_type=30 | postal community name | - | Add to AAI? Or include in ”city”?
civic_address_element.ca_value, where ca_type=31 | post office box (P.O. Box) | - | ?
civic_address_element.ca_value, where ca_type=32 | additional code | - | ?
civic_address_element.ca_value, where ca_type=33 | seat (desk, cubicle, workstation) | - | New for PNFs, add to AAI?
civic_address_element.ca_value, where ca_type=34 | primary road name | street1/street2 | Need to define in which order to copy fields from PNFD
civic_address_element.ca_value, where ca_type=35 | road section | street1/street2 | Need to define in which order to copy fields from PNFD
civic_address_element.ca_value, where ca_type=36 | branch road name | street1/street2 | Need to define in which order to copy fields from PNFD
civic_address_element.ca_value, where ca_type=37 | sub-branch road name | street1/street2 | Need to define in which order to copy fields from PNFD
civic_address_element.ca_value, where ca_type=38 | street name pre-modifier | street1/street2 | Need to define in which order to copy fields from PNFD
civic_address_element.ca_value, where ca_type=39 | street name post-modifier | street1/street2 | Need to define in which order to copy fields from PNFD
civic_address_element.ca_value, where ca_type=0 | language | N/A | How does AAI support multiple languages?
civic_address_element.ca_value, where ca_type=128 | script | N/A | How does AAI support multiple scripts?
civic_address_element.ca_value, where ca_type=255 | reserved | N/A | 
Cont…

## Slide 23: ETSI SOL001 PNFD LocationInfo vs. AAI Complex (3/3)
ETSI SOL001 PNFD LocationInfo | AAI Complex | description | Handling
- | physical-location-id | Unique identifier for physical location, e.g., CLLI | Generate witin ONAP
- | data-center-code | Data center code which can be an alternate way to identify a complex | ?
- | complex-name | Gamma complex name for LCP instance. | ?
- | identity-url | URL of the keystone identity service | ?
- | resource-version | Used for optimistic concurrency. Must be empty on create, valid on update and delete. | Generate witin ONAP
- | latitude |  | Geospatial coordinates not included in ETSI PNFD, needs to be added? (See RFC3825)
- | longitude |  | Geospatial coordinates not included in ETSI PNFD, needs to be added? (See RFC3825)
- | elevation |  | Geospatial coordinates not included in ETSI PNFD, needs to be added? (See RFC3825)
- | lata | Local access and transport area | Specific to USA (Canadian equivalent is Local interconnection region, LIR. Unclear what equivalents exist in other countries/areas.)

## Slide 25: Background slides

## Slide 26: ONAP R3 SDC AID data model: Resource Category/Subcategory
Resource category & subcategory are local to SDC and managed through SDC UI
  Used as grouping for resources in several places in SDC UI
  Default values hardcoded, see: https://wiki.onap.org/display/DW/Categories+to+use+in+SDC+project
Category | Sub Category
Network L2-3 | LAN Connectors WAN Connectors Router Gateway Infrastructure
Network L4+ | Common Network Resources
Application L4+ | Border Element Database Application Server Web Server Call Control Media Servers Load Balancer Firewall
Generic | Infrastructure Database Abstract Rules Network Elements
Network Connectivity | Connection Points Virtual Links
DCAE Component | Analytics Policy Utility Collector Source Microservice Database
Template | Monitoring Template
Allotted Resource | Tunnel XConnect IP Mux Demux Allotted Resource Security Zone Contrail Route Service Admin
Notes: Ref: https://wiki.onap.org/display/DW/ONAP+SDC+AID+Data+Model
Ref: https://wiki.onap.org/display/DW/Composition+%28Service+design%29+tab

## Slide 27: AAI Complex datatype (raw info)
<xs:element name="complex">
<xs:complexType>
<xs:annotation>
<xs:appinfo>
<annox:annotate target="class">description="Collection of physical locations that can house cloud-regions.",indexedProps="identity-url,data-center-code,complex-name,physical-location-id",searchable="physical-location-id,data-center-code,complex-name,street1,street2,postal-code",uniqueProps="physical-location-id",container="complexes",namespace="cloud-infrastructure",uriTemplate="/cloud-infrastructure/complexes/complex/{physical-location-id}",requiredProps="physical-location-id,physical-location-type,street1,city,postal-code,country,region")</annox:annotate>
</xs:appinfo>
</xs:annotation>
<xs:sequence>
<xs:element name="physical-location-id" type="xs:string" minOccurs="0">
<xs:annotation>
<xs:appinfo>
<annox:annotate target="field">isKey=true,description="Unique identifier for physical location, e.g., CLLI")</annox:annotate>
</xs:appinfo>
</xs:annotation>
</xs:element>
<xs:element name="data-center-code" type="xs:string" minOccurs="0">
<xs:annotation>
<xs:appinfo>
<annox:annotate target="field">description="Data center code which can be an alternate way to identify a complex")</annox:annotate>
</xs:appinfo>
</xs:annotation>
</xs:element>
<xs:element name="complex-name" type="xs:string" minOccurs="0">
<xs:annotation>
<xs:appinfo>
<annox:annotate target="field">description="Gamma complex name for LCP instance.")</annox:annotate>
</xs:appinfo>
</xs:annotation>
</xs:element>
<xs:element name="identity-url" type="xs:string" minOccurs="0">
<xs:annotation>
<xs:appinfo>
<annox:annotate target="field">description="URL of the keystone identity service")</annox:annotate>
</xs:appinfo>
</xs:annotation>
</xs:element>
<xs:element name="resource-version" type="xs:string" minOccurs="0">
<xs:annotation>
<xs:appinfo>
<annox:annotate target="field">description="Used for optimistic concurrency. Must be empty on create, valid on update and delete.")</annox:annotate>
</xs:appinfo>
</xs:annotation>
</xs:element>
<xs:element name="physical-location-type" type="xs:string" minOccurs="0">
<xs:annotation>
<xs:appinfo>
<annox:annotate target="field">description="Type, e.g., central office, data center.")</annox:annotate>
</xs:appinfo>
</xs:annotation>
</xs:element>
<xs:element name="street1" type="xs:string" minOccurs="0"/>
<xs:element name="street2" type="xs:string" minOccurs="0"/>
<xs:element name="city" type="xs:string" minOccurs="0"/>
<xs:element name="state" type="xs:string" minOccurs="0"/>
<xs:element name="postal-code" type="xs:string" minOccurs="0"/>
<xs:element name="country" type="xs:string" minOccurs="0"/>
<xs:element name="region" type="xs:string" minOccurs="0"/>
<xs:element name="latitude" type="xs:string" minOccurs="0"/>
<xs:element name="longitude" type="xs:string" minOccurs="0"/>
<xs:element name="elevation" type="xs:string" minOccurs="0"/>
<xs:element name="lata" type="xs:string" minOccurs="0"/>
<xs:element ref="tns:ctag-pools" minOccurs="0"/>
<xs:element ref="tns:relationship-list" minOccurs="0"/>
</xs:sequence>
</xs:complexType>
</xs:element>

## Slide 28: AAI Complex example values (raw info)
AAI Complex:
"physical-location-id": "clli2",
"data-center-code": "example-data-center-code-val-6667",
"complex-name": "clli2",
"identity-url": "example-identity-url-val-28399",
"physical-location-type": "example-physical-location-type-val-28399",
"street1": "example-street1-700MountainAvenue",
"street2": "example-street2-GlenSideRoad",
"city": "example-city-MurrayHill",
"state": "example-state-NewJersey",
"postal-code": "example-postal-code-07974",
"country": "example-country-UnitedStates",
"region": "example-region-val-28399",
"latitude": "111.1",
"longitude": "234.2",
"elevation": "example-elevation-538feet",
"lata": "example-lata-val-28399"

## Slide 29: onap.datatypes.ProviderDetails (from TPDM)
onap.datatypes.ProviderDetails:
description: |
Information provided in the onboarding model which is static and the same for every instance created from the descriptor's internal model.
derived_from: tosca.datatypes.Root
properties:
descriptor_id:
type: string # GUID
description: Globally unique identifier of the descriptor
descriptor_version:
type: string
description: Identifies the version of the descriptor
provider:
type: string
description: Provider of the asset and its descriptor
product_invariant_id:
type: string # UUID
description: a universally unique identifier that is the same across all versions of the descriptor for this asset
product_name:
type: string
description: Short name for the Product
software_version:
type: string
description: Software version of the asset
required: false
product_info_name:
type: string
description: Human readable name for the Product
required: false
product_info_description:
type: string
description: Human readable description of the Product
required: false
Notes: Ref: https://wiki.onap.org/display/DW/TIDM+onap.datatypes.ProviderInfo

## Slide 30: Example PNFD generated by SDC
tosca_definitions_version: tosca_simple_yaml_1_1
metadata:
invariantUUID: 999c43a1-23eb-46f0-9945-4666f27eeaf3
UUID: ec336fb8-f6c3-4de0-99ad-ea72c5702803
name: test
description:
type: PNF
category: Application L4+
subcategory: Application Server
resourceVendor: '123445'
resourceVendorRelease: '12344'
resourceVendorModelNumber: ''
imports:
- nodes:
file: nodes.yml #Mix of TOSCA normative types and OPEN ECOM types
- datatypes:
file: data.yml
- capabilities:
file: capabilities.yml
- relationships:
file: relationships.yml
- groups:
file: groups.yml
- policies:
file: policies.yml
topology_template:
inputs:
nf_function:
type: string
nf_role:
type: string
nf_type:
type: string
node_templates:
substitution_mappings:
node_type: org.openecomp.resource.abstract.nodes.PNF
pnf_test:
type: org.openecomp.resource.abstract.nodes.PNF
metadata:
invariantUUID: 999c43a1-23eb-46f0-9945-4666f27eeaf3
UUID: ec336fb8-f6c3-4de0-99ad-ea72c5702803
customizationUUID: 710fa64a-ef68-47b6-947d-7a4acb8a1093
version: '0.2'
name: test
description:
type: PNF
category: Application L4+
subcategory: Application Server
resourceVendor: '123445'
resourceVendorRelease: '12344'
resourceVendorModelNumber: ''
properties:
nf_function: { get_input: nf_function }
nf_role: { get_input: nf_role }
nf_type: { get_input: nf_type }
software_versions:
- abc
- def
Notes: Credit to Steve B. (Chapter 8 of ”Basic Onap Descriptor for PNF” study)

## Slide 31: Mapping: ONAP R3 SDC AID DM PNF vs. TPDM NetworkFunction
Current PNF, SDC AID DM | Current PNF, TPDM (onap.nodes.NetworkFunction) | Handling
uuid | provider_details.descriptor_id AND/OR catalog_info.uuid | Duplicated
resourceVendorRelease | provider_details.descriptor_version | Not really equivalent?
resourceVendor | provider_details.provider | Direct copy
name | provider_details.product_name | Direct copy
description | provider_details.product_info_description | Direct copy
invariantUUID | provider_details.product_invariant_id AND/OR catalog_info. invariant_uuid | Duplicated
nf_function | - | Properties within service  assumed not in NF
nf_role | - | Properties within service  assumed not in NF
nf_type | - | Properties within service  assumed not in NF
software_versions | provider_details.software_version | Properties within service  mismatch
- | provider_details.product_info_name | Not present in SDC  How is this used?
customizationUUID | catalog_info.customization_uuid | Direct copy
version | catalog_info.version | Direct copy
type | - | Hardcoded to PNF?  Implicit in node type(?)
category | - | Missing from TPDM?
subcategory | - | Missing from TPDM?
resourceVendorModelNumber | - | Missing from TPDM?
Notes: Ref: https://wiki.onap.org/display/DW/Target+Internal+DM+Reference

## Slide 32: Mapping: SOL001 PNFD vs. TPDM PNFD
Current PNFD, SOL001 | Current PNFD, TPDM (onap.datatypes.ProviderDetails) | Handling
descriptor_id | descriptor_id | Can be copied from PNFD
version | descriptor_version | Can be copied from PNFD
provider | provider | Can be copied from PNFD
name | product_name | Can be copied from PNFD
function_description | product_info_description | Can be copied from PNFD
descriptor_invariant_id | product_invariant_id | Can be copied from PNFD
geographical_location_info | - | Add to TPDM?
- | software_version | Add to SOL001?
- | product_info_name | Add to SOL001? (How is this used?)