## Slide 1: E2E Network Slicing Use Case: Requirements Proposal for Guilin
Participants: CMCC, Wipro, Huawei, AT&T, Amdocs, Verizon, Reliance Jio, Tencent, China Telecom
Authors: Lin Meng (CMCC), Swaminathan S (Wipro), Chuanyu Chen (Huawei), Seshu Kumar (Huawei), Borislav Glozman (Amdocs), Shankar P N (AT&T)
March 2, 2020
Reporters: Swami (Wipro) and Lin Meng (CMCC)

## Slide 2: Content
Overall high-level view of E2E Network Slicing in G release
  Architecture choice
  ONAP external Interfaces
  Network Slice LCM
Requirements for G release
  Overall list of requirements
  High-level details
      RAN sub-net slicing
      Transport sub-net slicing
      Intelligent network slicing

## Slide 3: ONAP-based Slice Management Overall Architecture Choices
NSMF (ONAP)
CSMF (ONAP)
Standard APIs
NSSMF(s)
(ONAP)
xNFs
NSMF (ONAP)
CSMF
NSSMF(s)
(ONAP)
xNFs
NSMF (ONAP)
CSMF
NSSMF(s)
xNFs
NSMF (ONAP)
CSMF (ONAP)
TMF APIs
NSSMF(s)
xNFs
NSMF
CSMF
NSSMF(s)
(ONAP)
xNFs
3rd party component
1
2
3
4
5
3GPP APIs
3GPP APIs
Standard APIs
Standard APIs
Internal call
Internal call
Internal call
Internal call
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
Standard APIs

To Be Done in G release
In F release, only Scenario 4 is implemented. Scenario 1 will be supported in G release and following releases. Subsequently, remaining scenarios 2,3,5 can be easily realized.

## Slide 4: ONAP interface support for all 5 architecture options: High-level view
ONAP
CSMF NB APIs
(From OSS/BSS)
(TM Forum)
NSMF APIs (From CSMF)
(3GPP)
NSSMF APIs
(From NSMF)
(3GPP/ETSI/MEF/IETF)
Notes
The guiding principle is when a Slice Management function is outside ONAP, standard interfaces/APIs to be supported by default. Any customization of such interfaces shall also be supported by ONAP using suitable plug-ins/adaptors.
Communication between Slice Management Functions within ONAP (e.g., CSMF and NSMF) shall use ONAP internal mechanisms such as workflow calls, DMaaP messages, etc. or standard APIs as appropriate. This means, both internal and external interface mechanisms should be supported by the corresponding ONAP module.
  For e.g., SO acting as NSMF should support API call directly from CSMF in ONAP, as well as API trigger from an external CSMF via EXT-API.
Standard 5G NF interfaces
(To 5G NFs)
(3GPP)
NSSMF APIs
(To NSSMF)
(3GPP/ETSI/MEF/IETF/O-RAN)
NB interfaces from ONAP
SB interfaces from ONAP






Frankfurt scope
Guilin scope

## Slide 5: ONAP-based Slice Management - NSI Life Cycle view
Scope for Frankfurt
Ref.: 3GPP TS 28.530
Design and pre-provision: Creation of necessary slice/slice sub-net templates.
Instantiation/Configuration & Activation/Deactivation of NSIs, including instantiation/mapping of its constituent slice sub-nets (RAN, Core and Transport).
Objective: Demonstrate e2e slice design and instantiation, including RAN, core and transport slice sub-net design and instantiation
Additional scope for Guilin (under discussion)
KPI Monitoring is added during the operation phase

## Slide 6: Summary of Requirements (Under Discussion)
Category | Requirement | Content | Priority
Functional requirements | Provide a full E2E Slicing solution involving RAN and Transport NSSMF | Integrate RAN NSSMF implementation within ONAP Align with CCVPN use case team for Transport slicing solution Improvements on top of Frankfurt content | HIGH
 | Intelligent Network Slicing | 5G service KPI Monitoring (Closed Loop) AI based NSI/NSSI selection … | HIGH
 | Service Modification | Customer SLA Requirement changes | MEDIUM
 | Integration with EXT-API to provide the fully e2e flow | EXT-API integration with ETSI/TMF-based APIs | MEDIUM
Modeling | 1:1 mapping between NSI and NSSI | 1:1 mapping between NSI and NSSI in 3GPP Not yet clear of the reason behind this. We’re open to explanation. | LOW

## Slide 7: NSSMF (within ONAP) – Functions and Classification
Function | Description | Classification
NSSI Allocation | Determine if an existing NSSI can be used, or a new one is needed | Optimization
 | Determine resources to be allocated to the NSSI (for a new NSSI) (Some parts such as PCE may be part of Domain Controllers) | Optimization
 | Instantiate/scale up necessary (virtual) resources (using NFVO) | Orchestration
 | Perform necessary (re) configuration (incl. NSSI stitching configs) | Configuration
NSSI (De)Activation | (De) Activate the NSSI resources | Configuration
NSSI Modification | (Virtual) Resource allocation updates | Optimization
 | (Re) Configuration of resources | Configuration
NSSI details exposure | Provide details of NSSI to NSMF, inventory (resources, capabilities) | Orchestration
NSSI Closed Loop | Perform closed loop control actions such as scaling, healing | Orchestration
NSSI De-Allocation | Tear down the NSSI and reclaim resources used | Orchestration
 | Update configurations | Configuration
Notes
The ONAP component mapping to above functions shall be discussed with ArchCom.
Yellow – Not in Guilin scope

## Slide 8: RAN & Transport Sub-net Slicing: Proposal
Scope for Guilin Release
Select RAN NSSI, determine RAN slice sub-net resources and then configure the RAN slice sub-net including:
  Association of xNFs to a Slice sub-net instance
  Allocation of ‘resources’ for a slice sub-net instance
  Configuration of RAN for a slice sub-net instance (including cell configuration such as bandwidth, etc.)
Assumptions
All RAN xNFs are created and pre-configured
*** Runtime Config DB is assumed to contain cell details including PNF mapping, etc.
Southbound interface from SDN-C (R) will be netconf for CM, and VES (in future) for FM/PM. We will try to align with O-RAN where feasible.
Scope for Guilin release
1. Implement TSCi (e.g., create TS definition model)
2. L1 (OTN) and L2 (E-line) service slicing (reuse many existing CCVPN features)
Assumption
Transport slicing solution includes 2 level of abstraction models: Transport Slice Definition Model and Transport Slice Implementation Model.
Approach
We propose IETF-draft based approach for realizing Transport slicing.
RAN Sub-net slicing
Transport Sub-net slicing

## Slide 9: Transport sub-net Slicing: Proposal
Transport Slice Definition Model
E2E NS controller, RAN Slice controller, CORE Slice controller
Optical Domain Controller
Optical Network
TSCi (draft-rokui-5G-transport-slice)
ACTN TE / L0/L1/L2 models
1. Implement TSCi (i.e., create TS definition model)
Transport Slice Implementation Models
2. L1 (OTN) and L2 (E-line) service slicing
NOTE: many existing CCVPN features can be reused.

## Slide 10: Intelligent Network Slicing
Use data (e.g., QoE data, network data, etc. ) from various sources as input and do analysis based on AI algorithms to obtain network capabilities that can match the SLA of tenants, and then dynamically adjust the service capabilities of network slices. It mainly consists of the following three scenarios:
Commissioning-Initial resource Assignment
Determine the initial resource assignment and configuration for a new slice by intelligent analysis based on SLA requirement. For e.g.:
Determine the resources in each domain especially for RAN
Guarantee the existed slices SLA when creating a new slice
Runtime-monitoring
Evaluate the SLA fulfillment and real time monitor QoE based on the QoE model trained by ML algorithms.
The QoE model is used to describe the relationship between the QoE collected from AFs （e.g., service MOS） and the KPIs produced by ONAP or network data from Core NFs.
The QoE model is mainly used in measuring and predicting QoE.
Closed-loop Update
Considering the limited resource and changing condition like the Signal to Noise Ratio and users on the slice, the initial resource configuration may not be able to satisfy the slice SLA during the lifecycle of the slice. ONAP can adjust or update the resource configuration of the slice in a close loop way triggered by the analysis of SLA fulfillment.
SLA fulfillment is evaluated based on the analysis of QoE info and KPIs.
1
2
3
KPI Monitoring for Guilin
QoE Monitoring as stretch goal
Not for Guilin
Simple closed loop control triggered by KPI monitoring for Guilin

## Slide 11
Drive Test Data
(UE level)
PM Data
(NF level)
KPI Data
(NSI/NSSI/S-NSSAI level)
Network Data
(5GC NF level)
E.g.: QoS flow data, UE location, etc.
QoE Model:
QoE evaluation and prediction
SLA Fulfillment Monitoring
OAM Data
Non OAM Data
Application Data
QoE Data
(AF level)
Close loop control
Intelligent analysis assists Slice SLA guarantee
Update Slice Resource Configuration
Data Collection
Data Analysis
Input
Input
Input
Input
Input
Input
Trigger
✅
✅
✅ refers to Guilin Scope
PM Data and Slice KPI monitoring is within scope of Guilin release.

## Slide 12: Business Drivers
Executive Summary
5G Network Slicing is one of the key features of 5G. The essence of Network Slicing is in sharing network resources (PNFs, VNFs, CNFs) while satisfying widely varying and sometimes seemingly contradictory requirements to different customers in an optimal manner. Same network is expected to provide different Quality of Experience to different consumers, use case categories and industry verticals including factory automation, connected home, autonomous vehicles, smart cities, remote healthcare, in-stadium experience and rural broadband. An End-to-End Network Slice consists of RAN, Transport and Core network slice sub-nets. This Use Case intends to demonstrate the modeling, orchestration and assurance of a simple network slice (e.g. eMBB). While 3GPP standards are evolving and 5G RAN and core are being realized, this Use Case will start with realizing an E2E Network Slice with a simple example of a 5G RAN, Core and Transport Network Slice sub-nets. It will also align with relevant standard bodies (e.g., 3GPP, ETSI, TM Forum) as well as other open initiatives such as O-RAN where relevant, w.r.to both interfaces as well as the functional aspects.
Business Impact
Network Slicing is a feature that almost every service provider will leverage. It allows a service provider to improve their network efficiency by maximizing the network throughput more tailored to each user's use of the network. It is seen as an imperative for efficient and optimal use of their network. This will be particularly relevant as 5G is expected to have upwards of 10,000x the traffic load over 4G and 20GB peak data rates.

## Slide 13
Business Markets
Network Slicing, for this use case, is specifically aimed at a simple 5G access, core and transport. In the future, this might be extended to other domains or applications such as fixed wireless convergence, Wi-Fi access, all aspects of transport including fronthaul, or unified network management orchestration. This is the functionality that almost every wireless service provider will find valuable. The concepts and modeling work being done for Network Slicing will find applications in other areas as well. (Industries) Some applications and industries such as smart cities, remote maintenance, video streaming vs life-saving first-responder type applications will demand different requirements from Network slicing. (Markets Regions) There are no regional specific aspects to Network Slicing.
Funding/Financial Impacts
Network slicing engenders the optimal use of resources for a Network. Thus, this represents OPEX savings for a service provider.
Organization Mgmt, Sales Strategies
There is no additional organizational management or sales strategies for this use case outside of a service providers "normal" ONAP deployment and its attendant organizational resources from a service provider.

## Slide 14
Thank You!