## Slide 1
Ben Cheung (Nokia)
Marge Hillis (Nokia)
Shankar N K (AT&T)
Ted Johnson (AT&T)
Claudio Gasparini
Zu Qiang (Ericsson)
Tony Finnerty (Ericsson)
Virtual Developer Design Forum (vDDF) / Oct 15, 2020 / version 12
Toine Siebelink (Ericsson)
Michela Bevilacqua (Ericsson)
Jacqueline Beaulac (Ericsson)
Rishi Chail (Ericsson)
Ciaran Johnston (Ericsson)
Joachim Blixt
Pawel Slowikowski (Samsung)
Swami N (Wipro)
Bruno Sakoto (Bell Canada)
Philippe Leger (Bell Canada)
Aditya Puthuparambil (Bell Canada)
Fred Feisullin (Verizon Wireless)
Configuration Persistence Service in R8+

## Slide 2
R8 DDF Presentation
TIME | AUG 17, 2020 CPS REQUIREMENTS SubComm AGENDA
10 min | Context for CPS & Agenda – Context for CPS & Basic problems to be addressed
10 min | Overview of CPS – Overview to CPS
15 min | Model Driven CPS Proof of Concept (PoC) & Demo – Overview of the Model-Driven CPS PoC for R7
5 min | R8 & Beyond Roadmap – Model Driven Proof of Concept (PoC) in R7, way forward in R8 Honolulu, New plan & roadmap
10 min | Use Cases using CPS Database – Overview of CPS Applications (State Mgmt)
10 min | Questions & Answers – Q&A
TIME | Q&A Session Post-Session
- | Follow-up questions – Follow-up meetings at CPS Team Call (Fridays)

## Slide 3
Context for
Configuration Persistence Service (CPS)
Context

## Slide 4
Configuration Persistence Service in R8
TOPIC | PROBLEM | SOLUTION
Heterogeneous Data Sources | Reconciling Multiple domains, multiple vendors, multiple functions and multiple versions | Model Driven Persistence
Shared Data Access | Expensive IO operations that should be shared rather than duplicated | Share Data access through model ownership
Model Handling | Because of the heterogeneous data sources need streamlined approach to support models without having platform life cycle events. | Model Driven Persistence

## Slide 5
Configuration Persistence Service in R8
Multiple vendors providing equipment / xNF
Several telecom networks one ONAP platform
Evolution of xNF and network standards
ONAP applications and use cases competing for access to the same CM data

## Slide 6
Configuration Persistence Service in R8
Shared data analogy of a teacher sharing knowledge with students

## Slide 7
Configuration Persistence Service in R8
Model ingestion during ONAP design & run time

## Slide 8
Configuration Persistence Service in R8
Model ingestion with C&PS solution (Run-time)

## Slide 9
Configuration Persistence Service in R8
Permission & Ownership of data

## Slide 10
Configuration Persistence Service in R8
ONAP
CPS Project
O1 compliant entity
CPS
xNF Proxy

## Slide 11
Overview for
Configuration Persistence Service (CPS)
Business Case
Architecture S/C
Overview
Technical Flows

## Slide 12
Configuration Persistence Service in R8
Executive Summary - The Configuration Persistence Service (CPS) is a real-time service that is designed to serve as a data repository for Run-time Network Element (configuration) data that needs to be persistent applicable to multiple domain (RAN, Transport, and Core). This was explored as a R7 PoC. Focus on storing run-time DATA RELATED to NETWORK ELEMENT instances. In R8, this is being proposed as a stand-alone project.
Business Impact - The ability for service operators to visualize and manage network element data in a network (PNFs, VNFs, and logical constructs) with ONAP is a critical business function because they are key Life Cycle Management (LCM) and OA&M operations. The project has business impacts to enhance the operation of data-handling within ONAP by providing efficient data layer services.
Business Markets - This project applies to any domain (wireless, transport, optical, and wireline) that ONAP may manage. It is not a market or geographical specific capability. It is expected that scaled ONAP installations such as Edge & Core ONAP deployments will also deploy the database across each installation.
Funding/Financial Impacts - This project represents a large potential Operating Expense (OPEX) savings for operators because of the ability to configure networks saving time and expenses.

## Slide 13
Configuration
Persistence Service
CPS in Architecture Context

## Slide 14
Configuration Persistence Service (CPS)
Active & Available Inventory (A&AI)
Configuration Information
Standards Defined VES Event
Controller
DU/PNF
CU/VNF
Configuration
Persistence
Service
CPS Database
NETWORK ELEMENT DATA
A&AI Sync
Read/Write
CPS Update
2
4
Micro-Services & Use Cases
Read/Write
Network Element Data
1
3
DU/PNF
CU/VNF

## Slide 15
Configuration Persistence Service (CPS)
A&AI
DCAE
SO
ONAP
RUN-TIME
Service Orchestration
APP-C, SDN-C
Real-Time Inventory
PNF
VNF
VES
Event
DCAE VES
Collector
Standards Defined
VES Event
for Configuration
DCAE Inventory
Controller
DU/PNF
CU/VNF
Micro-Service
PCI, E2ENS, A1P, MD PoC
Configuration
Persistence
Service
SDN-C, VF-C, APP-C
Netconf
O1
PNF
VNF
DU/PNF
CU/VNF
CM Notification
Change Config
A&AI DB
CPS Database
Run-Time Operational Data
Configuration Info
Exo-Inventory Data
State Information
(Yang modeled)
Controller DB
DMaaP
A&AI Sync
Read/Write
CPS Update
Read/Write
Read
Policy DB
SO
U/C DB
Management Framework Data
Network Element Data
Network Element Data
Configuration NameSpace topic
3GPP-Provisioning
1
2
3
4

## Slide 16
Configuration Persistence Service (CPS)
Configuration
Persistence
Service
CPS Database
Run-Time Operational Data
Configuration Info
Exo-Inventory Data
State Information
Network Element Data
RAN
CORE
TRANSPORT
UPF
SMF
UDM
AUSF
AMF
DU
CU
RU
UE
Hub
GUI
Model Driven PoC
OOF SON PCI
E2E Network
Slicing
A1 Adaptor
Extension
State
Management
Network Element Data
Application Parameters
Configuration Parameters
U/C Data
GUI Access
ONAP Micro-services, POCs & Use Cases
NB Open API
Router
Switch
CPS Update
1
4

## Slide 17
CPS READING: PNF Reports Configuration
DCAE
ONAP
RUN-TIME
Analytics
PNF
VNF
VES
Event
DCAE VES
Collector
DCAE Inventory
DU/PNF
CU/VNF
Configuration
Persistence Service
CPS Database
Run-Time Operational Data
Configuration Info
Exo-Inventory Data
RT Logical & Physical Connections
DMaaP
The PNF has a parameter update
to report. The update originates from the PNF and is reported through a Standards Defined VES event with a configuration NameSpace (3GPP-Provisioning)
Standards Defined VES Event is received by the DCAE VES Collector. DCAE publishes the VES Event onto the DMaaP Bus.
In R8+: CPS as a stand-alone component, subscribes to the DMaaP Topic and gets the DMaaP event from the DMaaP bus to update the internal database. The VES event has a Configuration namespace topic, 3GPP-Provisioning
Standards Defined
VES Event
for Configuration
Configuration NameSpace topic
3GPP-Provisioning
CPS Update
1

## Slide 18
A&AI Synchronization
A&AI
ONAP
RUN-TIME
Inventory, Listener
Configuration
Persistence
Service
A&AI DB
CPS Database
Run-Time Operational Data
Configuration Info
Exo-Inventory Data
RT Logical & Physical Connections
DMaaP
(1) During Network setup “getall” retrieves from A&AI the ENTIRE A&AI graph. Used to setup the initial view of CPS
(2) Updates additions/deletions of xNFs. “AAI-Event” (operation
Addition / delete)
In R8+: CPSDB is a stand-alone component. Performs “getall” A&AI update and atomic A&AI update. Atomic “updates” from A&AI add/remove of xNF is published by A&AI as an update on DMaaP bus
A&AI Sync
3

## Slide 19
CPS WRITING: Micro Service Update
ONAP
RUN-TIME
Micro Service
OOF/SON/PCI
Configuration
Persistence
Service
CPS Database
Run-Time Operational Data
Configuration Info
Exo-Inventory Data
RT Logical & Physical Connections
DMaaP
Read/(Write)
A Micro-Service, for example OOF/SON/PCI determines that an update is needed to CPSDB from operation/algorithm. It publishes to the DMaaP bus an update event.
In R8+: CPSDB is a stand-alone component. CPSDB subscribes to the DMaaP topic and gets the DMaaP event off the DMaaP bus to update itself.
4

## Slide 20
CPS WRITING: From Controller SDN-C
ONAP
RUN-TIME
APP-C, SDN-C
Controller
Configuration
Persistence
Service
SDN-C, VF-C, APP-C
Netconf
O1
PNF
VNF
DU/PNF
CU/VNF
CM Notification
Change Config
CPS Database
Run-Time Operational Data
Configuration Info
Exo-Inventory Data
RT Logical & Physical Connections
Controller DB
DMaaP
Read/Write
SO, Policy, or Control Loop has determined a parameter update is needed to the xNF. The Controller (SDN-C) eventually gets the configuration update. SDN-C publishes to the DMaaP bus a configuration update event.
R8+ The configuration & standards service as a stand-alone component subscribes to the DMaaP topic and gets the DMaaP event off the DMaaP bus to update the internal database. A configuration namespace topic is used, 3GPP-Provisioning
The Controller (SDN-C) also sends a message to the xNF to update the parameter. This may be done via NetConf/O1/Ansible
A
Controller (SDN-C) gets an ACK back from the xNF that the parameter change was successful.
B
C
E
xNF would may send a Standards Defined VES unless xNF configured to suppress event on ONAP origination
D
Configuration NameSpace topic
3GPP-Provisioning
2

## Slide 21
A&AI
CPS
Run-Time Operational Data
Configuration Info
Exo-Inventory Data
RT Connections
Network Element Data
Real-time Inventory
Network Topology
A&AI vs CPS
Network Element Objects
Concepts – A&AI conceptually stores Real-time inventory view of connected and “topology” of xNFs that ONAP sees. CPS stores Network Element Data. A&AI and CPS overlaps because they both need to know about Network Element objects so that can managed & orchestrated.
PNF
VNF
PNF
VNF
CPS Records

## Slide 22
R7 Model Driven Proof of Concept for
Configuration Persistence Service (CPS)
Proof of Concept

## Slide 23
R7 Model Driven CPS PoC
Demonstrate write/read operations for YANG data fragments using CPS and store them in a DB with a very simple generic schema
Demonstrate ability to deploy / upgrade YANG models at run-time
Demonstrate CPS behavior driven by YANG model
Provide architecture vision and roadmap for a target architecture, supported use cases, non-functional requirements towards an ONAP Project
Proof Points for PoC
Notes: PoC, so what do we want to proof….

## Slide 24
R7 Model Driven CPS PoC
Configuration Persistence Service
DCAE
DMaaP
SDC
DMaaP
A&AI
CSAR
StndDef
VES ++
3GPP-Configuration
(NameSpace)
Update
OOF/SON/PCI
E2E Network Slicing
A1 Extension, policies
CRUD
DBMS
Use case
Component
Work required
PNF
A&AI information
to uniquely identify a xNF
Mirroring
xNF Configuration Data
Model Driven
Schema
Synchronization
Service
Provider
Interface
CPS API
1
3
2
4
5
Temporal DB
R7: A&AI Stretch Goal
R7: Temporal DB Stretch
R7: Read/Write Data
(Base Scope)
R7: Select YANG model
(Stretch Goal)
R7: Model Deployed
(Base Scope)
Notes: Scope of CPS, interaction with other components like SDC, DmaaP
Use cases it can eventually support Like synhcronization with A&AI

## Slide 25
R7 Model Driven CPS PoC
Configuration Persistence Service
DCAE
DMaaP
SDC
DMaaP
A&AI
CSAR
StndDef
VES ++
3GPP-Configuration
(NameSpace)
Update
OOF/SON/PCI
E2E Network Slicing
A1 Extension, policies
CRUD
DBMS
PNF
A&AI information
to uniquely identify a xNF
Mirroring
xNF Configuration Data
Model Driven
Schema
Synchronization
Service
Provider
Interface
CPS API
1
3
2
4
5
Temporal DB
R7: A&AI Stretch Goal
R7: Temporal DB Stretch
R7: Read/Write Data
(Base Scope)
R7: Select YANG model
(Stretch Goal)
R7: Model Deployed
(Base Scope)
Use case
Component
Work required
Notes: Scope of the PoC or what we have achieved so far
SPI and implementation for datalayer (model driven)
REST API being developed with use cases in mind
Prepared for Upgrade scenario but require some work still

## Slide 26
R7 Model Driven CPS PoC
Weekly ONAP meeting hosted by Ben Cheung (Nokia)
PoC discussed with and approved by TSC
ONAP R8 Honolulu Project proposal accepted
  Use Cases & requirements : Configuration Persistence Service (CPS)
CPS presentations in many fora, O-Ran PlugFest, LFN Design Developer Forum (DDF) etc.
Resourcing
  Ericsson 3 full-time developers
  Bell Canada 3 part-time developers
Jira backlog, team ceremonies like scrums etc. established
  Developers Landing Page
Community Involvement & Resourcing

## Slide 27
R7 Model Driven CPS PoC
Base : N/A (new code) Main dependency : ODL Yang Tools 5.x (probably) https://javadoc.io/doc/org.opendaylight.yangtools
Design and Architecture discussions ongoing https://wiki.onap.org/display/DW/Issues+decisions+and+assumptions
PoC Ways of Working
Notes: Example of how we work on Friday
Major architecture decisions etc.

## Slide 28
R7 Model Driven CPS PoC
Architecture designed & implemented
Pluggable SPI Implementation (DB Layer)
Notes: Architecture in place and demo includes some E2E vertical slice interactions

## Slide 29
R7 Model Driven CPS PoC
PoC being developed on Nordix Branch to avoid impacts on production code in CCSDK Repo
Project structure set up completed
  Following ONAP standards and conventions
  Production code Quality (SonarQube & Checkstyle)
ODL Yang Tools integrated
  Parsing of Yang models
  Parsing of Yang data, JSON or XML with validation for given Yang model
First E2E iteration of 2 use cases completed
  Upload & Validate Yang Model (part of proof point 2)
  Upload JSON Data Object (part of proof point 1
Implementation Status

## Slide 30
R7 Model Driven CPS PoC
REST API Proposal
Notes: Future REST API structure being proposed (still under discussion)

## Slide 31
R7 Model Driven CPS PoC
Generic Schema Design Finalized
Can store any modelled data
Portable, can easily be adapted to any DB technology

## Slide 32: Early Performance Indicators (DB) (proof point 4)
R7 Model Driven CPS PoC
Insert
  450 records/sec (up to 2M records)
Queries
  XPath Query (while loading new data) < 100ms
  Tree-Walk (75K objects) count with condition < 1,000ms
Delete
  Delete Tree of 75K objects incl. constraint checks ~ 6 sec

## Slide 33: Demos
R7 Model Driven CPS PoC
JSON Data
  Upload valid JSON, store in DB
  Handle invalid JSON
Yang Model File (modules)
  Valid model file, store in DB
  Handle invalid model
Split JSON data for given model
  Split into ‘fragments’ ready for generic DB
  Handle model change

## Slide 34
R7 Model Driven CPS PoC
TOPIC | PoC RESULTS
SEED CODE | Seed Code to serve as a basis for CPS has been developed
PROOF POINTS | Create/read CRUD operations using YANG fragments using a simple schema or schema-less repository Deploy & upgrade YANG model fragments at run-time Validate based on YANG Constraints Provide architecture vision and roadmap for a target architecture.
ARCHITECTURE AGREEMENTS | Resolve key architectural Issues necessary for CPS as a stand-alone project
CPS CORE FUNCTIONALITY | Can demonstrate some key CPS operations; basic E2E & integration of Yang parser
PERFORMANCE LIMITS | Early performance indicators tested using generic schema with json-blob storage for attributes

## Slide 35
Roadmap for
Configuration Persistence Service (CPS)
Roadmap

## Slide 36
CPS Roadmap & R6-R8 Plan
Configuration Persistence Service (CPS) Roadmap –
CPS 1.1
R6 CPS Extensions
Evolution of CC-SDK/SDN-C solution REQ322
Supporting R7 Use Cases:
SON/OOF/PCI U/C
5G E2E Network Slicing
A1 Policy extension (Ericsson)
Model-Driven PoC
Write “base” CPS
Write NE Data
Read NE Data
Access Control
State Management PoC
State Management PoC (BellCA) self-contained
CPS 2.0
R8 CPS stand-alone project proposal
Deprecate CPS 1.0 & 1.1
Project proposals TSC/Architecture S/C
Setup Project Repo
CPS FUNCTIONALITY:
Data Recovery
Model Adaption (Dynamic Schema)
R6 Frankfurt
R7 Guilin
R8 Honolulu
June 5, 2020
December, 2020
June 2021
CPS 1.0
R6 CPS
CC-SDK/SDN-C solution
Evolution of “ConfigDB”
Supporting R6 Use Cases:
SON/OOF/PCI U/C
Legend:
RED text is CC-SDK/SDN-C solution
BLUE text is the PoC & stand-alone project

## Slide 37
CPS Roadmap & R8-R10 Plan
Configuration Persistence Service (CPS) Roadmap –
CPS 2.0
R8 CPS stand-alone project proposal
Deprecate CPS 1.0 & 1.1
Project proposals TSC/Architecture S/C
Setup Project Repo
CPS FUNCTIONALITY:
Data Recovery
Model Adaption (Dynamic Schema)
R8 Honolulu
R9 Istanbul
R10 Kyoto
June 2021
December 2021
June 2021
Legend:
RED text is CC-SDK/SDN-C solution
BLUE text is the PoC & stand-alone project
Rx (future) development
CPS FUNCTIONALITY:
Data Auditing Rules Driven
Data History
Roll-Back
Database Backup
Performance Optimization (Scaling)
Rx (future) development
CPS FUNCTIONALITY:
Data Auditing Model driven
Topology Traversal
Data Syncing

## Slide 38
State Management Use Case for
Configuration Persistence Service (CPS) in R8
Use Cases

## Slide 39
State Management PoC (Bell Canada)

## Slide 40
State Management PoC (Bell Canada)

## Slide 41
State Management PoC (Bell Canada)

## Slide 42
State Management PoC (Bell Canada)

## Slide 43
Use Cases for
Configuration Persistence Service (CPS)
Use Cases
Proof of Concept

## Slide 44: CPS Use Cases and Proof of Concepts in R8
5G USE CASE | DESCRIPTION
STATE MANAGEMENT POC | Bell Canada led PoC for State tracking and State management using CPS Integration with CPS (as a platform). Have the State management S/W now work with CPS using available swaggers/APIs
OOF - SON (5G) | Optimization and SON functions for 5G RAN. Self-optimization, Self-Healing, Self-configuration.
NETWORK SLICING (5G Use Case) | Network Slicing defines Slices for 5G RAN systems. Network Slicing is a long-lead (multi-release) development. (will be presented in its own lecture at the Virtual Face to Face)
MOBILITY STANDARDS HARMONIZATION/ A1 adapter | A1 adapter: Enhancing the A1 adapter/interface capabilities in ONAP to manage A1 Policies, support multiple A1 targets in the RAN and multi-version A1 interface for different A1 targets, introduce secure TLS communication.

## Slide 45
OOF / SON / PCI Use Case
DCAE
DCAE
PCI Handler MS
OOF
SDN-C*
Policy
Simulated RAN
~2000 Cells
Nbr_list, PCI values
2
5
6
1b
1c
Config Value
Change Notifn
(Netconf/Yang)
9
1d
1a
8
10
(*SDN-C work done
in SDN-R team)
4b
4a
Config Value Change
11
DMaaP Message
REST API
3a
7
ConfigDB
3b
FM/PM KPIs
SO
4c
DCAE Collector
(VES)
DCAE Database
FM/PM
1e
4d
PCI enhancements
ANR function
FM/PM Collector and Database
FM/PM Data
Query to allocate PCI for new cell (optional)

## Slide 46
OOF / SON / PCI Use Case

## Slide 47
End to End Network Slicing Use Case
3rd party component
1
2
3
4
5
NSMF (ONAP)
CSMF (ONAP)
Standard APIs
NSSMF(s)
(ONAP)
xNFs
NSMF (ONAP)
CSMF
NSSMF(s)
(ONAP)
xNFs
NSMF (ONAP)
CSMF
NSSMF(s)
xNFs
NSMF (ONAP)
CSMF (ONAP)
TMF APIs
NSSMF(s)
xNFs
NSMF
CSMF
NSSMF(s)
(ONAP)
xNFs
3GPP APIs
3GPP APIs
Standard APIs
Standard APIs
Internal call
Internal call
Internal call
Internal call
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
OSS/BSS/Apps
Standard APIs

## Slide 48
End to End Network Slicing Use Case
NetworkSlice | Network Slice NRM | operationalState
NetworkSlice | Network Slice NRM | administrativeState
NetworkSlice | Network Slice NRM | serviceProfileList
NetworkSlice | Network Slice NRM | networkSliceSubnetRef
NetworkSliceSubnet | Network Slice NRM | operationalState
NetworkSliceSubnet | Network Slice NRM | administrativeState
NetworkSliceSubnet | Network Slice NRM | nsInfo
NetworkSliceSubnet | Network Slice NRM | sliceProfileList
NetworkSliceSubnet | Network Slice NRM | managedFunctionRef
NetworkSliceSubnet | Network Slice NRM | networkSliceSubnetRef
ServiceProfile | Network Slice NRM | serviceProfileId
ServiceProfile | Network Slice NRM | sNSSAIList
ServiceProfile | Network Slice NRM | pLMNIdList
ServiceProfile | Network Slice NRM | perfReq
ServiceProfile | Network Slice NRM | maxNumberofUEs
ServiceProfile | Network Slice NRM | coverageAreaTAList
ServiceProfile | Network Slice NRM | latency
ServiceProfile | Network Slice NRM | uEMobilityLevel
ServiceProfile | Network Slice NRM | resourceSharingLevel
ServiceProfile | Network Slice NRM | sST
ServiceProfile | Network Slice NRM | availability
SliceProfile | Network Slice NRM | sliceProfileId
SliceProfile | Network Slice NRM | sNSSAIList
SliceProfile | Network Slice NRM | pLMNIdList
SliceProfile | Network Slice NRM | perfReq
SliceProfile | Network Slice NRM | maxNumberofUEs
SliceProfile | Network Slice NRM | coverageAreaTAList
SliceProfile | Network Slice NRM | latency
SliceProfile | Network Slice NRM | uEMobilityLevel
SliceProfile | Network Slice NRM | resourceSharingLevel

## Slide 49
A1 Policy Extension ORAN-ONAP Harmonize
Executive Summary - This requirement enhances the A1 adapter/interface capabilities provided in Rel 6 as part of 5G/ORAN & 3GPP Standards Harmonization requirement ( REQ-38). O-RAN has defined A1 interface specification in the context of the management of 5G RAN elements to provide intent based policies for optimization of the RAN network performance. Planned enhancements for Rel 7 include additional support for managing A1 Policies, multiple A1 targets in the RAN, multi-version support for different A1 targets, and secure TLS communication.

## Slide 50
Appendix
Benjamin Cheung

## Slide 51
Access, Syncing, Indexing Runtime Config DB
ACCESS TO CPS Database (READ/WRITE):
READ ONLY - Run-Time parameters can be READ by any ONAP platform component and any ONAP plug-in. Examples of ONAP platform components are A&AI, SDC, SDNC etc.
READ/WRITE - Parameters can be READ/WRITE from Controllers, DCAE (future), VES Collector/DMaaP, A&AI, Policy/CLAMP (future) and other components with permission settings.
DEFAULT - SO (future), DCAE, A&AI (indirectly), Controllers (CDS, APPC, SDNC) will have default read/write access to CPS Database
DEFINABLE - Other components will have default read-only access to Configuration Persistence Service but can be given Read/Write access on a per record basis.
SYNCING NEW xNF ADDED or DELETED (A&AI):
ELEMENT SYNC - Software keeps the A&AI elements with the elements in the RunTime Config DB in Sync. When the network first being established, a GetAllPNFs function from A&AI can be used on startup.
A&AI - A&AI is still the master of valid entities in the network and provides a dynamic view of the assets (xNFs) available to ONAP
CPS Database - The CPS Database is a master of the associate (exo-inventory) data associated with the entities.
DYNAMIC VIEW - When a xNF appears or is removed from the system, CPS Database records will be added/removed based on A&AI entries.
LOGIC - When a xNF appears is removed there is logic to determine how and when something is to be updated. There is some intelligence to know what elements of update.
INDEXING:
INDEXING - Data Records will be indexed by xNF (VNF, PNF, ANF). It would be an objective to have a similar indexing mechanism as A&AI. May also need an index to be a logical object ID.
RETRIEVAL - How are data records retrieved efficiently. This relates how the records are indexed.

## Slide 52
CPS
Database
SCOPE
DEPENDENCIES – need to operate
SDC Yang Model (to load schema)
ability to process & translate yang models into schemas
AAF (intra-ONAP security)
Database implementation for Data Persistence
(for example MariaDB)
DEPENDENCIES – value added
DMaaP (some use cases to work / indirect dependency)
Dependencies vs Scope
RECEIVE INFORMATION
WRITE INFORMATION
PUBLISH CHANGES
REFERENTIAL INTEGRITY
INGEST PACKAGES
LOGICAL OBJECTS
ASSOCIATIONS
CARDINALITY RULES
LINKING RESTRICTIONS
SYNCHRONIZATION
DATA INTEGRITY & RECOVERY

## Slide 53
RunTimeDB
RECORD ELEMENT
Temperature = 98
- Source of Truth,
- “Access”,
- TAG = xNF association,
Platform ONAP
(App-C, ms#10105)
(for PNF #106)
or Flex-Index
DCAE
Analytics
PNF
VES
Event
DCAE VES
Collector
APP-C, SDN-C
Controller
SDN-R, VF-C, APP-C
Read/Write
Other Module
OOF/SON/PCI
Read
PNF #106
PNF #106
Configuration Persistence Service (Run-Time)

## Slide 54
CPS DB
PNF #101
A&AI
PNF #102
PNF #103
PNF #104
PNF #101
PNF #102
PNF #103
PNF #104
PNF #101
PNF #102
PNF #103
PNF #104
A&AI correlated/Index to RunTimeDB
Publish changes in A&AI, notification on DMaaP
Indices into Configuration Persistence Service may also use Flex-Index (such as CellID)

## Slide 55
CPS Database
PNF #106
Cell #1 – Logical Object
Cell #2
Cell #3
RECORD ELEMENT
INDEX = PNF #106
Parameter #1
Parameter #2
Parameter #3
Logical object, Cell #1
Cell Parameter #1
Cell Parameter #2
Cell Parameter #3
RECORD ELEMENT
INDEX = Logical Object #111
Parameter #1
Parameter #2
Parameter #3
State Info
Associations
{ PNF #106 }
Cardinality Rules
Linking Restrictions
RECORD ELEMENT
INDEX = PNF #106
Parameter #1
Parameter #2
Parameter #3
State Info X.733
Associations
{ Logical Object #111 Cell #2 }
Cardinality Rules
Linking Restrictions
CPS Database (Run-Time View)

## Slide 56
CPS Information Model Design R7
0= Optional
1=Take Model “As Is”

## Slide 57
CPS Information Model Design R8