## Slide 1: BBS-Broadband Service Use case proposal for Dublin release Contributors: Swisscom, Huawei, Nokia, others are welcome

## Slide 2: Summary: BBS (Broadband Service) Use case Proposal for the Dublin release
Swisscom, Huawei, and Nokia would like to propose the “BBS use case” as a collaboration use case project for the Dublin release
The use case proposes using ONAP for the design, provisioning, lifecycle management and assurance of broadband services.
In a first step, multi-Gigabit Internet Connectivity services based on PON (Passive Optical Network) access technology will be considered.
It covers new scenarios, such as nomadic ONT and subscription plan changes.
It leverages on BBF (Broadband Forum) specifications*.
This use case shows the extensibility of the ONAP platform in supporting the orchestration of Services in many different technology Domains. We believe that this use case will cover several different ONAP components and may also introduce some new platform capabilities:
  A. Nomadic ONT devices
    PNF (Re-)Registration
    Service reconfiguration / service continuity
  B. Subscription plan change
    External API
  C. Data Collection, Analytics and Close-Loop
    Including custom Data collectors and Analytics Microservices
Metro A
Metro B
RG/ONT
CO X
CO Y
Backbone
BNG1
BNG2
Internet
Internet peering
Other services
1
RG/ONT
2
Gigabit Broadband Internet Access Service
3
PNF
PNF
ONAP provisions Broadband Internet Access Service
Customer moves to a new location without notifying the service provider
ONAP re-registers ONT (PNF) in a new location and re-provisions/reconfigures customer service
Nomadic ONT
Subscription plan change
Metro A
Metro B
CO X
CO Y
Backbone
BNG1
BNG2
Internet
Internet peering
Other services
1
RG/ONT
2
Gigabit Broadband Internet Access Service
3
PNF
4
Gigabit Broadband Internet Access Service
ONAP provisions 1Gbps Broadband Internet Access Service
Customer upgrades subscription plan to 10Gbps using customer portal
BSS requests ONAP to change the service for a given customer
ONAP reconfigures customer service to 10Gbps
(*) https://wiki.broadband-forum.org/pages/viewpage.action?pageId=52265462

## Slide 3: ONAP BBS. E2E CFS Onboarding & Service Design
Discovery

## Slide 4: ONAP BBS. CFS Service Ordering and Provisioning
Customer orders HSIA
using customer portal
1
CFS HSIA in SDC catalog
0
2
CFS ready
3
ONAP creates CFS and waits for ONT registration
HSIA
CFS HSIA provisioned
5
6
BSS sends CFS order request
4
ONAP orchestrates CFS

## Slide 5: ONAP BBS. Nomadic ONT and Service Reconfiguration
Customer moved
3
ONAP creates CFS and waits for ONT registration
CFS HSIA provisioned
5
6
4
HSIA
Detect ONT move
HSIA
1
Customer moves to new location and plugs CPE
2
3
Service reconfiguration
Service
Re-provisioned
4

## Slide 6: ONAP BBS. HSIA Service Subscription Plan Change
Customer orders bandwidth upgrade
using customer portal
1
2
Order ready
HSIA 1Gbps
CFS HSIA upgraded
4
5
BSS sends CFS modification request
3
ONAP updates RFS Internet Access
HSIA 10Gbps

## Slide 7
Thank you!
Use case wiki: https://wiki.onap.org/pages/viewpage.action?pageId=45297636
Contact persons:
David Pérez Caparrós <david.perezcaparros@swisscom.com>
Chaker Al Hakim <chaker.al.hakim@huawei.com>
Tim Carey <timothy.carey@nokia.com>