## Slide 1: OSC release A “Amber” OAM / O1/ O-RAN IM PoC/Plugfest
Tracy van Brakle || vanbrakle@att.com || last updated 11 November 2019

## Slide 2: SMO option = ONAP within OSC rel A (note: there are multiple operator-selectable options for SMO)
A1:REST
Service Management and Orchestration Management-Service (MnS)
CCSDK/SDNC - A1 and/or O1
Infrastructure Management Framework
VIM
Near-Real-Time RAN Intelligent Controller (RIC)
Infrastructure COTS / White Box / Peripheral Hardware & Virtualization layer
~NfVi
O1*
E2
O1:NetConf/YANG/CM
E1
O-CU-CP
O-CU-UP
O-RU
Open Fronthaul
F1-c
F1-u
O-DU
VES Collector (FCAPS)
Message bus (e.g DMaaP)
Data Analytics
Portal
Inventory
SO
Policy
Opt
AAF
LOG
O1:REST/VES/CM, FM, others
HV-VES Collector (FCAPS)
ConfigDB
O1:REST/VES/PM
High Velocity VES collector (HV-VES) for real-time event streaming needed for PM.
Standard VES collector for rare events like CM, FM.
O1*: Interface between Service Management and Orchestration Framework and Infrastructure Management Framework supporting O-RAN virtual network functions.
2019-08: will be available later in document “O-RAN Orchestration”.
CDS
nonRT-RIC

## Slide 3: WG1 O1 & WG4 Open FH use cases
Physical Network Function (PNF) Plug and Play (PnP) https://wiki.onap.org/pages/viewpage.action?pageId=40206485
PM Bulk request https://wiki.onap.org/pages/viewpage.action?pageId=40206494
Basic fault
Basic configuration
OOF-based 5G SON
https://wiki.onap.org/pages/viewpage.action?pageId=40206498
WG4 Open FH – Hybrid M-Plane Model
Equipment vendors participating:

## Slide 4: PNF Plug and Play Message flow
Service Management and Orchestration Management-Service (MnS) Consumer
O1:NetConf/YANG/CM
O-RAN PNF (O-DU or O-RU)
VES Collector
Message bus (e.g DMaaP)
Controller (O1)
PNF Registration Handler
Portal
Inventory
SO
Policy
Opt
AAF
LOG
O1:REST/VES/pnfRegistration
ConfigDB
CDS
1
Simplified view
2
3
O-RAN PNF sends VES pnfRegistration – preferred IPv6/TLS
Controller (O1) becomes awareness of the new O-RAN PNF via Message bus
Controller (O1) checks NetConf end-point on the O-RAN PNF (hello-message) – preferred: IPv6/TLS

## Slide 5: PM Bulk request
Service Management and Orchestration Management-Service (MnS) Consumer
O1:SFTP
O-RAN PNF (O-DU or O-RU)
VES Collector
Message bus (e.g DMaaP)
File Collector
Data analytics
Portal
Inventory
SO
Policy
Opt
AAF
LOG
O1:REST/VES/FileReady
ConfigDB
CDS
1
Simplified view
2
3
O-RAN PNF sends VES fileRead – preferred IPv6/TLS
Data analytics triggers the file transfer.
Data analytics requests file transfer – IPv6/TLS/FTPES
O-RAN PNF transfers file and Data analytics processes the file; Format is 3GPP XML (TS 32.435) with gzip compression.
4

## Slide 6: Basic Fault Message flow
Service Management and Orchestration Management-Service (MnS) Consumer
O1:NetConf/YANG/CM
O-RAN PNF (O-DU or O-RU)
VES Collector
Message bus (e.g DMaaP)
Controller (O1)
Data analytics
Portal
Inventory
SO
Policy
Opt
AAF
LOG
O1:REST/VES/fault
ConfigDB
CDS
1
Simplified view
2
O-RAN PNF sends VES fault – preferred IPv6/TLS
Controller (O1) requests configuration data of affected Managed Object Instance.
Controller (O1) requests affected configuration preferred: IPv6/TLS
Controller (O1) receives configuration data
Controller (O1) updates other ONAP components
4
3
5

## Slide 7: Basic Config
Service Management and Orchestration Management-Service (MnS) Consumer
O1:NetConf/YANG/CM
O-RAN PNF (O-DU or O-RU)
VES Collector
Message bus (e.g DMaaP)
Controller (O1)
Data analytics
Portal
Inventory
SO
Policy
Opt
AAF
LOG
O1:REST/VES/configuration
ConfigDB
CDS
3
Simplified view
1
Operator triggers a modification of configuration data on selected O-RAN PNF
Controller (O1) triggers the change via IPv6/TLS(NetConf
O-RAN PNF processes the edit-conf and after successful processing a configuration VES message is send.
Controller (O1) greps the configuration change from Message Bus (DMaaP)
Controller (O1) updates ConfigDB and Portal
2
5
4

## Slide 8: WG4 Open FH – Hybrid Arch

## Slide 9: Timeline
week: 36 | week: 37 | week: 38 | week: 39 | week: 40 | week: 41 | week: 42 | week: 43 | week: 44 | week: 45 | week: 46 | week: 47 | week: 48 | week: 49
Sep-02 | Sep-09 | Sep-16 | Sep-23 | Sep-30 | Oct-07 | Oct-14 | Oct-21 | Oct-28 | Nov-04 | Nov-11 | Nov-18 | Nov-25 | Dec-02
Sep-07 | Sep-14 | Sep-21 | Sep-28 | Oct-05 | Oct-12 | Oct-19 | Oct-26 | Nov-02 | Nov-09 | Nov-16 | Nov-23 | Nov-30 | Dec-07
Readout
PNF setup
recording
Finale SMO/VNF setup
Use case clarifications
Setup Test environment
Running Dev and Test environment
O-RAN-SC/SMO Development
O-RAN-SC/ONAP Tests
O-RAN PNF Development and tests
Integration tests

## Slide 10: OSC release B “Bronze”